## 15A-9.009 Servicing.

(1) The convicted person must present photo identification to the service provider for all required services.

(2) The service provider must:

(a) Provide service at intervals specified in the contract with the department;

(b) Calibrate the ignition interlock device;

(c) Retrieve data from the ignition interlock device data log for the previous period and electronically submit it to the department within 3 days of calibration;

(d) Record the odometer reading of the motor vehicle in which the ignition interlock device is installed; and,

(e) Check for signs of tampering and electronically report to the department any violation within 48 hours of servicing.

(3) All malfunctions of the ignition interlock device will be repaired or the ignition interlock device replaced by the service provider within 48 hours.

(4) A service provider will be available at the service center during specified hours, to answer questions and to deal with any mechanical concerns that may arise with a vehicle as a result of the ignition interlock device.

(5) The ignition interlock device shall record, at a minimum, the following data:

(a) The time and date of each failed breath test;

(b) The time and date of each passed breath test;

(c) The breath alcohol level of each test; and,

(d) The time and date of any attempt to tamper or circumvent the ignition interlock device.

(6) The manufacturer or service provider must maintain a toll-free 24-hour emergency phone service that may be used to request assistance in the event of failure of the ignition interlock device or motor vehicle problems related to operation of the ignition interlock device. The assistance provided by the authorized service provider shall include technical information, tow service, or road service. The ignition interlock device shall be made functional within 48 hours of the call for assistance or the ignition interlock device shall be replaced.

Rulemaking Authority 316.193, 316.1937, 316.1938 FS., Federal Register Vol. 57, No. 67, pages 11772-11787. Law Implemented 316.193, 316.1937, 316.193, 316.1937, 316.1938 FS., Federal Register Vol. 57, No. 67, pages 11772-11787. History–New 10-12-92, Amended 1-20-04.