## 64E-5.1317 Storage and Control of Volatiles and Gases.

(1) A licensee shall store volatile radioactive materials and radioactive gases in the shippers’ radiation shield and container or an equivalent shield and container.

(2) Unless otherwise specified in the license, a licensee shall store and use radioactive volatiles and gases in a properly functioning glove box or fume hood that will maintain airborne concentrations within the limits prescribed by State of Florida Bureau of Radiation Control ALIs, DACs, and Effluent Concentrations, June 2012, (see 64E-5.101, F.A.C.) Table I, Column 2, and Table II, Column 1.

(3) Unless otherwise specified in the license, the glove box or fume hood shall either be directly vented to the atmosphere through an air exhaust or provide for collection and decay or disposal of the volatile or gas.

Rulemaking Authority 404.051, 404.061, 404.071, 404.081 FS. Law Implemented 404.022, 404.051(1), (4), (6), (9), (10), 404.061(2), (3), 404.071(1), 404.081(1) FS. History–New 5-12-93, Amended 1-1-94, Formerly 10D-91.1423, Amended 12-26-13.