## 64E-5.307 Determination of Internal Exposure.

(1) To assess dose used to determine compliance with occupational dose equivalent limits when required as specified in Rule 64E-5.315, F.A.C., the licensee shall take suitable and timely measurements of:

(a) Concentrations of radioactive materials in air in work areas;

(b) Quantities of radionuclides in the body;

(c) Quantities of radionuclides excreted from the body, or

(d) Combinations of these measurements.

(2) Unless respiratory protective equipment is used as specified in Rule 64E-5.319, F.A.C., or the assessment of intake is based on bioassays, the licensee shall assume that an individual inhales radioactive material at the airborne concentration in which the individual is present.

(3) When specific information on the physical and biochemical properties of the radionuclides taken into the body or the behavior of the material in an individual is known, the licensee is permitted to:

(a) Use that information to calculate the committed effective dose equivalent, and, if used, the licensee shall document that information in the individual’s record;

(b) Upon prior approval of the department, adjust the DAC or ALI values to reflect the actual physical and chemical characteristics of airborne radioactive material, for example, aerosol size distribution or density; and,

(c) Separately assess the contribution of fractional intakes of Class D, W, or Y compounds of a given radionuclide to the committed effective dose equivalent. See State of Florida Bureau of Radiation Control ALIs, DACs, and Effluent Concentrations, June 2012.

(4) If the licensee chooses to assess intakes of Class Y material using the measurements given in paragraph 64E-5.307(1)(b) or (c), F.A.C., the licensee can delay the recording and reporting of the assessments for periods up to 7 months, unless otherwise required by Rule 64E-5.344 or 64E-5.345, F.A.C. This delay permits the licensee to make additional measurements basic to the assessments.

(5) If the identity and concentration of each radionuclide in a mixture are known, the fraction of the DAC applicable to the mixture for use in calculating DAC-hours shall be either:

(a) The sum of the ratios of the concentration to the appropriate DAC value, that is D, W, or Y, from State of Florida Bureau of Radiation Control ALIs, DACs, and Effluent Concentrations, June 2012, for each radionuclide in the mixture, or

(b) The ratio of the total concentration for all radionuclides in the mixture to the most restrictive DAC value for any radionuclide in the mixture.

(6) If the identity of each radionuclide in a mixture is known, but the concentration of one or more of the radionuclides in the mixture is not known, the DAC for the mixture shall be the most restrictive DAC of any radionuclide in the mixture.

(7) When a mixture of radionuclides in air exists, a licensee is permitted to disregard certain radionuclides in the mixture if:

(a) The licensee uses the total activity of the mixture in demonstrating compliance with the dose limits in Rule 64E-5.304, F.A.C., and in complying with the monitoring requirements in subsection 64E-5.315(2), F.A.C.;

(b) The concentration of any radionuclide disregarded is less than 10 percent of its DAC; and,

(c) The sum of these percentages for all of the radionuclides disregarded in the mixture does not exceed 30 percent.

(8) When determining the committed effective dose equivalent, the following information can be considered:

(a) To calculate the committed effective dose equivalent, the licensee can assume that the inhalation of one ALI or an exposure of 2,000 DAC-hours results in a committed effective dose equivalent of 5 rem (0.05 sievert) for radionuclides that have their ALIs or DACs based on the committed effective dose equivalent.

(b) For an ALI and the associated DAC determined by the nonstochastic organ dose limit of 50 rem (0.5 sievert), the intake of radionuclides that would result in a committed effective dose equivalent of 5 rem (0.05 sievert), that is, the stochastic ALI, as listed in parentheses in State of Florida Bureau of Radiation Control ALIs, DACs, and Effluent Concentrations, June 2012, (see Rule 64E-5.101, F.A.C.) Table I. The licensee can use the stochastic ALI to determine committed effective dose equivalent as a simplifying assumption. However, if the licensee uses the stochastic ALI, the licensee shall also demonstrate that the limit in subparagraph 64E-5.304(1)(a)2., F.A.C., is met.

Rulemaking Authority 404.051 FS. Law Implemented 404.022, 404.051(1), (4) FS. History–New 1-1-94, Formerly 10D-91.438, Amended 12-26-13.