## 62-296.703 Carbonaceous Fuel Burners.

(1) Applicability. The emission limitations set forth in Rule 62-296.703, F.A.C., shall apply to Carbonaceous Fuel Burning Equipment that has a total heat input capacity of 30 million BTU’s per hour or greater.

(2) Emission Limitations.

(a) Particulate Matter. No owner or operator of Carbonaceous fuel burning equipment shall cause, permit, or allow the emission of particulate matter from such equipment in excess of 0.2 pounds per million BTU heat input of Carbonaceous fuel plus 0.1 pounds per million BTU heat input of fossil fuel.

(b) Visible Emissions. No owner or operator of carbonaceous fuel burning equipment shall cause, permit, or allow visible emissions the density of which is greater than 30 percent opacity.

(3) Test Methods and Procedures. All emissions tests performed pursuant to the requirements of this rule shall comply with the following requirements.

(a) The test method for visible emissions shall be EPA Method 9, as described at 40 C.F.R. Part 60, Appendix A-4, adopted and incorporated by reference at Rule 62-204.800, F.A.C.

(b) The test method for particulate matter emissions shall be EPA Method 5, as described at 40 C.F.R. Part 60, Appendix A-3, adopted and incorporated by reference at Rule 62-204.800, F.A.C. The minimum sample volume shall be 30 dry standard cubic feet. For EPA Method 5, the filter temperature may not exceed 320 degrees Fahrenheit.

(c) Test procedures shall meet all applicable requirements of Chapter 62-297, F.A.C.

Rulemaking Authority 403.061 FS. Law Implemented 403.021, 403.031, 403.061, 403.087 FS. History–Formerly 17-2.650(2)(c)3., 17-296.703, Amended 11-23-94, 1-1-96, 7-10-14.