40C-42.023 Requirements for Issuance.

(1) To receive a general or individual permit under this chapter the applicant must provide reasonable assurance based on plans, test results and other information, that the stormwater management system:

(a) Will not result in discharges from the system to surface and ground water of the state that cause or contribute to violations of state water quality standards as set forth in Chapters 62-3, 62-4, 62-302 and 62-550, F.A.C., including any antidegradation provisions of paragraphs 62-4.242(1)(a) and (b), subsections 62-4.242(2) and (3), and Rule 62-302.300, F.A.C., and any special standards for Outstanding Florida Waters and Outstanding National Resource Waters set forth in subsections 62-4.242(2) and (3), F.A.C.;

(b) Will not adversely affect drainage and flood protection on adjacent or nearby properties not owned or controlled by the applicant;

(c) Will be capable of being effectively operated and maintained pursuant to the requirements of this chapter; and

(d) Meets any applicable basin criteria contained in subsections 40C-41.063(7) and (8), F.A.C.

(2)(a) A showing by the applicant that the stormwater management system complies with the applicable criteria in Rules 40C-42.024, 40C-42.025, 40C-42.026, and 40C-42.0265, F.A.C., shall create a presumption that the applicant provided reasonable assurance that the proposed activity meets the requirements in paragraph (1)(a), above.

(b) A showing by the applicant that the stormwater management system complies with the criteria of subsections 40C-42.025(8) and (9), F.A.C., shall create a presumption that the applicant provided reasonable assurance that the proposed activity meets the requirements in paragraph (1)(b), above.

(c) A showing by the applicant that the stormwater management system complies with the applicable criteria of Rules 40C-42.027, 40C-42.028, and 40C-42.029, F.A.C., shall create a presumption that the applicant provided reasonable assurance that the proposed activity meets the requirements in paragraph (1)(c), above.

Specific Authority 373.044, 373.113, 373.171, 373.418 FS. Law Implemented 373.413, 373.416, 373.418, 373.426, 373.461 FS. History–New 9-25-91, Amended 3-21-93, 10-3-95, 3-7-03.