40C-42.0265 Design and Performance Criteria for Wetlands Stormwater Management Systems.

(1) The wetlands stormwater management system design and performance criteria and other provisions relating to such systems are an initial but necessary step by the District in a field in which there exists limited knowledge. In an effort to further refine the District’s wetlands stormwater management system policies, monitoring data and other pertinent information relating to the performance criteria will be collected and analyzed and periodic reports of the results of this monitoring shall be made available to the public. The District must attempt to ensure that the wetlands stormwater management system is compatible with the ecological characteristics of the wetlands utilized for stormwater treatment and to ensure that water quality standards will not be violated by discharges from wetlands stormwater management system. To achieve these goals, specific performance criteria are set forth in this section for systems which incorporate wetlands for stormwater treatment.

(2) The only wetlands to be used for stormwater treatment are those:

(a) Which are isolated wetlands; and

(b) Which would be isolated wetlands, but for a hydrologic connection to other wetlands or surface waters via another watercourse that was excavated through uplands.

(3) In the review of wetlands stormwater management system permit applications, the District shall consider the following:

(a) Compliance of the wetlands stormwater management system permit with the performance criteria specified in subsection 40C-42.0265(5), F.A.C.

(b) If the applicant is unable to show compliance with the performance criteria in subsection 40C-42.0265(5), F.A.C., the applicant shall qualify for a wetlands stormwater management system permit using alternative design and performance criteria if the applicant affirmatively demonstrates that the use of the wetlands is compatible with the ecological characteristics of the wetland and the applicant complies with the standards in Rule 40C-42.023, F.A.C.

(c) If the applicant proposes to dredge or fill in the wetlands used for stormwater treatment, the District in its review of the permit application shall evaluate the adverse effects of the dredging or filling on the treatment capability of the wetland.

(4) A showing by the applicant that the wetlands stormwater management system design complies with the performance criteria listed below shall create a presumption in favor of the issuance of the permit:

(a) The system complies with the requirements of Rule 40C-42.025 and subsection 40C-42.0265(2), F.A.C.

(b) The system is part of a comprehensive stormwater management system that utilizes wetlands in combination with other best management practices to provide treatment of the runoff from the greater of the following:

1. First one inch of runoff; or

2. 2.5 inches times the impervious area.

(c) Those systems which direct discharge to Class I, Class II, or Outstanding Florida Waters shall provide an additional fifty percent of the applicable treatment volume specified in paragraph (b), above.

(d) The wetlands stormwater management system must provide treatment for the runoff as specified in paragraph 40C-42.0265(5)(b) or (c), F.A.C., within the wetlands. The design features of the system shall maximize residence time of the stormwater within the wetland. The outfall structure shall be designed to bleed down one-half the volume specified in paragraph 40C-42.0265(5)(b) or (c), F.A.C., within the first 60 to 72 hours.

(e) Stormwater shall be discharged into the wetlands utilized so as to minimize the channelized flow of stormwater by employing methods including, but not limited to, sprinklers, overland flow or spreader swales.

(f) The use of wetlands for stormwater treatment must meet the criteria in Section 12.0, Environmental Considerations, of the Applicant’s Handbook: Management and Storage of Surface Waters, adopted by reference in Rule 40C-4.091, F.A.C.

(5) In order to establish a reliable, scientifically valid data base upon which to evaluate the performance criteria and the performance of the wetlands stormwater management system, a monitoring program may be required. Monitoring programs shall provide the District with comparable data for different types of wetlands and drainage designs. Data to be collected shall include (unless irrelevant to the permitted system): sedimentation rate, sediment trace metal concentrations, sediment nitrogen and phosphorus concentrations, changes in the frequency, abundance and distribution of vegetation, and inflow and outflow water quality for nutrients, metals, turbidity, oils and greases, bacteria and other parameters related to the specific site conditions. Inflow and outflow water quality parameters will be monitored on such storm event occurrences as established by the District based on a site specific basis. The District shall eliminate the requirement to continue the monitoring program upon its determination that no further data is necessary to evaluate the performance criteria or ensure compliance with the performance criteria and applicable water quality standards.

Specific Authority 373.044, 373.113, 373.414, 373.418 FS. Law Implemented 373.413, 373.414, 373.416, 373.418, 373.426 FS. History–New 9-25-91, Amended 3-21-93, 10-3-95, 2-1-05.