40C-42.032 Limiting Conditions.

(1) The Governing Board shall impose upon any permit granted pursuant to this chapter such reasonable conditions as are necessary to assure that construction and operation of the permitted system will not be inconsistent with the District’s permitting standards set forth in Rule 40C-42.023, F.A.C., and will not be harmful to the water resources of the District.

(2)(a) In addition to project-specific special conditions, the following standard limiting conditions shall be attached to all permits issued pursuant to this Chapter unless waived by the Board upon a determination that the conditions are inapplicable for the work authorized by a given permit:

1. This permit for construction will expire five years from the date of issuance unless otherwise specified by a special condition of the permit.

2. Permittee must obtain a permit from the District prior to beginning construction of subsequent phases or any other work associated with this project not specifically authorized by this permit.

3. Before any offsite discharge from the stormwater management system occurs, the retention and detention storage must be excavated to rough grade prior to building construction or placement of impervious surface within the area served by those systems. Adequate measures must be taken to prevent siltation of these treatment systems and control structures during construction or siltation must be removed prior to final grading and stabilization.

4. The permittee must maintain a copy of this permit complete with all conditions, attachments, exhibits, and permit modifications, in good condition at the construction site. The complete permit must be available for review upon request by District representatives. The permittee shall require the contractor to review the complete permit prior to commencement of the activity authorized by this permit.

5. All activities shall be implemented as set forth in the plans, specifications and performance criteria as approved by this permit. Any deviation from the permitted activity and the conditions for undertaking that activity shall be considered a violation of this permit.

6. District authorized staff, upon proper identification, must be granted permission to enter, inspect and observe the system to insure conformity with the plans and specifications approved by the permit.

7. Prior to and during construction, the permittee shall implement and maintain all erosion and sediment control measures (best management practices) required to retain sediment on-site and to prevent violations of state water quality standards. All practices must be in accordance with the guidelines and specifications in chapter 6 of the Florida Land Development Manual: A Guide to Sound Land and Water Management (Florida Department of Environmental Regulation 1988), which are hereby incorporated by reference, unless a project specific erosion and sediment control plan is approved as part of the permit, in which case the practices must be in accordance with the plan. If site specific conditions require additional measures during any phase of construction or operation to prevent erosion or control sediment, beyond those specified in the erosion and sediment control plan, the permittee shall implement additional best management practices as necessary, in accordance with the specifications in chapter 6 of the Florida Land Development Manual: A Guide to Sound Land and Water Management (Florida Department of Environmental Regulation 1988). The permittee shall correct any erosion or shoaling that causes adverse impacts to the water resources.

8. If the permitted system was designed by a registered professional, within 30 days after completion of the stormwater system, the permittee must submit to the District the following: District Form No. 40C-1.181(13) (As Built Certification By a Registered Professional), signed and sealed by an appropriate professional registered in the State of Florida, and two (2) sets of “As Built” drawings when a) required by a special condition of this permit, b) the professional uses “As Built” drawings to support the As Built Certification, or c) when the completed system substantially differs from permitted plans. This submittal will serve to notify the District staff that the system is ready for inspection and approval.

9. If the permitted system was not designed by a registered professional, within 30 days after completion of the stormwater system, the permittee must submit to the District the following: District Form No. 40C-1.181(14) (As Built Certification), signed by the permittee and two (2) sets of “As Built” drawings when required by a special condition of this permit, or when the completed system substantially differs from permitted plans. This submittal will serve to notify the District staff that the system is ready for inspection and approval.

10. Stabilization measures shall be initiated for erosion and sediment control on disturbed areas as soon as practicable in portions of the site where construction activities have temporarily or permanently ceased, but in no case more than seven (7) days after the construction activity in that portion of the site has temporarily or permanently ceased.

11. Should any other regulatory agency require changes to the permitted system, the permittee shall provide written notification to the District of the changes prior to implementation so that a determination can be made whether a permit modification is required.

12. Within thirty (30) days after sale or conveyance of the permitted stormwater management system or the real property on which the system is located, the owner in whose name the permit was granted shall notify the District of such change of ownership. Transfer of this permit shall be in accordance with the provisions of Rule 40C-1.612, F.A.C. All terms and conditions of this permit shall be binding upon the transferee. The permittee transferring the permit shall remain liable for any corrective actions that may be required as a result of any permit violations prior to such sale, conveyance or other transfer.

13. The stormwater management system must be completed in accordance with the permitted plans and permit conditions prior to the initiation of the permitted use of site infrastructure. The system must be completed in accordance with the permitted plans and permit conditions prior to transfer of responsibility for operation and maintenance of the stormwater management system to a local government or other responsible entity.

14. The operation phase of the permit shall not become effective until the requirements of condition No. 8 or 9 have been met, the District determines that the system complies with the permitted plans, and the entity approved by the District in accordance with Rule 40C-42.027, F.A.C., accepts responsibility for operation and maintenance of the system. The permit cannot be transferred to such an approved responsible operation and maintenance entity until the requirements of Rule 40C-42.028, F.A.C., are met, and the operation phase of the permit becomes effective. Following inspection and approval of the permitted system by the District in accordance with Rule 40C-42.028, F.A.C., the permittee shall request transfer of the permit to the responsible approved operation and maintenance entity, if different from the permittee. Until the permit is transferred pursuant to subsection 40C-42.028(4), F.A.C., the permittee shall be liable for compliance with the terms of the permit.

15. Prior to lot or unit sales, or upon completion of construction of the system, whichever occurs first, the District must receive the final operation and maintenance document(s) approved by the District and recorded, if the latter is appropriate. For those systems which are proposed to be maintained by county or municipal entities, final operation and maintenance documents must be received by the District when maintenance and operation of the system is accepted by the local government entity. Failure to submit the appropriate final document will result in the permittee remaining personally liable for carrying out maintenance and operation of the permitted system.

16. This permit does not eliminate the necessity to obtain any required federal, state, local and special district authorizations prior to the start of any activity approved by this permit. This permit does not convey to the permittee or create in the permittee any property right, or any interest in real property, nor does it authorize any entrance upon or activities on property which is not owned or controlled by the permittee, or convey any rights or privileges other than those specified in the permit and Chapter 40C-42, F.A.C.

17. The permittee shall hold and save the District harmless from any and all damages, claims, or liabilities which may arise by reason of the activities authorized by the permit or any use of the permitted system.

18. The permittee shall immediately notify the District in writing of any previously submitted information that is later discovered to be inaccurate.

19. Activities approved by this permit shall be conducted in a manner which do not cause violations of state water quality standards.

(b) This section shall not be construed as a limitation on the authority of the Board to impose such other limiting conditions as may be necessary in order to assure that the permitted system is consistent with the requirements for issuance listed in Rule 40C-42.023, F.A.C.

Specific Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.409, 373.413, 373.416, 373.419, 373.423, 373.426 FS. History–New 3-21-93, Amended 10-3-95.