Notice of Proposed Rule

DEPARTMENT OF TRANSPORTATION

RULE NOS.:	RULE TITLES:

14-86.001	Purpose

14-86.002	Definitions

14-86.003	Permit, Assurance Requirements, and Exceptions

14-86.004	Permit Application Procedure

14-86.005	General Conditions for a Drainage Permit

14-86.006	Permit Suspension or Revocation

PURPOSE AND EFFECT: To update requirements for drainage connections entering Department of Transportation right-of-way.

SUMMARY: Revises process for drainage connection applications to on-line portal and updates drainage manual incorporated by reference.

SUMMARY OF STATEMENT OF ESTIMATED REGULATORY COSTS AND LEGISLATIVE RATIFICATION:

The Agency has determined that this will not have an adverse impact on small business or likely increase directly or indirectly regulatory costs in excess of $200,000 in the aggregate within one year after the implementation of the rule. A SERC has not been prepared by the Agency.

The Agency has determined that the proposed rule is not expected to require legislative ratification based on the statement of estimated regulatory costs or if no SERC is required, the information expressly relied upon and described herein: the rule is expected to decrease the regulatory cost of the application process.

Any person who wishes to provide information regarding a statement of estimated regulatory costs, or provide a proposal for a lower cost regulatory alternative must do so in writing within 21 days of this notice.

RULEMAKING AUTHORITY: 334.044(2)(15), FS.

LAW IMPLEMENTED: 334.044(15), FS.

IF REQUESTED WITHIN 21 DAYS OF THE DATE OF THIS NOTICE, A HEARING WILL BE SCHEDULED AND ANNOUNCED IN THE FAR.

THE PERSON TO BE CONTACTED REGARDING THE PROPOSED RULE IS: Susan Schwartz, Assistant General Counsel, Department of Transportation, 605 Suwannee Street, Tallahassee, Fl 32399, susan.schwartz@dot.state.fl.us

THE FULL TEXT OF THE PROPOSED RULE IS:

## 14-86.001 Purpose.

The purpose of this rule chapter is to regulate and prescribe conditions for the transfer of stormwater to the Department of Transportation’s right-of-way right of way as a result of manmade changes to adjacent property(ies), through a permitting process designed to ensure the safety and integrity of the Department of Transportation’s facilities and to prevent an unreasonable burden on adjacent and downstream lower properties. This rule chapter does not regulate dewatering activities.

Rulemaking Authority 334.044(2), (15) FS. Law Implemented 334.044(15) FS. History–New 11-12-86, Amended 1-20-09,             .

## 14-86.002 Definitions.

As used in this rule chapter the following terms shall have the following meanings:

(1) “Adjacent Property” means any real property or easement with a shared boundary to the Department’s right-of-way.

(2) “Applicant” means the owner of adjacent property or the owner’s authorized representative.

(3) “Applicable Water Quality Standards” means rules and regulations of state or federal governmental entity(ies) pertaining to stormwater discharges from the Department’s facilities to which the drainage connection is made.

(4) “Approved Stormwater Management Plan” or “Master Drainage Plan” means a plan adopted or approved by a city, county, water management district, or other agency with specific drainage or stormwater management authority provided that:

(a) Such plan is actively being implemented;

(b) Any required construction is substantially complete;

(c) Downstream mitigation measures have been provided for in the plan; and,

(d) The use of any Department facilities either existing or planned, which are part of such plan, have been approved by the Department.

(5) “Closed Basin” means a basin without any positive outlet, for the design storms applicable to this rule.

(4)(6) “Critical Duration” means the length of time of a specific storm frequency which creates the largest volume or highest rate of net stormwater runoff (post-improvement runoff less pre-improvement runoff) for typical durations up through and including the 10-day duration for closed basins, i.e. without a positive outlet, and up through the 3-day duration for basins with positive outlets. The critical duration for a given storm frequency is determined by calculating the peak rate and volume of stormwater runoff for various storm durations and then comparing the pre-improvement and post-improvement conditions for each of the storm durations. The duration resulting in the highest peak rate or largest net total stormwater volume is the “critical duration” storm (volume is not applicable for basins with positive outlets).

(5)(7) “Department” means the Florida Department of Transportation.

(6)(8) “Discharge” means the event or result of stormwater draining or otherwise transferring from one property to another or into surface waters.

(7)(9) “Drainage Connection” means any structure, pipe, culvert, device, paved or unpaved area, swale, ditch, canal, or other appurtenance or feature, whether naturally occurring or created, which is used or functions as a link to convey stormwater.

(8)(10) “Facility” or “Facilities” means anything built, installed, or maintained by the Department within the Department’s right-of-way.

(9)(11) “Impervious Area” means surfaces which do not allow, or minimally allow, the penetration of water. Examples of impervious areas are building roofs, all concrete and asphalt pavements, compacted traffic-bearing areas such as limerock roadways, lakes, retention/detention areas, wet ponds, pond liners, and other standing water areas, including some retention/detention areas.

(10)(12) “Improvement” means any man-made change(s) to adjacent property which establishes or alters the rate, volume, or quality of stormwater .

(11)(13) “Licensed Professional” means an individual licensed under Chapter 471, Florida Statutes, by a Florida professional licensing board, authorized by law to design and certify the stormwater management system under review.

(14) “Man-made Change” means any intentional physical change to or upon adjacent property resultant from an intentional physical change, which establishes or alters the rate, volume, or quality of stormwater.

(12)(15) “Permit” or “Drainage Connection Permit” means an authorization to establish or alter a drainage connection to the Department’s right-of-way issued pursuant to this rule chapter.

(13)(16) “Permittee” means the individual or entity to which a Drainage Connection Permit is issued.

(14)(17) “Positive Outlet” means a point of stormwater runoff into surface waters which under normal conditions would drain by gravity through surface waters ultimately to the Gulf of Mexico, or the Atlantic Ocean, or into sinks, closed lakes, or recharge wells provided the receiving waterbody has been identified by the appropriate Water Management District as functioning as if it recovered from runoff by means other than transpiration, evaporation, percolation, or infiltration.

(15)(18) “Post-improvement” means the condition of property after improvement.

(16)(19) “Pre-improvement” means the condition of property:

(a) Before November 12, 1986; or

(b) On or after November 12, 1986, with connections which have been permitted under this rule chapter or permitted by another governmental entity based on stormwater management requirements equal to or more stringent than those in this rule chapter.

(17)(20) “Right-of-Way” “Right of Way” means land in which the Department owns the fee or less than the fee, or for which the Department has an easement, devoted to or required for use as a transportation or stormwater management system facility.

(18)(21) “Stormwater” or “Stormwater Runoff” means the flow of water which results from and occurs immediately following a rainfall event.

(19)(22) “Stormwater Management System” means a facility system which is designed and constructed or implemented to control stormwater, incorporating methods to collect, convey, store, infiltrate, treat, use, or reuse stormwater to prevent or reduce flooding, overdrainage, pollution, and otherwise affect the quantity or quality for the receiving water body or downstream property of stormwater in the system.

(20)(23) “Surface Water” means water upon the surface of the earth whether contained in bounds created naturally or artificially or diffused. Water from natural springs shall be classified as surface water when it exits onto the earth’s surface.

(21)(24) “Watershed” means the region draining or contributing water to a common outlet, such as a stream, lake, or other receiving area.

Rulemaking Authority 334.044(2), (15) FS. Law Implemented 334.044(15) FS. History–New 11-12-86, Amended 1-20-09,                         .

## 14-86.003 Permit, Assurance Requirements, and Exceptions.

(1) Permit.

(a) No permits are required for properties without improvements on or after November 12, 1986.

(b) All improvements on or after November 12, 1986, require a A Drainage Connection Permit, Form 850-040-06 , rev. 9/18 (10/08),  and incorporated herein by reference at https://www.flrules.org/Gateway/reference.asp?No=Ref-10118 is required for all improvement(s) on an adjacent property whether or not the work is done in conjunction with a driveway connection, and whether or not the improvement retains stormwater runoff on the adjacent property up to and including the 100 year event of critical duration.

(2) Assurance Requirements.

(a) The applicant for a drainage connection permit shall provide reasonable assurances that :

1. The adjacent property has an approved stormwater management plan or master drainage plan adopted or approved by a city, county, water management district, or other agency with specific drainage or stormwater management authority, which plan includes downstream mitigation measures.  To the extent the plan relies on the use of any Department facilities, such use must have Department approval.

2. 1. The peak discharge rates and total volumes of stormwater discharging from the adjacent property to the Department’s right-of-way right of way are those provided for in an approved stormwater management plan or master drainage plan; otherwise the post-improvement stormwater runoff discharging from the adjacent property to the Department’s right-of-way right of way shall not exceed the more stringent of the following:

a. the peak discharge rates and total volumes allowed by applicable local regulation; or

b. the improvement shall not increase stormwater discharge rate above the pre-improvement discharge rate, and in watersheds which do not have a positive outlet, the post-improvement total volume of stormwater runoff shall not be increased beyond the pre-improvement volume considering worst case storms for up to the frequencies and durations contained in Rule paragraph 14-86.003(2)(c), F.A.C.

3.2. Any discharge pipe establishing or constituting a drainage connection from the adjacent property to the Department’s right-of-way right of way is limited in size based on the pre-improvement discharge rate, downstream conveyance limitations, downstream tailwater influences, and design capacity restrictions imposed by other governmental entities.

4.3. If the improvement changes the inflow pattern of stormwater or method of drainage connection to the Department’s right-of-way right of way, post-improvement discharge will not exceed the pre-improvement discharge to the Department’s right-of-way right of way, any new drainage connection will not threaten the safety or integrity of the Department’s right-of-way right of way, and will not increase maintenance costs to the Department. At a minimum pavement hydraulics, ditch hydraulics, storm drain hydraulics, cross drain hydraulics, and stormwater management systems facilities shall be analyzed by the applicant. The analysis must follow the methodology used in the design of the Department’s drainage facilities receiving the discharge and meet the criteria in chapters 2, 3, 4, and 6 of the Department’s Drainage Manual, Topic Number 625-040-002-c, eff. 1/19 May 2008, incorporated herein by reference at https://www.flrules.org/Gateway/reference.asp?No=Ref-10117  and  . The Drainage Manual is available from the Department at: http://www.fdot.gov/roadway/Drainage/Manuals and Handbooks

http://www.dot.state.fl.us/rddesign/dr/Manualsandhandbooks.shtm.

5.4. The quality of water conveyed by the proposed connection will meet meets all applicable water quality standards, and such assurance shall be certified in writing. In the event the discharge is identified as potentially causing or contributing to a violation of applicable water quality standards, the applicant permittee will be required to incorporate such abatement as necessary to bring the permittee’s discharge into compliance with applicable water quality standards.

(b) If the requirements set forth in paragraph 14-86.003(2)(a), F.A.C., cannot be fully complied with, the applicant may submit alternative drainage connection designs. The analysis supporting the proposed alternative drainage connection must follow the methodology used in the design of the Department’s drainage facilities receiving the proposed alternative drainage connection and meet the criteria in chapters 2, 3, 4, and 6 of the Department’s Drainage Manual. Deviation from a standard in the Drainage Manual is subject to approval by must be approved by the District Drainage Engineer. Acceptance of any alternative design must serve the purpose of this rule chapter and shall be based upon consideration of the following:

1. The type of stormwater management practice proposed;

2. The efficacy and costs of alternative controls;

3. The impact upon the operation and maintenance of the Department’s facilities; and,

4. The public interest served by the drainage connection.

(c) In providing reasonable assurances, the applicant shall:

1. Use a methodology which is compatible with the methodology employed in the design of the Department’s drainage facilities receiving the stormwater;

2. Determine the peak discharge rates considering various rainfall event frequencies up to and including a 100 year event of critical duration of up to three days; and,

3. In watersheds without a positive outlet, determine the stormwater runoff total volumes considering various rainfall amounts up to a 100 year rainfall frequency of critical durations of up to ten days. The pond retention volume must recover at a rate such that one-half of the volume is available in seven days with the total volume available in 30 days, with a sufficient amount recovered within the time necessary to satisfy applicable water treatment requirements.

(3) Exemptions Exceptions. The following exceptions do not require a Drainage Connection Permit:

(a) Adjacent properties without improvements.

(b) Improvements to adjacent properties made before November 12, 1986.

(c)(a) Improvements to adjacent properties not draining to the Department’s right-of-way in the pre-improvement and post-improvement condition.

(d)(b) Single-family residential improvements which are not part of a larger common plan of development improvement or larger common plan of sale.

(e)(c) Agricultural and silvicultural improvements that:

1. Are subject to regulation by the Department of Environmental Protection or regional Water Management Districts;

2. Are exempt under the provisions of Section 373.406, F.S.; or

3. Are implementing applicable best management practices adopted by the Florida Department of Agriculture and Consumer Services in Rule Chapter 5M or 5I-6, F.A.C.

(f)(d) Any other improvement, provided that all of the following apply:

1. The total impervious area, after improvement, is less than 5,000 square feet of cumulative impervious area and is less than 40% of that portion of the property that naturally drained to the Department’s right-of-way;

2. The improvement does not create or alter a drainage connection;

3. The improvement does not change flow patterns of stormwater to the Department’s right-of-way right of way, and does not increase the surface area draining to the Department’s right-of-way;

4. The property is located in a watershed which has a positive outlet; and,

5. The site or improvement is not part of a larger common plan of development improvement or larger common plan of sale.

(4) An exemption exception provided in subsection 14-86.003(3), F.A.C., shall not apply if any drainage connection from the adjacent property threatens the safety and integrity of the Department’s facilities or creates an unreasonable burden on downstream lower properties, including violations of applicable water quality standards.

Rulemaking Authority 334.044(2), (15) FS. Law Implemented 334.044(15) FS. History–New 11-12-86, Amended 1-20-09,_____.

## 14-86.004 Permit Application Procedure.

(1) An applicant shall submit a Drainage Connection Permit, Form 850-040-06 rev. 9/18 (10/08), incorporated herein by reference at https://www.flrules.org/Gateway/reference.asp?No=Ref-10118 and available for electronic submittal through https://osp.fdot.gov. This form may be obtained from any of the Department’s local area Maintenance Offices, District Offices, or on the internet at the Department’s website: http://www.dot.state.fl.us/onestoppermitting/.

(2) The applicant shall submit four completed Drainage Connection Permit packages. Each completed Drainage Connection Permit package shall include all applicable attachments. All applicable plans and supporting documentation shall be submitted on no larger than 11" x 17" multipurpose paper and included in PDF format on a compact disk.

(3) The Drainage Connection Permit shall be accompanied by:

(a) A location map, included in the construction plans, sufficient to show the location of the improvement and any drainage connection to the Department’s right-of-way right of way, and shall include the state highway number, county, city, and section, range, and township.

(b) A grading plan drawn to scale showing pre-improvement and post-improvement site conditions including all pervious and impervious surfaces, land contours, spot elevations, and all drainage facilities of the Department and of the adjacent property. The bench mark datum for the plans (whether NGVD 29 or NAVD 88) shall be noted on the plans. Contour information shall extend 50 feet beyond the property boundaries or be sufficient to clearly define the portion of the watershed which drains through the property to the Department’s right-of-way.

(c) Photographs which accurately depict pre-improvement and present conditions.

(d) Soil borings and water table data and, where percolation or infiltration is utilized in the design, appropriate percolation test methodology and results.

(e) Computations as required by subsection 14-86.003(2), F.A.C.

(f) The Drainage Connection Certification, Part 2 of the permit must be certified by a Licensed Professional that the complete set of plans and computations comply with either paragraph 14-86.003(2)(a) or 14-86.003(2)(b), F.A.C.

(3)(4) Improvements which otherwise meet the criteria of subparagraphs 14-86.003(3)(f)(d)1. and 14-86.003(3)(f)(d)4., F.A.C., but which create or alter a drainage connection to the Department’s right-of-way, will not require submittal of the information required by paragraphs 14-86.004(2)(3)(d) through (f), F.A.C., but will otherwise require the submittal of all other required information.

(4)(5) The Department recognizes that regulatory and permitting programs exist or may be developed in the future by local units of government, and state or federal agencies which may overlap with some or all of the requirements of this rule chapter. In order to avoid duplication the Department will:

(a) In lieu of the requirements in Rule 14-86.003, and subsection 14-86.004(2)(3), F.A.C., accept a permit that accomplishes the purposes of this rule chapter so long as the permit is issued by a governmental entity with specific stormwater management authority and is based on requirements equal to or more stringent than those in Rule 14-86.003, F.A.C.; or

(b) Accept any form, plans, specifications, drawings, calculations, or other data developed to support an application for a permit required by a governmental entity, pursuant to any rule which establishes requirements equal to or more stringent than Rule 14-86.003, F.A.C.

(5)(6) The Drainage Connection Permit serves as the application. Once approved by the Department, the drainage connection application form and supporting documents become the Drainage Connection Permit.

Rulemaking Authority 334.044(2), (15) FS. Law Implemented 334.044(15) FS. History–New 11-12-86, Amended 1-20-09,_____.

## 14-86.005 General Conditions for a Drainage Permit.

(1) A Drainage Connection Permit does not exempt the permittee from meeting all other applicable regulations and ordinances governing stormwater management.

(2) All work done in conjunction with the Drainage Connection Permit shall meet and adhere to all general and specific conditions and requirements contained in on the Permit.

(3) Within 15 working days after completion of the work authorized by an approved Drainage Connection Permit, the permittee shall notify the Department in writing of the completion; and for all design work that originally required certification by a Licensed Professional, this notification shall contain the As Built Certification, Part 8 of the Permit. The certification shall state that work has been completed in substantial compliance with the Drainage Connection Permit.

(4) The permittee or property owner, will be required to reimburse the Department for any fines, penalties and costs, e.g., abatement costs, mitigation costs, remediation costs, etc. incurred by the Department in the event the permittee’s discharge fails to meet the applicable water quality standards or minimum design and performance standards contrary to the permittee’s assurances provided in subsection 14-86.003(2), F.A.C.

Rulemaking Authority 334.044(2), (15) FS. Law Implemented 334.044(15) FS. History–New 11-12-86, Amended 1-20-09,_____.

## 14-86.006 Permit Suspension or Revocation.

A permit will be suspended or revoked if:

(1) The permitted drainage connection is not constructed, operated, or maintained in accordance with the permit;

(2) Emergency conditions or hazards exist;

(3) False or misleading information is submitted to the Department in the Drainage Connection Permit package;

(4) Another governmental entity revokes or suspends a permit which was the basis upon which a Department Drainage Connection Permit was obtained;

(5) The As-built Certificate required for the Drainage Connection Permit is not submitted in accordance with Rule subsection 14-86.005(3), F.A.C.; or

(6) Any discharge occurs above the permitted design discharge.

Rulemaking Authority 334.044(2), (15) FS. Law Implemented 334.044(15) FS. History–New 11-12-86, Amended 1-20-09,_____.

NAME OF PERSON ORIGINATING PROPOSED RULE: Carlos Spirio, P.E., Drainage Engineer

NAME OF AGENCY HEAD WHO APPROVED THE PROPOSED RULE: Mike Dew, Secretary

DATE PROPOSED RULE APPROVED BY AGENCY HEAD: November 07, 2018

DATE NOTICE OF PROPOSED RULE DEVELOPMENT PUBLISHED IN FAR: 8/24/18