62-25.801 General Permit for New Stormwater Discharge Facilities.

(1) A general permit is hereby granted to any person for the construction and operation of the following types of new stormwater discharge facilities as set forth in Rule 62-25.035, F.A.C., provided that notice to the Department pursuant to Rule 62-4.530, F.A.C., is submitted on Form 62-25.900(2) Revised April 1985. This general permit shall not expire and shall not be subject to subsection 62-4.540(13), F.A.C., unless suspended or revoked in accordance with subsection 62-4.530(4), F.A.C.:

(a) Facilities which discharge into a stormwater discharge facility which is permitted pursuant to Rule 62-25.040 or paragraph 62-25.035(1)(b) or (d), F.A.C., or which was previously approved pursuant to a noticed exemption under Rule 62-25.030, F.A.C., where the appropriate treatment criteria specified in Chapter 62-25, F.A.C., and applied to the permitted or exempt facility are not exceeded by the discharge; however, this exemption does not authorize discharge to the permitted or exempt facility without the facility owner’s prior written consent; or,

(b) Facilities which provide retention, or detention with filtration, of the runoff from the first one inch of rainfall; or, as an option, for projects or project subunits with drainage areas less than 100 acres, facilities which provide retention, or detention with filtration, of the first one-half inch of runoff. However, facilities which directly discharge to Outstanding Florida Waters shall provide additional treatment pursuant to subsection 62-25.025(9), F.A.C.; or,

(c) Modification or reconstruction by a city, county, state agency, special district with drainage responsibility, or water management district of an existing stormwater management system which is not intended to serve new development, and which will not increase pollution loading, or change points of discharge in a manner that would adversely affect the designated uses of waters of the state; or

(d) Facilities of stormwater management systems that include a combination of management practices including but not limited to retention basins, swales, pervious pavement, landscape or natural retention storage that will provide for the percolation of the runoff from a three-year one-hour design storm.

(2) Except as provided in subsection (1), this general permit is subject to the general conditions of Rule 62-4.540, F.A.C., and the following special conditions:

(a) The stormwater discharge facilities shall be designed and constructed in accordance with the design and performance standards set forth in Rule 62-25.025, F.A.C.; and,

(b) Adequate provisions have been made for the operation and maintenance of the proposed facility; and,

(c) The design, construction and operation of the stormwater discharge facility shall comply with all other applicable requirements of Chapter 62-25, F.A.C.; and,

(d) The permittee shall submit appropriate design analyses, calculations, drawings, specifications and other information necessary to describe, document and verify that the proposed stormwater discharge facility qualifies for the general permit; and

(e) The permittee or engineer of record shall file with the Department within 30 days after the facility’s completion of construction an as-built certification that the new stormwater discharge facility, as constructed, qualifies for the general permit.

(f) This general permit does not relieve the permittee of the responsibility for obtaining a dredge and fill permit where it is required.

Specific Authority 373.026(7), 373.043, 373.4145, 403.805(1) FS. Law Implemented 373.4145 FS. History–New 5-8-85, Formerly 17-4.71, 17-4.710, 17-25.801.