62-770.300 Interim Source Removal.

(1) Free Product Removal and Disposal.

(a) Except for those sites described in paragraph (1)(g) of this rule, within three days of discovery of free product the responsible party shall take steps to obtain cleanup services for product recovery or initiate product recovery. Product recovery shall be performed pursuant to paragraph 62-770.300(1)(b), F.A.C. The responsible party is required to complete product recovery provided that:

1. The product recovery method shall be selected pursuant to paragraph 62-770.300(1)(b), F.A.C.;

2. The product recovery shall not spread contamination into previously uncontaminated or less contaminated areas through untreated discharges, improper treatment, improper disposal, or improper storage;

3. Flammable products shall be handled in a safe manner; and

4. All sampling and analyses shall be performed pursuant to Rule 62-770.400, F.A.C.

(b) The following passive and active methods of product recovery may be implemented without requesting approval from the Department or FDEP local program:

1. Absorbent pads;

2. Skimmer pumps that include pumps with mechanical, electrical, or hand-bailed purging operations;

3. Hand or mechanical bailing; and

4. Fluid vacuum techniques (for example, vacuum pump trucks) or total fluid displacement pumps, as long as:

a. The technique used shall not smear or spread free product or contaminate previously uncontaminated or less contaminated media; and

b. The volume of groundwater recovered shall not be greater than two times the volume of free product recovered, except that the first 1,000 gallons of the total fluid recovered per discharge are exempt from meeting the required ratio of groundwater to free product.

(c) In addition to the product recovery methods specified in paragraph 62-770.300(1)(b), F.A.C., the responsible party may evaluate, propose, and submit other product recovery methods to the Department or to the FDEP local program for approval pursuant to Rule 62-770.890, F.A.C., prior to implementation. During the submittal and approval process, implementation of one or more of the collection methods specified in paragraph 62-770.300(1)(b), F.A.C., is required. The submittal shall include the results of the evaluation performed to determine the potential for product spreading or smearing, and the potential for air emissions, and a justification as to the environmental and economical benefits of the selected recovery method. The product recovery methods proposed may include:

1. Excavation of soil saturated with petroleum or petroleum products into, or below, the water table;

2. Dewatering or groundwater extractions that may influence the depth to the water table; or

3. Air/fluid extraction.

(d) Product recovery as an Interim Source Removal shall be deemed complete when free product has been removed to the maximum extent practicable pursuant to paragraphs 62-770.300(1)(a) and 62-770.300(1)(b), F.A.C.

(e) Within 10 days after initiation of product recovery, the responsible party shall provide written notification to the Department or to the FDEP local program on Form 62-770.900(1).

(f) Unless a different reporting period is approved pursuant to the provisions of subsection 62-770.800(4), F.A.C., the responsible party shall submit to the Department or to the FDEP local program for review two copies of an annual status report documenting the recovery progress and summarizing all recovery activities.

(g) At petroleum contamination sites eligible for State funding assistance under the Inland Protection Trust Fund where the discharge occurred prior to March 29, 1995, product recovery shall commence in accordance with the ranking established pursuant to Chapter 62-771, F.A.C., and shall be performed pursuant to paragraphs 62-770.300(1)(b) and 62-770.300(1)(c), F.A.C., and pursuant to Section 376.30711, F.S.

(2) Short-term Groundwater Recovery. A short-term groundwater recovery event may be performed as an interim source removal activity. Groundwater recovery from well(s) within the plume with screened intervals that intercept the water table, with the intent of achieving cleanup progress, may be performed prior to Department or FDEP local program approval of a Remedial Action Plan submitted pursuant to Rule 62-770.700, F.A.C., provided the following criteria are met:

(a) The groundwater contamination shall be established to be less than 1/4 acre and confined to shallow aquifer well(s) with screened intervals that intercept the water table, such that the pumping of a shallow aquifer well(s) within the plume may result in the site meeting the No Further Action criteria of Rule 62-770.680, F.A.C., or the Natural Attenuation Monitoring criteria of Rule 62-770.690, F.A.C.;

(b) Free product shall not be present;

(c) The duration of the groundwater recovery shall not exceed 30 days;

(d) The recovered groundwater shall not be treated on-site and shall be properly disposed at a permitted industrial water treatment facility, or at a publicly-owned treatment works with the approval of the sanitary sewer authority; and

(e) Sampling of representative monitoring wells to determine the effectiveness of the Short-term Groundwater Recovery event shall be performed at least 30 days after completion of the groundwater recovery.

(3) Soil Removal, Treatment, and Disposal.

(a) If contaminated soil exists at a site, excavation of contaminated soil for proper treatment or proper disposal may be performed. Consistent with the goals set forth in Section 403.061(33), F.S., the Department encourages treatment over disposal options to address contaminated soil. The treatment or disposal of contaminated soil may be performed prior to Department or FDEP local program approval of a Remedial Action Plan submitted pursuant to Rule 62-770.700, F.A.C., provided the following criteria are met:

1. Contamination shall not be spread into previously uncontaminated or less contaminated areas through untreated discharges, improper treatment, improper disposal, or improper storage;

2. Flammable products shall be handled in a safe manner;

3. When a soil vacuum extraction system is necessary to abate an imminent threat to human life, health, safety, or welfare within a structure or utility conduit, then the vacuum extraction system shall be designed and operated only to abate the imminent threat. The Department or the FDEP local program shall be notified, within 24 hours, of the imminent threat and the intent to use a soil vacuum extraction system. The air emissions monitoring and frequency of monitoring shall be performed pursuant to paragraphs 62-770.700(5)(a) and 62-770.700(11)(i), F.A.C.;

4. If one of the objectives of the interim source removal is to excavate all the contaminated soil, confirmatory soil samples shall be collected at the bottom of the excavation (unless the bottom is below the water table) and walls or perimeter of the excavation;

5. When excavated soil is temporarily stored or stockpiled on-site, the soil shall be placed on an impermeable surface to prevent leachate infiltration and secured in a manner that prevents human exposure to contaminated soil and prevents soil exposure to precipitation that may cause surface runoff, and any excavation shall be secured to prevent entry by the public. Excavated contaminated soil (including excessively contaminated soil) may be returned to the original excavation when petroleum storage tank systems have been removed or replaced, or if contaminated soil was encountered during construction activities, to be addressed pursuant to Rule 62-770.700, F.A.C.; and

6. Excavated contaminated soil (including excessively contaminated soil) shall not be stored or stockpiled on-site for more than 60 days, unless it is stockpiled on a right-of-way, in which case it shall be removed for proper treatment or proper disposal as soon as practical but no later than 30 days after excavation, or unless it is being land farmed pursuant to paragraph 62-770.300(3)(b), F.A.C., at which time the soil shall be returned to the original excavation, or removed and properly treated or properly disposed. Contaminated soil (including excessively contaminated soil) may be containerized in water tight drums and stored on-site for 90 days, after which time proper treatment or proper disposal of the contaminated soil shall occur, or it may be land farmed pursuant to paragraph 62-770.300(3)(b), F.A.C.

(b) Land farming of contaminated soil is allowed, provided the land farming operation is located on the same property as the source of contaminated soil unless it is land farmed at a permitted stationary facility. The following criteria shall be met for contaminated soil land farmed on the source property:

1. The land farm operation shall be at least 200 feet from any residence, school, or park;

2. An area large enough to spread the soil to a thickness of 6 to 12 inches shall be available;

3. The land farming area shall be secured in a manner that prevents entry by the public and prevents human exposure to contaminated soil;

4. The materials used to construct the land farm treatment area shall withstand the rigors of the land farming and weather;

5. The land farmed soil shall be placed over an impermeable liner or surface, and surrounded at all times by an impermeable liner supported by berms;

6. The land farmed soil shall be tilled at least biweekly;

7. The land farmed soil shall be covered when not being tilled to prevent water from entering or leaving the area;

8. A monitoring and sampling program shall be established to evaluate the effectiveness of the land farming operation and the effect on the environment, including monitoring of groundwater to confirm leaching is not occurring and of off gas emissions for air regulatory compliance. Before the land farming operation commences, the responsible party shall submit to the Department or to the FDEP local program the monitoring and sampling program, design specifications of the treatment area, and types and amounts of any proposed additives to the soil, to demonstrate that the objectives of this subparagraph will be met. Prior approval is not required for quantities less than 20 cubic yards, but the design specifications and results of the monitoring and sampling program shall be submitted in the Interim Source Removal Report;

9. Land farming of soil is limited to 180 days, at the end of which time proper disposal is required except if written approval pursuant to the provisions of subsection 62-770.800(4), F.A.C., to exceed this time frame, is obtained from the Department or from the FDEP local program; and

10. Land farmed soil that does not exceed the lower of the direct exposure residential CTLs and leachability based on groundwater criteria CTLs specified in Chapter 62-777, F.A.C., Table II may be disposed on-site or off-site. Responsible parties are advised that other federal or local laws and regulations may apply to these activities. Land farmed soil that exceeds the applicable CTLs specified in Chapter 62-777, F.A.C., Table II shall not be disposed or returned to the original excavation without obtaining approval from the Department or from the FDEP local program, pursuant to the provisions of Rule 62-770.890, F.A.C.

(c) Soil treatment, storage, or disposal techniques not authorized by applicable rules of the Department, or in paragraph 62-770.300(3)(b), F.A.C., require approval in a Remedial Action Plan submitted pursuant to Rule 62-770.700, F.A.C.

(d) At petroleum contamination sites eligible for State funding assistance under the Inland Protection Trust Fund, soil removal for treatment or disposal, if warranted and cost-effective, shall commence in accordance with the ranking established pursuant to Chapter 62-771, F.A.C., and shall be performed in accordance with the Department’s preapproval program procedures pursuant to a preapproval agreement.

(4) Authorizations. Authorization or receipt of approval pursuant to Rule 62-770.300, F.A.C., does not relieve the responsible party from the obligation to comply with other Department rules (for example, Chapters 62-701 and 62-730, F.A.C.) for product recovery, product disposal, groundwater recovery, or the handling, storage, disposal, or treatment of contaminated media. Responsible parties are advised that other federal or local laws and regulations may apply to these activities.

(5) Interim Source Removal Report.

(a) Within 60 days of completion of interim source removal activities, the responsible party shall submit to the Department or to the FDEP local program for review two copies of an Interim Source Removal Report. If analytical results obtained pursuant to paragraph 62-770.300(2)(e), F.A.C., and subparagraphs 62-770.300(3)(a)4. and 62-770.600(4)(m)3., F.A.C., as applicable, after completion of the interim source removal, demonstrate that the applicable No Further Action criteria of subsection 62-770.680(1), F.A.C., are met, a Site Assessment Report pursuant to subsection 62-770.600(7), F.A.C., may be submitted in lieu of the Interim Source Removal Report.

(b) Unless otherwise specified in a preapproval agreement, the Interim Source Removal Report shall contain the following information in detail, as applicable:

1. The volume of product that was discharged, if known;

2. The volume of free product and the volume of groundwater recovered;

3. The volume of contaminated soil excavated and treated or properly disposed;

4. The disposal or recycling methods for free product and contaminated soil;

5. The disposal methods for other contaminated media and any investigation-derived waste;

6. A scaled site map (including a graphical representation of the scale used) that shows the location(s) where free product and groundwater were recovered, the area of soil removed, and the approximate locations where all samples were collected;

7. A table that summarizes free product thickness in each monitoring well or piezometer, the total depth and screened interval of each monitoring well or piezometer, and the dates the measurements were made;

8. The type of field screening instrument, analytical methods, or other methods used;

9. The dimensions of the excavation(s) and location(s), integrity, capacities, and last known contents of storage tanks, integral piping, dispensers, or appurtenances removed;

10. The dimensions of the excavation(s) and location(s) and capacities of replacement underground storage tanks;

11. A table that indicates the identification, depth, and field soil screening results of each sample collected;

12. Separate tables by medium that summarize all available soil and groundwater analytical results, detection limits achieved for non-detected analytes, and analyses performed (listing all contaminants analyzed and their corresponding CTLs);

13. Depth to groundwater at the time of each excavation, measurement locations, and method used to obtain that information;

14. Type of petroleum or petroleum products discharged and a determination, if possible, of how the product was released;

15. A scaled site map (including a graphical representation of the scale used) that shows the locations and results of confirmatory soil samples, in relation to the area of soil removal;

16. Documentation or certification that confirms the proper treatment or proper disposal of the free product, contaminated groundwater, or contaminated soil, including disposal manifests for free product, a copy of the documentation or certification of treatment or acceptance of the contaminated soil, and results of analyses, if performed; and

17. For land farmed soil, a copy of the pre-treatment and post-treatment analytical results.

(c) Within 60 days of receipt of an Interim Source Removal Report, the Department or the FDEP local program shall:

1. Provide the responsible party with written approval of the Interim Source Removal Report submitted pursuant to the criteria of paragraph 62-770.300(5)(b), F.A.C.; or

2. Notify the responsible party in writing, stating the reason(s) why the Interim Source Removal Report does not conform with the applicable Interim Source Removal criteria of paragraph 62-770.300(5)(b), F.A.C.

(6) If the Interim Source Removal Report is incomplete in any respect, or is insufficient to satisfy the criteria of paragraph 62-770.300(5)(b), F.A.C., the Department or the FDEP local program shall inform the responsible party pursuant to subparagraph 62-770.300(5)(c)2., F.A.C., and the responsible party shall submit to the Department or to the FDEP local program for review two copies of an Interim Source Removal Report Addendum that addresses the deficiencies within 60 days after receipt of the notice.

(7) If the interim source removal is performed after submittal of the Site Assessment Report, the responsible party shall submit to the Department or to the FDEP local program for review two copies of a Site Assessment Report Addendum that updates the Site Assessment Report by summarizing the interim source removal activities and all sampling results obtained after submittal of the Site Assessment Report, and that includes a recommendation pursuant to paragraph 62-770.600(8)(b), F.A.C.

Specific Authority 376.303, 376.3071 FS. Law Implemented 376.3071, 376.30711 FS. History–New 11-1-87, Formerly 17-70.006, Amended 2-21-90, Formerly 17-770.300, Amended 9-3-96, 9-23-97, 8-5-99, 4-17-05.