62-770.750 Post Active Remediation Monitoring.

(1) Groundwater monitoring shall be performed following the completion of active groundwater remediation or soil remediation as described in Rule 62-770.700, F.A.C., unless the Department or the FDEP local program has concurred that groundwater sampling is unnecessary based on the site-specific conditions. When active groundwater remediation has met the No Further Action criteria of subsection 62-770.680(1), F.A.C., or the leveling off criteria of subsection 62-770.700(19), F.A.C., the responsible party shall submit to the Department or to the FDEP local program for review two copies of a Post Active Remediation Monitoring Plan prepared pursuant to subsection 62-770.750(5), F.A.C., and including analytical results demonstrating this conclusion.

(2) Applicable portions of the Post Active Remediation Monitoring Plan shall be signed and sealed by an appropriate registered professional pursuant to Rule 62-770.490, F.A.C.

(3) Within 60 days of receipt of a Post Active Remediation Monitoring Plan or of additional information pursuant to subsection 62-770.800(3), F.A.C., the Department or the FDEP local program shall:

(a) Provide the responsible party with written approval of the Post Active Remediation Monitoring Plan; or

(b) Notify the responsible party in writing, stating the reason(s) why the Post Active Remediation Monitoring Plan does not contain information adequate to support the conclusion that the applicable Post Active Remediation Monitoring criteria of Rule 62-770.750, F.A.C., have been met.

(4) If the Post Active Remediation Monitoring Plan is incomplete in any respect, or is insufficient to satisfy the objectives of subsection 62-770.750(1), F.A.C., the Department or the FDEP local program shall inform the responsible party pursuant to paragraph 62-770.750(3)(b), F.A.C., and the responsible party shall submit to the Department or to the FDEP local program for review two copies of a revised Post Active Remediation Monitoring Plan that addresses the deficiencies within 30 days after receipt of the notice. If the deficiencies are not timely corrected, or cannot be corrected, the responsible party shall resume the implementation of the approved Remedial Action Plan within 30 days after receipt of the notice.

(5) The monitoring program shall be performed as specified in the Post Active Remediation Monitoring Plan approval, as follows:

(a) A minimum of two monitoring wells is required:

1. At least one well shall be located at the downgradient edge of the plume; and

2. At least one well shall be located in the area(s) of highest groundwater contamination or directly adjacent to it if the area of highest groundwater contamination is inaccessible (for example, under a structure);

(b) The designated monitoring wells shall be sampled quarterly for analyses of applicable petroleum products’ contaminants of concern that were present prior to the initiation of active remediation;

(c) Water-level measurements in all designated wells and piezometers shall be made within 24 hours of initiating each sampling event;

(d) Within 60 days of sample collection, the responsible party shall submit to the Department or to the FDEP local program for review two copies of a Post Active Remediation Monitoring Report. The report shall include the analytical results (laboratory report), chain of custody record form [Form 62-770.900(2) or an equivalent chain of custody form that includes all the items required by Form 62-770.900(2)], the tables required pursuant to subparagraph 62-770.600(8)(a)25., F.A.C., updated as applicable, site maps that illustrate the analytical results, and the water-level elevation information (summary table and flow map);

(e) If analyses of groundwater samples indicate that concentrations of applicable petroleum products’ contaminants of concern exceed any action levels specified in the Post Active Remediation Monitoring Plan approval, the well or wells shall be resampled no later than 30 days after the initial positive result is known. If the results of the resampling confirm that the applicable action levels are exceeded, then the monitoring report referenced in paragraph 62-770.750(5)(d), F.A.C., shall be signed and sealed by an appropriate registered professional pursuant to Rule 62-770.490, F.A.C., and shall include a proposal to:

1. Perform a supplemental site assessment and submit a supplemental Site Assessment Report pursuant to Rule 62-770.600, F.A.C.;

2. Continue the implementation of the approved Post Active Remediation Monitoring Plan; or

3. Implement additional active remediation pursuant to Rule 62-770.700, F.A.C.; and

(f) A minimum of four groundwater sampling events is required and site rehabilitation shall be considered complete when the No Further Action criteria of subsection 62-770.680(1), 62-770.680(2), or 62-770.680(3), F.A.C., have been met for at least the last two quarterly or semiannual sampling events. However, if contamination was only present in the unsaturated zone during the site assessment and active remediation tasks, site rehabilitation shall be considered complete when the No Further Action criteria of subsection 62-770.680(1), 62-770.680(2), or 62-770.680(3), F.A.C., are met during only one sampling event.

(6) The remediation equipment shall be maintained in an inactive but operational status during the duration of post active remediation monitoring to avoid the possibility of having to re-install it if concentrations of petroleum products’ contaminants of concern rebound.

(7) When post active remediation monitoring is considered complete pursuant to paragraph 62-770.750(5)(f), F.A.C., the responsible party shall submit to the Department or to the FDEP local program for review two copies of a Site Rehabilitation Completion Report with a No Further Action Proposal. Applicable portions of the Site Rehabilitation Completion Report shall be signed and sealed by an appropriate registered professional pursuant to Rule 62-770.490, F.A.C. The Site Rehabilitation Completion Report shall include the documentation required in paragraph 62-770.750(5)(d), F.A.C., to support the opinion that site cleanup objectives have been achieved.

(8) Within 60 days of receipt of a Site Rehabilitation Completion Report or of additional information pursuant to subsection 62-770.800(3), F.A.C., the Department or the FDEP local program shall:

(a) Provide the responsible party with a Site Rehabilitation Completion Order as referenced in subsection 62-770.680(7), F.A.C., that approves the Site Rehabilitation Completion Report with the No Further Action Proposal; or

(b) Notify the responsible party in writing, stating the reason(s) why the Site Rehabilitation Completion Report does not contain information adequate to support the opinion that the cleanup objectives have been achieved. Site rehabilitation activities shall not be deemed complete until such time as a Site Rehabilitation Completion Report with a No Further Action Proposal is approved.

(9) If the Site Rehabilitation Completion Report is incomplete in any respect, or is insufficient to satisfy the objectives of subsection 62-770.750(7), F.A.C., the Department or the FDEP local program shall inform the responsible party pursuant to paragraph 62-770.750(8)(b), F.A.C., and the responsible party shall submit to the Department or to the FDEP local program for review two copies of a revised Site Rehabilitation Completion Report that addresses the deficiencies within 30 days after receipt of the notice. If the deficiencies are not timely corrected, or cannot be corrected, the responsible party shall resume the implementation of the approved Post Active Remediation Monitoring Plan within 30 days after receipt of the notice.

(10) The Site Rehabilitation Completion Order shall constitute final agency action regarding cleanup activities at the site.

Specific Authority 376.303, 376.3071, 403.061, 403.0877 FS. Law Implemented 376.3071, 403.0877 FS. History–New 9-23-97, Amended 8-5-99, 4-17-05.