## 62-331.240 General Permit for Stormwater Management Facilities.

(1) This general permit authorizes the following activities:

(a) Dredging or filling in state-assumed waters for the construction of stormwater management facilities, including stormwater detention basins and retention basins and other stormwater management facilities;

(b) The construction of water control structures, outfall structures and emergency spillways;

(c) The construction of low impact development integrated management features such as bioretention facilities (e.g., rain gardens), vegetated filter strips, grassed swales, and infiltration trenches; and the construction of pollutant reduction green infrastructure features designed to reduce inputs of sediments, nutrients, and other pollutants into waters to meet reduction targets established under Total Daily Maximum Loads set under the Clean Water Act.

(d) To the extent that a Section 404 permit is required, dredging or filling in state-assumed waters for the maintenance of stormwater management facilities, low impact development integrated management features, and pollutant reduction green infrastructure features.

(2) This general permit does not authorize:

(a) Dredging or filling in non-tidal wetlands adjacent to tidal retained waters.

(b) Dredging or filling for the construction of new stormwater management facilities in perennial streams.

(c) Activities within Golden Gate Estates, south of Alligator Alley in Collier County.

(d) Activities within the Belle Meade South bounded by I-75 to the north, CR 951 to the west, Miller Canal to the east, and U.S. 41 to the south in Collier County.

(3) The authorized activities are subject to the following conditions:

(a) The activity must not cause the loss of greater than 1⁄2-acre of state-assumed waters.

(b) The activity must not cause the loss of more than 300 linear feet of stream bed, unless for intermittent and ephemeral stream beds the Agency waives the 300 linear foot limit by making a written determination concluding that the activity will result in no more than minimal adverse environmental effects.

(c) The loss of stream bed plus any other losses of state-assumed waters caused by the activity cannot exceed 1⁄2-acre.

(4) A notice of intent to use this general permit shall be submitted to the Agency for:

(a) Dredging or filling in state-assumed waters for the construction of new stormwater management facilities or pollutant reduction green infrastructure features,

(b) Expansion of existing stormwater management facilities or pollutant reduction green infrastructure features,

(c) Activities in wetlands adjacent to Deer Lake and its tributaries, Bay County.

(d) Maintenance activities do not require notice of intent if they are limited to restoring the original design capacities of the stormwater management facility or pollutant reduction green infrastructure feature.

(5) Projects adjacent to Tribal lands shall not be authorized without prior written approval from the respective Tribal entity.

Editor notes: The effective date of the rule will be the effective date of assumption, which is the date identified by EPA as published in the Federal Register §373.4146, F.S.

Rulemaking Authority 373.026(7), 373.043, 373.118(1), 373.4131, 373.414(9), 373.4145, 373.4146(2), 403.805(1) FS. Law Implemented 373.118, 373.129, 373.136, 373.413, 373.4131, 373.414, 373.4145, 373.4146, 373.416, 373.422, 373.423, 373.429 FS. History–New 12-22-20.