## 64E-11.014 Mobile Food Units.

All mobile food units required to have vehicle identification numbers shall submit their vehicle identification number to the department on the application for licensure. The license decal shall be affixed to the mobile food unit. Mobile food units shall comply with Rules 64E-11.001 through 64E-11.008, and 64E-11.011 through 64E-11.013, F.A.C., except that such mobile food units shall not be required to have employee/patron toilet facilities or mop sinks. Moreover, no license shall be granted to a mobile food unit until the following additional requirements have been met:

(1) A potable water supply system of sufficient capacity (minimum 5 gallons) to furnish an adequate quantity of hot and cold water for food preparation, cleaning and handwashing purposes shall be provided during all periods of operation. The water inlet shall be located so that it will not be contaminated by waste discharge, road dust, oil or grease, and it shall be kept capped unless being filled. It shall be provided with a transition connection of a size or type that will prevent its use for any other service.

(2) A suitable liquid waste system, including a waste tank having a capacity at least 15 percent greater than the water supply system, shall be provided. All connections on the unit for servicing mobile food unit waste disposal facilities shall be of a different size or type than those used for supplying potable water to the mobile food units. The waste tank shall be capable of being completely drained and flushed.

(3) Serving openings shall not be larger than necessary for the particular operation conducted and shall be kept closed at all times except when food is actually being served. Mobile food units shall provide only single-service articles for use by the consumer.

(4) Waste containers shall be provided for the deposit of food scraps, food wrappings, cups, napkins and discarded single-service articles.

(5) Mobile food units shall operate from an approved commissary that meets all applicable requirements of this rule. The commissary must be provided with potable water and adequate facilities for disposal of liquid and solid waste. The mobile food unit must report to the commissary to store or replenish supplies, clean utensils and equipment or dispose of liquid and solid waste. Mobile food units which are self-sufficient for equipment, storage, and utilities must report to the commissary at least once weekly or as often as needed to replenish supplies, clean the interior of the unit, or dispose of liquid or solid wastes. A letter from the commissary will be submitted as part of the application confirming the arrangements above. A mobile food unit which is self-sufficient includes a three compartment sink for washing, rinsing, and sanitizing of equipment and utensils, a separate handwash sink, adequate refrigeration and storage capacity, full provision of power utilities including electrical, LP gas, or a portable power generation unit, and a liquid waste disposal system and potable water holding tank in accordance with subsections (1) and (2), of this rule. Mobile food units which are not self-sufficient must report to their commissary at least once daily. The exterior of the unit may be washed in any location, provided the waste water does not create a sanitary nuisance.

(6) When a service area is provided at the commissary for cleaning and servicing mobile food units, the service area shall include at least overhead protection for any supplying, cleaning or servicing operation. Such area shall be physically separated from other food operations; shall be equipped to furnish approved potable water in accordance with applicable provisions of Chapters 62-550 and 62-555 or 64E-8, F.A.C.; and shall provide facilities for the drainage and disposal of liquid wastes in accordance with applicable provisions of Chapter 64E-6 or 62-600, F.A.C., and the plumbing authority. The surface of the servicing area shall be constructed of a smooth nonabsorbent material such as concrete or machine laid asphalt and shall be maintained in good repair, kept clean and be graded to drain.

(7) Mobile food units which are limited to the sale of non-potentially hazardous food only shall be exempt from:

(a) The requirements of employee hand washing sink, provided that only pre-packaged items are offered; and,

(b) A utensil washing sink will not be required when all necessary washing and sanitizing of utensils and equipment are conducted at a designated approved commissary or fixed food establishment. An adequate supply of spare preparation or serving utensils shall be maintained on the unit and used to replace any utensils that become contaminated.

(8) Mobile food units may temporarily connect to an approved utility system for a time period not to exceed one day’s operation, provided the utility system is adequate to meet the needs of the unit, sanitary facilities are made available for employees and patrons in accordance with the applicable plumbing authority, and the unit returns to its base commissary at least on a daily basis as described in subsection (5), of this rule.

Rulemaking Authority 381.0072 FS. Law Implemented 381.0072 FS. History–New 3-15-98, Amended 7-14-03.