64E-26.007 Housing.

(1) Floors, walls, ceilings, windows, doors and all appurtenances of the structure shall be of sound construction, properly maintained, easily cleanable and shall be kept clean. Walls, ceilings, and area partitions shall be of light color.

(2) All areas of the detention facility other than closets or cabinets shall be well lighted. Cell areas, dormitories, toilets and dayrooms shall have light fixtures capable of providing at least twenty (20) foot candles of illumination to permit observation, cleaning, maintenance and reading. Light fixtures shall be kept clean and maintained.

(3) Sufficient space shall be provided in all living and sleeping quarters to satisfy sanitary needs of all individuals incarcerated. Every bed, cot or bunk shall have a clear space of at least twelve inches (12") from the floor. There shall be a clear ceiling height of not less than thirty-six inches (36") above any mattress and there shall be a clear space of not less than twenty-seven inches (27") between the top of the lower mattress and the bottom of the upper bunk of a double deck facility. Single beds, cots or bunks shall be spaced not less than thirty inches (30") laterally or end to end and double-deck facilities shall be spaced not less than thirty-six inches (36") laterally or end to end. Sleeping arrangements shall insure that a minimum distance of six feet (6') is provided between inmate heads.

(4) All housing facilities shall be kept free of offensive odors with adequate ventilation.

(a) If natural ventilation is utilized, the opened window area for ventilation purposes shall be equal to one-tenth  (1/10) of the floor space in the inmate residential area.

(b) When mechanical ventilation or cooling systems are employed, the system shall be kept clean and properly maintained. Intake air ducts shall be designed and installed so that dust or filters can be readily removed. In inmate residence areas and segregation cells with solid doors, mechanical ventilation systems shall provide a minimum of ten (10) cubic feet of fresh or purified recycled air per minute for each inmate occupying the area.

(c) All toilet rooms shall be provided with direct openings to the outside or provided with mechanical ventilation to the outside.

(d) Adequate heating facilities shall be provided to maintain a minimum temperature of 60° F. at a point twenty inches (20") above the floor in inmate sleeping areas.

Specific Authority 381.006 FS. Law Implemented 381.006(6) FS. History–New 11-18-76, Formerly 10D-7.07.