## 14-85.013 Definitions.

All terms in this rule chapter shall have the same meanings as defined in Section 479.261, F.S. Additionally, the following terms are defined:

(1) “Business” means a commercial establishment providing gas, food, lodging or camping services, attractions, and other services located at a single site qualified interchange, as authorized by the Manual on Uniform Traffic Control Devices, incorporated herein by reference in Rule 14-15.010, F.A.C.

(2) “Business Logo” means a sign mounted on the display panel of a logo structure showing the name, symbol, trademark, or combination thereof for a business within a category of motorist services available at an interchange.

(3) “Category” means the motorist services of gas, food, lodging, camping, attraction, and other services, as authorized under the Manual on Uniform Traffic Control Devices.

(4) “Combination Logo Structure” means a logo structure designed to display a combination of business logos in no more than three categories.

(5) “Crossroad” means a road intersecting the interstate highway to which access is provided by means of an interchange.

(6) “Department” means the Florida Department of Transportation.

(7) “Display Panel” means the facing or surface of a logo structure to which business logos are affixed.

(8) “Double Exit Interchange” means an interchange configuration where, for a given direction of travel on the mainline, two exit ramps provide access to the crossroad, one for each direction of travel on the crossroad.

(9) “Dual Business Logo” means a logo displaying two businesses located under the same roof.

(10) “Exit Ramp” means the traffic lane or lanes at an interchange on an interstate highway leading from the mainline to the crossroad.

(11) “Full Size Logo Structure” means a mainline or ramp logo structure capable of displaying six business logos.

(12) “Half Size Logo Structure” means a mainline or ramp logo structure capable of displaying three business logo signs.

(13) “Logo Structure” means the support columns and display panel upon which separate business logos may be displayed.

(14) “Logo Trailblazer Signs” means signage in addition to mainline and ramp logo structures necessary to provide additional direction to otherwise qualifying businesses that are not located on, or visible from, the crossroad. Logo trailblazer signs shall consist of a business logo identical to a ramp business logo, a directional arrow, and supports.

(15) “Mainline” means the traffic lanes on the Interstate Highway System intended for through travel.

(16) “Mainline Business Logo Structure” means those logo structures located along the mainline.

(17) “Permit” means written authorization for the display of a business logo.

(18) “Permittee” means legal company/owner name to which a permit is issued.

(19) “Prepared Food” means hot or deli style food prepared on site.

(20) “Program Administrator” means the contractor hired by the Department to provide services relating to the logo sign program.

(21) “Project Manager” means the Department employee with oversight responsibility for the program.

(22) “Qualified Interchange” means an interchange that meets the requirements of Rule 14-85.015, F.A.C.

(23) “Ramp Logo Structure” means those logo structures located along an exit ramp.

(24) “Rural Area” means all areas outside an urban area.

(25) “Sign Configuration” means the arrangement of the logo categories on a display panel.

(26) “Single Exit Interchange” means an interchange configuration where, for a given direction of travel on the mainline, one exit ramp provides access to the crossroad for both directions of travel on the crossroad.

(27) “Traffic Control Device” means all signs, signals, markings, and devices placed on, over, or adjacent to a street or highway by authority of a public body or official having jurisdiction to regulate, warn, or guide motorists, as defined by the Manual on Uniform Traffic Control Devices.

(28) “Urban Area” means as defined in Section 334.03(32), F.S.

(29) “Wait List” means a compilation of businesses, by individual category, which have applied to participate in the logo program at a particular interchange at which there is currently no space available. Wait lists are maintained by interchange, category and application date.

Rulemaking Authority 334.044(2), 479.261(7) FS. Law Implemented 334.044(2), 479.261 FS. History–New 12-15-09.