# CHAPTER 28-27

# LAND PLANNING – PART VI BOUNDARY AND REGULATIONS FOR THE

# GREEN SWAMP AREA OF CRITICAL STATE CONCERN – POLK COUNTY

# 28-27.001	Short Title

# 28-27.002	Purpose and Intent

# 28-27.003	Agricultural Exemption

# 28-27.004	Vested Rights in Property

# 28-27.005	Definitions

# 28-27.006	Boundary

# 28-27.007	Applicability

# 28-27.008	General Minimum Standards

# 28-27.009	Permit Requirements

# 28-27.010	Minimum Requirements

# 28-27.011	Appeals and Notification (Repealed)

# 28-27.012	Variances

# 28-27.013	Amendments (Repealed)

# 28-27.014	Enforcement (Repealed)

# 28-27.015	Severability

## 28-27.001 Short Title.

This chapter shall be known as the Polk County Green Swamp Development Code.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.01, 27F-6.01, 27F-6.001.

## 28-27.002 Purpose and Intent.

Pursuant to Section 7, Article II, of the Florida Constitution and Section 380.05, F.S., it is the purpose of these regulations to conserve and protect the environmental and economic resources of the Green Swamp Area of Critical State concern and to provide a land and water management system to protect such resources and facilitate orderly and well planned growth. To effectively and equitably accomplish such purposes, these regulations should be implemented by the local government through existing administrative procedures and pursuant to Chapter 28-26, F.A.C., to achieve the following objectives:

(1) Minimize the adverse impacts of development on resources of the Floridan Aquifer, wetlands and flood-detention areas.

(2) Protect the normal quantity, quality and flow of ground water and surface water which are necessary for the protection of resources of state and regional concern.

(3) Protect the water available for aquifer recharge.

(4) Protect the functions of the Green Swamp Potentiometric High of the Floridan Aquifer.

(5) Protect the normal supply of ground and surface water.

(6) Prevent further salt-water intrusion into the Floridan Aquifer.

(7) Protect or improve existing ground and surface-water quality.

(8) Protect the water-retention capabilities of wetlands.

(9) Protect the biological-filtering capabilities of wetlands.

(10) Protect the natural flow regime of drainage basins.

(11) Protect the design capacity of flood-detention areas and the water-management objectives of these areas through the maintenance of hydrological characteristics of drainage basins.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.02, 27F-6.02, 27F-6.002.

## 28-27.003 Agricultural Exemption.

The use of any land for the purpose of growing plants, crops, trees, and other agricultural or forestry products; raising livestock; or for other purposes directly related to all such uses are exempt from these regulations, for example, but not limited to, wells, access roads, utilities, and utility lines. Lands lying fallow are deemed to be used for agricultural purposes. However, whenever any person carries out any activity defined herein, as development or applies for a development permit, as defined herein, to develop exempted land, these regulations shall apply to such application and to such land.

Rulemaking Authority 380.05 FS. Law Implemented 380.05 FS. History–New 7-20-75, Formerly 22F-6.03, 27F-6.03, 27F-6.003.

## 28-27.004 Vested Rights in Property.

Where vested rights in property exist pursuant to Section 380.05(18), F.S., these regulations shall not abridge them. Any person whose rights may have vested pursuant to Section 380.05(18), F.S., may seek a determination from the local government having jurisdiction over development or the state land planning agency. Request for vested rights determination from the state land planning agency shall be submitted as a petition for a declaratory statement pursuant to Section 120.565, F.S., and upon a form as prescribed by the agency.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.04, 27F-6.04, 27F-6.004.

## 28-27.005 Definitions.

(1) “Administration commission” or “commission” means the Governor and the Cabinet, and for purposes of this chapter, the commission shall act on a simple majority.

(2) “Aquifer” means an underground formation, or group of formations, or part of a formation, that is permeable enough to transmit and store usable quantities of water.

(3) “Artesian Aquifer” means an aquifer that contains artesian water.

(4) “Artesian Water” means ground water that is under sufficient pressure to rise above the level at which it is encountered by a well, but which does not necessarily rise to or above the surface of the ground.

(5) “Board” means the Polk County Board of County Commissioners.

(6) “Development,” see definition (46).

(7) “Development order” means any order granting, denying, or granting with conditions an application for a development permit.

(8) A “development permit” includes any building permit, zoning permit, plat approval, or rezoning, certification, variance, or other action having the effect of permitting development as defined in this chapter.

(9) “Developer” means any person, including a governmental agency, undertaking any development as defined in this chapter.

(10) “Discharge” means the outflow of water from a site, aquifer, or drainage basin.

(11) “Drainage Facilities” means any canal, ditch, culvert, dike or other facility which lowers the surface or ground water table, acts as a conduit, diverts or directs the flow of water or otherwise affects the natural flow regime.

(12) “Effective Precipitation” means that part of the precipitation (rainfall) which contributes to direct surface runoff.

(13) “Flood Frequency” means the statistically determined average for how often a specific flood level of discharge may be equaled or exceeded.

(14) “Floridan Aquifer” means the aquifer which consists of a series of limestone formations which range from middle Eocene to Miocene in age and that underlies most of Florida and is a major source of ground water for the state.

(15) “Governmental agency” means:

(a) The United States or any department, commission, agency, or other instrumentality thereof;

(b) This state or any department, commission, agency, or other instrumentality thereof;

(c) Any local government, as defined in this chapter, or any department, commission, agency, or other instrumentality thereof;

(d) Any school board or other special district, authority, or other governmental entity.

(16) “Green Swamp” means those lands within Polk County which lie within the boundaries delineated by the legal description in Rule 28-26.002, F.A.C.

(17) “Ground Water” means water beneath the surface of the ground, whether or not flowing through known and definite channels.

(18) “Hydroperiod” means that portion of the hydrologic cycle during which water is at or on the soil surface.

(19) “Land” means the earth, water, and air, above, below, or on the surface, and includes any improvements or structures customarily regarded as land.

(20) “Land development regulations” include local zoning, subdivision, building, and other regulations controlling the development of land.

(21) “Land use” means the development that has occurred on land.

(22) “Local government” means any county or municipality and, where relevant, any joint airport zoning board.

(23) “Major public facility” means any publicly owned facility of more than local significance.

(24) “Natural Flow Regime” means the velocity, volume, and direction of the surface or ground water flow presently occurring for any given portion of the Area of Critical State Concern.

(25) “Parcel of land” means any quantity of land capable of being described with such definiteness that its location and boundaries may be established, which is designated by its owner or developer as land to be used or developed as a unit, or which has been used or developed as a unit.

(26) “Peak Surface – Water Discharge” means the maximum discharge rate subsequent to an occurrence of effective precipitation.

(27) “Person” means an individual, corporation, governmental agency, business trust, estate, trust, partnership, association, two or more persons having a joint or common interest, or any other legal entity.

(28) “Pine Flatwoods” means those discrete areas which have one or more of the following naturally occurring soils, or any other soil classified by the U. S. Soil Conservation Service as indicative of a pine flatwood:

| Bushnell | Broward |
| --- | --- |
| Immokalee | Eureka |
| Ona | Myakka (Leon) |
| Scranton | Panasoffkee |
| Wabasso (Leon loamy substrata) | St. Johns |
| Pompano Sand, acid | Wauchula (Leon, heavy substrata) |
| Placid sand, slightly wet |  |

(29) “Potentiometric Surface” means the imaginary surface coinciding with levels of artesian pressure.

(30) “Recharge” means the downward percolation of surface water into any underground formation.

(31) “Regional planning agency” means the agency designated by the state land planning agency to exercise responsibilities under this chapter in a particular region of the state.

(32) “Regulatory Flood Level” means the level of the flood which is representative of large floods known to have occurred generally in the area and reasonably characteristic of what can be expected to occur on a particular stream. The Regulatory Flood generally has a flood frequency of approximately 100 years as determined from an analysis of floods in a particular area.

(33) “Rule” means a rule adopted under Chapter 120, F.S.

(34) “Rural Residence” means a single family residence which is to be a dwelling for the property owner.

(35) “Site Alteration” means a development including, but not limited to, removal of, or damage to, vegetation; by filling, ditching, dredging, draining, excavation, earth moving, water containment and changes in the natural flow regime, or the effects of such actions.

(36) “State land development plan” means a comprehensive statewide plan or any portion thereof setting forth state land development policies.

(37) “State land planning agency” means the agency designated by law to undertake statewide comprehensive planning.

(38) “Structure” means anything constructed, installed, or portable, the use of which requires a location on a parcel of land. It includes a movable structure while it is located on land which can be used for housing, business, commercial, agricultural, or office purposes either temporarily or permanently. Structure also includes fences, billboards, swimming pools, poles, pipelines, transmission lines, tracks, and advertising signs.

(39) “Surface Water” means water upon the surface of the earth, whether contained in bounds created naturally or artificially or diffused. Water from natural springs or wells shall be classified as surface water when it exits from the spring or well onto the earth’s surface.

(40) “Total Site” means land which is part of common plan of development, rental, advertising or sale.

(41) “Total Surface-Water Discharge” means the total volume of surface water discharged subsequent to the occurrence of effective precipitation.

(42) “Underground Formation” means any geological unit, part of a unit, or group of units lying beneath the surface of the ground.

(43) “Uplands” means discrete areas which have one or more of the following naturally occurring soils, or any other soil classified by the U. S. Soil Conservation Service as indicative.

| Lake | Astatula (Lakeland) |
| --- | --- |
| Apopka (Blanton) | Cassia |
| Lucy | Orlando |
| Paola (Lakewood) | Pomello |
| St. Lucie | Tavares |
| Vaucluse |  |

(44) “Water Quality” means the chemical, physical and bacteriological composition of water determined by the measurements of appropriate tests as cited in 40 Code of Federal Regulations 136, and Chapter 62-19, F.A.C.

(45) “Wetlands” means discrete areas which have one or more of the following naturally occurring soils, or any other soil classified by the U. S. Soil Conservation Service as indicative of a wetland:

| Anclote | Pamlica |
| --- | --- |
| Basinger (Plummer) | Placid (Rutlege) |
| Iberia | Iberia & Manatee |
| Oklawaha | Fellowship |
| Pelham | Emeralda |
| Pompano | Feldo |
| Anclote & Myakka | Ocoee |
| Placid & Myakka | Peace River Soils |
| Brighton | Swamp |
| Manatee | Myakka & Placid |

(46)(a) “Development” means the carrying out of any building or mining operation or the making of any material change in the use or appearance of any structure or land and the dividing of land into three or more parcels.

(b) The following activities or uses shall be taken for the purposes of this chapter to involve development, as defined in this section:

1. A reconstruction, alteration of the size, or material change in the external appearance, of a structure on land.

2. A change in the intensity of use of land, such as an increase in the number of dwelling units in a structure or on land or a material increase in the number of businesses, manufacturing establishments, offices, of dwelling units in a structure or on land.

3. Alteration of a shore or bank of a seacoast, river, stream, lake, pond, or canal, including any coastal construction as defined in Section 161.021, F.S.

4. Commencement of drilling (except to obtain soil samples) mining, or excavation on a parcel of land.

5. Demolition of a structure.

6. Clearing of land as an adjunct of construction.

7. Deposit of refuse, solid or liquid waste, or fill on a parcel of land.

(c) The following operations or uses shall not be taken for the purpose of this chapter to involve development as defined in this section:

1. Work by a highway or road agency or railroad company for the maintenance or improvement of a road or railroad track, if the work is carried out on land within the boundaries of the rights-of-way.

2. Work by any utility and other persons engaged in the distribution or transmission of gas or water, for the purpose of inspecting, repairing, renewing, or constructing on established rights-of-way any sewers, mains, pipes, cables, utility tunnels, power lines, towers, poles, tracks, or the like.

3. Work for the maintenance, renewal, improvement, or alteration of any structure, if the work affects only the interior or the color of the structure or the decoration of the exterior of the structure.

4. The use of any structure or land devoted to dwelling uses for any purpose customarily incidental to enjoyment of the dwelling.

5. The use of any land for the purpose of growing plants, crops, trees, and other agricultural or forestry products; raising livestock; or for other agricultural purposes.

6. A change in use of land or structure from a use within a class specified in an ordinance or rule to another use in the same class.

7. A change in the ownership or form of ownership of any parcel or structure.

8. The creation or termination of rights of access, riparian rights, easements, covenants concerning development of land or other rights in land.

(d) “Development,” as designated in an ordinance, rule, or development permit includes all other development customarily associated with it unless otherwise specified. When appropriate to the context, development refers to the act of developing or to the result of development. Reference to any specific operation is not intended to mean that the operation or activity, when part of other operations or activities, is not development. Reference to particular operations is not intended to limit the generality of subsection (1).

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.05, 27F-6.05, 27F-6.005.

## 28-27.006 Boundary.

These rules shall apply to the Polk County portion of the Green Swamp Area of Critical State Concern as designated by Rule 28-26.002, F.A.C.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.06, 27F-6.06, 27F-6.006.

## 28-27.007 Applicability.

The regulations set forth in this Code shall only apply to that portion of Polk County within the Green Swamp Area of Critical State Concern. These regulations shall be construed as being supplementary and complementary to the regulations imposed on the same lands by Polk County or any other governmental jurisdiction.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.07, 27F-6.07, 27F-6.007.

## 28-27.008 General Minimum Standards.

All development within the Green Swamp Area of Critical State Concern shall meet the following standards and criteria:

(1) The developer shall provide for the release of surface water runoff, collected or uncollected, in a manner approximating the natural, surface water flow regime of the area.

(2) The first floor or basement floor of all structures shall be constructed at least one (1) foot above the Regulatory Flood Level for the particular area.

(3) Treatment of storm-water runoff shall be provided by settling ponds, soil fixatives, control of non-point chemical pollutants, or the performance equivalent structures or systems when such runoff may contaminate surface or ground water resources.

(4) Except for roads, any nonpermeable surface greater than 20,000 square feet shall provide for release of surface runoff, collected or uncollected, in a manner approximating the natural surface water flow regime of the area.

(5) Soils exposed during site alteration shall be stabilized and retention ponds or performance equivalent structures or systems maintained in order to retain runoff and siltation on the construction site.

(6) Any altered site shall be revegetated and such revegetation shall be subsequently completed within 180 days following completion of a development. Revegetation shall be accomplished with pre-existing species or other suitable species except that undesirable exotic species shall not be replanted or propagated.

(7) Fill areas and related dredge or borrow ponds shall be aligned substantially in the direction of local surface water flows and shall be separated from other fill areas and ponds by areas of vegetation of comparable size. Dredge or borrow ponds shall provide for the release of storm waters as sheet flow from their downstream end and into areas of vegetation. Access roads to and between fill areas shall provide for the passage of water in a manner approximating the natural flow regime and designed to accommodate the 50 year storm. Fill areas and related ponds shall not substantially retain or divert the total flow.

(8) Man-made lakes, ponds, or other containment works shall be constructed with a maximum slope of 30 degrees to a depth of six feet of water. Whenever mineral extraction is completed in new quarries, shoreline sloping, revegetation, and contouring of soils or tailings shall be completed before abandonment. Existing quarry lakes shall be exempt from this provision, except that whenever any person carries out any activity defined as development or applies for a development permit, as defined herein, to develop any existing quarry lake area, these regulations shall apply.

(9) Development shall not detrimentally change the quantity of ground and surface water available for recharge to the Floridan Aquifer. A developer shall not cause storm water from the site to discharge or runoff into an existing sinkhole.

(10) The development shall not impair the water retention and filtering capacity of wetlands soils or vegetation.

(11) New drainage facilities shall release water in a manner approximating the natural local surface flow regime, through a spreader pond or performance equivalent structure or system, either on site or to a natural retention or natural filtration and flow area. New drainage facilities shall also maintain a ground water level sufficient to protect wetland vegetation through the use of weirs or performance equivalent structures or systems. Said facilities shall not retain, divert, or otherwise block or channel the naturally occurring flows in a strand or slough.

(12) Solid waste disposal sites shall meet all the requirements of this code.

(13) Site alteration shall be permitted only when such alteration will not cause siltation of wetlands or reduce the natural retention and filtering capabilities of wetlands.

(14) Ground water withdrawal shall comply with the standards and regulations of the Southwest Florida Water Management District or its successor agency.

(15) Placement of structures shall be consistent with sound floodplain management practices such as compliance with Flood District Disaster Protection Act of 1973.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.08, 27F-6.08, 27F-6.008, Amended 1-15-14.

## 28-27.009 Permit Requirements.

(1) Any development as defined herein undertaken in the Green Swamp Area of Critical State Concern shall require a development permit. Development permits for any change in zoning, plat approvals or vacancies shall be issued in the form of a development order as defined in these regulations. An application for a development permit shall be submitted to the Polk County Planning Department, or the Polk County Building and Zoning Codes Department, whichever shall be designated by the Board, together with any reasonable fee set by the Board.

(2) Prior to issuance of any development permit, an applicant shall submit a development plan to the county agency designated by the Board pursuant to subsection (1) of this rule. The development plan shall affirmatively demonstrate that the proposed development meets or exceeds the requirements of this code. No permit shall be issued until the requirements of this code are met. The development plan shall include the description and scope of the proposed project in report form. The development plan shall include, but not be limited to, the following documents and information:

(a) A certified survey of the site showing topography in no more than one (1) foot contours in the wetlands and the pine flatwoods and two (2) foot contours in the uplands by a land surveyor registered in the State of Florida.

(b) A soil analysis prepared by a registered professional engineer or the U.S. Soil Conservation Service which will be detailed and accurate enough to allow for the soils determination required in paragraph 28-27.008(4)(a), F.A.C., of this code.

(c) A statement by a registered professional engineer indicating expected changes in surface and ground water quality discharge, and artesian aquifer recharge characteristics of the site before, during, and after development and specifying any measures necessary to approximate existing quality and quantity in surface and ground waters.

(d) A vegetation map of the site.

(e) A development implementation schedule.

(f) A site plan indicating any proposed alteration or development.

(g) A Impact Assessment Statement as required by zoning change procedures.

(3) A development plan shall not be required in the following three (3) instances unless specifically requested by a county agency:

(a) The modification of any single-family residential structure for the uses of a single family.

(b) The construction of any rural residence, as referred to in this code, shall require only the site plan and certified soil analysis.

(c) The four laning of U.S. 98 by the Florida Department of Transportation between I-4 and the Polk County Line, and any construction or alteration caused by acquiring the right-of-way needed for this facility.

(4) A development permit shall not be required by this chapter in the following two (2) instances unless otherwise required by these applicable county ordinances or regulations:

(a) The modification of any existing residential structure that does not exceed ten (10) percent of the square footage of its original structure.

(b) One residential accessory structure may be added, not to exceed six hundred (600) square feet, provided such structure does not exceed the site coverage stipulated in paragraph 28-27.008(4)(a), F.A.C., of this chapter.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Amended 4-19-77, Formerly 22F-6.09, 27F-6.09, 27F-6.009.

## 28-27.010 Minimum Requirements.

The provisions of this Code shall be considered to be minimum requirements for the protection and promotion of the public health, safety, or general welfare. Whenever the requirements of this code are at variance with the requirements of any other rules, regulations or codes, which are a proper exercise of authority of a governmental jurisdiction, the more restrictive standards shall govern.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.10, 27F-6.10, 27F-6.010.

## 28-27.011 Appeals and Notification.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.11, 27F-6.11, 27F-6.011, Repealed 7-30-98.

## 28-27.012 Variances.

Variance procedures provided in local ordinances shall apply to the Green Swamp Area of Critical State Concern. However, in addition to the standards provided in such ordinances, no variance shall be granted for any development within the critical area unless such development is designed consistent with critical area regulations to have minimum adverse impact on the area’s water storage capacity, surface water flow and wetlands. The applicant shall have the affirmative burden of establishing that the development will have a minimum adverse impact on such resources.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.12, 27F-6.12, 27F-6.012.

## 28-27.013 Amendments.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.13, 27F-6.13, 27F-6.013, Repealed 7-30-98.

## 28-27.014 Enforcement.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.14, 27F-6.14, 27F-6.014, Repealed 7-30-98.

## 28-27.015 Severability.

If any one or more of the provisions of these regulations or the application of such provisions to any situation, circumstance or person shall for any reason be held invalid, such invalidity shall not affect any other provision of these regulations or the application of such regulations to any other situation, circumstance or person.

Rulemaking Authority 380.05 FS. Law Implemented 380.05(8) FS. History–New 7-20-75, Formerly 22F-6.15, 27F-6.15, 27F-6.015.