# CHAPTER 40A-3

# REGULATION OF WELLS

# 40A-3.011	Policy and Purpose

# 40A-3.021	Definitions

# 40A-3.031	Implementation (Repealed)

# 40A-3.032	Delegation (Repealed)

# 40A-3.037	Water Well Contractor Licensing

# 40A-3.038	Violations of Licensing Requirements (Repealed)

# PART I PERMITTING OF WELLS

# 40A-3.040	Scope of Part I (Repealed)

# 40A-3.041	Permits Required

# 40A-3.051	Exemptions

# 40A-3.201	Permit Application Fees

# 40A-3.301	Conditions for Issuance of Permits

# 40A-3.321	Duration of Permits

# 40A-3.341	Disapproval of Wells

# 40A-3.342	Permit Denial

# 40A-3.411	Completion Reports

# 40A-3.451	Emergency Authorization

# 40A-3.461	Inspections

# 40A-3.492	Violations of Permits

# PART II  CONSTRUCTION, REPAIR, AND ABANDONMENT STANDARDS

# 40A-3.500	Scope and Part II (Repealed)

# 40A-3.502	Construction Methods

# 40A-3.504	Location

# 40A-3.507	Casing and Liner Pipe Standards

# 40A-3.512	Standard Well Construction Methods

# 40A-3.517	Grouting and Sealing

# 40A-3.521	Well Seals

# 40A-3.525	Explosives

# 40A-3.529	Flowing Wells

# 40A-3.531	Abandoned Well Plugging

# 40A-3.550	Violations of Construction Standards

# 40A-3.701	Construction Standards (Repealed)

# PART III DRILLER REGISTRATION

# 40A-3.721	Driller Registration (Repealed)

# 40A-3.725	Responsibility of Contractor (Repealed)

# 40A-3.727	Type of Registration (Repealed)

# 40A-3.733	Exemptions (Repealed)

# 40A-3.751	Enforcement and Penalties (Transferred)

# 40A-3.752	Refusal, Suspension, or Revocation of Registration (Repealed)

# 40A-3.763	Examinations (Repealed)

# 40A-3.901	Forms and Instructions

# PART IV SUSPENSION AND REVOCATION OF WATER WELL CONTRACTOR LICENSES

# 40A-3.951	Introduction

# 40A-3.952	Violations

# 40A-3.953	Procedure (Repealed)

# 40A-3.954	Reporting of Drillers Not Required to be Licensed (Repealed)

# 40A-3.955	Suspension; Suspension with Conditions (Repealed)

# 40A-3.956	Revocation (Repealed)

# PART V ENFORCEMENT AND PENALTIES

# 40A-3.980	Enforcement and Penalties

## 40A-3.011 Policy and Purpose.

(1) The purpose of Chapter 40A-3, F.A.C., is to implement the duties and responsibilities of the District under Part III, Chapter 373, F.S., and those responsibilities and duties delegated to the District by the Department of Environmental Protection relative to regulating the location, construction, repair, or abandonment of wells, and the licensing of water well contractors. It is the policy of the Board that these rules are a reasonable necessity to insure the protection and management of water resources and the health, safety, and general welfare of the people of this District.

(2) The rules in this chapter implement the regulation of wells and licensing of water well contractors.

(3) Rules relating to water well contractor licensing are found in Chapter 62-531, F.A.C., effective 6-22-14, https://www.flrules/org/Gateway/reference.asp?No=Ref-09102, adopted by reference in Rule 40A-3.037, F.A.C., of these rules.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.333, 373.337 FS. Law Implemented 373.306, 373.308, 373.309, 373.313, 373.316, 373.323(2), 373.324, 373.326, 373.329, 373.333, 373.342 FS. History–New 4-14-80, Amended 2-1-82, 10-1-84, 1-9-86, Formerly 16G-3.01, Amended 8-1-89, 8-15-18.

## 40A-3.021 Definitions.

The following words and phrases, when used in these rules, shall have the following meanings, except where the context clearly indicates a different meaning:

(1) “Abandonment” means the act, whether intentional or unintentional, of allowing a well to attain the condition of an abandoned well.

(2) “Abandoned Well” means a well the use of which has been permanently discontinued. Any well shall be deemed abandoned which is in such a state of disrepair, as determined by a representative of the District, that continued use for the purpose of obtaining ground water or disposing of water or liquid wastes is impracticable.

(3) “Aesthetic Use” means the use of water for fountains, waterfalls, and landscape lakes and ponds where such uses are ornamental and decorative.

(4) “Agricultural Irrigation Use” means the use of water for the commercial production of crops or the growing of farm products, including vegetables, citrus, pasture, nursery stock, turf grass, and sod.

(5) “Annulus” or “Annular Space” means any artificially created void existing between a well casing or liner pipe and a borehole wall.

(6) “Aquacultural Use” includes the use of water for spawning, cultivating, harvesting, or marketing of fin-fish, shellfish, crustaceans, frogs, turtles, and other aquatic organisms that have a sport or other economic value.

(7) “Aquifer” means a subsurface geologic unit capable of yielding significant quantities of water to wells and springs.

(8) “Aquifer Restoration Well” means a well used for the withdrawal of water for the purpose of recovering contaminant(s) to restore or improve the quality of the water within an aquifer.

(9) “Artificial Recharge” means the intentional introduction of water into any underground formation by means of a recharge or injection well.

(10) “Artificial Recharge Facility” means any facility constructed for the intentional introduction of water into any underground formation.

(11) “Board” means the Governing Board of the Northwest Florida Water Management District.

(12) “Certified Receipt” means the date and time an application for a permit is stamped as received in the District office.

(13) “Commercial Use” includes small businesses and facilities in which water is the prime ingredient of the service rendered, such as a car wash and laundromat.

(14) “Contractor” means any person licensed in accordance with Chapter 62-531, F.A.C., and engaged in the business of construction, repair, or abandonment of wells.

(15) “Department” means the Department of Environmental Protection (DEP) or its successor agency or agencies.

(16) “Domestic Self Supply Use” means the use of water for household purposes such as drinking, bathing, cooking, sanitation, or cleaning, which occurs in a private residence, and includes no more than one rental residence or no more than four nonrental residences served by one well.

(17) “Dewatering Use” means the removal of water from a specific area to facilitate mining or construction.

(18) “District” means the Northwest Florida Water Management District operating under the authority of Chapter 373, F.S.

(19) “Diversion and Impoundment into Non-District Facilities Use” means the diversion or extraction of water into non-District impoundments and delivery systems designed for such purposes as maintaining structural integrity, providing agricultural water and other non-recreational, non-aesthetic use.

(20) “Drive Shoe” means any device specifically designed, fabricated, and installed to protect the bottom end of a water well casing or liner pipe from collapse or other damage while the casing or liner pipe is being driven into place in a well.

(21) “Essential Use” includes the use of water strictly for fire-fighting purposes, health and medical purposes, and the use of water to satisfy federal, state, or local public health and safety requirements.

(22) “Freeze Protection” includes the periodic and infrequent use of water to protect agricultural and nursery crops from permanent damage due to low temperatures.

(23) “Golf Course Irrigation Use” is the use of water to irrigate golf courses.

(24) “Grout” means a mixture consisting of water and Portland cement (American Concrete Institute type I or American Concrete Institute type III), sand and Portland cement mixed at three parts sand to one part cement by weight, or other approved types of cement and acceptable amounts of those additives approved by the District for use in cement grouts. The use of alternative methods or materials shall not cause degradation of the water resource. Grout composition shall not exceed six (6) gallons of water per cubic foot or sack of cement.

(25) “Heating or Cooling Use” means the use of water for heating, air-conditioning, or other cooling uses.

(26) “Industrial Use” includes those many uses wherein the water serves the purposes of manufacturing, commerce, trade or industry.

(27) “Injection Well” means a well for the express purpose of introducing under pressure any water into underground formations. This includes return wells for air conditioning systems and injection of water under pressure into underground formations for the possible purpose of storage and later recovery.

(28) “Landscape Irrigation Use” is the outside watering of plants, shrubs, grass, trees, and other such flora in landscapes surrounding homes, non-commercial house-hold gardens, industrial buildings, parks, recreational areas, cemeteries, public right-of-ways, and medians.

(29) “Livestock and Other Animals Use” includes water for drinking by or washing of livestock, including zoo animals.

(30) “Mining Use” includes use wherein the water is applied for the extraction, transportation, or processing of minerals.

(31) “Navigation Use” means water discharged from ground or surface sources either to tide water or to downstream lakes or reaches of rivers or canals for the purpose of permitting or protecting boating activity.

(32) “Nursery Irrigation Use” (Non agricultural) is the use of water on premises on or in which nursery stock is held for sale, distribution or is sold or reshipped. This term does not apply to water used for production of nursery stock.

(33) “Other Outside Use” means the use of water outdoors for dust control, maintenance, cleaning, and washing of structures and mobile equipment, including automobiles and the washing of streets, driveways, sidewalks, and similar areas.

(34) “Limited Use Public Supply” means the use of water in public water systems not covered under the definitions of Domestic Self Supply use or Public Water Supply Use of this section, and which is further defined as either:

(a) “Limited Use Commercial Public Water Systems Use” means the use of water by one or more nonresidential establishments; or

(b) “Limited Use Community Public Water System Use” means the use of water by five or more private residences or two or more rental residences.

(35) “Perishable Food Processing Use” includes industrial uses involving the processing of perishable food.

(36) “Power Production Use” includes use for steam or co-generation and the use of water for cooling and for replenishment of cooling reservoirs.

(37) “Public Water Supply Use” is the use of water as defined by the Florida Safe Drinking Water Act, and means the use of water by a Public Water System.

(38) “Public Water System” means a system for supplying water for human consumption, if such system has at least 15 service connections or regularly serves at least 25 individuals daily at least 60 days out of the year. A Community Water System is a public water system which has at least 15 service connections used by year-round residents or which regularly serves at least 25 year-round residents. A non-Community Water System is a public water system which serves at least 25 individuals daily at least 60 days out of the year but the individuals served are not year-round residents and may be transients.

(39) “Recharge Well” means a well for the express purpose of introducing any waters into any underground formation. This definition shall include drainage or connector wells.

(a) “Drainage Well” generally describes a well for the express purpose of disposing of excess surface waters by gravity flow into any underground formation.

(b) “Connector Well” is a well for the express purpose of draining one aquifer and allowing this water to recharge another aquifer (interaquifer transfer).

(40) “Recreation Area Irrigation Use” is the use of water to irrigate recreational areas such as soccer, baseball, and football fields or playgrounds.

(41) “Sanitation Use” includes supplying water for toilet facilities, and for cleaning, when the use is in a non-residence. This use does not include drinking water or water used in cooking.

(42) “Soil Flooding Use” means the use of water for raising of water levels on agricultural lands for purposes not directly related to such purposes as crop growth, soil preservation, crop harvesting, and pest control.

(43) “Test Well” or “Test Hole” is a well constructed for temporary use, designed to allow specific geological or groundwater parameters to be examined prior to the construction of a permanent well.

(44) “Water-Based Recreation Use” is the use of water for public or private swimming and wading pools and other water-oriented recreation such as fishing, boating, and swimming, and including water slides.

(45) “Well Completion” means a well that meets all construction standards specified in Part II.

(46) “Well Seal” means an arrangement or device that prevents contaminants from entering the well at the upper terminal and that is approved by the District as satisfying the requirements of Rule 40A-3.521, F.A.C., of this rule.

(47) “Onsite Sewage Disposal System (OSDS)” means a sewage treatment and disposal facility, which may contain a standard subsurface, filled, or mound drainfield system, an aerobic treatment unit, a graywater system tank, a laundry wastewater system tank, a septic tank, a grease interceptor, a dosing tank, a solids or an effluent pump, alternative system or experimental system.

(48) “Sanitary Hazard” means a physical condition which involves or affects any part of a drinking water system or the raw water source, and that creates an imminent or potentially serious risk to the health of any person who consumes water from that system.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.303, 373.306, 373.308, 373.309, 373.313, 373.316, 373.319, 373.323(2) FS. History–New 4-14-80, Amended 2-1-82, 3-29-84, 10-1-84, 1-9-86, Formerly 16G-3.02, Amended 4-5-88, 8-1-89, 12-1-90, 11-1-92, 11-1-93, 11-1-95, 7-1-98, 8-15-18.

## 40A-3.031 Implementation.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.103(1), 373.306, 373.308, 373.309, 373.313, 373.314, 373.316, 373.319, 373.323(2), 373.326, 373.329, 373.333, 373.342 FS. History–New 4-14-80, Amended 2-1-82, 3-29-84, 10-7-82, 1-9-86, Formerly 16G-3.03, Repealed 7-1-98.

## 40A-3.032 Delegation.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.308, 373.309(2), 373.342 FS. History–New 1-9-86, Repealed 7-1-98.

## 40A-3.037 Water Well Contractor Licensing.

(1) Chapter 62-531, F.A.C., effective 8-7-19, which requires the licensing of water well contractors, is hereby incorporated by reference, https://www.flrules.org/Gateway/reference.asp?No=Ref-11589, a copy can be obtained from District offices upon request. The licensing program shall be administered and enforced by the District under the authority delegated to it by the Department of Environmental Protection by Order dated July 11, 1984.

(a) The Water Well Contractor Continuing Education Program Manual, effective 8-7-19, http://www.flrules.org/Gateway/reference.asp?No=Ref-11590, is referenced in Chapter 62-531, F.A.C., and is hereby incorporated by reference, and requires the use of the following forms, which are also incorporated by reference:

1. Coursework Certificate of Attendance and Evaluation, Florida Water Well Contractor Continuing Education Program, Form 1, effective 6-22-14, http://www.flrules.org/Gateway/reference.asp?No=Ref-09478.

2. Florida Water Well Contractor Continuing Education Program, Certificate of Completion, Form 2, effective 6-22-14, http://www.flrules.org/Gateway/reference.asp?No=Ref-09479.

3. Application for Continuing Education Coursework Approval, Florida Water Well Contractor Continuing Education Program, Form 3, effective 6-22-14, http://www.flrules.org/Gateway/reference.asp?No=Ref-09617.

4. Application for Continuing Education Course Provider, Florida Water Well Contractor Continuing Education  Program, Form 4, effective 6-22-14, http://www.flrules.org/Gateway/reference.asp?No=Ref-09618.

Copies of the Water Well Contractor Continuing Education Program Manual and the forms referenced therein can be obtained from District offices upon request.

(b) The Water Well Construction Disciplinary Guidelines and Citations Dictionary, effective 6-22-14, http://www.flrules.org/Gateway/reference.asp?No=Ref-09619, is referenced in Chapter 62-531, F.A.C., and is hereby incorporated by reference, and a copy can be obtained from District offices upon request.

(2) Unlicensed persons violating the provisions of Chapter 373, F.S., or these rules, or orders of the District are subject to the disciplinary procedures prescribed in Section 373.323, F.S.

Rulemaking Authority 373.044, 373.113, 373.323, 373.337 FS. Law Implemented 373.323 FS. History–New 10-1-84, Amended 8-1-89, 8-15-18, 5-20-20.

## 40A-3.038 Violations of Licensing Requirements.

Rulemaking Authority 373.044, 373.113, 373.171, 373.323, 373.337 FS. Law Implemented 373.323, 373.333, 373.336 FS. History–New 1-9-86, Amended 8-1-89, 12-1-90, 11-1-92, Repealed by Section 3, Chapter 2012-31, Laws of Florida, 5-27-12.

## 40A-3.040 Implementation.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.303, 373.308, 373.309, 373.316, 373.326, 373.324 FS. History–New 1-9-86, Repealed 7-1-98.

## 40A-3.041 Permits Required.

(1) Unless expressly exempted by Statute or District rule, a permit must be obtained from the District prior to construction, repair, or abandonment of a well and the well must be constructed, repaired, or abandoned by a licensed water well contractor. Any potable water well proposed within an area of ground water contamination, as delineated by the Department, will be permitted as follows.

(a) The maps identified below, which are incorporated herein by reference, effective 6-27-00, show surface areas delineated by the Department as areas within which ground water contamination is known to exist or which encompasses vulnerable areas or areas in which the Department provides a subsidy for restoration or replacement of contaminated drinking water supplies. Each map listed contains a month and year which corresponds to the date the Department prepared the most recent map showing any portion of a delineated area. Copies of these maps can be obtained from District offices upon request.

1. ESCAMBIA COUNTY:

Cantonment 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09455;

Pensacola 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09485;

Seminole (AL) 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09486;

West Pensacola 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09456.

2. JACKSON COUNTY:

Alford 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09457;

Bascom 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09458;

Campbellton 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09459;

Cottondale East 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09483;

Cottondale West 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09484;

Cypress 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09460;

Dellwood 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09461;

Fairchild (GA) 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09462;

Graceville 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09463;

Kynesville 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09464;

Malone 11/94, https://www.flrules.org/Gateway/reference.asp?No=Ref-09465;

Marianna 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09466;

Oakdale 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09467;

Grangeburg (AL) 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09468;

Saffold (AL) 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09469;

Sills 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09470;

Sneads 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09471;

Steam Mill (GA) 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09472.

3. LEON COUNTY:

Tallahassee 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09473.

4. SANTA ROSA COUNTY:

Milton South 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09474;

Pace 11/94, http://www.flrules.org/Gateway/reference.asp?No=Ref-09475.

(b) Well Construction Requirements:

1. New potable water wells shall comply with the minimum construction standards contained in Chapter 40A-3, F.A.C., and additional requirements assigned by the permitting authority relative to depth restrictions, location of screened or open hole interval, and length of casing where warranted by local specific information.

2. Methods of constructing new potable water wells shall be limited to rotary drilling, boring, or other method specificallly approved by the permitting authority which meets the water well construction criteria in this chapter and as required below:

a. Well casing and liner pipe shall be new, free of breaks, corrosion and dents, straight and true, and not out of round. Welded or seamless black or galvanized steel pipe or casing, or stainless steel pipe or casing, or approved types of nonmetallic pipe shall be used for well casing or liner pipe.

b. Solvent-bonded couplings shall be prohibited in areas with known ground water contamination which includes solvent components.

c. To prevent the interchange of water and loss of artesian pressure, contaminated, unconfined ground water intervals shall be sealed off prior to drilling through the underlying confining interval. Uncontaminated, unconfined ground water intervals shall be sealed off or otherwise protected prior to drilling into deeper, contaminated ground waters.

d. For any well casing installed in a bore hole with an annular space around the casing, the annular space shall be filled from bottom to top with not less than a nominal two inch thickness of neat cement grout.

e. A concrete pad measuring three feet by three feet by four inches shall be constructed around the elevated portion of the casing so that the casing is centered in the pad to prevent soil erosion and seepage of surface contamination into the annular space.

f. A minimum elevation of one foot of casing above land surface shall be required.

g. A raw water tap shall be provided to allow sampling of the well before exposure to storage or treatment.

h. The well casing shall be visibly and permanently marked above the land surface with the latitude and longitude and the permit number issued by the permitting authority for that well.

i. To the extent practical, potable water wells shall be located outside any delineated area identified in paragraph 40A-3.041(1)(a), F.A.C.

j. Where the source of contamination and the direction of ground water flow are known, in a delineated area identified in paragraph 40A-3.041(1)(a), F.A.C., to the extent practical, potable water wells shall be located upgradient of the source.

k. New potable water wells shall be located on ground least subject to inundation.

l. Any new potable water well constructed within a delineated area that does not meet the construction standards of this section shall be abandoned and plugged in accordance with Rule 40A-3.531, F.A.C., and applicable water mangement district rules.

3. New potable water wells shall be tested by the Department or other delegated authority using methods as specified by the Department in accordance with Section 373.309, F.S., for the presence in the untreated water of the ground water contamination which resulted in the delineation. The Department shall accept only test results obtained from water samples collected and analyzed by the Department of Health. The well construction permit applicant shall be responsible for the cost of sample collection, shipping, and analysis.

a. If no ground water contamination is found upon testing of a new potable well in a delineated area, the Department of Health shall be responsible for the issuance of a letter of clearance to the well construction permit applicant.

b. If ground water contamination is found upon testing or other ground water contamination is found, a well shall not be cleared for use without a demonstration, through water quality testing, that a filter or other permament remedy prevents the users of the well from being exposed through ingestion, inhalation, or dermal absorption, as appropriate for a contaminant, to ground water contamination.

4. Exemption from the requirements for construction of wells in delinated areas shall be granted to an applicant by the District or the permitting authority upon demonstration using hydrogeological, water quality, and other pertinent information that the exemption will not result in the impairment of the intent and purpose of this chapter. Detailed requirements for each exemption shall be negotiated between the permit applicant and the permitting authority on a case by case basis.

(c) Permit Requirements:

1. A construction or modification permit shall be obtained pursuant to Rule 40A-3.041, F.A.C., for all new potable wells prior to installation or conversion. Applicants shall submit a proposed well design with the completed application, and the permit fee, to the District. In addition to the general requirements of this chapter, the permit shall address the following requirements through special conditions:

a. Well construction including method of construction, depth, location of cased and screened intervals, casing material and grouting.

b. Any special cleaning requirements for casing or drilling equipment.

c. Water quality testing.

d. Unique well identifiers where needed.

2. Permitting and construction of new potable water wells, except for a well to be used for a public water system, are prohibited in delineated areas where a distribution line of an available potable water system is within 500 feet of the boundary of the property for which a well construction permit is being sought. Such prohibition applies unless the property owner or applicant obtains documentation from the public water system or the Department’s Water Supply Restoration and Replacement Program, and submits such documentation to the permitting entity, which demonstrates either of the following:

a. That economic factors caused by physical or legal impediments to construction to a distribution line prevent the property owner or permit applicant from obtaining potable water through connection to the distribution line; or

b. That necessary water distribution line extension (excluding plumbing and meters) cannot be completed within 30 days of application to the Department for water supply restoration or replacement.

(d) Prohibited Acts:

1. It shall be a violation of Section 373.309, F.S., and this chapter to construct, repair, convert from non-potable use, or abandon any potable water well, or use for human consumption any well subject to permit under this chapter without having obtained a permit pursuant to this section. This prohibition shall apply to both the water well contractor and the well owner.

2. It shall be a violation of Section 373.309, F.S., and this chapter to use for human consumption, after delineation, any water well subject to permit under this section without having performed water quality testing pursuant to subparagraph 40A-3.041(1)(b)3., F.A.C.

3. It shall be a violation of Section 373.309, F.S., and this chapter to use for human consumption, after delineation, any water well subject to permit under this section in which contaminants have been found without a demonstration through water quality testing that a filter or other means of preventing the users of such well from being exposed to ground water contamination is effective.

(e) Penalties.

1. Any person who violates any provision of this chapter pertaining to delineated areas, orders regarding delineated areas, or permits issued in delineated areas under the authority of this chapter shall, upon conviction, be guilty of a misdemeanor of the second degree, punishable as provided in Sections 775.082 and 775.083, F.S. Continuing violation after an order or conviction shall constitute a separate violation for each day the violation occurs.

2. Any water well contractor who is in violation of subparagraph 40A-3.041(1)(d)1., F.A.C., shall, in addition to subparagraph 40A-3.041(1)(e)1., F.A.C., also be subject to the penalty provisions in Chapter 62-531, F.A.C., which is incorporated by reference in subsection 40A-3.037(1), F.A.C., including the license suspension and revocation provisions contained therein.

(2) A permit to construct, repair, modify or abandon any water well meeting the provisions of Chapter 373, Part III, F.S., and Chapter 40A-3, F.A.C., will be issued by the Executive Director. However, if a permit request is considered for denial or a written objection is filed to the issuance of a permit, or the application is for the construction of an artificial recharge facility, then the application shall be processed in accordance with the applicable provisions of Rule 40A-1.203, F.A.C., and acted upon by the District’s Governing Board.

(3) Permit applications shall be filed with the District on Department Form Number 62-532.900(1), State of Florida Permit Application to Construct, Repair, Modify, or Abandon a Well, hereby incorporated by reference, effective 10-7-10, https://www.flrules.org/Gateway/reference.asp?No=Ref-09094, and a copy can be obtained from District offices upon request. The required fee shall be submitted with the permit application. Applications to construct an artificial recharge facility shall be accompanied by a completed copy of the Application to Construct/Operate/Abandon Class I, III, or V Injection Well Systems, effective 6-24-97, Department Form Number 62-528.900(1), F.A.C., hereby incorporated by reference, effective 6-24-97, https://www.flrules.org/Gateway/reference.asp?No=Ref-09104, and a copy can be obtained from District offices upon request.

(4) Permits for water use must be obtained under the provisions of Chapter 40A-2, F.A.C. A well shall not be constructed until an Individual water use permit is granted, if a water use permit is required.

(5) Additional information may be required such as: geophysical logs, geologic samples and logs, a list of proposed construction methods, a description of proposed pump tests, a list of well specifications, a description of the proposed water quality monitoring systems, and a description of the proposed total monitoring system.

(6) Receipt of the permit will constitute permission to begin well construction, repair, or abandonment.

(7) The District permit for a public water supply well does not constitute approval of the public water system. A separate application must be submitted to the Department in accordance with subsection 62-555.102(2), F.A.C., to obtain a permit to construct or alter a public water supply system.

(8) The permit shall be available at the site of the well during construction, repair or abandonment.

(9) Any permittee who desires to change the location of a well or otherwise amend a permit shall apply to the District for an amendment. No charge shall be made to amend the permit. As a condition to approving any amendment, the District may require remedial action to bring any work accomplished under the original permit into compliance with provisions of this chapter.

(10) A repair permit is not necessary if remedial work is performed on a well before the expiration date of the construction permit; however, an updated completion report should be filed with the District if the well depth or casing depth is increased.

(11) Permits will not be granted after a water well has been constructed, repaired, or abandoned, except in the case of subsection (12) below. As a condition to the enforcement action taken, a contractor will be required to submit a permit application and completion report for the District’s records.

(12) A permit to abandon is required for any well which was constructed and found unsuitable for use. If the contractor is in the drilling process and needs to abandon, he may perform the work prior to obtaining a permit; however, the permit must be obtained by telephone or in person no later than 24 hours following the well abandonment. The hole must be properly abandoned (plugged) according to the standards of subsection 40A-3.531(4), F.A.C.

(13) If a well unsuitable for use is abandoned (plugged), and the contractor plans to construct a new well, he may use the construction permit granted for the first well, provided that it has not expired.

(14) Receipt of a permit from the District does not alleviate the responsibility of the applicant to obtain other permits that may be necessary from local, state, or federal agencies. If more stringent rules concerning construction standards for water wells are promulgated by local permitting authorities, those standards shall apply.

(15) A permit to abandon a test well or test hole is required to be obtained by the property owner, through a licensed water well contractor, within six (6) months from the date of well construction permit issuance. However, if the test well or test hole was constructed to permanent well standards and meets all applicable setback requirements, the well may be converted to permanent well status by obtaining an additional construction permit for the new permanent well type. A new permit application fee must also be submitted in accordance with the proposed permanent well type.

(16) A single permit may be obtained for the construction, repair, or abandonment of the following multiple well systems provided the wells have similar construction into the same geologic formation, are completed in the same hydrogeologic unit, are located on contiguous tract(s) of land for which the applicant demonstrates a legal right to construct, repair or abandon a well(s), have individual total well depths equal to or less than fifty (50) feet below land surface, have individual well nominal casing with inner diameters equal to or less than four (4) inches, meet the criteria in Rule 40A-3.301, F.A.C., and comply with all applicable construction, location, casing and grouting requirements set forth in Chapter 40A-3, F.A.C.:

(a) Up to ten (10) monitor wells; or

(b) Up to ten (10) site investigation wells. Site investigation wells shall be abandoned under a separate permit no later than 90 days after construction is completed.

Rulemaking Authority 373.044, 373.113, 373.171, 373.337 FS. Law Implemented 373.106, 373.109, 373.306, 373.308, 373.309, 373.313, 373.314, 373.316, 373.337, 373.342, FS. History–New 4-14-80, Amended 4-13-81, 2-1-82, 10-7-82, 3-29-84, 1-9-86, Formerly 16G-3.04, 16G-3.11, Amended 8-1-89, 12-1-90, 2-14-91, 11-1-95, 7-1-98, 8-15-18, 5-20-20.

## 40A-3.051 Exemptions.

(1) A permit is not required prior to the construction, repair, or abandonment of any well exempted by Sections 373.303(7) and 373.326, F.S. (any well for the purpose of obtaining or prospecting for oil, natural gas, minerals, or products of mining or quarrying; wells for inserting media to dispose of oil brines, or to repressure oil or natural gas-bearing formations; wells for storing petroleum or natural gas or other products; or wells used for temporary dewatering for construction purposes).

(2) When the District finds that compliance with all requirements of this chapter would result in undue hardship, supported by information which demonstrates that the intent and purpose of the rule will not be impaired, an exemption from any one or more such requirements shall be granted by the District to the extent necessary to ameliorate such undue hardship. Such information may include water quality sampling or other reasonable information or action deemed necessary to assure the well will not adversely impact the water resource. The request for an exemption must be submitted in writing and detail the reasons why compliance with the requirements of this chapter will create a hardship.

(3) A water well contractor license is not required for a homeowner when he/she plans to construct a well two (2) inches or less inside diameter on his/her own or leased property, intended for use only in a single family house which is his/her residence or intended for use only for farming purposes on his/her farm, and when the waters to be produced are not intended for use by the public or any residence other than his/her own. However, the well construction must meet all applicable standards of this chapter.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.303, 373.306, 373.308, 373.309, 373.313, 373.316, 373.326 FS. History–New 4-14-80, Amended 2-1-82, 5-17-83, 3-29-84, 1-9-86, Formerly 16G-3.05, 16G-3.12, Amended 8-1-89, 12-1-90, 11-1-92, 7-1-98, 8-15-18.

## 40A-3.201 Permit Application Fees.

(1) There shall be an application fee according to the following schedule, unless the well is a potable well within a delineated area as established by the Department, pursuant to Chapter 62-524, F.A.C.:

|  | OUTSIDE DIAMETER | FEE* |
| --- | --- | --- |
|  | OF CASING |  |
| Public Supply Wells, Construction and Repair | All Diameters | $250.00 |
| Limited Use Public Supply Wells, Construction and Repair | All Diameters | $200.00 |
| All Other Wells, Construction and Repair, | 6 Inches and larger | $100.00 |
| Not Listed Above | Diameter |  |
| All Other Wells, Construction and Repair, | 4 Inch Diameter, but less | $50.00 |
| Not Listed Above | than 6 Inch Diameter |  |
| All Other Wells, Construction and Repair, | Less than 4 Inch Diameter | $35.00 |
| Not Listed Above |  |  |
| Monitor Wells | All Diameters | $30.00 |
| Well Abandonment | All Diameters | $10.00 |
| Emergency Telephone Authorization – Added to |  |  |
| Regular Permit Fee | All Diameters | $25.00 |
| Exemption (variance) Added to | 6 Inches and Larger | $150.00 |
| Regular Permit Fee | Less Than 6 Inches | $50.00 |

(2) There shall be an application fee according to the following schedule, for those potable wells constructed within an area of groundwater contamination, as delineated by the Department pursuant to Chapter 62-524, F.A.C.:

|  | OUTSIDE DIAMETER | FEE* |
| --- | --- | --- |
|  | OF CASING |  |
| Public and Limited Use | All Diameters | $500.00 |
| Public Supply Wells |  |  |
| Potable Wells Serving | All Diameters | $100.00 |
| Single Family Residences |  |  |
| Exemption (variance) | 6 Inches and Larger | $150.00 |
| Added to Regular Permit Fee | Less Than 6 Inches | $50.00 |
| *All permit application fees shall be non-refundable. |  |  |

Note: The Emergency Telephone Authorization Fee and Exemption Fee are in addition to the standard permit fees listed above, and shall accompany applications for permits.

Rulemaking Authority 373.044, 373.109, 373.113, 373.171, 373.337 FS. Law Implemented 373.109, 373.309 FS. History–New 4-14-80, Amended 6-11-80, 4-13-81, 2-1-82, 5-17-83, 1-9-86, Formerly 16G-3.20, 16G-3.13, Amended 8-1-89, 1-1-90, 12-1-90, 2-14-91, 11-1-93.

## 40A-3.301 Conditions for Issuance of Permits.

(1) The District shall complete action upon any permit application within fourteen (14) days after receipt of a complete application, except in the case of water wells constructed for public water supply systems as defined in subsection 62-532.200(23), F.A.C., and wells constructed for the artificial recharge of water, wells requiring an Individual Water Use Permit under provisions of Chapter 40A-2, F.A.C., in which case permit action shall be completed within 90 days of receipt of a complete application for the construction of an artificial recharge well or Chapter 40A-2, F.A.C., application.

(2) The issuance of a permit is dependent upon:

(a) The application being accompanied by the required fee, and containing the information required on Department Form Number 62-532.900(1), State of Florida Permit Application to Construct, Repair, Modify, or Abandon a Well, incorporated by reference in subsection 40A-3.041(3), F.A.C., effective 10-7-10, https://www.flrules.org/Gateway/reference.asp?No=Ref-09094. An application will be deemed incomplete if any portion of the application form is left blank or if the required sketch is illegible, does not provide the means to locate the proposed well, or is not consistent with the land coordinates provided in the application.

(b) The proposed construction, repair, or abandonment being in accordance with applicable law, rules, and orders.

(c) The work being done for a purpose and in a manner which is consistent with generally accepted engineering, hydrologic, and hydrogeologic practices.

(d) Whether the construction of the well will adversely affect the ground water resources.

(e) Whether the proposed well’s proximity to an area of ground water contamination delineated under the provisions of Chapter 62-524, F.A.C., may adversely affect the ground water resources or present a threat to the health, safety, and welfare of individuals who, through ingestion, inhalation, or dermal absorption may be exposed to ground water contamination.

(f) Whether the Governing Board has approved the issuance of an Individual Water Use permit or the construction of an artificial recharge well, if applicable.

(3) A permit may be granted with certain conditions or restrictions, such as:

(a) Collection and submittal of geologic samples;

(b) Geophysical logs required;

(c) Conducting and submitting data from an aquifer performance test;

(d) Borehole diameter restricted;

(e) Total depth restricted;

(f) Length of casing specified;

(g) Capacity of pump restricted;

(h) Water use permit required;

(i) Grouting notification required;

(j) Grout specified;

(k) Water quality sampling and data submittal required;

(l) Water Treatment Systems (including filters);

(m) In areas delineated under the provisions of Chapter 62-524, F.A.C., a water well construction permit shall not be issued unless the well is constructed to criteria intended to protect the water resources from further contamination and the health, safety, and welfare of individuals who, through ingestion, inhalation, or dermal absorption may be exposed to ground water contamination. This criteria shall include stipulations on any of the following items: casing depth, construction method, well depth, water quality sampling, grout specifications, the installation of a water treatment system such as a filter and setback distance from a specific known source of contamination;

(n) Other such reasonable conditions as are necessary to assure that the well will comply with the requirements of Chapter 373, F.S., and will not adversely impact the water resources of the District.

(4) If the permit is obtained by the owner, the permit will be granted with the condition that the permit document be signed by the licensed water well contractor who will perform the work and return the permit to the District prior to construction, repair, or abandonment.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.109, 373.306, 373.308, 373.309, 373.313, 373.323, FS. History–New 4-14-80, Amended 2-1-82, 10-7-82, 5-17-83, 3-29-84, 1-9-86, Formerly 16G-3.30, 16G-3.14, Amended 8-1-89, 11-1-92, 11-1-95, 7-1-98, 8-15-18.

## 40A-3.321 Duration of Permits.

All permits shall be valid for a period of ninety (90) days. If construction, repair or abandonment is not completed within that time, the District shall extend the permit for a period not to exceed ninety (90) days provided the conditions of the original permit application have not changed. Public water supply well permits may be renewed for a period of up to one (1) year from the date of permit issuance (in increments of ninety days per renewal request only). The District must receive a written request for an extension from the permittee or permittee’s agent before the original permit expires.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.308, 373.309 FS. History–New 1-9-86, Formerly 40A-3.041, Amended 8-10-87, 8-1-89, 12-1-90, 11-1-95.

## 40A-3.341 Disapproval of Wells.

(1) The District shall disapprove any water well or abandoned well if the District finds, after inspection, that the well does not comply with the provisions of this chapter.

(2) The District shall disapprove any well if the well is determined not to be suitable for the intended use identified in the application submitted to the District or if the well represents a threat to the water resources, or if the well is determined by the Department of Environmental Protection or the Department of Health and Rehabilitative Services to pose a threat to the health, safety, or welfare of the user.

(3) No well which has been disapproved may be used until it has been brought into compliance with this chapter. A well that cannot be brought into compliance with the District’s rules shall be abandoned as required by subsection 40A-3.531(4), F.A.C.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.306, 373.308, 373.309, 373.319 FS. History–New 4-14-80, Amended 4-13-81, 2-1-82, 10-1-84, Formerly 16G-3.34, 16G-3.18, Amended 8-1-89, 7-1-98, 8-15-18.

## 40A-3.342 Permit Denial.

(1) The District shall issue a notice of Intent to Deny whenever it determines that an application for a permit under Rule 40A-3.041, F.A.C., fails to meet the requirements of Chapter 373, F.S., or Chapter 40A-3, F.A.C., or any rule, order, or standard adopted pursuant thereto.

(2) The Notice of Intent to Deny shall:

(a) State the grounds for denial;

(b) Give the date of the Governing Board meeting at which the recommendation for denial shall be presented according to the procedures set forth in subsection 40A-3.342(3), F.A.C.; and

(c) Be served in writing upon the contractor and owner at their last known addresses by registered or certified mail.

(3) The Governing Board shall be presented with a recommendation for denial of a permit application at the first regularly scheduled Board meeting following the determination that an application for a permit under Rule 40A-3.041, F.A.C., fails to meet the requirements of Chapter 373, F.S., or Chapter 40A-3, F.A.C., or any rule, order, or standard adopted pursuant thereto. At that time pertinent facts concerning the basis for denial shall be presented, and the contractor and owner will have an opportunity to present pertinent information. The Governing Board shall then decide to:

(a) Grant a permit to construct, repair, or abandon a water well as specified in the application;

(b) Grant a permit as in paragraph (a), above, except that certain conditions or restrictions authorized by law are imposed; or,

(c) Deny a permit, stating the reason for such denial.

(4) The District shall notify the contractor and owner of final Board action described in subsection 40A-3.342(3), F.A.C., within fourteen (14) days after the action. The Notice of Denial shall:

(a) State the grounds for denial; and

(b) Be served in writing upon the contractor and owner at their last known addresses by registered or certified mail.

(5) Any person receiving a denial may request a hearing by filing a written petition with the District within 21 days of the mailing of the notice.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.306, 373.313 FS. History–New 4-14-80, Amended 2-1-82, 1-9-86, Formerly 16G-3.17, 16G-3.31, Amended 4-5-88, 11-1-92, 7-1-98.

## 40A-3.411 Completion Reports.

(1) Within thirty (30) days after the expiration of a permit, a well completion report shall be filed with the District on the forms provided by the District and in accordance with the instructions provided thereon.

(2) If no work is performed or if the well is not completed, a report shall be filed within thirty (30) days of the expiration of the permit stating that no well construction was performed under the permit or outlining the status of the incomplete well.

(3) Department Form Number 62-532.900(2), State of Florida Permit Well Completion Report, hereby incorporated by reference, effective 10-7-10, https://www.flrules.org/Gateway/reference.asp?No=Ref-09091, shall be used to report the completion of construction, repair, or abandonment of any well within District jurisdiction. A copy can be obtained from district offices upon request.

(4) The water well contractor shall provide the well owner a copy of the well completion report.

(5) The information filed as a part of the completion report shall be truthful and accurate in providing the specifications and characteristics of the constructed well. (See subsection 40A-3.901(3), F.A.C.)

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.308, 373.309, 373.313 FS. History–New 4-14-80, Amended 5-17-83, 1-9-86, Formerly 16G-3.41, 16G-3.15, Amended 8-1-89, 11-1-95, 8-15-18.

## 40A-3.451 Emergency Authorization.

(1) Permission to begin construction, repair, or abandonment of any well may be applied for by telephone when conditions exist which would justify such a request. The District may grant such permits at its discretion. However, a serious set of unforeseen circumstances must exist to create an emergency. Mere carelessness, lack of planning on the part of the applicant (the owner or the contractor for the owner) or a desire to expedite the required work shall not be sufficient grounds to warrant the granting of an emergency authorization.

(2) Emergency permits shall be obtained from the District Headquarters only.

(3) Emergency permit applications shall be accompanied by a $25.00 fee in addition to the standard fee.

(4) The recipient of an emergency authorization shall submit an application in writing in accordance with the provision of Rule 40A-3.041, F.A.C., Permits Required. Permit applications shall be postmarked within 24 hours of the time the emergency authorization was granted by the District; the application shall also be accompanied by a handwritten note stating the nature of the emergency. All other provisions of these rules shall remain in force.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.109, 373.308, 373.309, 373.313, 373.326, 373.342, 373.333 FS. History–New 4-14-80, Amended 1-9-86, Formerly 16G-3.45, 16G-3.16, Amended 5-20-20.

## 40A-3.461 Inspections.

(1) The District is authorized to inspect any water well or abandoned water well within its area of responsibility. The District may cause to be made such inspections as it deems necessary to insure conformity with applicable standards of this rule chapter. Duly authorized representatives of the District may, at reasonable times, enter upon and shall be given access to any premises for the purpose of such inspection.

(2) If, upon the basis of such inspections, the District finds the standards of this rule chapter have not been met, the District shall give the owner and contractor written notice stating which rules have been violated and shall order that necessary corrective action be taken within a reasonable time to be prescribed in such order. Failure to act in accordance with the order of the District after receipt of written notice shall be grounds for disapproval of the well.

(3) A site inspection must be completed by an authorized representative of the District or the Department prior to issuing a permit for construction of a public water supply well.

(4) The District shall be notified at least 24 hours in advance of placement of grout in the annular space of any public supply water well; failure to notify the District sufficiently in advance may result in delay of completion of the well. A District representative will be on site to observe the grouting. If the District is properly notified and an inspector is not at the site at the appointed time, the grouting may be accomplished in his absence.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.119, 373.308, 373.309, 373.319, 373.333 FS. History– New 4-14-80, Amended 2-1-82, 1-9-86, Formerly 16G-3.46, 16G-3.22, Amended 7-1-98, 3-2-00.

## 40A-3.492 Violations of Permits.

(1) Actions, omissions, or conduct which shall be considered as violations for the purposes of Part I, Permitting, shall include the following:

(a) Failure to obtain a permit where required under Rule 40A-3.041, F.A.C.

(b) Failure to provide accurate information in the application for a permit.

(c) Failure to fulfill the guidelines for obtaining an emergency permit.

(d) Failure to comply with any or all permit conditions.

(e) Failure to submit a completion report within the time period specified in Rule 40A-3.411, F.A.C.

(f) Failure to file an accurate completion report.

(g) Failure to report to the District within thirty (30) days of expiration of the permit when no work is performed or the well is not completed.

(h) Failure to notify the District 24 hours prior to the grouting of the annular space of any public supply well.

(i) Failure to fulfill any other applicable requirements of Chapter 373, Part III, F.S., or Chapter 40A-3, F.A.C.

(2) Actions which may be taken by District staff upon determination that a violation has occurred are outlined in Rule 40A-3.980, F.A.C., of these rules.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.306, 373.308, 373.309, 373.319 FS. History–New 1-9-86, Formerly 40A-3.953, Amended 11-1-92, 11-1-95.

## 40A-3.500 Scope of Part II.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.308, 373.309, 373.313 FS. History–New 1-9-86, Repealed 7-1-98.

## 40A-3.502 Construction Methods.

(1) Wells must be so constructed, cased, grouted, plugged, capped, or sealed as to prevent uncontrolled surface flow, uncontrolled movement of water from one aquifer or zone to another, contamination of ground water or surface water resources, or other adverse impacts.

(a) For public water supply wells connected to a community water system on or after August 28, 2003, except those connected under a construction permit for which the Department received a complete application before August 28, 2003, continuing protection of the well from the sanitary hazards shall be provided during the entire useful life of the well through one of the following means:

1. Ownership by the water supplier of all land within 100 feet of the well;

2. Control by the water supplier of all land within 100 feet of the well via easements, lease agreements, or deed restrictions that appropriately limit use of the land; or

3. Wellhead protection, zoning, or other land use regulations that appropriately limit use of all land within 100 feet of the well.

(b) Public water supply wells shall be located to comply with the setback distances identified in Table I below.

| Table I |
| --- |
| Water Well Setback Distances for Drinking Water Supply Wells Serving Public Water Systems or Bottled Water Plant Wells |
| Hazard Type | Installation | Setback in feet (footnote) |
| Reuse of Reclaimed Water and Land Application | Slow Rate Land Application Restricted Public Access | 500 (1.) |
|  | Rapid Rate Land Applications | 500 (2.) |
|  | Overland Flow Systems | 500 |
|  | Transmission Facilities Conveying Reclaimed Water to Restricted Public Access Slow Rate Land Application Systems, Rapid Rate Land Applications Systems, or Overland Flow Systems. | 100 |
|  | Public Access, Residential Irrigation, or Edible Crop Slow-Rate Land Application Systems | 75 |
|  | Transmission Facilities Conveying Reclaimed Water to Public Access, Residential Irrigation, or Edible Crop Slow-Rate Land Application Systems | 75 |
| Domestic Wastewater Residuals | Domestic Wastewater Residuals Land Application Areas | 500 |
| Phosphogypsum Management | Phosphogypsum Stack Systems | 500 (3.) |
| Storage Tank Systems | Aboveground or Underground Storage Tanks | 100 |
| Solid Waste Management Facilities | Solid Waste Disposal Facilities | 500 |
|  | Yard Trash Disposal, Storage, or Processing | 200 |
|  | Storage or Treatment of Solid Waste in Tanks | 100 |
| Onsite Sewage Treatment and Disposal Systems | Septic systems and associated transfer tanks and drainfields | 200 |
| Other Sanitary Hazards | Specific sanitary hazards defined in footnotes. | 100 (4., 5.) |
| Feedlot and Dairy Wastewater Treatment and Management | Dairy Farm Waste – Unlined Storage and Treatement, or High Intensity Areas | 300 |
|  | Dairy Farm Waste – Land Application Areas | 200 |

Footnotes:

1. This distance shall be reduced to 200 feet if facility Class I reliability is provided and shall be reduced to 100 feet if both facility Class I reliability and high-level disinfection are provided.

2. This distance shall be reduced to 200 feet if both facility Class I reliability and high-level disinfection are provided and if the applicant provides reasonable assurance that applicable water quality standards will not be violated at the point of withdrawal.

3. This distance applies only to shallow water supply wells (i.e., potable water wells that pump from an unconfined water table aquifer).

4. The following examples are of sanitary hazards that pose a potentially high risk to ground water quality and public health: active or abandoned mines; airplane or train fueling or maintenance areas at airports and railroad yards; concentrated aquatic animal production facilities; domestic wastewater collection/transmission systems; drainage or injection wells, oil or gas production wells, and improperly constructed or abandoned wells (i.e., wells not constructed or abandoned in accordance with this chapter); fertilizer, herbicide, or pesticide storage areas at agricultural sites, golf courses, nurseries, and parks; graveyards; impoundments and tanks that process, store, or treat domestic wastewater, domestic wastewater residuals, or industrial fluids or waste and that are not regulated by the Department; industrial waste land application areas other than those regulated by the Department; junkyards and salvage or scrap yards; pastures with more than five grazing animals per acre; cattle dip vats; pipelines conveying petroleum products, chemicals, or industrial fluids or wastes; and underground storage tanks that are not regulated by the Department, but are used for bulk storage of a liquid pollutant or hazardous substance other than sodium hypochlorite solution.

5. The following examples are of sanitary hazards that pose a moderate risk to ground water quality and public health: aboveground storage tanks that are not regulated by the Department, but are used for bulk storage of a liquid pollutant or hazardous substance other than sodium hypochlorite solution; fertilizer, herbicide, or pesticide application areas that are not under the ownership or control of the supplier of water at agricultural sites, golf courses, nurseries, and parks; railroad tracks; stormwater detention or retention basins; and surface water (the surface water setback does not apply to multi-family and private wells).

(c) New public water supply wells shall be located on their sites in such a manner that the wells are in an area free from, or least subject to, inundation with surface drainage and flood water; and to the extent practicable, new public water supply wells shall be located on their sites in such a manner that the wells are “upstream” from on-site or off-site sanitary hazards when considering the direction of ground water movement.

(2) The well construction regulations promulgated by the Department governing the construction of potable wells in delineated areas in subsection 40A-3.041(1), F.A.C., shall apply to all potable wells constructed, altered, repaired, or abandoned in those delineated areas of the District.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.306, 373.308, 373.309 FS. History–New 1-9-86, Amended 12-1-90, 2-19-91, 11-1-95, 8-15-18.

## 40A-3.504 Location.

(1) Wells shall be located so as not to pose a threat of contamination to the District’s water resources and to provide for the protection of the health, safety, and welfare of the user.

(2) Minimum spacing between wells and sanitary hazards such as septic tanks, drainfields, ground water contamination areas, cesspools, etc. shall be as specified by Section 381.0065, and Chapter 373, Part III, F.S., and the respective rules of the Department of Health and Rehabilitative Services and the Florida Department of Environmental Protection.

(3) The following minimum distances shall apply, unless an exemption has been obtained:

(a) Landscape and recreational area irrigation wells shall be located a minimum of seventy-five (75) feet from a sanitary hazard.

(b) Landscape and recreational area irrigation wells shall be located outside ground water contamination areas delineated by the Department of Environmental Protection in Rule 62-524.430, F.A.C.

(c) Domestic Self Supply water wells shall be located a minimum distance of twenty-five (25) feet from building foundations treated with pesticides.

(d) Domestic Self Supply water wells shall be located a minimum distance of seventy-five (75) feet from a sanitary hazard, such as an onsite sewage disposal system (OSDS).

(e) Domestic Self Supply water wells shall be located a minimum distance of one hundred and seventy-five (175) feet from storage and treatment facilities of livestock farms.

(f) Domestic Self Supply water wells within ground water contamination areas delineated by the Department of Environmental Protection shall be located as specified in Rule 62-524.500, F.A.C. The delineated areas are found in Rule 62-524.430, F.A.C.

(g) Limited Use Public Supply wells shall be located a minimum distance of one hundred (100) feet from a sanitary hazard, such as an onsite sewage disposal system (OSDS), if the sewage flow is less than 2,000 gallons per day or 200 feet from an OSDS with sewage flows of 2,000 gallons per day or more.

(h) Limited Use Public Supply wells, within ground water contamination areas delineated by the Department of Environmental Protection shall be located as specified in subparagraph 40A-3.041(1)(c)2., F.A.C.

(i) Public water supply wells must be located a minimum distance of two hundred (200) feet from a sanitary hazard, such as an onsite sewage disposal system (OSDS).

(j) Public water supply wells shall be located a minimum distance of one hundred (100) feet from other sanitary hazards.

(k) Public water supply wells shall be located a minimum distance of three hundred (300) feet from storage and treatment facilities of livestock farms.

(l) Public water supply wells shall be located a minimum distance of five hundred (500) feet from areas used for land application of reclaimed water.

(m) Public water supply wells within ground water contamination areas shall be located as specified in paragraph 40A-3.041(1)(b), F.A.C.

(4) The District shall increase these distances if necessary to protect the health, safety, and welfare of individuals who may be exposed to ground water contamination through ingestion, inhalation, or dermal absorption.

(5) Exemptions to the above specified distances may be obtained from the District as provided by Rule 40A-3.051, F.A.C. The exemption request will be evaluated on such criteria as gradient, well location, natural barriers, impermeable geological strata, water quality sampling, grouting, and the use of water treatment systems acceptable to the Department of Environmental Protection or the local health unit.

(6) In subdivisions platted after January 1, 1972, domestic self-supplied potable wells may be located on lots with onsite sewage disposal systems (OSDS), provided that each lot has a minimum area of at least one-half acre and either a minimum dimension of one hundred (100) feet or mean of at least one hundred (100) feet of the side bordering the street and the distance formed by a line parallel to the side bordering the street drawn between the two most distant points of the remainder of the lot, and providing the projected daily domestic sewage flow does not exceed an average of 1,500 gallons per acre per day.

Rulemaking Authority 373.026, 373.044, 373.103, 373.113, 373.171, 373.308, 373.309, 373.326, 373.337 FS. Law Implemented 373.306, 373.308, 373.309, 373.326 FS. History–New 1-9-86, Amended 4-5-88, 8-1-89, 12-1-90, 2-19-91, 11-1-92, 11-1-93, 11-1-95, 8-15-18.

## 40A-3.507 Casing and Liner Pipe Standards.

(1) For the construction of water wells, well contractors shall comply with the well casing, liner pipe, coupling, and well screen requirements in subsection 62-532.500(1), F.A.C., which is incorporated by reference in paragraph 40A-3.504(3)(g), F.A.C.

(2) For well casing or liner pipe installed by driving, the casing or pipe shall not butt together inside threaded couplings unless the joint is electrically welded so as to be completely watertight. A drive shoe is required for use on pipe installed by driving unless exempted by the District.

(3) Well casing installed by driving shall not have less than the dimensions and weights specified in Table 1, and the requirements of paragraph 62-532.500(1)(b), F.A.C., which is incorporated by reference in paragraph 40A-3.504(3)(g), F.A.C.

| TABLE 1 |
| --- |
| MINIMUM NOMINAL DIMENSIONS AND WEIGHTS FOR BLACK OR GALVANIZED STEEL CASING OR LINER PIPE INSTALLED BY DRIVING |
| Nominal | Outside | Wall | Plain End |
| Size | Diameter | Thickness | Weight |
| (in.) | (in.) | (in.) | (lb. ft.) |
| 1.25 | 1.660 | 0.140 | 2.27 |
| 1.5 | 1.900 | 0.145 | 2.72 |
| 2 | 2.375 | 0.154 | 3.65 |
| 3 | 3.500 | 0.216 | 7.58 |
| 3.5 | 4.000 | 0.226 | 9.11 |
| 4 | 4.500 | 0.237 | 10.79 |
| 5 | 5.563 | 0.258 | 14.62 |
| 6 | 6.625 | 0.280 | 18.97 |
| 8 | 8.625 | 0.277 | 24.70 |
| 10 | 10.750 | 0.307 | 34.24 |
| 12 | 12.750 | 0.330 | 43.77 |
| 14-30 |  | 0.375 (standard wall, Schedule 40) |  |
| Greater than 30 |  | 0.500 (standard wall, Schedule 40) |  |

Note: A 4 inch nominal size casing with a wall thickness of 0.188 and a plain end weight of 8.66 may be used if it conforms to standard API 5L-6/91, Grade B, 60 KSI tensile strength. For example A53-89A, Grade B, may also be substituted.

(4) Black or galvanized steel casing or liner pipe set into place without driving shall not have less than the dimensions and weights specified in Table 2.

| TABLE 2 |
| --- |
| MINIMUM NOMINAL DIMENSIONS AND WEIGHTS FOR BLACK OR GALVANIZED STEEL CASING OR LINER PIPE SET INTO PLACE WITHOUT DRIVING |
| Nominal | Outside | Wall | Plain End |
| Size | Diameter | Thickness | Weight |
| (in.) | (in.) | (in.) | (lb. ft.) |
| 1.25 | 1.660 | 0.140 | 2.27 |
| 1.5 | 1.900 | 0.145 | 2.72 |
| 2 | 2.375 | 0.154 | 3.65 |
| 2.5 | 2.875 | 0.203 | 5.79 |
| 3 | 3.500 | 0.188 | 6.65 |
| 3.5 | 4.000 | 0.188 | 7.65 |
| 4 | 4.500 | 0.188 | 8.66 |
| 5 | 5.500 | 0.188 | 10.79 |
| 6 | 6.625 | 0.188 | 12.92 |
| 8 | 8.625 | 0.188 | 16.94 |
| 10-16 |  | 0.250 |  |
| Greater than 16 |  | 0.375 |  |

(5) For the construction of water wells using PVC casing, well contractors shall comply with the requirements of paragraph 62-532.500(1)(e), F.A.C., which is incorporated by reference in paragraph 40A-3.504(3)(g), F.A.C.

(6) Steel well casing and liner pipe shall be joined in a watertight manner by threaded couplings, electrical welding methods or other methods approved by the District. PVC pipe shall be joined by heat welding, solvent bonding, threaded couplings or other methods approved by the District, which shall meet the strength requirements of the casing as specified in subsection (5), above.

(7) Nonmetallic and stainless steel well casing or liner pipe shall not be installed or seated by driving unless it can be shown the casing or pipe will maintain its integrity so as to prevent degradation of the water resource. The Department of Environmental Protection, under the provisions of paragraph 62-532.500(1)(f), F.A.C., requires all alternative well casing, not listed in Table 1 to receive Department approval prior to use. Prior approval for the use of alternative materials shall also be obtained from the District.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.308, 373.309 FS. History–New 1-9-86, Formerly 40A-3.701(1)(a), Amended 4-5-88, 8-1-89, 12-1-90, 11-1-92, 8-15-18.

## 40A-3.512 Standard Well Construction Methods.

(1) In the construction of a well, reasonable caution shall be taken to maintain the premises in sanitary condition and to minimize the entrance of contaminants into the water resource. Water and materials used in construction shall be reasonably free of contamination.

(2) For wells which penetrate multiple aquifers or zones, the well shall be completed so as to prevent cross-connections of different aquifers or zones and to prevent leakage of water from one aquifer or zone to another aquifer or zone. If a well cannot be properly completed to prevent such an interchange of water between water-bearing zones or to prevent a loss of artesian pressure, the well shall be abandoned and plugged in accordance with Rule 40A-3.531, F.A.C., of these rules or other specifications provided by the District, as may be appropriate for the geological conditions encountered.

(3) For wells completed into unconsolidated aquifers, casing shall extend from land surface to the well screen. The well screen shall be attached to the casing with a watertight seal.

(4) For wells obtaining water from consolidated aquifers, a continuous casing shall extend from the land surface into the producing aquifer, and such casing must extend below the static water level of the aquifer intended to supply the water to the well unless it can be shown an alternative placement of the casing will prevent degradation of the water resource. All caving zones shall be cased or screened. Prior approval for the use of alternative methods shall be obtained from the District.

(5) Wells constructed to provide water for irrigation systems are required to have installed an anti-syphon device adequate to protect against contamination of the water supply, pursuant to the requirements of Section 487.064, F.S.

(6) All water wells intended to provide potable water shall be thoroughly cleaned of all foreign substances and obstructing material after the well has been constructed. The well shall be developed by pumping, surging, bailing, or other means which effectively remove sediment, well cuttings, and foreign material from in and around the well. Such wells shall be properly disinfected after construction in accordance with Section 11, Well Disinfection, American Water Works Association Standard for Water Wells, AWWA A100-84, dated June 10, 1984, which is hereby incorporated by reference.

(7) It is the intent that all wells shall be constructed to prevent caving and pumping of sand. In areas where the potential exists for sand to enter the well, a screen shall be used. If a screen is not used and the completed well pumps sand, the well will be determined not to be suitable for its intended use and the well will have to be repaired or abandoned.

(8) The well casing shall extend a minimum of twelve (12) inches above ground level and shall not be cut off below ground level unless prior approval is obtained from the District. Circumstances for which such approval shall be considered include the practice of installing the well top, pump and pump control apparatus in a water tight below grade box specifically designed and installed for such purpose for a well whose location is not subject to flooding or inundation. Persons wishing to apply for approval shall submit their request to the District on NWFWMD Form No. 122, Request For Below Grade Well Casing Approval. The request will be reviewed in the same manner as exemption requests specified in Rule 40A-3.051, F.A.C.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.306, 373.308, 373.309 FS. History–New 1-9-86, Formerly 40A-3.701(2), Amended 8-10-87, 4-5-88, 8-1-89, 12-1-90, 11-1-92.

## 40A-3.517 Grouting and Sealing.

Wells shall be grouted and sealed to protect the water resource from degradation caused by movement of waters along the well annulus either from the surface to the aquifer or between aquifers, and to prevent loss of artesian pressure in artesian aquifers. All wells shall be constructed and sealed using a method which insures that an open or unnaturally permeable annular space does not remain when a well is completed.

(1) Rotary wells located south of grout line. The grout line is established in a Florida Department of Environmental Regulation Grout Exemption Letter, effective 9-10-1980, http://www.flrules.org/Gateway/reference.asp?No=Ref-08941, and is hereby incorporated by reference and can be obtained from the District’s website (nwfwater.com) or from District offices upon request. Wells constructed by the rotary method and located south of the grout line shall have an annular space between the casing and the borehole wall of not less than two inches and shall be sealed according to the following criteria:

(a) All diameter wells constructed by the rotary method and completed into a consolidated formation shall be sealed by filling the annular space with a two-inch thickness of grout from the bottom of the casing to the land surface.

(b) Wells constructed by the rotary method and completed into an unconsolidated formation shall be sealed by filling the annular space with a two-inch thickness of grout from a point above the top of the screen to the land surface if:

1. The well is a public water system as defined in subsection 40A-3.021(39), F.A.C., of this rule;

2. The well is for Limited Use Public Supply use as defined in subsection 40A-3.021(35), F.A.C., of this rule;

3. The well has a diameter of six inches or larger;

4. The well penetrates a confining bed;

5. The well is to be located within one thousand (1,000) feet of any source of pollution, including plants processing hazardous or toxic substances, sanitary landfills (active or closed), sewage percolation ponds, sewage spray irrigation fields, toxic waste disposal systems of any kind including known ground water contamination areas, or other such sources of pollution; or

6. The well, with an approved exemption from the District, is to be located within seventy-five (75) feet of an onsite sewage disposal system (OSDS).

(c) Wells constructed by the rotary method and completed into an unconsolidated formation, but which do not meet the conditions identified in paragraph (1)(b), shall be sealed by filling the annular space with uncontaminated, well-compacted sand and sealing the top of the casing with grout that contains a minimum of one (1) cubic foot of cement.

(2) Rotary wells located north of the grout line. The grout line is established in a Florida Department of Environmental Regulation Grout Exemption Letter, effective 9-10-1980, http://www.flrules.org/Gateway/reference.asp?No=Ref-08941, and is incorporated by reference in subsection 40A-3.517(1), F.A.C., and can be obtained from the District’s website (nwfwater.com) or from District offices upon request. Wells constructed by the rotary method and located north of the grout line shall have an annular space between the casing and the borehole wall of not less than two inches and shall be sealed according to the following criteria:

(a) Wells constructed by the rotary method and completed into a consolidated formation shall be sealed by filling the annular space with a two-inch thickness of grout from the bottom of the casing to the land surface if:

1. The well is a public water system as defined in subsection 40A-3.021(39), F.A.C., of this rule;

2. The well is for Limited Use Public Supply use as defined in subsection 40A-3.021(35), F.A.C., of this rule;

3. The well has a diameter of six (6) inches or larger;

4. The well is to be located within one thousand (1,000) feet of any source of pollution, including plants processing hazardous or toxic substances, sanitary landfills (active or closed), sewage percolation ponds, sewage spray irrigation fields, toxic waste disposal systems of any kind including known ground water contamination areas, or other such sources of pollution; or

5. The well, with an approved exemption from the District, is to be located within seventy-five (75) feet of an onsite sewage disposal system (OSDS).

(b) Wells constructed by the rotary method and completed into a consolidated formation, but which do not meet the conditions identified in paragraph (2)(a), shall be sealed by filling the annular space with a two-inch thickness of grout from the bottom of the casing up to a minimum distance of twenty (20) feet, or into the last confining bed encountered, whichever is greater. The remainder of the annular space shall be filled with uncontaminated, well-compacted sand, clay, or other material that is appropriate for the specific geological conditions encountered and that will prevent degradation of the water resource. The top of the casing shall be sealed with grout that contains a minimum of one (1) cubic foot of cement. Prior approval for the use of alternative methods or materials shall be obtained from the District.

(c) Wells constructed by the rotary method and completed into an unconsolidated formation shall be sealed by filling the annular space with a two-inch thickness of grout from a point above the top of the screen to the land surface if:

1. The well is a public water system as defined in subsection 40A-3.021(39), F.A.C., of this rule;

2. The well is for Limited Use Public Supply use as defined in subsection 40A-3.021(35), F.A.C., of this rule;

3. The well has a diameter of six inches or larger;

4. The well penetrates a confining bed;

5. The well is to be located within one thousand (1,000) feet of any source of pollution, including plants processing hazardous or toxic substances, sanitary landfills (active or closed), sewage percolation ponds, sewage spray irrigation fields, toxic waste disposal systems of any kind including known ground water contamination areas, or other such sources of pollution; or

6. The well, with an approved exemption from the District, is to be located within seventy-five (75) feet of an onsite sewage disposal system (OSDS).

(d) Wells constructed by the rotary method and completed into an unconsolidated formation, but which do not meet the conditions identified in paragraph (2)(c), shall be sealed by filling the annular space with uncontaminated, well-compacted sand and sealing the top of the casing with grout that contains a minimum of one (1) cubic foot of cement.

(3) Driven wells located north or south of the grout line. Wells with casing which is driven starting at the land surface and thence to its final depth in a borehole that is equal to or smaller in diameter than the outside diameter of the casing, or which is driven starting at the land surface and thence to its final depth ahead of the drill bit, shall be sealed with grout if:

(a) Any part of the well is constructed by setting the casing in a previously constructed borehole which is larger in diameter than the outside diameter of the final casing, or, for any other reason, a space is created between the borehole and the casing. Such a well shall be sealed by filling the annular space with grout from bottom to top.

(b) The well is a public water system as defined in subsection 40A-3.021(39), F.A.C., of this rule or is for Limited Use Public Supply use as defined in subsection 40A-3.021(35), F.A.C., and the well is constructed by driving casing into a consolidated formation. Such a well shall be sealed by under-cutting or under-reaming the last five (5) feet of the hole before seating the casing. A minimum of one (1) foot of the enlarged hole must be in the consolidated formation in which the casing will be seated. The entire enlarged portion of the hole shall be filled with grout and the casing driven through the grout to refusal. The upper twenty (20) feet of the well shall have an annulus not less than two inches, and shall be sealed by filling the annular space with grout.

(4) Grouting and sealing of water wells shall be accomplished in the following manner unless an exemption is granted by the District for the use of alternative methods or materials that are appropriate for the specific geological conditions encountered and that prevent degradation of the water resource.

(a) Composition of neat cement grout shall not exceed six (6) gallons of water per cubic foot or 94-pound sack of Portland cement.

(b) The casing shall be centered in the borehole prior to grouting and sealing.

(c) In all cases, neat cement grout will be introduced into the annular space from bottom to top.

(d) The minimum set time for grouting of casing before drilling operations may continue will be as specified in Table 3 below.

| TABLE 3 |
| --- |
| GROUT SETTING REQUIREMENTS |
| TYPE OF WELL | STEEL CASING | PVC CASING |
| Public Supply Well | MINIMUM OF 72 HOURS | MINIMUM OF 72 HOURS |
| Limited Use Public Supply | MINIMUM OF 12 HOURS | MINIMUM OF 12 HOURS |
| Well |  |  |
| Other Wells: |  |  |
| 4 Inches and | Driven into a consolidated | Constructed into a |
| Smaller in | formation with drive shoe | consolidated formation |
| Diameter | MINIMUM OF 2 HOURS | utilizing a shell packer |
|  |  | MINIMUM OF 4 HOURS |
|  | Not driven into a | Constructed into a |
|  | consolidated formation | consolidated formation |
|  | but utilizing a shell | not utilizing |
|  | packer | a shell packer |
|  | MINIMUM OF 4 HOURS | MINIMUM OF 12 HOURS |
|  | Sand-and-gravel wells | Sand-and-gravel |
|  | which penetrate a confining | wells which penetrate |
|  | bed which do not | a confining |
|  | utilize a shell packer | bed and which do not |
|  | MINIMUM OF 12 HOURS | utilize a shell |
|  |  | packer |
|  |  | MINIMUM OF 12 HOURS |
| Larger than 4 |  |  |
| Inches in |  |  |
| Diameter | MINIMUM OF 12 HOURS | MINIMUM OF 12 HOURS |

(5) Other approved methods and materials may be used if they are appropriate for the specific geological conditions encountered and if they prevent degradation of the water resource. Prior approval for the use of alternative methods or materials shall be obtained from the District.

(6) In those cases where, during grouting operations, circulation of the neat cement grout is lost so that the annular space being grouted cannot be filled in one continuous operation, a tremie pipe shall be installed in the annular space to a point immediately above the zone of lost circulation; and the annulus shall be bridged at that point by sand or other suitable material introduced through the pipe until a level is reached at which grouting can be continued.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.306, 373.308, 373.309 FS. History–New 1-9-86, Formerly 40A-3.701(2)(e), Amended 8-10-87, 4-5-88, 8-1-89, 12-1-90, 11-1-92, 11-1-93, 8-15-18.

## 40A-3.521 Well Seals.

(1) Temporary Well Seals. Whenever there is a temporary interruption in work on the well during construction, repair, or abandonment, the well opening shall be sealed with a substantial watertight cover. Except for those areas of the District with the concurrence of the Department, any well in which pumping equipment is installed seasonally or periodically shall, whenever pumping equipment is not installed, be capped with a watertight cap or valve.

(2) Permanent Well Seals. Wells located on ground subject to flooding shall be properly sealed to prevent the movement of contaminants and surface water into the well. The upper end of the well casing shall include a watertight seal with any vent above the 100-year flood level. Pumping equipment and any necessary pipe or electrical connections shall be so installed as to prevent inadvertent introduction of contaminants into the well. Pumping equipment and any necessary piping or electrical connections installed within the casing shall be installed through a well seal. An unobstructed inspection port equipped with a removable plug shall be provided and be accessible at the wellhead.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.306, 373.308, 373.309 FS. History–New 1-9-86.

## 40A-3.525 Explosives.

The use of explosives in well construction or development is prohibited unless it can be shown their use will not cause degradation of the water resource and will not endanger the health, safety, or welfare of the people. The use of explosives must be specifically approved by the District.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.306, 373.308, 373.309 FS. History–New 1-9-86, Amended 4-5-88.

## 40A-3.529 Flowing Wells.

If the well flows at land surface, a valve shall be provided and maintained for controlling the discharge from the well. For newly constructed wells, the responsibility for controlling the discharge from the well becomes the owner’s upon the water well contractor’s submission of a well completion report to the District.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.206, 373.209, 373.306, 373.308, 373.309 FS. History–New 1-9-86, Formerly 40A-3.701(4).

## 40A-3.531 Abandoned Well Plugging.

(1) All abandoned wells shall be plugged.

(2) It shall be the responsibility of:

(a) The water well contractor to plug any well drilled under his license which is not completed or is not suitable for its intended use when work is completed. Wells which are not completed by the contractor shall be plugged prior to the well drilling rig being removed from the site. A well which is determined to be unsuitable for its intended use shall be plugged within fourteen (14) days of notification from the District.

(b) The property owner to have properly plugged any existing abandoned well on his property, or any well on his property which, following construction, attains the state of an abandoned well as defined in subsection 40A-3.021(1), F.A.C., of these rules.

(3) Any well which was not constructed in accordance with the standards of Part II of these rules and fails to be corrected within a time certain may be deemed an abandoned well.

(4) Abandoned wells and wells shall be plugged by filling them from bottom to top with grout, unless otherwise provided in writing by the District. The use of alternative methods or materials shall not cause degradation of the water resource.

(5) Abandoned wells shall be plugged only by a licensed water well contractor.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.206, 373.207, 373.209, 373.306, 373.308, 373.309 FS. History–New 1-9-86, Formerly 40A-3.701(5), Amended 4-5-88, 8-1-89.

## 40A-3.550 Violations of Construction Standards.

(1) Acts or omissions which constitute violations of Part II of these rules governing well construction standards, shall include:

(a) Failure to meet the location requirements of Rule 40A-3.504, F.A.C.

(b) Failure to meet the casing specifications provided in Rule 40A-3.507, F.A.C.

(c) Failure to provide an antisyphon device on wells for irrigation systems.

(d) Failure to disinfect a well constructed for potable use.

(e) Failure to provide a nominal two-inch annulus in rotary constructed wells.

(f) Failure to properly seal the annular space of any well.

(g) Failure to plug an abandoned well.

(h) Failure to comply with any order for corrective work.

(i) Failure to fulfill any other applicable requirements of Chapter 373, Part III, F.S., or Chapter 40A-3, F.A.C.

(2) Actions which may be taken by the District staff upon determination that a violation has occurred are outlined in Rule 40A-3.980, F.A.C., of these rules.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.306, 373.308, 373.309, 373.319 FS. History–New 1-9-86, Amended 11-1-92.

## 40A-3.701 Construction Standards.

Rulemaking Authority 373.044, 373.812, 403.861(8), (9), 373.309 FS. 17-1.04(8), F.A.C. Law Implemented 373.313, 373.316 FS. 17-21, F.A.C. History–New 4-14-80, Amended 10-27-80, 4-13-81, 2-1-82, 3-29-84, Formerly 16G-3.70, 16G-3.21, Repealed 1-9-86.

## 40A-3.721 Driller Registration.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.308, 373.323, 373.326 FS. History–New 10-1-84, Amended 1-9-86, Repealed 8-1-89.

## 40A-3.725 Responsibility of Contractor.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.308, 373.323, 373.326 FS. History–New 10-1-84, Repealed 8-1-89.

## 40A-3.727 Type of Registration.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.308, 373.323, 373.326 FS. History–New 10-1-84, Repealed 8-1-89.

## 40A-3.733 Exemptions.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.308, 373.323, 373.326 FS. History–New 10-1-84, Repealed 1-9-86.

## 40A-3.751 Enforcement and Penalties.

Rulemaking Authority 373.044 FS. 17-21 F.A.C. Law Implemented 373.126, 373.333 FS. History–New 4-14-80, Formerly 16G-3.75, 16G-3.76, 16G-3.31, 16G-3.32, Transferred to 40A-980.

## 40A-3.752 Refusal, Suspension, or Revocation of Registration.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.308, 373.323, 373.326 FS. History–New 10-1-84, Amended 1-9-86, Repealed 8-1-89.

## 40A-3.763 Examinations.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.308, 373.323, 373.326 FS. History–New 10-1-84, Repealed 8-1-89.

## 40A-3.901 Forms and Instructions.

The following forms are used in the implementation of this chapter and are hereby incorporated by reference into this rule.

(1) DEP Form 62-532.900(1), effective 10-7-10, http://www.flrules.org/Gateway/reference.asp?No=Ref-09094, and incorporated by reference in subsection 40A-3.041(3), F.A.C.

(2) DEP Form 62-532.900(2), effective 10-7-10, http://www.flrules.org/Gateway/reference.asp?No=Ref-09091, and incorporated by reference in subsection 40A-3.411(3), F.A.C.

(3) NWFWMD Form 122; Request For Below Grade Well Casing Approval, effective 11-1-92, http://www.flrules.org/Gateway/reference.asp?No=Ref-09094, and incorporated by reference in subsection 40A-3.512(8), F.A.C.

Forms may be obtained from:

District Headquarters, 152 Water Management Drive, Havana, FL 32333-9700, (850)539-5999;

DeFuniak Springs Service Office, 700 US Highway 331 S, DeFuniak Springs, FL 32435.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS., 62-532, F.A.C. Law Implemented 373.306, 373.308, 373.309 FS. History–New 4-14-80, Amended 10-27-80, 2-1-82, 1-9-86, Formerly 16G-3.90, Amended 8-1-89, 12-1-90, 2-14-91, 11-1-92, 11-1-93, 11-1-95, 8-15-18.

## 40A-3.951 Introduction.

The purpose of this part is to implement the delegation of Section 373.333, F.S., under provisions of subsection 62-101.040(10), F.A.C., by the Department of Environmental Protection to the Northwest Florida Water Management District. This delegation provides authority to the District to suspend or revoke the license issued pursuant to Section 373.333, F.S., of any holder of such license who has violated any provision of Part III, Chapter 373, F.S., or any rule or regulation adopted pursuant to this part.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS., 17-1.04(8), F.A.C. Law Implemented 373.333(6) FS. History–New 2-1-82, Amended 1-9-86, 11-1-93.

## 40A-3.952 Violations.

(1) Violations for purposes of this Part IV shall mean the failure of any licensee or his agents or employees to comply with the provisions of Chapter 373, F.S., Chapter 40A-3, 62-531, 62-532 or 62-555, F.A.C.

(2) A licensee will be notified of any violation according to the procedures specified in Chapter 62-531, F.A.C., herein adopted by reference.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.323 FS. History–New 2-1-82, Amended 1-9-86, 8-1-89.

## 40A-3.753 Procedure.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.323 FS. History–New 2-1-82, Repealed 8-1-89.

## 40A-3.954 Reporting of Drillers Not Required to be Licensed.

Rulemaking Authority 17-1.04(8) F.A.C. Law Implemented 373.323(3), (6) FS. History–New 2-1-82, Repealed 1-9-86.

## 40A-3.955 Suspension; Suspenion with Conditions.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.323 FS. History–New 2-1-82, Repealed 8-1-89.

## 40A-3.956 Revocation.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.323 FS. History–New 2-1-82, Repealed 8-1-89.

## 40A-3.980 Enforcement and Penalties.

(1) Enforcement of these rules shall be as provided by Chapter 373, F.S., and Chapter 62-531, F.A.C., adopted herein by reference.

(2) Penalties for violation of these rules shall be as provided by Chapter 373, F.S., and Chapter 62-531, F.A.C., adopted herein by reference.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.333, 373.336 FS. History–New 4-14-80, Amended 10-1-84, Formerly 16G-3.75, 16G-3.76, 16G-3.31, 16G-3.32, 40A-3.751, Amended 8-1-89.