# CHAPTER 40D-8

# WATER LEVELS AND RATES OF FLOW

# 40D-8.011	Policy and Purpose

# 40D-8.021	Definitions

# 40D-8.031	Implementation

# 40D-8.041	Minimum Flows

# 40D-8.603	Management Levels for Lakes and Other Impoundments (Repealed)

# 40D-8.605	Cyclic Variations for Minimum Water Level (Repealed)

# 40D-8.611	Minimum Flood Levels (Repealed)

# 40D-8.613	Ten (10) Year Flood Warning Levels (Repealed)

# 40D-8.616	Posted Notice (Repealed)

# 40D-8.621	Operating Levels for Lakes with District-Owned Management Structures

# 40D-8.623	Minimum Wetland Levels

# 40D-8.624	Guidance and Minimum Levels for Lakes

# 40D-8.626	Minimum Aquifer Levels

## 40D-8.011 Policy and Purpose.

(1) The purpose of Chapter 40D-8, F.A.C., is to establish Minimum Flows and Levels at specific locations throughout the District pursuant to Sections 373.042 and 373.0421, F.S., to describe Guidance Levels for lakes, and to describe how the Minimum Flows and Levels will be used by the District. Minimum Flows and Levels are intended to prevent significant harm to the water resources or ecology of the area as provided in Section 373.042, F.S. In those areas where the Long-term flow or water level is below the Minimum Flow or Level the District will implement a recovery strategy which will be contained within the District’s Water Management Plan and, if required by law, portions or all shall be adopted by rule.

(2) Where appropriate, Minimum Flows and Levels may reflect seasonal variations and may include a schedule of variations and other measures appropriate for the protection of non-consumptive uses and the water resources.

(3) A further purpose of Chapter 40D-8, F.A.C., is to establish Guidance Levels for surface waters which are anticipated to occur on a somewhat regular basis, and which shall serve as a precautionary warning to all persons who would propose to construct facilities which may be damaged by periodic high or low water levels.

(4) Minimum Flows and Levels prescribed in Chapter 40D-8, F.A.C., are used in water resource planning, as one of the criteria in evaluating applications for water use permits under Chapter 40D-2, F.A.C., and, in the design, construction and management of surface water management systems as specified in subsection 40D-8.031(3), F.A.C. The existence of a Minimum Flow or Level for a water body, where that water body is proposed to be impacted by an activity that requires a permit under Chapter 40D-2, Consumptive Use Permitting, or Chapter 40D-4, F.A.C., Environmental Resource Permits, does not override the applicability of all other permitting criteria nor alter the manner in which the District evaluates compliance with permitting criteria, except to the extent that the MFL criteria is supplemental to all other criteria.

(5) The Minimum Flows and Levels established in this Chapter 40D-8, F.A.C., are based on the best information available at the time the Flow or Level was established. The best available information in any particular case will vary in type, scope, duration, quantity and quality and may be less than optimally desired. In addition, in many instances the establishment of a Minimum Flow or Level requires development of methodologies that previously did not exist and so are applied for the first time in establishing the Minimum Flow or Level. The District has many ongoing environmental monitoring and data collection and analysis programs, and will develop additional programs over time. The District intends to coordinate with local governments, Tampa Bay Water, government-owned and privately-owned utilities, environmental regulation agencies, Tampa Bay Estuary Program, public interest groups and other affected and interested parties to design, create, and implement the program. Together with all the parties’ designated experts, a long-term independent scientific peer review shall be included in the programs. These programs will supplement the District’s available information upon which Minimum Flows and Levels can be established and reviewed. These programs collectively provide information to assist in 1) characterizing water regimes in wetland systems, and the relationships between and among surficial features, the surficial aquifer, and the Floridan aquifer; and 2) evaluating the measures available to prevent significant harm to the water resources and ecology, in addition to withdrawal management, and the effectiveness of those measures. Therefore, to apprise the Governing Board of advancements made under those programs, the District shall annually update the Governing Board regarding:

(a) The status of the water levels for those water bodies for which Minimum Flows or Levels have been established; and

(b) Any additional information or methodologies, as appropriate, that could be applied to:

1. Assess established Minimum Flows or Levels; or

2. Establish Minimum Flows or Levels for additional water bodies; or

3. Determine compliance with Minimum Flows or Levels.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.042, 373.0421, 373.216, 373.219, 373.223, 373.413, 373.414, 373.416 FS. History–New 6-7-78, Amended 1-22-79, Formerly 16J-8.01, Amended 8-7-00.

## 40D-8.021 Definitions.

The terms set forth herein shall have the meanings ascribed to them unless the context clearly indicates otherwise, and such meanings shall apply throughout these rules. The terms defined in Rule 40D-1.102, F.A.C., shall also apply throughout Chapter 40D-8, F.A.C., and the terms defined in this Rule 40D-8.021, F.A.C., apply throughout the District rules except that where there is a conflict or a difference between Rule 40D-1.102, F.A.C. and this Rule 40D-8.021, F.A.C., the definition in this Chapter 40D-8, F.A.C., will control.

(1) “Current” means a recent Long-term period during which Structural Alterations and hydrologic stresses are stable.

(2) “Guidance Levels” means water levels, determined by the District using the best available information and expressed in feet relative to National Geodetic Vertical Datum (of 1929), or in feet relative to the North American Vertical Datum (of 1988), used as advisory information for the District, lake shore residents and local governments, or to aid in the management or control of adjustable structures. Established Guidance Levels include the Low Level and the High Level.

(3) “Historic” means a Long-term period when there are no measurable impacts due to withdrawals and Structural Alterations are similar to current conditions.

(4) “Hydrologic Indicators” means those biological and physical features, which are representative of previous water levels as listed in Section 373.4211(20), F.S.

(5) “Long-term” means an evaluation period used to establish Minimum Flows and Minimum Water Levels, determine compliance with established Minimum Flows and Minimum Water Levels, and assess withdrawal impacts on established Minimum Flows and Minimum Water Levels that represents a period which spans the range of hydrologic conditions which can be expected to occur based upon historical records, ranging from high water levels to low water levels. In the context of an average water level, the average will be based upon the historic expected range and frequency of levels. Relative to Minimum Flow and Level establishment and compliance, the best available information, selected through application of reasonable scientific judgement, that is sufficiently representative of Long-term conditions will be used.

(6) “Minimum Flow” means the flow for a surface watercourse at which further withdrawals would be significantly harmful to the water resources or ecology of the area and which may provide for the protection of non-consumptive uses.

(7) “Minimum Level” means the Long-term level of surface water, water table, or potentiometric surface at which further withdrawals would be significantly harmful to the water resources of the area and which may provide for the protection of nonconsumptive uses. Such a level shall be expressed as an elevation, in feet relative to National Geodetic Vertical Datum (1929) or in feet relative to the North American Vertical Datum (1988) and includes Minimum Wetland Levels, High Minimum Lake Levels, Minimum Lake Levels, and Minimum Aquifer Levels.

(8) “P10” means the percentile ranking represented by the elevation of the water surface of a lake or wetland that is equaled or exceeded 10 percent of the time as determined from a Long-term stage frequency analysis.

(9) “P50” means the percentile ranking represented by the elevation of the water surface of a lake or wetland that is equaled or exceeded 50 percent of the time as determined from a Long-term stage frequency analysis.

(10) “P90” means the percentile ranking represented by the elevation of the water surface of a lake or wetland that is equaled or exceeded 90 percent of the time as determined from a Long-term stage frequency analysis.

(11) “Structural Alteration” means human alteration of an inlet outlet of a lake or wetland that affects water levels.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.036, 373.0361, 373.042, 373.0421, 373.086, 373.216, 373.219, 373.223, 373.229, 373.413, 373.414, 373.416 FS. History–New 6-7-78, Amended 1-22-79, Formerly 16J-8.02, Amended 8-7-00, 1-8-04, 2-18-08, 9-27-21.

## 40D-8.031 Implementation.

(1) No Guidance Levels shall be prescribed for any reservoir or other artificial structure which is located entirely within lands owned, leased, or otherwise controlled by the user, and which require water only for filling, replenishing, and maintaining of the water level thereof, provided however:

(a) That Chapter 40D-2, F.A.C., rules shall apply to the use of water for such filling, replenishing, and maintaining of the water level, and

(b) That the High Level, determined pursuant to the procedures set forth in Rule 40D-8.624, F.A.C., may be established for any lake determined by the Board to be in the public interest.

(2) No Guidance Levels shall be prescribed for Lake Manatee in Manatee County, Evers Reservoir in Manatee County, the City of Tampa Reservoir on the Hillsborough River in Hillsborough County, and the Peace River/Manasota Regional Water Supply Authority Reservoir in DeSoto County.

(3) New water use or surface water management activity shall not cause an existing water level or flow to be reduced or suppressed below an established Minimum Flow or Minimum Water Level. The manner in which the Minimum Flows and Minimum Water Levels established in this Chapter 40D-8, F.A.C., are implemented in the District’s Consumptive Use and Environmental Resource Permitting Programs is described in Rule 40D-2.301, F.A.C., and Water Use Permit Applicant’s Handbook Part B, Section 3.9 adopted by reference in Rule 40D-2.091, F.A.C., and Section 3.6.1 of the Environmental Resource Permit Applicant’s Handbook Volume II adopted by reference in Rule 62-330.010, F.A.C.

(4)(a) At the time a Minimum Flow or Minimum Water Level is initially adopted, if the water body is below or is projected to fall within 20 years below, the minimum flow or level, the District shall simultaneously approve the recovery or prevention strategy required by Section 373.0421(2), F.S.

(b) After the initial adoption, when a Minimum Flow or Minimum Water Level is revised, if the water body is below or is projected to fall within 20 years below, the revised minimum flow or level, the District shall simultaneously approve the recovery or prevention strategy required by Section 373.0421(2), F.S., or modify an existing recovery or prevention strategy. The District may adopt the revised Minimum Flow or Minimum Water Level prior to the approval of the recovery or prevention strategy if the revised minimum flow or level is less constraining on existing or projected future consumptive uses.

(c) For water bodies without a prevention or recovery strategy, when the District determines the water body has fallen below, or is projected to fall within 20 years below, an adopted Minimum Flow or Minimum Water Level, the District shall expeditiously approve a recovery or prevention strategy.

(5) Establishment of a Minimum Flow or Minimum Water Level shall not be deemed to supersede or replace any other permitting criteria unless specifically provided for by such permitting criteria nor to be a determination by the Governing Board that any quantity above the established minimum flow or level is available for allocation to consumptive uses. For example, the District may by regulation or order reserve such quantities as it deems necessary pursuant to Section 373.223(3), F.S.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.042, 373.0421, 373.216, 373.219, 373.223, 373.413, 373.414, 373.416 FS. History–New 6-7-78, Amended 10-16-78, 1-22-79, Formerly 16J-8.03, Amended 3-23-81, 8-7-00, 2-18-08, 5-19-14, 9-27-21.

## 40D-8.041 Minimum Flows.

(1) Minimum Flows for the Lower Hillsborough River.

(a) For the purposes of Minimum Flows, the Lower Hillsborough River is defined as the River downstream of Fletcher Avenue. A tributary of the Lower Hillsborough River is Sulphur Springs, an artesian spring which enters the River via a short spring run at a point 2.2 miles downstream of the City’s dam.

(b) The Minimum Flows for the Lower Hillsborough River are based on extending a salinity range less than 5 ppt from the Hillsborough River Dam toward Sulphur Springs. The Minimum Flows for the Lower Hillsborough River are 20 cubic feet per second (“cfs”) freshwater equivalent from July 1 through March 31 and 24 cfs fresh water equivalent from April 1 through June 30 at the base of the dam as adjusted based on a proportionate amount that flow at the United States Geological Survey Gauge No. 0203000 near Zephyrhills, Florida (“Gauge”) is below 58 cfs. The adjustment is that for each one cfs that Hillsborough River flow at the Gauge is below 58 cfs, when 20 cfs freshwater equivalent is otherwise required, the Minimum Flow is adjusted by reducing it by 0.35 cfs; when 24 cfs freshwater equivalent is otherwise required, the Minimum Flow is adjusted by reducing it by 0.40 cfs. For purposes of this paragraph 40D-8.041(1)(b), F.A.C., freshwater equivalent means water that has a salinity concentration of 0.0 ppt for modeling purposes.

(2) Minimum Flows for the upper Hillsborough River.

(a) The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the river are met.

(b) Minimum Flows for the upper Hillsborough River at the USGS Hillsborough River near Morris Bridge Gage USGS #02303330 (“Morris Bridge Gage”) are set forth in Table 8-12 below. The long-term compliance standards set forth in Table 8-13 are established based on the application of the Minimum Flows to the lowest anticipated natural flow conditions. Minimum Flows for the upper Hillsborough River are both seasonal and flow dependent. Two standards are flow based and applied continuously regardless of season. The first is a Minimum Low Flow threshold of 52 cfs at the Morris Bridge Gage. The second is a Minimum High Flow threshold of 470 cfs at the Morris Bridge Gage. The Minimum High Flow is based on changes in the number of days of inundation of floodplain features. There are also three seasonally dependent or Block specific Minimum Flows. The Block 1 and Block 2 Minimum Flows are based on potential changes in habitat availability for fish species and macroinvertebrate diversity. The Block 3 Minimum Flow is based on changes in the number of days of connection with floodplain features.

| Table 8-12 Minimum Flow for Upper Hillsborough River at USGS Hillsborough River near Morris Bridge Gage |
| --- |
| Period | Effective Dates | Where Flow on Previous Day Equals: | Minimum Flow Is |
| Annually | January 1 to December 31 | (52 cfs (52cfs and (470 cfs ≥470 cfs | 52 cfs Seasonally dependent – see Blocks below Previous day flow minus 8% |
| Block 1 | April 20 to June 24 | (52 (52cfs and (470 cfs ≥470 cfs | 52 cfs previous day flow minus 10% Previous day flow minus 8% |
| Block 2 | October 28 to April 19 | (52 (52cfs and (470 cfs ≥470 cfs | 52 cfs previous day flow minus 11% previous day flow minus 8% |
| Block 3 | June 25 to October 27 | (52 cfs (52 cfs and (470cfs ≥470 cfs | 52 cfs previous day flow minus 13% previous day flow minus 8% |

(c) Compliance – The Minimum Flows are met when the flows in Table 8-13 are achieved.

| Table 8-13 Compliance Standards for the Hillsborough River near Morris Bridge Gage |
| --- |
| Minimum Flow | Hydrologic Statistic | Flow (cfs) |
| Annual Flow | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 190 96 149 74 |
| Block 1 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 74 62 57 52 |
| Block 2 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 153 89 105 72 |
| Block 3 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 287 150 235 107 |

(3) Minimum Flow for Sulphur Springs – The Minimum Flow for Sulphur Springs is based on minimization of salinity incursions into the Upper Sulphur Springs Run (“Upper Run”) from the Lower Hillsborough River (“LHR”) and to moderate temperature levels within the manatee protection zone of the LHR.

(a) As of October 1, 2012, the City of Tampa shall maintain a Minimum Flow for Sulphur Springs of:

1. 18 cfs, as measured at the United States Geological Survey Sulphur Springs Gauge No. 02306000 at Sulphur Springs, Florida, or;

2. 13 cfs when water levels in the Hillsborough River reservoir fall below 19 feet NGVD; and

3. 10 cfs during low tide stages in the LHR, provided that salinity incursions from the LHR into the upper spring run do not occur. Salinity incursions shall be defined as when salinity values in the upper spring run as measured at the United States Geological Survey Gauge Sulphur Springs Run at Sulphur Springs, Florida (#023060003) are greater than 1 ppt than the concurrent salinity value in the spring pool as measured at the United States Geological Survey Gauge Sulphur Springs Run at Sulphur Springs, Florida (#023060000) for a period of greater than 1 hour.

(b) Notwithstanding paragraph 40D-8.041(2)(a), F.A.C., above, and beginning the effective date of this rule, when spring flow is available, a Minimum Flow of 18 cfs shall be required if the temperature of either surface or bottom waters in the LHR near the Spring Run’s outlet is below 15○ C.

(c) The City of Tampa may propose to the District modifications to the weirs and gates located within the upper and lower spring run that affect the flow rates and salinity levels in the Upper Run and the LHR. The District shall evaluate the modifications to determine whether the flow resulting from the operating capabilities of the modifications and modeling simulations of the resulting salinity incursions into the Upper Spring Run achieve the salinity goal of the Minimum Flow for Sulphur Springs. If the District determines that flows different from the Minimum Flows (“Different Flows”) will achieve the salinity goal and otherwise protect the resources of the Upper Spring Run, the District, upon request by the City, will recommend to the Governing Board revision of the Minimum Flow to reflect the Different Flow.

(4) The Minimum Flow for the Tampa Bypass Canal at structure 160 shall be 0 cfs.

(5) Minimum Flows for Middle Peace River.

(a) The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the river are met.

(b) Minimum Flows for the Middle Peace River at the USGS Peace River Arcadia Gage (“Arcadia Gage”) are set forth in Table 8-6 below. The long-term compliance standards set forth in Table 8-7 are established based on the application of the Minimum Flows to the lowest anticipated natural flow conditions. Minimum Flows for the Middle Peace River are both seasonal and flow-dependent. Two standards are flow-based and applied continuously regardless of season. The first is a Minimum Low Flow threshold of 67 cfs at the Arcadia Gage. The second is a Minimum High Flow threshold of 1,362 cfs at the Arcadia Gage. The Minimum High Flow is based on changes in the number of days of inundation of floodplain features. There are also three seasonally dependent or Block-specific Minimum Flows. The Block 1 and Block 2 Minimum Flows are based on potential changes in habitat availability for fish species and macroinvertebrate diversity. The Block 3 Minimum Flow is based on changes in the number of days of connection with floodplain features.

| Table 8-6 Minimum Flow for Middle Peace River at USGS Peace River at Arcadia Gage |
| --- |
| Period | Effective Dates | Where Flow on Previous Day Equals: | Minimum Flow Is: |
| Annually | January 1 to December 31 | ≤67 ≤67 cfs and 1,362 >1,362 | 67 cfs Seasonally dependent – see Blocks below Previous day flow minus 8% |
| Block 1 | April 20 to June 25 | ≤67 >67 cfs and 75 cfs >75 cfs and 1,362 >1,362 | 67 cfs 67 cfs previous day flow minus 10% previous day flow minus 8% |
| Block 2 | October 27 to April 19 | ≤67 >67 cfs and 82 cfs >82 cfs and 1,362 >1,362 | 67 cfs 67 cfs previous day flow minus 18% previous day flow minus 8% |
| Block 3 | June 26 to October 26 | ≤67 cfs >67 cfs and 73 cfs >73 cfs and 1,362 cfs >1,362 | 67 cfs 67 cfs previous day flow minus 13% previous day flow minus 8% |

| Table 8-7 Compliance Standards for Middle Peace River at Arcadia Gage |
| --- |
| Minimum Flow | Hydrologic Statistic | Flow (cfs) |
| Annual Flow (January 1 through December 31) | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 547 243 534 196 |
| Block 1 (April 20 through June 25) | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 219 121 160 64 |
| Block 2 (October 27 through April 19) | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 359 182 300 122 |
| Block 3 (June 26 through October 26) | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 977 631 790 382 |

(c) Compliance – The Minimum Flows are met when the flows in Table 8-7 are achieved.

(6) Minimum Flows for Myakka River.

(a) Upper Myakka River.

1. The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the river are met.

2. Minimum Flows for the Myakka River at the USGS Myakka River near Sarasota Gage USGS #02298830 (“Sarasota Gage”) are set forth in Table 8-10 below. The long-term compliance standards set forth in Table 8-B are established based on the application of the Minimum Flows to the lowest anticipated natural flow conditions. Minimum Flows for the Myakka River are both seasonal and flow dependent. Two standards are flow-based and applied continuously regardless of season. The first is a Minimum Low Flow threshold of 0 cfs at the Sarasota Gage. The second is a Minimum High Flow threshold of 577 cfs at the Sarasota Gage. The Minimum High Flow is based on changes in the number of days of inundation of floodplain features. There are also three seasonally dependent or Block specific Minimum Flows. The Block 1 and Block 2 Minimum Flows are based on potential changes in habitat availability for fish species and macroinvertebrate diversity. The Block 3 Minimum Flow is based on changes in the number of days of connection with floodplain features.

| Table 8-10 Minimum Flow for Myakka River at USGS Myakka River near Sarasota Gage |
| --- |
| Period | Effective Dates | Where Flow on Previous Day Equals: | Minimum Flow Is |
| Annually | January 1 to December 31 | 0 cfs 0 cfs | 0 cfs Seasonally dependent see Blocks below |
| Block 1 | April 20 to June 25 | 0 cfs >0 cfs | 0 cfs previous day flow minus 15% |
| Block 2 | October 27 to April 19 | 0 cfs >0 cfs | 0 cfs previous day flow minus 5% |
| Block 3 | June 26 to October 26 | 0 cfs >0 cfs and >577 cfs >577 cfs | 0 cfs previous day flow minus 16% previous day flow minus 7% |

3. Compliance – The Minimum Flows are met when the flows in Table 8-11 are achieved.

| Table 8-11 Compliance Standards for Myakka River at USGS Myakka River near Sarasota Gage |
| --- |
| Minimum Flow | Hydrologic Statistic | Flow (cfs) |
| Annual Flow | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 172 12 149 5 |
| Block 1 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 23 0 4 0 |
| Block 2 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 28 4 15 3 |
| Block 3 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 324 181 241 133 |

(b) Lower Myakka River.

1. The Minimum Flows are necessary to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the Lower Myakka River are met. The Lower Myakka River extends from the outlet of Lower Myakka Lake to the mouth of the river at Charlotte Harbor.

2. The Lower Myakka River receives flows from the Upper Myakka River sub-basin at the location of the USGS gage Myakka River near Sarasota No. 02298830 (the “Myakka Gage”) that are in excess of the naturally occurring flows. The District will remove the excess flows at rates between 0 and 130 cfs in the upper river sub-basin in order to restore natural flows.

3. The Minimum Flows for the Lower Myakka River at the Myakka Gage is 90% of the adjusted flow, when the adjusted flow exceeds 400 cfs. The adjusted flow at the Myakka Gage shall be calculated by adding the flows measured at the Myakka Gage and the excess flows removed by the District from the Upper Myakka River.

(7) Minimum Flows for upper Peace River.

(a) Over the last several decades there has been a significant decline in flow in the upper Peace River, especially during the dry season. One of the major contributing factors is the elimination of baseflow as a result of ground water withdrawals that have lowered the potentiometric surface of the upper Floridian aquifer. In addition, surface-water drainage alterations, reduction in surface storage, long-term cyclical declines in rainfall and karst openings in the riverbed have played significant roles in reducing flow in the upper Peace River.

(b) The minimum flows are to ensure that the minimum hydrologic requirements of fish and natural systems associated with the river are met and not jeopardized by withdrawals. At this time only Minimum Low Flows are being established. It is anticipated that mid- and high-minimum flows will be established once the controlling factors that affect those flows are better understood.

(c) The Minimum Low Flows for the upper Peace River are set forth in Table 8-8 below. The Minimum Low Flows are established based on the lowest acceptable flow under the lowest anticipated flow conditions. This is determined by providing for the hydrologic requirements of biological communities associated with the upper Peace River system, as well as considering non-consumptive uses including fishing, wildlife observation, general recreation, aesthetic enjoyment, canoeing and boating. This determination uses professional experience and judgment to identify key habitats and hydrologic requirements for specific biotic assemblages. This approach results in establishing Minimum Low Flows for the upper Peace River based on maintaining the higher of the water elevations needed for fish passage (0.6 feet or 7.2 inches) or the lowest wetted perimeter inflection point (as much stream bed coverage as possible for the least amount of flow) as set forth below. A ninety-five percent annual exceedance occurs when the flow is greater than the Minimum Low Flow at least ninety-five percent of the days, or 350 days, of a calendar year.

| Table 8-8 Minimum Flows for the upper Peace River |
| --- |
| Location/Gage: | Minimum Flow (cubic feet per second): |
| Bartow / USGS Bartow River Gage No. 02294650 | Annual 95% exceedance flow of 17 cfs |
| Ft. Meade / USGS Ft. Meade River Gage No. 02294898 | Annual 95% exceedance flow of 27 cfs |
| Zolfo Springs / USGS Zolfo Springs River Gage No. 02295637 | Annual 95% exceedance flow of 45 cfs |

(d) Compliance – The Minimum Low Flow is achieved when the measured flow rate is at or above the Minimum Low Flow for three consecutive years. Once the Minimum Low Flow has been achieved for three consecutive years, the Minimum Low Flow is not met when the measured flow rate is below the Minimum Low Flow for two out of ten years commencing the year after achievement. If the two years below the minimum flow occur anytime before the ten year period is complete, the upper Peace River is deemed below its Minimum Low Flow and the three consecutive years above the Minimum Low Flow is again required for compliance. Once the ten-year period is complete, the period will roll forward one year each year.

(8) Minimum Flows for the lower Peace River.

(a) For purposes of this rule, the lower Peace River in DeSoto County, FL and Charlotte County, FL includes the watercourse from U.S. Geological Survey Peace River at SR 70 at Arcadia, FL Gage #02296750 to Charlotte Harbor.

(b) Minimum Flows for the lower Peace River are based on the sum of the daily average, combined, adjusted flows of the USGS Peace River Arcadia, FL Gage (“Gage No. 02296750”), the flow at the U.S. Geological Survey Joshua Creek at Nocatee, FL Gage (“Gage No. 02297100”), and the U.S. Geological Survey Horse Creek at SR 72 near Arcadia, FL Gage (“Gage No. 02297310”) as set forth in Table 8-20. Adjusted flow is defined as flow that would exist in the absence of withdrawal impacts. Minimum Flows for the lower Peace River are flow dependent, and were developed based on the daily average, combined flow at Gage No. 02296750, Gage No. 02297100 and Gage No. 02297310 adjusted for withdrawals for the period of record from January 1, 1950 through December 31, 2018. There are seven flow dependent Minimum Flows. Permitted withdrawals shall cease when the sum of the mean daily flows for the three gages denoted above is below 130 cfs. Also, the total permitted maximum withdrawals on any day from the lower Peace River shall not exceed 400 cfs.

| Table 8-20 Minimum Flow for Lower Peace River Based on the Combined (i.e., summed) Flows from the USGS Peace River at SR 70 at Arcadia, FL, Joshua Creek at Nocatee, FL, and Horse Creek at SR 72, near Arcadia, FL Gages Adjusted for Upstream Withdrawals |
| --- |
| If Adjusted Combined Flow in cubic feet per second (cfs) on the previous Day is: | Minimum Flow is: |
| ≤130 cfs | Combined flow on the previous day |
| >130 cfs and ≤149 cfs | 130 cfs |
| >149 cfs and ≤ 297 cfs | 87% of combined flow on the previous day |
| > 297 cfs and ≤ 335 cfs | 258 cfs |
| > 335 cfs and ≤ 622 cfs | 77% of combined flow on the previous day |
| > 622 cfs and ≤ 798 cfs | 479 cfs |
| > 798 cfs | 60% of combined flow on the previous day |

(c) Status assessments of the Minimum Flows for the lower Peace River will be completed to determine whether the flow is below or projected to fall below the Minimum Flows. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of each status assessment, the District will use the following approach:

1. The District will evaluate the Minimum Flow annually to determine the extent to which the flow of the lower Peace River has been reduced due to withdrawals as of the date of each status assessment at Gage No. 02296750, Gage No. 02297100 and Gage No. 02297310. The annual evaluation will be completed through a review of:

(a) Flow data;

(b) Water withdrawals;

(c) Aquifer water levels;

(d) Rainfall data; and

(e) Hydrologic modeling.

2. The District will also evaluate the Minimum Flows every five years as part of the regional water supply planning process. This evaluation will include the use of hydrologic modeling.

3. If the Minimum Flows are being met based on the annual evaluation or the evaluation performed as a part of the regional water supply planning process, then no further actions are required beyond continued monitoring.

(9) Minimum Flows for the Braden River.

(a) The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the river are met.

(b) Minimum Flows for the Braden River at the USGS Braden River near Lorraine Gage USGS #02300032 (“near Lorraine Gage”) are set forth in Table 8-14 below. The long-term compliance standards set forth in Table 8-15 are established based on the application of the Minimum Flows to the lowest anticipated natural flow conditions. Minimum Flows for the Braden River are both seasonal and flow dependent. Two standards are flow based and applied continuously regardless of season. The first is a Minimum Low Flow threshold of 7 cfs at the near Lorraine Gage. The second is a Minimum High Flow threshold of 54 cfs at the near Lorraine Gage. The Minimum High Flow is based on changes in the number of days of inundation of floodplain features. There are also three seasonally dependent or Block specific Minimum Flows. The Block 1 and Block 2 Minimum Flows are based on potential changes in habitat availability for fish species and macroinvertebrate diversity. The Block 3 Minimum Flow is based on changes in the number of days of connection with floodplain features.

| Table 8-14 Minimum Flow for Braden River at USGS Braden River near Lorraine Gage |
| --- |
| Period | Effective Dates | Where Flow on Previous Day Equals: | Minimum Flow Is |
| Annually | January 1 to December 31 | (7 cfs (7cfs and (54 cfs ≥54 cfs | 7 cfs Seasonally dependent – see Blocks below Previous day flow minus 10% |
| Block 1 | May 7 to June 19 | (7 (7 cfs | 7 cfs previous day flow minus 10% |
| Block 2 | October 25 to May 6 | (7 (7 cfs and (54 cfs ≥54 cfs | 7 cfs previous day flow minus 11% previous day flow minus 10% |
| Block 3 | June 20 to October 24 | (7 cfs (7 cfs and (54 cfs ≥54 cfs | 7 cfs previous day flow minus 19% previous day flow minus 10% |

(c) Compliance – The Minimum Flows are met when the flows in Table 8-15 are achieved.

| Table 8-15 Compliance Standards for Braden River near Lorraine Gage |
| --- |
| Minimum Flow | Hydrologic Statistic | Flow (cfs) |
| Annual Flow | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 31 3 26 2 |
| Block 1 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 5 1 2 0 |
| Block 2 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 20 3 10 1 |
| Block 3 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 65 23 43 7 |

(10) Minimum Flows for Crystal Springs Located Within the Hillsborough River Basin, Hillsborough County, Florida.

(a) The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the upper Hillsborough River are met.

(b) The Minimum Flow for Crystal Springs is stated as the flow measured by USGS physical measurements. Flows from Crystal Springs are calculated as the difference between upstream flow measurements at USGS Gage No. 02301990 – Hillsborough River Above Crystal Springs near Zephyrhills, FL and downstream flow measurements at USGS Gage No. 02302010 – Hillsborough River Below Crystal Springs near Zephyrhills, FL measurements and constitute the combined flow of the main spring vent and numerous smaller vents in the river channel. The minimum flow for the Crystal Springs complex is 46 cfs based on a 5-year running mean and median.

(11) Minimum Flows for Alafia River – Freshwater Segment.

(a) The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the river are met.

(b) Minimum Flows for the Alafia River at the USGS Alafia River at Lithia Gage USGS # 02301500 (“Lithia Gage”) are set forth in Table 8-16 below. The long-term compliance standards set forth in Table 8-17 are established based on the application of the Minimum Flows to the lowest anticipated natural flow conditions. Minimum Flows for the Alafia River are both seasonal and flow dependent. Two standards are flow-based and applied continuously regardless of season. The first is a Minimum Low Flow threshold of 59 cfs at the Lithia Gage. The second is a Minimum High Flow threshold of 375 cfs at the Lithia Gage. The Minimum High Flow is based on changes in the number of days of inundation of floodplain features. There are also three seasonally dependent or Block specific Minimum Flows. The Block 1 and Block 2 Minimum Flows are based on potential changes in habitat availability for fish species and macroinvertebrate diversity. The Block 3 Minimum Flow is based on changes in the number of days of connection with floodplain features.

| Table 8-16 Minimum Flow for Alafia River at USGS Alafia River at Lithia Gage |
| --- |
| Period | Effective Dates | Where Flow on Previous Day Equals: | Minimum Flow Is |
| Annually | January 1 to December 31 | (59 cfs (59 cfs and (374 cfs (374 cfs | 59 cfs Seasonally dependent – see Blocks below Previous day flow minus 8% |
| Block 1 | April 20 to June 25 | (57 cfs (57 cfs and (66 cfs (66 cfs and (374 cfs (374 cfs | 59 cfs 67 cfs previous day flow minus 10% previous day flow minus 8% |
| Block 2 | October 27 to April 19 | (59 cfs (59 cfs and (69 cfs (69 cfs and (374 cfs (374 cfs | 59 cfs 67 cfs previous day flow minus 15% previous day flow minus 8% |
| Block 3 | June 26 to October 26 | (59 cfs (59 cfs and (64 cfs (64 cfs and (374 cfs (374 cfs | 59 cfs 67 cfs previous day flow minus 13% previous day flow minus 8% |

(c) Compliance – The Minimum Flows are met when the flows in Table 8-17 are achieved.

| Table 8-17 Compliance Standards for Alafia River at Lithia Gage |
| --- |
| Minimum Flow | Hydrologic Statistic | Flow (cfs) |
| Annual Flow | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 192 101 163 86 |
| Block 1 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 85 35 53 27 |
| Block 2 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 137 82 110 66 |
| Block 3 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 318 179 276 163 |

(12) Minimum Flow for Lower Alafia River System.

(a) For purposes of this rule, the Lower Alafia River System includes the watercourse downstream of the USGS Gage No. 02301500 Alafia River at Lithia, FL (the “Alafia River at Lithia Gage”) including Lithia Springs, Buckhorn Spring, and their associated spring runs.

(b) The Minimum Flow is to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the Lower Alafia River System are met. Daily flows to the Lower Alafia River System are calculated by multiplying mean daily flow values at the Alafia River at Lithia Gage by a factor of 1.117, then adding the mean daily flows from Lithia Spring Major and Buckhorn Spring. Flows are calculated in the absence of withdrawals and are based on mean flows at the Alafia River at Lithia Gage from the previous day and the most recently recorded periodic values from Lithia Spring Major and Buckhorn Spring. The Minimum Flow for the Lower Alafia River System is intended to preserve 81% of the natural flow to the Lower Alafia River System when flows exceed a low-flow threshold of 120 cfs.

(c) The Minimum Flow is 81% of the daily flow to the Lower Alafia River System that is above 120 cfs.

(d) Minimum five-year and ten-year moving average values are set forth in Table 8-19 as a tool to assess whether flows to the Lower Alafia River remain above flow rates that are expected to occur with implementation of the Minimum Flow. These values represent minimum values of the averages of yearly mean and median flows to the Lower Alafia River System calculated over moving five-year and ten-year periods. These values were calculated by applying the potential maximum withdrawals that do not violate the Minimum Flow to historic flow records. It is, therefore, expected that flows to the Lower Alafia River System will not go below these values if compliance with the Minimum Flow is maintained. However, future climatic conditions or structural alterations in the watershed of the Lower Alafia River System could potentially affect surface water or ground contributions to the Lower Alafia River System’s flow regime. The District will, therefore, periodically evaluate whether these minimum moving average values expected with application of the Minimum Flow, or other factors, have possibly caused flows in the Lower Alafia River System to decline.

| Table 8-19 Minimum Values of Five-year and Ten-year Moving Averages of Yearly Mean and Median Flows to the Lower Alafia River System |
| --- |
| Value | Flow (cfs) |
| Minimum 10-Year Moving Average (Based On Yearly Mean Flows) | 247 |
| Minimum 10-Year Moving Average Median (Based On Yearly Median Flows) | 150 |
| Minimum 5-Yearly Mean Flows (Based on Yearly Mean Flows) | 217 |
| Minimum 5 Year Moving Average (Based On Yearly Median Flows) | 120 |

Flows to the Lower Alafia River System were estimated for the period of record at the Alafia River at Lithia Gage. The period from 1987 to 2003 was used to create a relationship between daily flows at the Gage and total flows to the Lower Alafia River System. Five-year and ten-year moving average statistics were then calculated for estimated long-term flows to the Lower Alafia River System that were derived from the Alafia River at Lithia Gage.

(13) Minimum Flows for Weeki Wachee River System located within Hernando County, Florida.

(a) The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the Weeki Wachee River System are met. The Minimum Flow for the Weeki Wachee River System is intended to maintain 90% of the natural flow of the Weeki Wachee River System. For purposes of this rule, the Weeki Wachee River System includes the watercourse from the Weeki Wachee Spring to the Gulf of Mexico including Twin Dees Spring, Mud River (including Salt Spring) from Mud Spring to the confluence with the Weeki Wachee River and Jenkins Springs and associated spring run.

(b) The Minimum Flow for the Weeki Wachee River System is 90% of its natural flow. This Minimum Flow is inclusive of spring flow, the freshwater and the estuarine portion of the Weeki Wachee River.

(c) The Minimum Flow applies upstream of the USGS Gage No. 02310525 at Weeki Wachee River near Brooksville (“Brooksville Gage”) to the Weeki Wachee Spring vent and downstream of the Brooksville Gage to the Gulf of Mexico. The Minimum Flow shall be met continuously and is evaluated on a daily basis.

(d) Because climatic variation can influence river flow regimes, five and ten year mean and median standards have been developed and are set forth in Table 8-18 (“Means and Medians”) as a tool to assess whether compliance with the Minimum Flow maintains 90% of the natural flow of the Weeki Wachee River System. The Means and Medians are hydrologic statistics that represent flows expected to occur during long-term periods when the Minimum Flows are being met. The Means and Medians are generated from flow records that are representative of a period devoid of significant anthropogenic impacts. The District will periodically evaluate the Means and Medians. These are evaluated as the mean and medians of annual means and medians, evaluated from January 1 through December 31 of each year. The evaluation is for both the flow at the Brooksville Gage and at the USGS Weeki Wachee Well No. 283201082315601. The flow at the Brooksville Gage is evaluated directly against Table 8-18. The well data is converted to flow with the relation Q (cfs) = -47.487 + 12.38 (well level) (ft) and then evaluated against Table 8-18. The Means and Medians were developed using the Minimum Flow and the presumed historic flow records. Therefore, it is expected that the Means and Medians will be met if compliance with the Minimum Flow is maintained. However, since future structural alterations could potentially affect surface water or groundwater flow characteristics within the watershed and additional information pertaining to Minimum Flows development may become available, the District is committed to periodic review and revision of the Minimum Flows, as necessary.

| Table 8-18 Five and Ten Year Means and Medians for the Weeki Wachee River System |
| --- |
| Criterion | Flow (cfs) |
| Minimum 10 Year Moving Average (Based On Annual Average Flows) | 141 |
| Minimum 10 Year Moving Average (Based On Annual Median Flows) | 131 |
| Minimum 5 Year Moving Average (Based On Annual Average Flows) | 136 |
| Minimum 5 Year Moving Average (Based On Annual Median Flows) | 128 |

(e) Water Use Permits issued after May 10, 2009 that authorize surface water withdrawals from, or ground water withdrawals that impact Mud Spring, Salt Spring or Jenkins Spring, shall gauge the flow of the applicable spring and report the flow to the District as provided in the Water Use Permit.

(14) Minimum Flows for the Dona Bay/Shakett Creek System below Cow Pen Slough located within the Manasota Basin, Sarasota County, Florida.

(a) The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources and ecology of the natural systems associated with the Dona Bay/Shakett Creek System are met. For purposes of this rule, the Dona Bay/Shakett Creek System includes the watercourse and its tributaries from the most downstream control structure on Cow Pen Slough, known as CPS-2 and operated by Sarasota County (hereinafter referred to as “CPS-2”) to the Gulf of Mexico including Shakett Creek, Salt Creek, Fox Creek and Dona Bay.

(b) The Minimum Flow for the Dona Bay/Shakett Creek System is 100% of the natural flow of the system contributed by the watershed below CPS-2. This Minimum Flow is exclusive of flow, which is generated from the channelized watershed above CPS-2. Flow generated from the channelized watershed above CPS-2 shall be based on the flow records from CPS-2.

(15) Minimum Flows for the Anclote River.

(a) The Minimum Flows are to ensure that the minimum hydrologic requirements of the water resources or ecology of the natural systems associated with the freshwater and estuarine reaches of the Anclote River are met.

(b) Minimum Flows for the freshwater and estuarine reaches of the Anclote River are based on the natural flow at the USGS Anclote River near Elfers Gage No. 02310000 (the “Elfers Gage”) and are set forth in Table 8-22 (estuarine reach downstream of the Elfers Gage) and Table 8-23 (freshwater reach upstream of Elfers Gage). Natural flow is defined as flow that would exist in the absence of withdrawal impacts. There are three seasonally dependent or Block specific Minimum Flows for each reach. In addition, the Minimum Flows for the freshwater reach are flow-based. The Minimum Low Flow Threshold for the freshwater reach is applied continuously regardless of season. No surface water withdrawal from the freshwater reach will be permitted that would cumulatively cause the natural flow to be reduced below the Minimum Low Flow Threshold of 12 cfs. Additionally, permitted withdrawals shall cease when flows are below the Minimum Low Flow Threshold of 12 cfs. In addition, the total permitted maximum withdrawals from the freshwater reach on any given day from July 22 through April 11 shall not exceed eight percent of the previous day’s flow when natural flow equals or exceeds 138 cfs at the Elfers Gage.

| Table 8-22 Minimum Flow for Anclote River below USGS Anclote River near Elfers Gage USGS No. 02310000 (Estuarine Reach) |
| --- |
| Period | Effective Dates | Minimum Flow Is |
| Block 1 | April 12 through July 21 | Previous day’s flow minus 12% |
| Block 2 | October 15 through April 11 | Previous day’s flow minus 16% |
| Block 3 | July 22 through October 14 | Previous day’s flow minus 18% |
| The Minimum Flow at any given point below the Elfers Gage is based on the previous day’s natural flow at that point minus the percentage specified above corresponding to the applicable Block. |

| Table 8-23 Minimum Flow for Anclote River above USGS Anclote River near Elfers Gage USGS No. 02310000 (Freshwater Reach) |
| --- |
| Period | Effective Dates | Where Flow on Previous Day Equals: | Minimum Flow Is |
| Annually | January 1 to December 31 | (12 cfs (12 cfs and (138 cfs ≥138 cfs | Actual flow Seasonally dependent – see Blocks below Seasonally dependent – see Blocks below |
| Block 1 | April 12 through July 21 | (12 cfs (12 cfs | Actual flow Previous day’s flow minus 11% but not less than 12 cfs |
| Block 2 | October 15 through April 11 | (12 cfs (12 cfs and (138 cfs ≥138 cfs | Actual flow Previous day’s flow minus 14% but not less than 12 cfs Previous day’s flow minus 8% |
| Block 3 | July 22 through October 14 | (12 cfs (12 cfs and (138 cfs ≥138 cfs | Actual flow Previous day’s flow minus 18% but not less than 12 cfs Previous day’s flow minus 8% |

(c) Minimum five-year and ten-year moving annual average values are set forth in Table 8-22 as a tool to assess whether flows to the Anclote River remain above flow rates that are expected to occur with implementation of the Minimum Flow described in Table 8-24. The Means and Medians are based on evaluation of daily flow records for the Elfers Gage, adjusted for withdrawal impacts for the period 1955 through 2006. Yearly means and medians are computed for January 1 through December 31 of each year. Therefore, the Means and Medians are hydrologic statistics that represent the flows that will be met or exceeded if compliance with the Minimum Flow is maintained during hydrologic conditions similar to the 1955-2006 period. However, since changes in the watershed such as future structural alterations and climatic change could potentially affect surface water or groundwater flow characteristics and additional information relevant to Minimum Flows development may become available, the District is committed to periodic re-evaluation of the Minimum Flows.

| Table 8-24 Minimum Five-Year and Ten-Year Moving Mean and Median Flows for the Anclote River above USGS Anclote River near Elfers Gage USGS No. 02310000 Based on Application of the Table 8-23 Minimum Flow on Adjusted Flows at USGS 02310000 |
| --- |
| Minimum Flow | Hydrologic Statistic | Flow (cfs) |
| Annual Flow | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 48 17 36 15 |
| Block 1 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 13 7 11 6 |
| Block 2 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 25 17 21 15 |
| Block 3 | 10-Year Mean 10-Year Median 5-Year Mean 5-Year Median | 92 64 81 56 |

(16) Minimum Flow for the Chassahowitzka River System.

(a) For purposes of this rule, the Chassahowitzka River System includes the watercourse from the Chassahowitzka Main Springs Complex to the Gulf of Mexico, including contributing tributaries and all named and unnamed springs that discharge to the Chassahowitzka River, and Blind Springs.

(b) The Minimum Flow for the Chassahowitzka River System is 92% of the natural flow as measured at the United States Geological Survey (USGS) Gage Chassahowitzka River near Homosassa Gage No. 02310650. Natural flow is defined for the purpose of this rule as the flow that would exist in the absence of water withdrawal impacts. The Minimum Flow is based on an 8% reduction from the natural flow of 61 cubic feet per second, which was adjusted for groundwater withdrawals using hydrologic modeling for the period of record from February 20, 1997, through October 15, 2018, at the USGS Chassahowitzka River near Homosassa, FL Gage No. 02310650.

(c) Status assessments of the Minimum Flow for the Chassahowitzka River System will be completed to determine whether the flow is below or projected to fall below the Minimum Flow. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of each status assessment, the District will use the following approach:

1. The District will evaluate the Minimum Flow annually to determine the extent to which the flow of the Chassahowitzka River System has been reduced due to withdrawals as of the date of each status assessment at the USGS Chassahowitzka River near Homosassa, FL Gage No. 02310650. The annual evaluation will be completed through a review of:

(a) Flow data;

(b) Water withdrawals;

(c) Aquifer water levels;

(d) Rainfall data; and

(e) Hydrologic modeling.

2. The District will also evaluate the Minimum Flow every five years as part of the regional water supply planning process. This evaluation will include the use of hydrologic modeling.

3. If the Minimum Flow is being met based on the annual evaluation or the evaluation performed as a part of the regional water supply planning process, then no further actions are required beyond continued monitoring.

(d) The District will reevaluate the Minimum Flow by December 2029.

(17) Minimum Flow for the Homosassa River System.

(a) For purposes of this rule, the Homosassa River System includes the watercourse from the Homosassa Main Springs Complex to the Gulf of Mexico, including the southeast fork of the Homosassa River, Halls River, Hidden River and all named and unnamed springs that discharge to the Homosassa River.

(b) The Minimum Flow for the Homosassa River System is 95% of the combined natural flow as measured at the United States Geological Survey (USGS) Homosassa Springs at Homosassa Springs, FL Gage No. 02310678, and the USGS SE Fork Homosassa Spring at Homosassa Springs, FL Gage No. 02310688. Natural flow is defined for the purpose of this rule as the flow that would exist in the absence of water withdrawal impacts. The Minimum Flow is based on a 5% reduction from the combined natural flow of 149 cubic feet per second, which was adjusted for groundwater withdrawals using hydrologic modeling for the period of record from October 1, 2000, through October 1, 2018, at the USGS Homosassa Springs at Homosassa Springs, FL Gage No. 02310678 and the USGS SE Fork Homosassa Spring at Homosassa Springs, FL Gage No. 02310688.

(c) Status assessments of the Minimum Flow for the Homosassa River System will be completed to determine whether the flow is below or projected to fall below the Minimum Flow. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of each status assessment, the District will use the following approach:

1. The District will evaluate the Minimum Flow annually to determine the extent to which the flow of the Homosassa River System has been reduced due to withdrawals as of the date of each status assessment at the USGS Homosassa Springs at Homosassa Springs, FL Gage No. 02310678 and the USGS SE Fork Homosassa Spring at Homosassa Springs, FL Gage No. 02310688. The annual evaluation will be completed through a review of:

(a) Flow data;

(b) Water withdrawals;

(c) Aquifer water levels;

(d) Rainfall data; and

(e) Hydrologic modeling.

2. The District will also evaluate the Minimum Flow every five years as part of the regional water supply planning process. This evaluation will include the use of hydrologic modeling.

3. If the Minimum Flow is being met based on the annual evaluation or the evaluation performed as a part of the regional water supply planning process, then no further actions are required beyond continued monitoring.

(d) The District will reevaluate the Minimum Flow by December 2029.

(18) Minimum Flow for Gum Slough Spring Run.

(a) For purposes of this rule, Gum Slough Spring Run includes the watercourse from the Gum Slough Springs Group headspring to the Withlacoochee River, including all named and unnamed springs that discharge to the spring run.

(b) The Minimum Flow for Gum Slough Spring Run is 94% of the natural flow as measured at the United States Geological Survey Gum Springs near Holder, FL Gage (Gage No. 02312764), or as measured at any point downstream from this Gage. Natural flow is defined for the purpose of this rule as the flow that would exist in the absence of water withdrawal impacts.

(c) The Minimum Flow for Gum Slough Spring Run also includes a flow-based Minimum Low Flow Threshold of 43 cfs at this Gage. No surface water withdrawal shall be permitted that would individually or cumulatively cause the natural flow to be reduced below the Minimum Low Flow Threshold of 43 cfs.

(d) The District will re-evaluate the Minimum Flow within ten years of adoption of this rule.

(19) Minimum Flow for the Crystal River/Kings Bay System.

(a) For purposes of this rule, the Crystal River/Kings Bay System includes the watercourse from Kings Bay to the Gulf of Mexico, including contributing tributaries, Kings Bay, and all named and unnamed springs that discharge to the river or bay.

(b) The Minimum Flow for the Crystal River/Kings Bay System is a long-term tidally-filtered average flow of 406 cubic feet per second (“cfs”) at the United States Geological Survey Crystal River at Bagley Cove near Crystal River, FL Gage (“United States Geological Survey Gage No. 02310747”). The Minimum Flow is based on an 11% reduction from the long-term tidally-filtered average flow of 456 cfs adjusted for groundwater withdrawals for the period of record from 2002 through 2015 at the United States Geological Survey Gage No. 02310747.

(c) Status assessments of the Minimum Flow for the Crystal River/Kings Bay System will be completed to determine whether the long-term tidally-filtered average flow is below or projected to fall below the criteria adopted in this section. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of each status assessment, the District will use the following approach:

1. The District will evaluate the Minimum Flow annually to determine the extent to which the long-term tidally-filtered average flow of the Crystal River/Kings Bay System has been reduced due to withdrawals for the period of record from 2002 to the date of each status assessment at the United States Geological Survey Gage No. 02310747.

2. The District will also evaluate the Minimum Flow every five years as part of the regional water supply planning process.

3. If the Minimum Flow is being met based on long-term tidally-filtered average flows adjusted for withdrawals, then no further actions are required beyond continued monitoring.

(d) The District will re-evaluate the Minimum Flow within ten years of adoption of this rule.

(20) Minimum Flows for the Lower Pithlachascotee River.

(a) For purposes of this rule, the Lower Pithlachascotee River in Pasco County, FL includes the watercourse from the bridge across the river at Rowan Road (Pasco County Road 77) to the Gulf of Mexico, and tributaries to the watercourse segment.

(b) Minimum Flows for the Lower Pithlachascotee River are based on the adjusted flow at the U.S. Geological Survey Pithlachascotee River near New Port Richey, FL Gage (“Gage No. 02310300”) and are set forth in Table 8-25. Adjusted flow is defined as flow that would exist in the absence of withdrawal impacts. There are two flow-based Minimum Flows that were developed using average four-day flows at Gage No. 02310300 adjusted for withdrawals, with a long-term average of 27 cubic feet per second (“cfs”) for the period of record from June 22, 1989 through December 31, 2000. The total reduction in flow from the adjusted flow shall not exceed twenty-five percent of the previous four day’s average adjusted flow when the previous four-day’s adjusted flow is less than or equal to a Minimum High Flow Threshold of 60 cfs at Gage No. 02310300, and shall not exceed thirty-five percent of the previous four day’s average adjusted flow when the previous four-day’s adjusted flow exceeds a Minimum High Flow Threshold of 60 cfs at Gage No. 02310300.

| Table 8-25 Minimum Flows for the Lower Pithlachascotee River at the U.S. Geological Survey Pithlachascotee River near New Port Richey, FL gage (No. 02310300) |
| --- |
| Period | Effective Dates | Where the Adjusted Average Flow for the Preceding Four Days Equals: | Minimum Flow Is: |
| Annually | January 1 to December 31 | (60 cfs | Previous four day’s average adjusted flow minus 25% |
| Annually | January 1 to December 31 | >60 cfs | Previous four day’s average adjusted flow minus 35% |

(c) Status assessments of the Minimum Flows for the Lower Pithlachascotee River will be completed to determine whether the long-term, four-day average flow is below or projected to fall below the criterion adopted in this rule. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this rule subsection. As part of each status assessment, the District will use the following approach:

1. The District will evaluate flows in the Lower Pithlachascotee River annually to: determine the extent to which the long-term average of four-day average flows in the Lower Pithlachascotee River has been reduced due to withdrawals for the period of record from June 22, 1989 to the date of each status assessment at Gage No. 02310300.

2. The District will also evaluate flows in the Lower Pithlachascotee River every five years as part of the regional water supply planning process.

3. If the Minimum Flows are being met based on the long-term average of the four-day average flows at Gage No. 02310300, then no further actions are required beyond continued monitoring.

(21) Minimum Flows for the Upper Pithlachascotee River.

(a) For purposes of this rule, the Upper Pithlachascotee River in Pasco County, FL includes the watercourse from the outlet of Crews Lake to the bridge across the river at Rowan Road (Pasco County Road 77), and tributaries to the watercourse segment.

(b) Minimum Flows for the Upper Pithlachascotee River are based on the adjusted flow at the U.S. Geological Survey Pithlachascotee River near New Port Richey, FL Gage (“Gage No. 02310300”) and are set forth in Table 8-26. Adjusted flow is defined as flow that would exist in the absence of withdrawal impacts. There are three seasonally dependent, i.e., block-specific, Minimum Flows that were developed based on daily average flows at Gage No. 02310300 adjusted for withdrawals, with a long-term average of 27 cubic feet per second (“cfs”) for the period of record from June 19, 1989 through December 31, 2000. In addition, the Minimum Flows are flow-based. The Minimum Low Flow Threshold is applied continuously regardless of season. No surface water withdrawal will be permitted that would cumulatively cause the adjusted flow to be reduced below the Minimum Low Flow Threshold of 11 cfs. Additionally, permitted surface withdrawals shall cease when flows are below the Minimum Low Flow Threshold of 11 cfs. In addition, the total reduction in flow from the adjusted flow on any given day from June 24 through October 16 shall not exceed sixteen percent of the previous day’s adjusted flow when the adjusted flow is less than a Minimum High Flow Threshold of 50 cfs at Gage No. 023103300 and shall not exceed nine percent of the previous day’s adjusted flow when the adjusted flow equals or exceeds a Minimum High Flow Threshold of 50 cfs at Gage No. 02310300.

| Table 8-26 Minimum Flows for the Upper Pithlachascotee River at the U.S. Geological Survey Pithlachascotee River near New Port Richey, FL Gage (No. 02310300) |
| --- |
| Period | Effective Dates | Where the Adjusted Flow on the Previous Day Equals: | Minimum Flow Is: |
| Annually | January 1 to December 31 | (11 cfs (11 cfs and (50 cfs ≥ 50 cfs | Actual flow Seasonally dependent – see Blocks below Seasonally dependent – see Blocks below |
| Block 1 | April 25 through June 23 | (11 cfs (11 cfs | Actual flow Previous day’s adjusted flow minus 18% but not less than 11 cfs |
| Block 2 | October 17 through April 24 | (11 cfs (11 cfs | Actual flow Previous day’s adjusted flow minus 17% but not less than 11 cfs |
| Block 3 | June 24 through October 16 | (11 cfs (11 cfs and (50 cfs ≥50 cfs | Actual flow Previous day’s adjusted flow minus 16% but not less than 11 cfs Previous day’s adjusted flow minus 9% but not less than 11 cfs |

(c) Status assessments of the Minimum Flows for the Upper Pithlachascotee River will be completed to determine whether the long-term, daily average flow and the daily average flows are below or projected to fall below the criteria adopted in this rule. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this rule. As part of each status assessment, the District will use the following approach:

1. The District will evaluate flows in the Upper Pithlachascotee River annually to: determine the extent to which the long-term average of the daily average flows of the Upper Pithlachascotee River has been reduced due to withdrawals for the period of record from June 19, 1989 to the date of each status assessment at Gage No. 02310300; and to determine whether daily average flows at Gage No. 02310300 have been reduced below 11 cfs due to surface water withdrawals.

2. The District will also evaluate flows in the Upper Pithlachascotee River every five years as part of the regional water supply planning process.

3. If the Minimum Flows are being met based on the long-term average of the daily average flows at Gage No. 02310300, and based on the determination that surface water withdrawals have not reduced daily average flows at Gage No. 0230300 below 11 cfs, then no further actions are required beyond continued monitoring.

(22) Minimum Flow for the Rainbow River System.

(a) For purposes of this rule, the Rainbow River System includes the watercourse from the Rainbow Springs Group headsprings to the Withlacoochee River, including contributing tributaries, and all named and unnamed springs that discharge to the river.

(b) The Minimum Flow for the Rainbow River System is 95% of the natural flow as measured at the United States Geological Survey Rainbow River at Dunnellon, FL Gage No. 02313100. Natural flow is defined for the purpose of this rule as the flow that would exist in the absence of water withdrawal impacts. The Minimum Flow is based on a 5% reduction from the natural flow of 683 cubic feet per second, which was adjusted for groundwater withdrawals using hydrologic modeling for the period of record from 1965–2015 at the United States Geological Survey Rainbow River at Dunnellon, FL Gage No. 02313100.

(c) Status assessments of the Minimum Flow for the Rainbow River System will be completed to determine whether the flow is below or projected to fall below the Minimum Flow. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of each status assessment, the District will use the following approach:

1. The District will evaluate the Minimum Flow annually to determine the extent to which the flow of the Rainbow River System has been reduced due to withdrawals as of the date of each status assessment at the United States Geological Survey Rainbow River at Dunnellon, FL Gage No. 02313100. The annual evaluation will be completed through a review of:

(a) Flow data;

(b) Water withdrawals;

(c) Aquifer water levels;

(d) Rainfall data; and

(e) Hydrologic modeling.

2. The District will also evaluate the Minimum Flow every five years as part of the regional water supply planning process. This evaluation will include the use of hydrologic modeling.

3. If the Minimum Flow is being met based on the annual evaluation or the evaluation performed as a part of the regional water supply planning process, then no further actions are required beyond continued monitoring.

(d) The District will re-evaluate the Minimum Flow by December 2027.

(23) Minimum Flows for the lower Shell Creek.

(a) For purposes of this rule, the lower Shell Creek in Charlotte County, FL, includes the watercourse from the base of the downstream side of the Hendrickson Dam to its confluence with the Peace River.

(b) Minimum Flows for the lower Shell Creek are based on the daily average flow at the United States Geological Survey (USGS) Shell Creek near Punta Gorda, FL Gage, No. 02298202, adjusted for withdrawals and  agricultural runoff, for the period of record from January 1, 1972, through December 31, 2018, as set forth in Table 8-27.

| Table 8-27 Minimum Flows for Lower Shell Creek Based on flow at the USGS Shell Creek near Punta Gorda, FL Gage Adjusted for Surface Withdrawals from the Shell Creek Reservoir and Agricultural Runoff to the Reservoir. |
| --- |
| If adjusted flow in cubic feet per second (cfs) on the previous day is: | Minimum Flow is: |
| ≤56 cfs | 87% of adjusted flow on the previous day |
| >56 cfs and ≤137cfs | 77% of adjusted flow on the previous day |
| >137 cfs | 60% of adjusted flow on the previous day |

Status assessments of the Minimum Flows for the lower Shell Creek will be completed to determine whether the flow is below or projected to fall below the Minimum Flows.  Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of status assessment, the District will use the following approach:

1. The District will evaluate the Minimum Flow annually to determine the extent to which the flow of the lower Shell Creek has been reduced due to withdrawals as of the date of each status assessment at Gage No. 02298202. The annual evaluation will be completed through a review of:

a. Flow data;

b. Water withdrawals data;

c. Agricultural runoff data;

d. Rainfall and evaporation data; and

e. Hydrologic modeling.

2. The District will also evaluate the Minimum Flows every five years as part of the regional water supply planning process. This evaluation will include the use of hydrologic modeling.

3. If the Minimum Flows are being met based on the annual evaluation or the evaluation performed as a part of the regional water supply planning process, then no further actions are required beyond continued monitoring.

(24) Minimum Flows for the Upper Little Manatee River.

(a) 	For purposes of this rule, the Upper Little Manatee River in Hillsborough County, FL and Manatee County, FL includes the watercourse from its headwaters to the Environmental Protection Commission of Hillsborough County Water Quality Monitoring Station No. 1616 located at 82.40557 W, 27.66662 N, and tributaries to the watercourse.

(b) 	Minimum Flows for the Upper Little Manatee River are based on the daily average flow at the United States Geological Survey (USGS) Little Manatee River at US 301 near Wimauma, FL Gage No. 02300500, adjusted for withdrawals, for the period of record from April 1, 1939, through December 31, 2021, as set forth in Table 8-28.

| Table 8-28 Minimum Flow for the Upper Little Manatee River Based on the Flows from the USGS Little Manatee River at US 301 near Wimauma, FL Gage No. 02300500 Adjusted for Upstream Withdrawals |
| --- |
| If Adjusted Flow in cubic feet per second (cfs) on the previous Day is: | Minimum Flow is: |
| ≤29 cfs | Flow on the previous day |
| >29 cfs and ≤ 96 cfs | 29 cfs or 88% of flow on the previous day, whichever is greater |
| >96 cfs and ≤ 224 cfs | 85 cfs or 87% of flow on the previous day, whichever is greater |
| >224 cfs | 90% of flow on the previous day |

(c) Status assessments of the Minimum Flows for the Upper Little Manatee River will be completed to determine whether the flow is below or projected to fall below the Minimum Flows. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of each status assessment, the District will use the following approach:

1. The District will evaluate the Minimum Flow annually to determine the extent to which the flow of the Upper Little Manatee River has been reduced due to withdrawals as of the date of each status assessment at Gage No. 02300500. The annual evaluation will be completed through a review of:

(a) Flow data;

(b) Water withdrawals;

(c) Aquifer water levels;

(d) Rainfall data; and

(e) Hydrologic modeling.

2. The District will also evaluate the Minimum Flows every five years as part of the regional water supply planning process. This evaluation will include the use of hydrologic modeling.

3. If the Minimum Flows are being met based on the annual evaluation or the evaluation performed as a part of the regional water supply planning process, then no further actions are required beyond continued monitoring.

(25) Minimum Flows for the Lower Little Manatee River.

(a) 	For purposes of this rule, the Lower Little Manatee River in Hillsborough County, FL includes the watercourse from the Hillsborough County Environmental Protection Commission Water Quality Monitoring Station No. 1616 located at 82.40557 W, 27.66662 N, to Tampa Bay, and tributaries to the watercourse.

(b) 	Minimum Flows for the Lower Little Manatee River are based on the daily average flow at the United States Geological Survey (USGS) Little Manatee River at US 301 near Wimauma, FL Gage No. 02300500, adjusted for withdrawals, for the period of record from April 1, 1939, through December 31, 2021, as set forth in Table 8-29.

| Table 8-29 Minimum Flow for the Lower Little Manatee River Based on the Flows from the USGS Little Manatee River at US 301 near Wimauma, FL Gage No. 02300500 Adjusted for Upstream Withdrawals |
| --- |
| If Adjusted Flow in cubic feet per second (cfs) on the previous Day is: | Minimum Flow is: |
| ≤ 29 cfs | Flow on the previous day |
| > 29 cfs and ≤ 96 cfs | 29 cfs or 87% of flow on the previous day, whichever is greater |
| > 96 cfs | 84 cfs or 68% of flow on the previous day, whichever is greater |

(c) Status assessments of the Minimum Flows for the Lower Little Manatee River will be completed to determine whether the flow is below or projected to fall below the Minimum Flows. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of each status assessment, the District will use the following approach:

1. The District will evaluate the Minimum Flow annually to determine the extent to which the flow of the Lower Little Manatee River has been reduced due to withdrawals as of the date of each status assessment at Gage No. 02300500. The annual evaluation will be completed through a review of:

(a) Flow data;

(b) Water withdrawals;

(c) Aquifer water levels;

(d) Rainfall data; and

(e) Hydrologic modeling.

2. The District will also evaluate the Minimum Flows every five years as part of the regional water supply planning process. This evaluation will include the use of hydrologic modeling.

3. If the Minimum Flows are being met based on the annual evaluation or the evaluation performed as a part of the regional water supply planning process, then no further actions are required beyond continued monitoring.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.036, 373.042, 373.0421 FS. History–New 10-5-74, Amended 12-31-74, Formerly 16J-0.15, 40D-1.601, Amended 10-1-84, 8-7-00, 2-6-06, 4-6-06, 1-1-07, 11-25-07, 2-18-08, 3-2-08, 5-12-08, 5-10-09, 3-23-10, 3-28-10, 7-12-10, 8-2-10 (8), 8-2-10 (15), 10-16-12, 3-20-13(16), 3-20-13(17), 6-20-16, 3-15-18, 6-19-18, 4-15-20, 8-9-20, 4-12-21, 4-7-22, 3-27-24.

## 40D-8.603 Management Levels for Lakes and Other Impoundments.

Rulemaking Authority 373.016, 373.023, 373.044, 373.103 FS. Law Implemented 373.016, 373.042, 373.044 FS. History–New 6-7-78, Formerly 16J-8.67, Repealed 8-7-00.

## 40D-8.605 Cyclic Variations for Minimum Water Level.

Rulemaking Authority 373.016, 373.023, 373.044, 373.103 FS. Law Implemented 373.016, 373.042, 373.044 FS. History–New 6-7-78, Formerly 16J-8.671, Repealed 8-7-00.

## 40D-8.611 Minimum Flood Levels.

Rulemaking Authority 373.016, 373.023, 373.044, 373.103 FS. Law Implemented 373.016, 373.042, 373.044 FS. History–New 6-7-78, Formerly 16J-8.672, Repealed 8-7-00.

## 40D-8.613 Ten (10) Year Flood Warning Levels.

Rulemaking Authority 373.016, 373.023, 373.044, 373.103 FS. Law Implemented 373.016, 373.042, 373.044 FS. History–New 1-22-79, Formerly 16J-8.6721, Repealed 8-7-00.

## 40D-8.616 Posted Notice.

Rulemaking Authority 373.016, 373.023, 373.044, 373.103 FS. Law Implemented 373.016, 373.042, 373.044 FS. History–New 6-7-78, Formerly 16J-8.673, Repealed 8-7-00.

## 40D-8.621 Operating Levels for Lakes with District-Owned Management Structures.

(1) Schedules, levels, and procedures for operation of lakes with a District-owned management structure shall be established by the Board.

(2) The operating range for a structure of a lake shall be prescribed as that between the high operating level and the low operating level.

(a) High operating level shall be established by the Board in consideration of the Guidance Levels, any applicable established High Minimum Lake Level, public testimony and in keeping with the best lake management practices.

(b) Low operating level shall be established by the Board in consideration of Guidance Levels, any applicable Minimum Lake Level, public testimony and in keeping with the best lake management practices.

(3) Best lake management practices in the design, construction, operation, and maintenance of structures or devices requires a consideration and evaluation of both Long-term and short-term effects of the activity upon the water resources of the District, and mandatory compliance with any High Minimum Lake Level and Minimum Lake Level established for the lake. Factors to be considered include the following:

(a) Conservation and proper utilization of surface water;

(b) Prevention of damage from floods, soil erosion, and excessive drainage;

(c) Protection of natural resources, fish and wildlife;

(d) Storage for aquifer recharge; and

(e) Non-consumptive uses, including but not limited to, navigation, recreation, and aesthetics.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.042, 373.0421, 373.086 FS. History–New 6-7-78, Formerly 16J-8.677, Amended 8-7-00.

## 40D-8.623 Minimum Wetland Levels.

(1) Minimum Wetland Levels are established and incorporated into Table 8-1 below.

| TABLE 8-1 Adopted Minimum Wetland Levels |
| --- |
| Wetland Site | Minimum Wetland Level (feet NGVD) | Latitude (Decimal Degrees) | Longitude (Decimal Degrees) |
| (a) Cypress Creek W-11 | 67.8 | 28.2957 | -82.3854 |
| (b) Cypress Creek W-12 | 62.0 | 28.2922 | -82.3942 |
| (c) Cypress Creek W-17 | 62.8 | 28.2854 | -82.3950 |
| (d) Cypress Creek W-56 (G) | 62.7 | 28.2726 | -82.4051 |
| (e) Starkey S-99 | 29.6 | 28.2563 | -82.6272 |
| (f) Starkey Central | 43.3 | 28.2449 | -82.5961 |
| (g) Starkey Z | 39.7 | 28.2362 | -82.5854 |
| (h) Starkey Eastern (S-73) | 44.6 | 28.2464 | -82.5658 |
| (i) Starkey S-75 | 45.4 | 28.2507 | -82.5604 |
| (j) Starkey M (S-69) | 43.1 | 28.2431 | -82.5735 |
| (k) Starkey N | 45.2 | 28.2424 | -82.5527 |
| (l) Morris Bridge Entry Dome (MBR-35) | 33.8 | 28.1144 | -82.3069 |
| (m) Morris Bridge X-4 (MBR-89) | 40.4 | 28.1239 | -82.3373 |
| (n) Morris Bridge Clay Gully Cypress (MBR-88) | 39.6 | 28.1233 | -82.3456 |
| (o) Morris Bridge Unnamed (MBR-16) | 32.1 | 28.1064 | -82.3426 |
| (p) Eldridge Wilde 5 | 27.1 | 28.1559 | -82.6631 |
| (q) Eldridge Wilde 11 (NW-44) | 36.4 | 28.1684 | -82.6312 |
| (r) South Pasco 2 (NW-49) | 57.2 | 28.1839 | -82.5077 |
| (s) South Pasco South Cypress | 56.9 | 28.1814 | -82.5078 |
| (t) South Pasco 6 (NW-50) | 57.4 | 28.1883 | -82.5080 |
| (u) Cypress Bridge 16 | 58.4 | 28.2085 | -82.3719 |
| (v) Cypress Bridge 25 | 70.5 | 28.2330 | -82.3592 |
| (w) Cypress Bridge 32 | 48.7 | 28.1678 | -82.3674 |
| (x) Cypress Bridge 4 | 69.2 | 28.2290 | -82.3658 |
| (y) Cross Bar T-3 | 68.5 | 28.3484 | -82.4952 |
| (z) Cross Bar Q-1 | 72.5 | 28.3464 | -82.4695 |
| (aa) Cone Ranch 1 | 86.9 | 28.1325 | -82.1214 |
| (bb) Cone Ranch 2 | 90.5 | 28.1225 | -82.1207 |
| (cc) Cone Ranch 3 | 95.4 | 28.1107 | -82.1213 |
| (dd) Cone Ranch 4 | 99.0 | 28.1140 | -82.0984 |
| (ee) Cone Ranch 5 | 105.2 | 28.0984 | -82.0815 |
| (ff) Cone Ranch 6 | 96.0 | 28.1257 | -82.0991 |
| (gg) North Pasco 3 | 44.4 | 28.3167 | -82.5757 |
| (hh) North Pasco 21 | 44.5 | 28.2892 | -82.5751 |

(2) Wetland water levels are deemed to be below the Minimum Wetland Level when the Long-term Current P50 is below the Minimum Wetland Level. If insufficient data exists to determine if a wetland is below its Minimum Wetland Level, the wetland can be determined to be below the Minimum Wetland Level based on a comparison with wetlands that are hydrologically or hydrogeologically similar or, located in close proximity or, in the same drainage basin or, by use of aerial photographs or evaluation of hydrologic data or Hydrologic Indicators in the subject wetland.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.036, 373.042, 373.0421 FS. History–New 8-7-00, Amended 4-6-20, 11-11-20, 4-12-21, 5-17-23.

## 40D-8.624 Guidance and Minimum Levels for Lakes.

(1) Levels for lakes adopted during or after August 7, 2000, are set forth in Table 8-2 in subsection 40D-8.624(7), F.A.C. There are two Minimum Levels for these lakes, the High Minimum Lake Level and the Minimum Lake Level. For lakes with levels adopted during or after August 7, 2000, a reference in the District’s rules to the applicable minimum level or to established minimum water levels shall refer to the adopted High Minimum Lake Level and Minimum Lake Level described in this Rule 40D-8.624, F.A.C.

(2) Levels for lakes adopted prior to August 7, 2000, are set forth in Table 8-3 in subsection 40D-8.624(8), F.A.C. There are two Guidance Levels for these lakes, the High Level and the Low Level.

For lakes with levels adopted before August 7, 2000, a reference within the District’s rules to the applicable minimum level or to established minimum water levels shall refer to the Low Level described in this Rule 40D-8.624, F.A.C. Such a Low Level shall not be deemed a minimum level pursuant to Section 373.042, F.S.

(3) The High Minimum Lake Level (HMLL) is the elevation that a lake’s water levels are required to equal or exceed ten percent of the time on a Long-term basis. The High Minimum Lake Level is established to ensure that a lake reaches higher levels on a periodic basis.

(4) The Minimum Lake Level (MLL) is the elevation that the lake’s water levels are required to equal or exceed fifty percent of the time on a Long-term basis.

(5) Status assessments of the Minimum Levels for lakes for which Minimum Levels have been adopted will be completed annually to determine whether the respective lake’s level is below or projected to fall below the Minimum Levels. Each status assessment is independent from and not a determination of water use permit compliance or environmental resource permit compliance. Permit compliance is a regulatory function that is not within the scope of this subsection. As part of each status assessment, the District will use the following approach:

(a) The District will evaluate the Minimum Levels to determine the extent to which the water levels have been reduced due to withdrawals as of the date of each status assessment. The annual evaluation will be completed through a review of:

1. Surface Water Levels;

2. Water withdrawals;

3. Aquifer water levels;

4. Rainfall; and

5. Hydrologic modeling.

(b) The District will also evaluate the Minimum Levels every five years as part of the regional water supply planning process. This evaluation will include the use of hydrologic modeling.

(c) If the Minimum Levels are being met based on the annual evaluation or the evaluation performed as a part of the regional water supply planning process, then no further actions are required beyond continued monitoring.

(6) Levels for lakes established during or after August 7, 2000, are set forth in the following table. Guidance Levels for lakes established prior to August 7, 2000, are set forth in Table 8-3 in subsection 40D-8.624(7), F.A.C., below.

| Table 8-2 Minimum Levels Established During or After August 7, 2000. Levels are elevations, in feet above the National Geodetic Vertical Datum of 1929. |
| --- |
| Location by County and Basin | Name of Lake and Section, Township and Range Information | High Minimum Lake Level | Minimum Lake Level |
| (a) In Charlotte County Within the Peace River Basin RESERVED |  |  |  |
| (b) In Citrus County Within the Coastal Rivers Basin RESERVED |  |  |  |
| (c) In Citrus County Within the Withlacoochee River Basin | Fort Cooper, Lake S-27, T-19S, R-20E | 30.1' | 28.7' |
|  | Tsala Apopka, Lake (Lakes and wetlands comprising the Floral City Pool), S-14, T-20S, R-20E | 41.2' | 39.8' |
|  | Tsala Apopka, Lake (Lakes and wetlands comprising the Hernando Pool), S-26, T-18S, R-19E | 38.7' | 37.3' |
|  | Tsala Apopka, Lake (Lakes and wetlands comprising the Inverness Pool), S-08, T-19S, R-20E | 40.1' | 38.7' |
| (d) In DeSoto County Within the Peace River Basin RESERVED |  |  |  |
| (e) In Hardee County Within the Peace River Basin RESERVED |  |  |  |
| (f) In Hernando County Within the Coastal Rivers Basin | Hunters, Lake S-32, T-23S, R-17E | 18.6' | 16.4' |
|  | Tooke Lake S-13 & 24, T-22S, R-17E | 20.4' | 16.3' |
|  | Whitehurst Pond S-13 & 24, T-22S, R-17E | 22.4' | 17.5' |
|  | Weekiwachee Prairie, Lake (Lake Theresa) S-23, T-23S, R-17E | 21.4' | 18.3' |
| (g) In Hernando County Within the Hillsborough River Basin RESERVED |  |  |  |
| (h) In Hernando County Within the Withlacoochee River Basin | Lindsey, Lake S-25, T-21S, R-19E | 67.6' | 65.3' |
|  | Mountain, Lake S-16, T-23S, R-20E | 102.0' (CAT 3) | 98.7' (CAT 3) |
|  | Neff, Lake S-20, T-23S, R-20E | 100.7' | 93.7' |
|  | Spring, Lake S-15, T-23S, R-20E | 180.1' | 179.0' |
| (i) In Highlands County Within the Peace River Basin | Angelo, Lake S-25, T-33S, R-28E | 101.3' | 100.0' |
|  | Anoka, Lake S-27, T-33S, R-28E | 122.8' | 121.7' |
|  | Damon, Lake S-3, T-33S, R-28E | 97.4' | 96.3' |
|  | Denton, Lake S-02, T-34S, R-28E | 114.1' | 112.8' |
|  | Jackson, Lake S-30, T-34S, R-29E | 102.3' | 101.2' |
|  | June-In-Winter, Lake S-34, T-36S, R-29E | 74.5' | 74.0' |
|  | Letta, Lake S-31, T-33S, R-29E | 98.8' | 97.7' |
|  | Little Jackson, Lake S-06, T-35S, R-29E | 102.3' | 101.2' |
|  | Lotela, Lake S-26, T-33S, R-28E | 106.1' | 105.0' |
|  | Placid, Lake S-24, T-37S, R-29E | 92.6' | 91.4' |
|  | Tulane, Lake S-27, T-33S, R-28E | 117.9' | 116.6' |
|  | Verona, Lake S-23, T-33S, R-28E | 117.4' | 115.8' |
| (j) In Hillsborough County Within the Alafia River Basin | Wimauma, Lake S-9 and 16, T-32S, R-20E | 81.0' | 78.4' |
| (k) In Hillsborough County Within the Hillsborough River Basin | Hanna, Lake S-18, T-27S, R-19E | 61.2' | 59.2' |
|  | Hooker, Lake S-1, 12, T-29S, R-20E | 43.7' | 42.1' |
|  | Keene, Lake S-7, T 27S, R-19E | 61.5' | 60.1' |
|  | Kell, Lake S-13, 24, T-22S, R-17E | 65.6' | 64.2' |
|  | Stemper, Lake S-13, T-27S, R-18E | 60.8' | 59.4' |
| (l) In Hillsborough County Within the Northwest Hillsborough Basin | Alice, Lake S-16, T-27S, R-17E | 40.7' | 38.9' |
|  | Allen, Lake S-10, T-27S, R-18E | 61.6' | 60.7' |
|  | Barbara, Lake S-19, T-27S, R-18E | 53.1' | 51.4' |
|  | Bird, Lake S-26, T-27S, R-18E | 49.3' | 48.1' |
|  | Brant, Lake S-14, T-27S, R-18E | 57.6' | 55.9' |
|  | Calm, Lake S-14, T-27S, R-17E | 49.6' | 47.7' |
|  | Carroll, Lake S-10, 11, 14, 15, T-28S, R-18E | 36.8' | 35.4' |
|  | Charles, Lake S-23, T-27S, R-18E | 53.3' | 51.9' |
|  | Church, Lake S-28, T-27S, R-17E | 35.2' | 34.4' |
|  | Crenshaw, Lake S-22, T-27S, R-18E | 54.45' | 53.45' |
|  | Crescent, Lake S-10, T-27S, R-17E | 41.3' | 40.3' |
|  | Crystal, Lake S-14, T-27S, R-18E | 59.8' | 58.2' |
|  | Cypress, Lake S-24, T-27S, R-17E | 48.9' | 47.4' |
|  | Dan, Lake S-6, T-27S, R-17E | 32.3' | 30.9' |
|  | Deer, Lake S-1, T-27S, R-18E | 66.5' | 65.1' |
|  | Dosson Lake S-20, T-27S, R-18E | 53.2' | 52.1' |
|  | Echo, Lake S-28, T-27S, R-17E | 35.2' | 34.4' |
|  | Ellen, Lake S-19, T-27S, R-18E | 53.1' | 51.4' |
|  | Fairy (Maurine), Lake S-34, T-27S, R-17E | 32.5' | 32.1' |
|  | Garden, Lake S-17, T-27S, R-17E | 30.5' | 29.5' |
|  | Halfmoon, Lake S-31, T-27S, R-18E | 42.5' | 41.1' |
|  | Harvey, Lake S-3, T-27S, R-18E | 61.6' | 60.7' |
|  | Helen, Lake S-19, T-27S, R-18E | 53.1' | 51.4' |
|  | Hobbs, Lake S-1, T-27S, R-18E | 64.9' | 63.2' |
|  | Horse, Lake S-26, T-27S, R-17E | 44.9' | 43.9' |
|  | Jackson, Lake S-17, T-27S, R-17E | 32.2' | 31.2' |
|  | Juanita, Lake S-22, T-27S, R-17E | 41.0' | 39.5' |
|  | Little Moon, Lake S-28, T-27S, R-17E | 39.6' | 38.2' |
|  | Merrywater, Lake S-22, T-27S, R-18E | 56.6' | 55.2' |
|  | Mound, Lake S-11, T-27S, R-17E | 50.7' | 49.3' |
|  | Platt, Lake S-35, T-27S, R-18E | 49.5' | 48.1' |
|  | Pretty, Lake S-26, T-27S, R-17E | 43.9' | 42.5' |
|  | Rainbow, Lake S-22, T-27S, R-17E | 39.6' | 38.2' |
|  | Raleigh, Lake S-27, T-27, R-17 | 41.1' | 37.9' |
|  | Reinheimer, Lake S-15, T-27S, R-18E | 58.9' | 57.5' |
|  | Rogers, Lake S-27, T-27, R-17 | 38.7' | 35.6' |
|  | Round, Lake S-22, T-27S, R-18E | 54.1' | 53.1' |
|  | Saddleback, Lake S-22, T-27S, R-18S | 53.6' | 52.7' |
|  | Sapphire, Lake S-14, T-27S, R-18E | 62.7' | 61.0' |
|  | Starvation, Lake S-21, T-27S, R-18E | 52.7' | 50.4' |
|  | Strawberry (North Crystal), Lake S-14, T-27S, R-18E | 59.3' | 58.3' |
|  | Sunset, Lake S-17, T-27S, R-17E | 32.8' | 31.5' |
|  | Sunshine Lake S-20, T-27S, R-18E | 53.2' | 52.1' |
|  | Taylor, Lake S-16, T-27S, R-17E | 37.6' | 36.6' |
|  | Virginia, Lake S-3, T-27S, R-18E | 61.6' | 60.7' |
| (m) In Lake County Within the Green Swamp Basin RESERVED |  |  |  |
| (n) In Levy County Within the Withlacoochee River Basin | Marion, Lake S-02, T-14S, R-17E | 52.6' | 49.4' |
| (o) In Manatee County Within the Manasota River Basin RESERVED |  |  |  |
| (p) In Marion County Within the Withlacoochee River Basin | Bonable, Lake S-31, T-15, R-18 | 62.8' | 58.3' |
|  | Little Bonable, Lake S-30, T-15, R-18 | 57.8' | 52.2' |
|  | Tiger, Lake S32, T15, R-18 | 62.8' | 58.3' |
| (q) In Pasco County Within the Coastal Rivers Basin | Big Fish, Lake S-21, T-24, R-19E | 75.4' | 72.8' |
|  | Crews, Lake S-20, T-24S, R18E | 52.4' | 51.0' |
|  | Green, Lake S-16, T-26, R-18E | 74.2' | 71.9' |
|  | Moon, Lake S-28, T-25, R-17E | 39.6' | 38.2' |
|  | Pierce Lake S-9, T-25S, R-18E | 71.9' | 69.8' |
|  | Unnamed Lake No. 22 S-27, T-24S, R-18E | 59.3' | 55.8' |
| (r) In Pasco County Within the Green Swamp Basin RESERVED |  |  |  |
| (s) In Pasco County Within the Hillsborough River Basin | Bell, Lake S-13, T-26, R-18E | 70.8' | 69.4' |
|  | Bird, Lake S-36, T-26, R-18E | 66.6' | 65.2' |
|  | Buddy, Lake S-17, T-25S, R-21E | 92.5' | 87.6' |
|  | Hancock, Lake S-5, T-24S, R-20E | 101.7' | 99.4' |
|  | Iola, Lake S-15, T-24S, R-20E | 146.5' | 141.9' |
|  | Jessamine Lake S-11, T-24S, R-20E | 140.3' | 133.3' |
|  | King Lake S-7, T-26S, R-19E | 72.4' | 70.8' |
|  | King Lake (East) S-22, T-25S, R-20E | 105.1' | 102.7' |
|  | Middle, Lake S-4, T-24S, R-20E | 102.5' | 100.2' |
|  | Padgett, Lake S-24, T-26S, R-18E | 70.0' | 68.6' |
|  | Pasadena, Lake S-16, T-25S, R-21E | 92.5' | 87.6' |
| (t) In Pasco County Within the Pinellas-Anclote River Basin | Camp, Lake S-34, T-26, R-18E | 63.4' | 62.0' |
|  | Linda, Lake S-26, T-26S, R-18E | 66.2' | 64.7' |
|  | Parker (Ann), Lake S-35, T-26, R-17E | 48.1' | 46.7' |
| (u) In Pasco County Within the Withlacoochee River Basin | Clear, Lake S-1, T-25S, R-20E | 126.2' | 124.9' |
| (v) In Pinellas County Within the Pinellas-Anclote River Basin RESERVED |  |  |  |
| (w) In Polk County Within the Alafia River Basin RESERVED |  |  |  |
| (x) In Polk County Within the Green Swamp Basin RESERVED |  |  |  |
| (y) In Polk County Within the Hillsborough River Basin RESERVED |  |  |  |
| (z) In Polk County Within the Ocklawaha River Basin |  |  |  |
|  | Lowery, Lake S-14, T-27S, R-26E | 129.7' | 127.9' |
| (aa) In Polk County Within the Peace River Basin | Annie, Lake S-3, T-29S, R-27E | 115.2' | 112.8' |
|  | Aurora, Lake S13, T30S, R28E | 110.3' | 97.3' |
|  | Easy, Lake S19, T30S, R28E | 109.8' | 106.5' |
|  | Eva, Lake S-32, T-27S, R-27E | 119.2' | 118.1' |
|  | Bonnie, Lake S-31, T-29S, R-28E | 105.8' | 102.1' |
|  | Clinch, Lake S-31, T-31S, R-28E | 105.7' | 103.2' |
|  | Crooked, Lake S-01, T-31S, R-27E | 120.7' | 117.7' |
|  | Crystal, Lake S-02, T-30S, R-27E | 117.5' | 114.2' |
|  | Dinner, Lake S-15, T-29S, R-27E | 113.6' | 110.6' |
|  | Eagle Lake S-01, T-29S, R-25E | 131.2' | 129.1' |
|  | Hancock, Lake S-08, T-29S, R-25E | 98.8' | 97.6' |
|  | Lee, Lake S-10, T-29S, R-27E | 116.0' | 113.9' |
|  | Mabel, Lake S-11, T-29S, R-27E | 106.7' | 103.9' |
|  | McLeod, Lake S-07, T-29S, R-26E | 130.3' | 128.3' |
|  | North Lake Wales S-01, T-30S, R-27E | 109.2' | 105.7' |
|  | Parker, Lake S-8, T-28S, R-24E | 130.3' | 129.3' |
|  | Starr, Lake S-14, T-29S, R-27E | 106.4' | 103.2' |
|  | Venus Lake S-9, T-29S, R-27E | 120.4' | 118.2' |
|  | Wailes Lake S-01, T-30S, R-27E | 107.7' | 104.8' |
| (bb) In Sarasota County Within the Manasota Basin RESERVED |  |  |  |
| (cc) In Sumter County Within the Green Swamp Basin RESERVED |  |  |  |
| (dd) In Sumter County Within the Withlacoochee River Basin | Big Gant, Lake S-14, T-22S, R-22E | 76.3' | 74.9' |
|  | Black, Lake S-23, T-18S, R-23E | 53.9' | 51.3' |
|  | Deaton, Lake S-14, T-19S, R-23E | 64.8' | 63.2' |
|  | Miona, Lake S-27, T-18S, R-23E | 53.9' | 51.3' |
|  | Okahumpka, Lake S-21, T-19S, R-23E | 58.1' | 56.7' |
|  | Panasoffkee, Lake S-29, T-19S, R-22E | 40.8' | 39.4' |

(7) Guidance Levels established for lakes prior to August 7, 2000, are set forth in the following table:

| Table 8-3 Guidance Levels established prior to August 7, 2000 |
| --- |
| Location of Impoundment by County and Basin | High Level in Feet Above Mean Sea Level (msl) | Low Level in Feet Above Mean Sea Level (msl) |
| (a) In Charlotte County Within the Peace River Basin |  |  |
| (b) In Citrus County Within the Coastal Rivers Basin |  |  |
| (c) In Citrus County Within the Withlacoochee River Basin |  |  |
| Bradley, Lake S23, T20S, R20E | 42.50' | 40.25' |
| Cato, Lake S5, T19S, R20E | 38.00' | 35.50' |
| Connell, Lake S6, T19S, R20E | 35.50' | 32.00' |
| Cooter, Lake S17, T19S, R20E | 40.50' | 38.25' |
| Hog Pond, Lake (Nina) S2, T19S, R19E | 34.50' | 32.00' |
| Holden, Lake (Inverness) S32, T19S, R20E | 32.00' | 29.50' |
| Magnolia, Lake S3, T20S, R20E | 31.00' | 28.50' |
| Rush, Lake (Williams) S03, T17S, R18E | 35.75' | 33.25' |
| Little, Lake (Consuella) S15, T20S, R20E | 41.50' | 39.00' |
| Twin, Lake S6, T19S, R20E | 37.00' | 35.00' |
| (d) In DeSoto County Within the Peace River Basin |  |  |
| (e) In Hardee County Within the Peace River Basin |  |  |
| (f) In Hernando County Within the Coastal Rivers Basin |  |  |
| (g) In Hernando County Within the Hillsborough River Basin LAKES |  |  |
| Nicks, Lake S29, T23S, R20E | 113.00' | 110.50' |
| St. Clair, Lake S33, T23S, R20E | 113.00' | 110.50' |
| (h) In Hernando County Within the Withlacoochee River Basin LAKES |  |  |
| Elizabeth, Lake S11, T23S, R21E | 60.25' | 57.00' |
| Francis, Lake S11, T23S, R21E | 60.25' | 57.00' |
| Geneva, Lake S11, T23S, R21E | 60.25' | 57.00' |
| Sparkman, Lake S24, T23S, R19E | 91.50' | 89.00' |
| (i) In Highlands County Within the Peace River Basin LAKES Sec. Twsp. Rng. |  |  |
| Adelaide, Lake S5, T33S, R28E | 106.50' | 104.00' |
| Apthhorpe, Lake S18, T36S, R30E | 71.50' | 68.00' |
| Blue, Lake S30, T36S, R30E | 77.50' | 75.00' |
| Bonnet, Lake S8, T34S, R29E | 90.75' | 88.00' |
| Brentwood, Lake S10, T33S, R28E | 102.75' | 99.50' |
| Buck, Lake S29, T37S, R30E | 94.00' | 91.50' |
| Byrd, Lake S9, T33S, R28E | 108.25' | 105.50' |
| Carrie, Lake S21, T36S, R29E | 75.50' | 73.00' |
| Charlotte, Lake S17, T35S, R29E | 93.75' | 91.25' |
| Chilton, Lake S7, T33S, R28E | 114.00' | 111.00' |
| Clay, Lake S29, T36S, R30E | 78.75' | 76.00' |
| Crews, Lake S32, T36S, R29E | 119.50' | 117.00' |
| Dinner, Lake S17, T34S, R29E | 102.50' | 98.50' |
| Francis, Lake S22, T36S, R29E | 70.50' | 67.50' |
| Glenada, Lake S34, T33S, R28E | 120.00' | 117.00' |
| Grassy, Lake S17, T37S, R30E | 91.50' | 88.50' |
| Harry, Lake S1, T36S, R29E | 67.50' | 63.00' |
| Henry, Lake S25, T36S, R29E | 75.50' | 73.00' |
| Hill, Lake S17, T36S, R29E | 99.25' | 96.00' |
| Huckleberry, Lake S7, T35S, R29E | 104.50' | 102.00' |
| Huntley, Lake S5, T37S, R30E | 83.75' | 81.00' |
| Josephine, Lake S32, T35S, R29E | 72.50' | 69.00' |
| Lake Lachard S36, T36S, R29E | 78.50' | 76.00' |
| Lelia, Lake S34, T33S, R29E | 114.50' | 112.50' |
| Little Bonnet, Lake S36, T33S, R28E | 100.00' | 97.00' |
| Little Red Water, Lake S14, T36S, R29E | 103.25' | 100.50' |
| Lost, Lake S12, T37S, R29E | 88.00' | 84.00' |
| McCoy, Lake S6, T37S, R30E | 87.00' | 84.00' |
| Mirror, Lake S7, T37S, R30E | 93.50' | 90.00' |
| Center Nellie S13, T36S, R29E | 71.50' | 67.00' |
| Nellie N.W., Lake S13, T36S, R29E | 71.50' | 67.00' |
| Nellie S.E., Lake S13, T36S, R29E | 71.50' | 67.00' |
| Olivia, Lake S6, T33S, R28E | 117.50' | 114.50' |
| Pearl, Lake S6, T37S, R30E | 87.00' | 84.00' |
| Persimmon, Lake S10, T36S, 29E | 68.25' | 65.00' |
| Pioneer, Lake S11, T33S, R28E | 108.00' | 104.50' |
| Pythias, Lake S2, T33S, R28E | 101.00' | 98.00' |
| Red Beach Lake S15, T35S, R29E | 76.50' | 73.75' |
| Red Water Lake S14, T36S, R29E | 70.50' | 67.50' |
| Ruth, Lake S18, T35S, R29E | 94.00' | 91.50' |
| Saddlebags, Lake S6, T37S, R30E | 84.00' | 81.00' |
| Sebring, Lake S14, T34S, R28E | 107.25' | 104.50' |
| Simmons, Lake S24, T36S, R29E | 72.50' | 68.00' |
| Sirena, Lake S1, T37S, R29E | 87.00' | 84.00' |
| Trout, Lake S34, T32S, R28E | 101.00' | 98.00' |
| Unnamed Lake (B) S20, T37S, R30E | 91.50' | 88.50' |
| Unnamed Lake (F) S24, T36S, R29E | 78.00' | 74.00' |
| Viola, Lake S14, T33S, R28E | 109.50' | 105.75' |
| Wolf Lake S24, T35S, R28E | 92.50' | 90.00' |
| (j) In Hillsborough County Within the Alafia River Basin LAKES |  |  |
| Carlton, Lake S7, T29, R21 | 93.50' | 90.50' |
| Edward Medard Reservoir S36, T32, R21 | 62.75' | 57.50' |
| Grady, Lake S26, T29, R20 | 39.00' | 36.00' |
| Hickory Hammock, Lake S34, T32, R21 | 32.25' | 30.50' |
| Unnamed Lake #2 S22, T32, R21 | 56.00' | NO RECOMMENDATION |
| (k) In Hillsborough County Within the Hillsborough River Basin LAKES |  |  |
| Bellows, Lake (East Lake) S2, T29, R19 | 23.75' | 21.50' |
| Burrell, Lake S31, T27, R19 | 50.00' | 47.50' |
| Commiston, Lake S12, T27, R18 | 63.00' | 60.50' |
| Eckles, Lake S11, T28, R18 | 32.50' | 30.00' |
| Egypt, Lake S27, T28, R18 | 37.50' | 35.00' |
| Gornto, Lake S21, T29, R20 | 38.50' | 36.00' |
| Hart, Lake S6, T27, R19 | 66.00' | 64.00' |
| Hog Island, Lake S1, T27, R18 | 66.00' | 64.00' |
| Kathy, Lake S20, T29, R20 | 43.50' | 42.50' |
| Long, Lake S36, T27, R18 | 50.25' | 48.00' |
| Long Pond S13, T29, R20 | 46.50' | 44.00' |
| Mud, Lake (Lake Walden) S6, T29, R22 | 115.00' | 112.50' |
| Thonotosassa, Lake S14, T28, R20 | 37.00' | 34.50' |
| Unnamed Lake S18, T27, R19 | 63.00' | 60.50' |
| Unnamed Lake S7, T27, R19 | 61.00' | 58.50' |
| Valrico, Lake S24, T29, R20 | 45.00' | 42.50' |
| Weeks, Lake S2, T29, R20 | 43.25' | 41.00' |
| (l) In Hillsborough County Within the Northwest Hillsborough Basin LAKES Sec. Twsp. Rng. |  |  |
| SWEETWATER CREEK WATERSHED |
| Avis, Lake S15, T28S, R18E | 37.00' | 34.50' |
| Bay, Lake S3, T28, R18 | 46.75' | 44.00' |
| Boat, Lake S15, T28, R18 | 35.50' | 33.75' |
| Brooker, Lake S2, T27, R18 | 64.25' | 61.00' |
| Chapman, Lake S25, T27, R18 | 52.25' | 49.50' |
| Cooper, Lake S11, T27, R18 | 61.75' | 59.75' |
| Elaine, Lake S15, T28S, R18E | 37.00' | 34.50' |
| Ellen, Lake S15, T28S, R18E | 41.50' | 39.00' |
| Gass, Lake S36, T27, R18 | 49.50' | 46.25' |
| George, Lake S10, T28, R18 | 48.00' | 45.00' |
| Geraci, Lake S15, T27, R18 | 63.50' | 61.50' |
| Halls, Lake S3, T28S, R18E | 50.00' | 47.50' |
| Lipsey, Lake S10, T28, R18 | 41.50' | 39.00' |
| Magdalene, Lake S35, T27, R18 | 50.00' | 47.50' |
| Thomas, Lake S11, T27, R18 | 63.50' | 61.25' |
| Twin, Lake S22, T28, R18 | 32.00' | 30.00' |
| White Trout, Lake S15, T28, R18 | 36.50' | 34.00' |
| ROCKY CREEK WATERSHED |
| Armistead, Lake S25, T27, R17 | 44.00' | 40.50' |
| Browns, Lake S2, T27, R18 | 63.50' | 60.75' |
| Josephine, Lake S25, T27, R17 | 46.00' | 42.75' |
| LeClare, Lake S30, T27, R18 | 52.00' | 49.50' |
| Rock, Lake S25, T27, R17 | 46.00' | 42.75' |
| Turkey Ford, Lake S18, T27, R18 | 54.00' | 51.50' |
| DOUBLEBRANCH CREEK WATERSHED |
| Hixon, Lake S3, T28, R17 | 36.50' | 33.25' |
| Unnamed Lake #1 S2, T28S, R17E | 37.50' | 35.00' |
| Unnamed Lake #2 S2, T28S, R17E | 37.50' | 35.00' |
| BROOKER CREEK WATERSHED |
| Artillery, Lake S3, T27S, R17E | 44.00' | 40.50' |
| Buck, Lake S28, T27, R17 | 35.00' | 32.00' |
| Elizabeth, Lake S11, T27, R17 | 53.00' | 51.00' |
| Fern, Lake S10, T27, R17 | 46.00' | 43.00' |
| Frances, Lake S4, T27, R17 | 40.50' | 38.00' |
| Island Ford, Lake S10, T27, R17 | 41.50' | 39.00' |
| James, Lake S23, T27S, R17E | 46.50' | 43.50' |
| Keystone, Lake S15, T27, R17 | 42.00' | 39.75' |
| Little, Lake S23, T27S, R17E | 46.50' | 43.50' |
| Velburton, Lake S21, T27, R17 | 40.00' | 37.25' |
| ANCLOTE RIVER WATERSHED |
| Hiawatha, Lake S2, T27, R17 | 50.50' | 48.00' |
| Osceola, Lake S3, T27, R17 | 46.50' | 44.50' |
| (m) In Lake County Within the Green Swamp Basin |  |  |
| (n) In Levy County Within the Withlacoochee River Basin |  |  |
| (o) In Manatee County Within the Manasota Basin |  |  |
| (p) In Marion County Within the Withlacoochee River Basin |  |  |
| (q) In Pasco County Within the Coastal Rivers Basin LAKES |  |  |
| Garden, Lake S16, T25S, R16E | 19.00' | 16.25' |
| Richey, Lake S3, T26S, R16E | 13.00' | 10.00' |
| Worrell, Lake (Bass Lake) S26, T25S, R16E | 19.00' | 16.25' |
| (r) In Pasco County Within the Green Swamp Basin |  |  |
| (s) In Pasco County Within the Hillsborough River Basin LAKES |  |  |
| Catfish, Lake S30, T25S, R19E | 68.00' | 65.50' |
| Cow (East), Lake S19, T26S, R19E | 78.50' | 76.00' |
| Floyd, Lake S36, T26S, R19E | 68.50' | 66.00' |
| Gooseneck, Lake S29, T26S, R19E | 73.50' | 71.00' |
| Hog (Joyce), Lake S19, T26S, R19E | 76.50' | 73.50' |
| JoAnn, Lake S30, T26S, R19E | 68.00' | 65.50' |
| Moody, Lake S10, T24S, R20E | 110.00' | 107.50' |
| Myrtle, Lake S30, T26S, R19E | 68.00' | 65.50' |
| Saxon, Lake S30, T26S, R19E | 71.25' | 69.00' |
| Tampa (Turtle), Lake S32, T26S, R19E | 65.50' | 63.00' |
| Toni, Lake S30, T26S, R19E | 68.00' | 65.50' |
| Twin, Lake S28, T26S, R19E | 67.50' | 65.00' |
| Unnamed Lake #26 S25, T26S, R18E | 68.00' | 65.50' |
| (t) In Pasco County Within the Pinellas-Anclote River Basin LAKES |  |  |
| Bass, Lake (Holiday) S34, T26S, R17E | 48.75' | 45.75' |
| Big Lake Vienna S23, T26S, R18E | 70.25' | 67.00' |
| Fishing, Lake S34, T26S, R17E | 48.75' | 45.75' |
| Geneva, Lake (Mud) S26, T26S, R17E | 50.00' | 48.00' |
| Little Moss (Como), Lake S35, T26S, R18E | 66.00' | 63.00' |
| Minniola, Lake S34, T26S, R17E | 50.00' | 48.00' |
| Moss, Lake S35, T26S, R18E | 64.00' | 61.50' |
| Seminole, Lake S35, T26S, R17E | 48.75' | 46.00' |
| Thomas, Lake S11, T26S, R18E | 75.00' | 72.50' |
| Wistaria, Lake S2, R26S, R18E | 74.00' | 71.00' |
| (u) In Pasco County Within the Withlacoochee River Basin LAKES |  |  |
| (v) In Pinellas County Within the Pinellas-Anclote River Basin LAKES |  |  |
| Lake Tarpon Sec.Twsp.Rng. S7, T27S, R16E S8, T27S, R16E S16, T27S, R16E S17, T27S, R16E S18, T27S, R16E S19, T27S, R16E S20, T27S, R16E S21, T27S, R16E S28, T27S, R16E S29, T27S, R16E S30, T27S, R16E S32, T27S, R16E S33, T27S, R16E S4, T28S, R16E | 3.80' | 2.20' |
| (w) In Polk County Within the Alafia River Basin LAKES |  |  |
| Scott, Lake S17, T29, R24 | 168.00' | 165.00' |
| (x) In Polk County Within the Green Swamp Basin LAKES |  |  |
| Agnes, Lake S4, T27, R25 | 135.75' | 134.75' |
| Alfred, Lake S30, T27S, R26E | 130.75' | 128.25' |
| Arietta, Lake S27, T27, R25 | 144.00' | 141.00' |
| Camp, Lake S20, T27, R26 | 134.50' | 132.00' |
| Clearwater Lake S5, T27, R25 | 143.50' | 141.00' |
| Cummings, Lake S31, T27S, R26E | 131.00' | 127.50' |
| Eva, Lake S29, T27S, R26E | 131.50' | 129.00' |
| Grassy, Lake (Big Glades) S19, T27, R26 | 132.00' | 129.50' |
| Griffin, Lake S30, T27S, R26E | 131.50' | 129.00' |
| Gum, Lake S17, T27, R26 | 131.00' | 128.50' |
| Haines, Lake S33, T27, R26 | 128.75' | 126.50' |
| Helene, Lake S34, T26, R25 | 144.00' | 141.00' |
| Juliana, Lake S15, T27, R25 | 132.50' | 130.00' |
| Little Lake Agnes S3, T27, R25 | 136.00' | 133.00' |
| Little Van, Lake S26, T27, R25 | 139.00' | 136.50' |
| Mattie, Lake S14, T27, R25 | 132.50' | 130.00' |
| Mud, Lake S6, T27, R25 | 141.50' | 137.75' |
| Myrtle, Lake S32, T27, R25 | 141.00' | 138.50' |
| Swoope, Lake S29, T27, R26 | 132.50' | 130.00' |
| Tennessee, Lake S9, T27, R25 | 134.00' | 130.00' |
| Van, Lake S26, T27, R25 | 132.75' | 130.00' |
| Whistle, Lake S33, T27, R25 | 137.50' | 135.00' |
| (y) In Polk County Within the Hillsborough River Basin LAKES |  |  |
| Bonnet, Lake S14, T28, R23 | 148.00' | 145.00' |
| Hunter, Lake S24, T28, R23 | 162.75' | 160.25' |
| (z) In Polk County Within the Peace River Basin |  |  |
| Ada, Lake S33, T28S, R27E | 123.00' | 120.00' |
| Altamaha, Lake S11, T30S, R27E | 122.50' | 120.00' |
| Amoret, Lake S24, T30S, R27E | 115.25' | 113.00' |
| Ariana, Lake S3, T28S, R25E | 137.00' | 134.50' |
| Banana, Lake S10, T29S, R24E | 106.50' | 103.50' |
| Belle, Lake S11, T30S, R27E | 120.00' | 117.00' |
| Bess, Lake S18, T29S, R27E | 125.25' | 123.00' |
| Big Gum, Lake S26, T29S, R28E | 95.00' | 92.00' |
| Blue, Lake S13, T28S, R25E | 149.00' | 146.50' |
| Blue Lake S24, T30S, R27E | 117.00' | 114.00' |
| Bonny, Lake S20, T28S, R24E | 130.50' | 128.00' |
| Buckeye, Lake S22, T28S, R26E | 129.00' | 126.00' |
| Buffum, Lake S12, T31S, R26E | 132.25' | 129.25' |
| Cannon, Lake S19, T28S, R26E | 132.00' | 129.50' |
| Connie, Lake S9, T28S, R26E | 128.75' | 126.50' |
| Cooper (Worth) S02, T30S, R27E | 123.50' | 121.00' |
| Crystal, Lake S21, T28S, R27E | 122.00' | 119.00' |
| Crystal, Lake S23, T29S, R26E | 129.50' | 127.00' |
| Cypress, Lake S36, T29S, R28E | 98.50' | 95.00' |
| Lake Daisy S6, T29S, R27E | 130.00' | 127.00' |
| Lake Deer S25, T28S, R25E | 140.75' | 138.50' |
| Dell, Lake S28, T28S, R27E | 123.75' | 121.50' |
| Lake Dexter S2, T29S, R26E | 132.00' | 129.00' |
| Easy, Lake S19, T30S, R28E | 115.25' | 113.00' |
| Echo, Lake S05, T28S, R26E | 131.00' | 128.00' |
| Effie, Lake S3, T30S, R27E | 118.00' | 115.00' |
| Elbert, Lake S22, T28S, R26E | 135.50' | 133.00' |
| Eloise, Lake S3, T29S, R26E | 132.00' | 129.50' |
| Fannie, Lake S11, T28S, R26E | 125.75' | 123.50' |
| Lake Florence S35, T28S, R26E | 128.75' | 127.00' |
| Lake Fox S6, T29S, R27E | 135.00' | 132.00' |
| Garfield, Lake S5, T30S, R26E | 104.75' | 101.00' |
| Gator, Lake S26, T30S, R26E | 133.00' | 130.75' |
| George, Lake S06, T28S, R26E | 130.00' | 127.50' |
| Gibson, Lake S25, T27S, R23E | 143.50' | 141.50' |
| Gordon, Lake S16, T28S, R27E | 119.00' | 116.00' |
| Lake Grassy S2, T29S, R25E | 129.00' | 126.50' |
| Lake Gross (Grassy) S14, T29S, R26E | 136.00' | 133.50' |
| Hamilton, Lake S18, T28S, R27E | 121.50' | 119.00' |
| Hart, Lake S24, T29S, R26E | 124.50' | 122.00' |
| Hartridge, Lake S8, T28S, R26E | 132.00' | 129.50' |
| Henry, Lake S16, T31S, R26E | 159.00' | 156.00' |
| Henry, Lake S36, T27S, R26E | 126.50' | 124.50' |
| Hickory, Lake S17, T32S, R28E | 98.50' | 96.00' |
| Howard, Lake S30, T28S, R26E | 132.00' | 129.50' |
| Ida, Lake S28, T31S, R28E | 79.00' | 76.50' |
| Ida, Lake S17, T28S, R26E | 135.25' | 132.00' |
| Idyl, Lake S16, T28S, R26E | 134.00' | 131.50' |
| Idylwild, Lake S18, T28S, R26E | 132.00' | 129.50' |
| Jessie, Lake S12, T28S, R25E | 132.00' | 129.50' |
| Josephine, Lake S13, T30S, R27E | 120.00' | 116.50' |
| Josephine, Lake S27, T28S, R27E | 121.50' | 118.00' |
| Lee, Lake S16, T28S, R27E | 123.50' | 121.50' |
| Lena, Lake S9, T28S, R25E | 137.00' | 134.50' |
| Leonore, Lake S10, T31S, R28E | 87.00' | 84.50' |
| Link, Lake S27, T28S, R26E | 128.00' | 125.00' |
| Little Aurora S13, T30, R28 | 100.50' | 98.00' |
| Little Gum, Lake S35, T29S, R28E | 96.50' | 94.00' |
| Little Lake Hamilton S5, T28S, R27E | 121.50' | 119.00' |
| LuLu, Lake S4, T29S, R26E | 132.00' | 129.50' |
| Mariam, Lake S27, T28S, R26E | 124.75' | 122.75' |
| Marie, Lake S27, T28S, R27E | 121.00' | 118.00' |
| Martha, Lake S21, T28S, R26E | 142.00' | 139.00' |
| Maude, Lake S21, T28S, R26E | 140.50' | 137.50' |
| May, Lake S29, T28S, R26E | 132.00' | 129.50' |
| Medora, Lake S36, T27S, R25E | 138.00' | 134.50' |
| Menzie, Lake S28, T28S, R27E | 122.00' | 120.00' |
| Middle Lake Hamilton S7, T28S, R27E | 121.50' | 119.00' |
| Lake Millsite S11, T29S, R25E | 123.50' | 121.00' |
| Mirror, Lake S20, T28S, R27E | 132.00' | 129.50' |
| Moody, Lake S17, T31S, R28E | 93.50' | 91.00' |
| Myrtle, Lake S19, T29S, R27E | 118.50' | 116.50' |
| Lake Ned S1, T29S, R26E | 128.50' | 126.00' |
| Otis, Lake S28, T28S, R25E | 128.00' | 125.00' |
| Pansy, Lake S08, T28S, R26E | 129.00' | 126.50' |
| Parker, Lake S32, T29S, R27E | 122.00' | 119.50' |
| Parks, Lake S36, T29S, R28E | 102.50' | 100.00' |
| Polecat, Lake S27, T30S, R26E | 142.00' | 139.50' |
| Reedy, Lake S35, T31S, R28E | 79.75' | 77.25' |
| Reeves, Lake S13, T29S, R26E | 124.50' | 122.00' |
| Lake River S1, T29S, R26E | 139.50' | 136.00' |
| Rochelle, Lake S4, T28S, R26E | 128.75' | 126.50' |
| Round, Lake S13, T29S, R26E | 129.25' | 126.50' |
| Roy, Lake S34, T28S, R26E | 132.00' | 129.50' |
| Ruby, Lake S12, T29S, R26E | 125.25' | 123.00' |
| Ruth, Lake S28, T28S, R27E | 121.50' | 117.50' |
| Saddlebag, Lake S6, T30S, R29E | 105.00' | 102.00' |
| Saint Anne Lake S14, T30S, R28E | 96.00' | 93.00' |
| Sanitary (Mariana), Lake S01, T28S, R25E | 137.50' | 135.00' |
| Sara, Lake S17, T28S, R27E | 121.50' | 119.00' |
| Scott, Lake S18, T29S, R24E | 168.00' | 165.00' |
| Lake Sears S36, T28S, R25E | 141.00' | 138.00' |
| Serena, Lake S12, T30S, R27E | 118.00' | 115.00' |
| Shipp, Lake 32, T28S, R26E | 132.00' | 129.50' |
| Silver, Lake S5, T32S, R28E | 103.00' | 100.50' |
| Silver, Lake S20, T28S, R26E | 146.50' | 144.00' |
| Smart, Lake S9, T28S, R26E | 128.75' | 126.50' |
| Lake Spirit S35, T28S, R25E | 131.50' | 129.00' |
| Spring, Lake S20, T28S, R27E | 132.00' | 129.50' |
| Streety, Lake S24, T32S, R27E | 105.50' | 102.50' |
| Summit, Lake S34, T28S, R26E | 132.00' | 129.50' |
| Sunset, Lake S10, T30S, R28 | 98.00' | 95.50' |
| Surveyors, Lake S26, T30S, R26E | 133.00' | 130.75' |
| Thomas, Lake S1, T30S, R28E | 99.50' | 97.00' |
| Lake Thomas S35, T28S, R25E | 132.00' | 128.00' |
| Tractor, Lake S14, T30S, R27E | 123.25' | 121.00' |
| Trask, Lake S22, T28S, R27E | 113.00' | 108.00' |
| Trout, Lake S34, T32S, R28E | 101.00' | 98.00' |
| Twin, Lakes S11, T30S, R27E | 123.75' | 120.00' |
| Walker, Lake S21, T30S, R26E | 141.00' | 137.00' |
| Warren, Lake S11, T30S, R27E | 123.50' | 121.00' |
| Weader (Weaver), Lake S03, T30S, R27E | 121.75' | 119.00' |
| Winterset, Lake S11, T29S, R26E | 132.00' | 129.50' |
| (aa) In Sarasota County Within the Manasota Basin |  |  |
| (bb) In Sumter County Within the Green Swamp Basin |  |  |
| (cc) In Sumter County Within the Withlacoochee River Basin LAKES |  |  |
| Cherry, Lake S24, T18S, R23E | 55.00' | 53.00' |

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.036, 373.042, 373.0421, 373.086, 373.709 FS. History–New 6-7-78, Amended 1-22-79, 4-27-80, 10-21-80, 12-22-80, 3-23-81, 4-14-81, 6-4-81, 10-15-81, 11-23-81, 1-5-82, 3-11-82, 5-10-82, 7-4-82, 9-2-82, 11-8-82, 1-10-83, 4-3-83, 7-5-83, 9-5-83, 10-16-83, 12-12-83, 5-8-84, 7-8-84, 12-16-84, 2-7-85, 5-13-85, 6-26-85, 11-3-85, 3-5-86, 6-16-86, Formerly 16J-8.678, Amended 9-7-86, 2-12-87, 9-2-87, 2-18-88, 6-27-88, 2-22-89, 3-23-89, 9-26-89, 7-26-90, 10-30-90, 3-3-91, 9-30-91, 10-7-91, 7-26-92, 3-1-93, 5-11-94, 6-6-96, 2-23-97, 8-7-00, 1-8-04, 12-21-04 (13), 12-21-04 (13), 6-5-05, 5-2-06, 1-1-07, 2-12-07, 1-10-08, 2-18-08, 4-7-08, 5-20-08, 5-10-09, 4-13-11, 3-12-12, 11-25-12, 2-21-13 (12)(f), 2-21-13 (12)-(13), 9-3-13, 1-7-15, 7-1-15, 9-21-15, 11-30-16, 12-28-16, 2-12-17 (12)(s), 2-12-17 (12)(z), 2-12-17 (12)(z), 2-19-17 (12)(l), 2-19-17 (12)(q), 3-2-17 (12)(l), 3-2-17 (12)(z), 3-22-17, 4-2-17 (12)(q), 4-2-17 (12)(z), 4-20-17 (12)(i), 4-20-17 (12)(i), 2-5-18, 3-20-18, 5-30-18, 1-23-19, 2-11-19, 3-20-19, 4-28-19, 7-17-19, 5-27-20, 8-9-20, 4-12-21, 6-1-21, 9-27-21.

## 40D-8.626 Minimum Aquifer Levels.

(1) Hillsborough County North of State Road 60, and Pasco and Pinellas Counties Salt Water Intrusion within this area has not been regional in nature, but is of localized concern in some coastal areas. The District has chosen the North Pinellas, Southwest Pasco and Northwest Hillsborough Counties region as the priority area for the establishment of Salt Water Intrusion Minimum Aquifer Levels (“SWIMAL”) to prevent regional seawater intrusion because of the availability of data and the potential for future intrusion. The SWIMALs for the Upper Floridan aquifer shall be established as follows:

(a) The location of the SWIMAL sites serves to monitor the area where early signs of regional salt water intrusion can best be detected.

(b) The SWIMALs shall be established by setting levels in coastward transects of wells whose potentiometric levels define the Long-term average hydraulic gradient of the Upper Floridan aquifer potentiometric surface.

(c) The Salt Water Intrusion Minimum Aquifer Levels are as set forth in the following table. Aquifer levels are deemed to be below the SWIMAL when the Long-term average elevation is below the SWIMAL.

| TABLE 8-4 SALT WATER INTRUSION |
| --- |
| MINIMUM AQUIFER LEVELS |
| Well Name | Saltwater Intrusion Minimum Aquifer Level (feet NGVD) |
| Sheldon Road Deep (RMP-16D) | 7.7 |
| RMP-13D | 16.4 |
| RMP-8D1 | 26.8 |
| Tarpon Rd. Deep | 9.9 |
| SWI-18S | 14.8 |
| 201-M | 13.7 |
| EW 2S Deep | 10.3 |

(2) SWUCA Salt Water Intrusion Minimum Aquifer Level.

(a) The District has determined that ground water withdrawals in the SWUCA have contributed to water level declines that advance saltwater intrusion. The coastal portion of the SWUCA in southern Hillsborough, Manatee and northern Sarasota counties (the Most Impacted Area or MIA) is a priority area for the establishment of minimum aquifer levels because of its proximity to the saltwater interface and the large effect on interface movement caused by lowering of the potentiometric surface in this area. The Salt Water Intrusion Minimum Aquifer Level (SWIMAL) is established to stabilize regional water level declines so that long-term management efforts can slow the rate of regional saltwater intrusion in the MIA. This is based on an average value to address the regional nature of the problem and avoids the potential for localized lowering of a minimum level.

(b) The SWIMAL over the surface of the MIA is 13.1 feet (National Geodetic Vertical Datum of 1929 or NGVD 1929). The SWIMAL is derived using the method set forth in paragraph (2)(c) below.

(c) The reference period for which the SWIMAL is calculated is the period 1990 through 1999. Ten wells from within or adjacent to the MIA (Table 8-5), are used to determine the minimum level. The annual average elevation for each of the years 1990 through 1999 is established utilizing monthly water level data for each of the wells. The annual averages over the period are then used to calculate the decadal average for the period. The 1990-99 average Upper Floridan aquifer potentiometric surface of the MIA is constructed by calculating the average of these annual average values weighted spatially using the Thiessen polygon methodology. The resulting Minimum Level over the surface of the MIA is 13.1 feet (National Geodetic Vertical Datum of 1929).

Table 8-5: Wells utilized to determine the Salt Water Intrusion Minimum Aquifer Level.

| Site |  |  |
| --- | --- | --- |
| Number | Sequence Number | Site Name |
| 564 | 0 | KIBLER DEEP |
| 87 |  | ROMP 123 Hawthorn/Ocala HAWTHORN/OCALA |
| 10914 | 0 | ROMP 50 TAMPA/OCALA |
| 10883 | 0 | ROMP TR 10-2 TAMPA |
| 287 | 0 | ROMP TR 7-1 TAMPA |
| 10926 | 0 | ROMP TR 7-4 Suwannee/Ocala SUWANNEE/OCALA |
| 10920 | 0 | ROMP TR 8-1 Upper Avon Park PARK |
| 10909 | 1 | ROMP TR 9-3 Ocala/Avon Park |
| 561 | 0 | SARASOTA 9 DEEP |
| 456 | 0 | VERNA T 0-4 |

(d) Implementation of The SWUCA Salt Water Intrusion Minimum Aquifer Level – The SWIMAL shall be used to gauge the status of the ground water resource with respect to saltwater intrusion in the region. Determining the status of the rate of movement of the saltwater interface shall be based on comparison of the average Floridan aquifer water level over the MIA with the Floridan aquifer minimum level over ten-year moving windows of time. The ten-year average water level for a particular year shall be calculated as the average water level for that year and the previous nine years. The process of calculating the ten-year average is the same as described in paragraph (c), above, for calculating the minimum level.

(e) Compliance – The objective of the District’s management efforts is for the ten-year moving annual average water level to fluctuate in a range at or above the minimum level. The minimum level is achieved if the ten-year moving annual average water level has fluctuated at or above the minimum level for a minimum of five consecutive years. Once the minimum level is achieved, the minimum level is no longer met when the ten-year moving annual average water level falls below the minimum level for more than two consecutive years. Then, the five consecutive years above the minimum level is again required for compliance.

(3) Dover/Plant City Water Use Caution Area Minimum Aquifer Level.

(a) The District has determined that groundwater withdrawals in the Dover/Plant City area have contributed to water level declines that are significantly harmful to the water resources of the area. The Minimum Aquifer Level is established as part of a comprehensive management program intended to arrest water level declines during frost/freeze events to minimize the potential for impacts to existing legal uses and sinkhole occurrence.

(b) The Minimum Aquifer Level is the 10 ft. potentiometric surface elevation (NGVD 1929) at District Well DV-1 Suwannee, located as shown in Figure 8-4. The Minimum Aquifer Level is the level below which the greatest impact occurred in terms of well failures and sinkholes during the 2010 frost/freeze event.

(c) To address the effects of local and regional groundwater withdrawals and the variable hydrogeologic factors within the region, a Minimum Aquifer Level Protection Zone is established. The Minimum Aquifer Level Protection Zone is the area within the 30 ft. drawdown contour that resulted from the January, 2010 frost/freeze event, as shown in Figure 8-4.

(d) Compliance with the Minimum Aquifer Level is evaluated annually using a groundwater flow model simulation of a frost/freeze event and the effects of the event on aquifer water levels in the Dover/Plant City Water Use Caution Area. If the resulting potentiometric level is at or above 10 ft. (NGVD 29) at District Well DV-1 Suwannee, the Minimum Aquifer Level is met. If the resulting level is below 10 ft. (NGVD 1929) at District Well DV-1 Suwannee, the Minimum Aquifer Level is not met.

Figure 8-4. Minimum Aquifer Level District Well DV-1 Suwannee and Minimum Aquifer Level Protection Zone

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.036, 373.042, 373.0421, 373.709 FS. History–New 8-7-00, Amended 1-1-07, 6-16-11, 2-17-22.