# CHAPTER 5K-10

# MILK, MILK PRODUCTS AND FROZEN DESSERTS

# 5K-10.001	Documents Incorporated by Reference and Definitions

# 5K-10.002	Permits, Licenses and Inspections

# 5K-10.003	Dating; Standards for Milk, Milk Products, Manufactured Milk Products and Frozen Desserts

# 5K-10.004	Future Dairy Farms, Milk Plants, Manufacturing Milk Plants and Frozen Dessert Plants

# 5K-10.006	Hemp Extract

## 5K-10.001 Documents Incorporated by Reference and Definitions.

(1) The following materials are hereby incorporated by reference and shall apply in the interpretation and enforcement of Chapter 502, F.S. Copies of all referenced materials are available at the Florida Department of Agriculture and Consumer Services, Division of Food Safety, Bureau of Dairy Industry, 3125 Conner Boulevard, Suite C, Tallahassee, Florida 32399-1650 and online as indicated.

(a) Grade A Pasteurized Milk Ordinance (“PMO”), 2017 Revision, Public Health Service/Food and Drug Administration, its Appendices and notes available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12004.

(b) The Procedures Governing the Cooperative State-Public Health Service/Food and Drug Administration Program of the National Conference on Interstate Milk Shipments, 2017 Revision, available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12005.

(c) Methods of Making Sanitation Rating of Milk Shippers and the Certifications/Listings of Single-Service Containers and/or Closures for Milk and/or Milk Products Manufacturers (MMSR), 2017 Revision, available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12055 and http://www.flrules.org/Gateway/reference.asp?No=Ref-12056.

(d) Evaluation of Milk Laboratories, 2017 Revision, available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12006.

(e) 21 Code of Federal Regulations, Parts 7, 11,101, 108, 110, 113, 114, 117, 130.10, 130.17, 131, 133, 135, 173.10, 174-178, 182.6285, 184.1666, 184.1979, 1240.61, Revised April 1, 2017, available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12018 and http://www.flrules.org/Gateway/reference.asp?No=Ref-12019.

(f) 40 Code of Federal  Regulations, Parts 141, 152.500, 156.10, 158, 180.940, Revised July 1, 2017 and available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12023 and http://www.flrules.org/Gateway/reference.asp?No=Ref-12020.

(g) 7 Code of Federal Regulations, Part 58, Subpart B, 58.101(e), (g), (n), (t), (u), (v), (w); 58.125-58.131; 58.142, 58.147; 58-148 (B)-(F); 58.150-58.154; 58.205-58.247; 58.305-58.344; 58.405-58.445; 58.605-58.645; 58.647-58.654; 58.705-58.732; and 58.805-58.811, Revised January 1, 2017, available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12016.

(h) Frozen Desserts Processing Guidelines, 1st edition, October 1989 published by the Milk Safety Branch, Division of Cooperative Programs, U.S. Food and Drug Administration. Copies are available for inspection during regular business hours at the Florida Administrative Code and Register, R.A. Gray Building, 500 South Bronough Street, Tallahassee, FL 32399-0250 and at the Florida Department of Agriculture and Consumer Services, Division of Food Safety, 3125 Conner Boulevard, Tallahassee, FL 32399-1650. Posting of the aftermentioned materials on the internet for purposes of public examination would violate federal copyright law.

(i) United States Standards for Grades of Nonfat Dry Milk (Spray Process), February 2, 2001. Available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12007.

(j) United States Standards for Grades of Dry Whole Milk, April 13, 2001. Available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12008.

(k) United States Standards for Dry Whey, December 14, 2000. Available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12009.

(l) Milk for Manufacturing Purposes and its Production and Processing (“MMPPP”), July 21, 2011. Available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-12010.

(m) Standard Methods for the Examination of Dairy Products, 17th Edition, June 1, 2004 published by the American Public Health Association. Copies may be obtained from APHA Headquarters, 800 I Street N.W., Washington D.C. 20001or https://secure.apha.org/imis/APHA/Store/Search_Bookstore and are also available for public inspection during regular business hours at the Florida Administrative Code and Register, R.A. Gray Building, 500 South Bronough Street, Tallahassee, FL 32399-0250 and at the Florida Department of Agriculture and Consumer Services, Division of Food Safety, 3125 Conner Boulevard, Tallahassee, FL 32399-1650. Posting of the aftermentioned materials on the internet for purposes of public examination would violate federal copyright law.

(n) Standard Methods for the Examination of Water and Wastewater, 23rd Edition, (2017), published by the American Public Health Association, American Water Works Association, Water Environment Federation. Copies may be obtained from AWWA, 6666 W. Quincy Ave., Denver, CO 80235 or https://www.awwa.org/Store/Product-Details/productId/65266295, and are also available for public inspection during regular business hours at the Florida Administrative Code and Register, R.A. Gray Building, 500 South Bronough Street, Tallahassee, FL 32399-0250 and at the Florida Department of Agriculture and Consumer Services, Division of Food Safety, 3125 Conner Boulevard, Tallahassee, FL 32399-1650. Posting of the aftermentioned materials on the internet for purposes of public examination would violate federal copyright law.

(2) Definitions. In addition to the definitions in Chapter 502, F.S., and the definitions in the materials incorporated by reference, the following definitions shall apply:

(a) “Adulterated” means any milk, milk product or frozen dessert if:

1. It bears or contains any poisonous or deleterious substance in a quantity which may render it injurious to health.

2. It consists, in whole or in part, of any substance unfit for human consumption.

3. It has been produced, processed, prepared, packed, or held under unsanitary conditions.

4. Its container is composed, in whole or in part, of any poisonous or deleterious substance which may render the contents injurious to health, or;

5. Any substance has been added thereto or mixed or packed therewith so as to increase its bulk or weight, reduce its quality or strength, or make it appear better or of greater value than it is.

(b) “Bulky Flavored” means Frozen desserts, Mix or other defined products flavored with a bulky flavor ingredient such as chocolate, fruit, nut, malted milk, confectionery, or cereal.

(c) “Bulk Milk Hauler/Sampler” means any person who collects official samples and may transport raw milk from a farm and/or raw milk products to or from a milk plant, receiving station or transfer station and has in their possession a permit from any Regulatory Agency to sample such products. This term also includes “milk haulers.”

(d) “Bulk Milk Hauling Service” means any person who hauls or causes to be hauled bulk milk or milk products from a dairy farm, transfer station, receiving station or milk and milk products plant to another location and/or a person or entity responsible for a bulk milk pickup tanker.

(e) “Butter” means a food product usually known as butter, and which is made exclusively from milk or cream, or both, with or without common salt, with or without additional coloring matter, and containing not less than 80 percent by weight of milkfat, of which all tolerances having been allowed.

(f) “Certified Direct Load Operator” means any person permitted by the Department and employed by a milk producer to operate a direct load system on a permitted dairy farm. This includes the cleaning and sanitizing of in-line samplers and the preparation of bulk milk tankers to receive raw milk from the dairy farm.

(g) “Cheese” means a fresh or matured product obtained by draining after coagulation of milk, cream, skimmed, or partly skimmed milk or a combination of some or all of these products and including any cheese that conforms to the requirements of the Food and Drug Administration for cheeses and related cheese products in 21 CFR part 133 incorporated by reference in paragraph (1)(e).

(h) “Degraded milk” means milk that fails to meet the minimum requirements of subsection 5K-10.003(3), F.A.C.

(i) “Department” means the Department of Agriculture and Consumer Services.

(j) “Depot” means any place, premise or establishment in which Mix, Frozen desserts, defined products, ingredients, containers, or supplies are stored for further distribution.

(k) “Frozen Yogurt” means food which is prepared by freezing, while stirring, a Mix composed of one or more of the optional dairy ingredients provided for in ice cream and frozen custard and which may contain other safe and suitable ingredients. Its dairy ingredients, with or without other ingredients, is (are) pasteurized and subsequently cultured with bacteria, Lactobacillus bulgaricus and Streptococcus thermophilus. The titratable acidity of the cultured frozen yogurt may not be less than 0.5 percent, calculated as lactic acid, except if the frozen yogurt is flavored by the addition of a non-fruit characterizing ingredient(s). Its milkfat content may not be less than 3.25 percent by weight, except that when bulky characterizing ingredients are used the percentage milkfat may not be less than 2.5 percent. The finished frozen yogurt shall weigh not less than 5 pounds per gallon.

(l) “Interstate Milk Shippers (IMS) List” means a list of facilities certified by Milk Sanitation Rating Officers as having attained a score of 90% or greater for sanitation and enforcement compliance rating based on the USPHS/FDA Grade “A” Pasteurized Milk Ordinance, 2017 Revision incorporated by reference in paragraph (1)(a) and produce products in accordance with the procedures set forth in the Methods of Making Sanitation Rating of Milk Shippers and the Certifications/Listing of Single Service Containers and/or Closures for Milk and/or Milk Products Manufacturers (MMSR), 2015 Revision incorporated by reference in paragraph (1)(c).

(m) “Manufacturing Milk Plant” means any place, premises, or establishment where milk is received, collected and used for the production of non-Grade “A” dairy products, such as cheese and butter.

(n) “Manufactured Milk Products” include cheese, butter, non-Grade “A” milk powder, evaporated and condensed milk and such other products, for human consumption, as may be otherwise designated.

(o) “Mix” means a blend of milk, cream, sugar, and stabilizers that could have flavoring packaged for commercial use to be made into ice cream.

(p) “Sealed” means to secure or fasten an opening, connection, or device to prevent intentional and/or unintentional adulteration or tampering of the device or product within.

(q) “Single-Service Container Manufacturer” means any place, premises, or establishment that produces containers and closures used for packaging milk and/or milk products intended for only one (1) use.

(r) “Sold” means a transfer of milk or milk products that involves any direct or indirect form of compensation in exchange for the right to acquire such milk or milk products.

(s) “Temporary Seal Applicator” means any person permitted by the Department and employed by a manufacturing milk plant, wholesale manufacturer of Frozen dessert and/or Mix or milk plant, to test and replace public health seals on pasteurization equipment.

(t) “Wholesale Manufacturer of Frozen Dessert and/or Mix” means any place, premises or establishment that produces for wholesale distribution, Frozen dessert as defined in section 502.012, F.S., 21 CFR 135, and/or Mix as defined in paragraph (2)(o) of this rule. This term includes facilities within the State of Florida and facilities selling Frozen Dessert and/or Mix in Florida.

Rulemaking Authority 502.014, 570.07(23) FS. Law Implemented 502.012, 502.014, 502.053, 502.091 FS. History–New 7-24-70, Amended 1-26-81, 8-31-82, 10-9-86, Formerly 5D-1.01, Amended 12-29-88, 6-27-90, 8-29-93, 12-4-94, 7-2-95, 11-29-95, 10-15-03, 4-14-08, Formerly 5D-1.001, Formerly 5K-4.041, Amended 9-9-20.

## 5K-10.002 Permits, Licenses and Inspections.

(1) General Permits.

(a) All Milk Plants, Washing Stations, Out-of-State Processors of Milk and Milk Products, Receiving Stations, Transfer Stations, Single Service Container Manufacturers and Operators of Milk Plants shall submit an application on Form DACS-05019 Application for Permit as a Manufacturer of Milk, Milk Products, Cheese, or Containers (Rev. 10/07), hereby incorporated by reference. Milk and Milk Product Distributors shall submit an application on Form DACS-05071 Application for Permit as a Distributor of Milk and Milk Products (Rev. 10/07), hereby incorporated by reference. Copies may be obtained from the Department of Agriculture and Consumer Services, Division of Dairy Industry, 3125 Conner Boulevard, Tallahassee, Florida 32399-1650. To secure and maintain a permit, the applicant must conform to and comply with the provisions of the PMO and Chapter 502, F.S.

(b) All Bulk Milk Hauling Services shall submit an application on Form DACS-05012 Application for a Milk Hauling Service Permit (Rev. 10/07), hereby incorporated by reference. All Bulk Milk Hauler/Samplers shall submit an application on Form DACS-05060 Application for a Bulk Milk Hauler/Sampler Permit (Rev. 10/07), hereby incorporated by reference. Copies may be obtained from the Department of Agriculture and Consumer Services, Division of Dairy Industry, 3125 Conner Boulevard, Tallahassee, Florida 32399-1650. To secure and maintain a permit, the applicant must conform to and comply with the provisions of the PMO and Chapter 502, F.S.

(2) Milkfat Tester Permit. To secure and maintain a Milkfat Tester’s Permit, a person must:

(a) Submit, with the $125.00 application fee, a properly completed Form DACS-05029 Application for Milkfat Tester’s License (Rev. 10/07), hereby incorporated by reference. Copies may be obtained from the Department of Agriculture and Consumer Services, Division of Dairy Industry, 3125 Conner Boulevard, Tallahassee, Florida 32399-1650.

(b) Successfully complete on-site evaluation based on the criteria set forth in Chapter 502, F.S., and Section 6 of the PMO, conducted by the department.

(c) Successfully complete a set of split samples provided by the department, by analyzing with each method for which permitting is sought.

(d) Continue to demonstrate the knowledge, ability and equipment to conduct the analysis by the methods permitted and otherwise comply with Chapter 502, F.S., during the permit’s duration.

(e) Permitted milkfat testers, when changing from one approved method to another or when implementing an additional approved method, must give written notice to the department prior to installation of equipment so that an on-site inspection and evaluation can be conducted and permits amended.

(3) Licenses for Frozen Dessert Plants, both local and out-of-state, selling product in Florida.

(a) Every frozen dessert plant that manufactures “frozen desserts” and other foods as defined in Section 503.011, F.S., 21 CFR Part 135, and this chapter, which is produced or offered for sale within the State of Florida, shall hold a valid State of Florida license.

(b) Frozen dessert plants shall meet the following requirements in order to secure and maintain said license:

1. Submit, with the appropriate fee, a properly completed application on Form DACS-05016 Application for License as a Wholesale Manufacturer of Frozen Desserts and/or Mix (Rev. 10/07), hereby incorporated by reference. Copies may be obtained from the Department of Agriculture and Consumer Services, Division of Dairy Industry, 3125 Conner Boulevard, Tallahassee, Florida 32399-1650.

2. Submit labels for approval.

a. In-State Plant must submit, for approval, a label for each product produced.

b. Out-of-State Plant must submit, for approval, a label for each product distributed in Florida.

3. Appropriate Facility Inspection.

a. In-State Plant must pass a sanitation inspection. Inspection criteria is that of the PMO.

b. Out-of-State Plant must submit its most recent inspection report from its local regulatory agency and provide a list of its distribution points in Florida.

(4) Milk Producer’s Permit. All Milk Producers shall submit an application on Form DACS-05026, Application for Permit as a Florida Milk Producer (Rev. 10/07), hereby incorporated by reference. Copies may be obtained from the Department of Agriculture and Consumer Services, Division of Dairy Industry, 3125 Conner Boulevard, Tallahassee, Florida 32399-1650. To secure and maintain a permit, the applicant must conform to and comply with the provisions of the PMO and Chapter 502, F.S.

(5) In-state Manufacturing Milk Plants.

(a) All in-state Manufacturing Milk Plants shall submit an application on Form DACS-05019, Application for Permit as a Manufacturer of Milk, Milk Products, Cheese, or Containers (Rev. 10/07), hereby incorporated by reference. Copies may be obtained from the Department of Agriculture and Consumer Services, Division of Dairy Industry, 3125 Conner Boulevard, Tallahassee, Florida 32399-1650. To secure and maintain a permit, the applicant must conform to and comply with the provisions of the MMPPP and Chapter 502, F.S.

(b) Firms within the state holding a milk plant permit do not require an additional permit to process manufactured milk products but must comply with the provisions of the MMPPP.

(6) Penalties for Enforcement and Reinstatement of Permits and Licenses.

(a) General Permits listed in subsection (1). Enforcement shall be pursuant to the PMO.

(b) Milkfat Tester’s Permit. Each permitted tester who fails to successfully complete one set of split samples shall have the permit placed in conditional status until the next set of split samples issued by the department has been successfully completed. A permit shall remain conditional for a period not to exceed six months. A milkfat tester shall not:

1. Fail to successfully complete two consecutive sets of split samples, or

2. Falsify records.

(c) Frozen Dessert Plant License.

1. When any requirement of Chapter 503, F.S., or rule under this chapter is violated, the license holder is subject to the suspension of his license. The department shall forego suspension of the license if the product or products in violation are not sold or offered for sale.

2. Any frozen desserts plant whose license has been suspended may make written application for the reinstatement of its license. The standards for reinstatement are those set forth in the PMO for a milk plant.

(d) Manufacturing Milk Plant Permit. Any manufacturing milk plant whose permit has been suspended may make written application for the reinstatement of its permit. The standards for reinstatement are those set forth in the MMPPP.

(7) Routine Inspections and Tests.

(a) Each business and individual regulated pursuant to this chapter shall permit access of officially designated persons to all parts of its establishment or facilities to determine compliance with the provisions of this chapter. A distributor, plant operator or hauler shall furnish the department, for official use only, a true statement of the actual quantities of products manufactured, and a list of all sources of milk and milk products, records of inspections, tests, and pasteurization time and temperature records as requested. Whenever a milk tank truck has been cleaned and sanitized as required by the department, the outlet valve and manhole dust cover shall be sealed.

(b) General permittees, described in subsection (1) of this rule within the State of Florida shall be subject to ongoing inspections to assure compliance with the PMO’s requirements.

(c) Milkfat Testers shall be subject to periodic split sample tests to assure proficiency.

(d) Frozen Dessert and Manufacturing Milk Plants within the state shall be subject to inspections based upon the criteria and frequency established for milk plant inspections in the PMO. Sampling and testing shall be quarterly, unless test results indicate a more frequent sampling and testing is necessary. Raw milk cheeses shall be tested for pathogens semi-annually.

(e) Pasteurization systems in Manufacturing Milk Plants shall be subject to testing based upon the criteria and frequency established for milk plants in the PMO.

(f) Milk Producers shall be subject to inspections based upon the criteria and frequency described in the PMO.

Rulemaking Authority 502.014, 503.031 FS. Law Implemented 502.014, 502.032, 502.053, 502.091, 502.165, 502.231, 503.031, 503.041, 503.051 FS. History–New 9-21-67, Amended 1-26-81, 8-31-82, 8-16-84, Formerly 5D-1.03, Amended 10-9-86, 12-29-88, 6-27-90, 8-29-93, 7-2-95, 10-15-03, 4-14-08, Formerly 5D-1.003, Formerly 5K-4.042.

## 5K-10.003 Dating, Standards for Milk, Milk Products, Manufactured Milk Products and Frozen Desserts.

(1) Shelf-Life Dating and Expiration Dating.

(a) All milk and milk products shall be legibly labeled with their shelf-life date. The date or date code for frozen desserts and other manufactured milk products shall be approved by the department and shall indicate the date of manufacture of the product or the last day the product is to be offered for sale. The standards for labeling for all products shall be in accordance with 21 CFR, Part 101, adopted by reference in paragraph 5D-1.001(1)(b), F.A.C.

(b) The methods for the determination of the shelf-life of milk and milk products shall be microbiological and organoleptical.

(c) The shelf-life expiration date shall appear in conspicuous and easily legible bold-face print or type in distinct contrast to the background, by typography, layout, color, embossing, debossing, or molding of other matter on the package, and shall be placed on that part of the container most likely to be displayed, presented, or shown, or examined under customary conditions of display for retail sale, and shall not interfere with legibility or other mandatory labeling requirements of the product. However, cup containers that are labeled with the date on the bottom shall have displayed on the cap information concerning the location of the date.

(d) The shelf-life expiration date shall be expressed by the three letters of the month followed by the numeral or numerals constituting the appropriate calendar date or numerically. For example: “June 1” shall be expressed “JUN 1” or “0601.”

(e) No milk or milk products shall be offered for sale as a grade A product after the shelf-life expiration date shown on the container. All milk and milk products offered for sale after the shelf-life expiration date will be deemed to be misbranded and subject to be impounded and made unsalable or otherwise disposed of by the department, under the provisions of Section 502.231, F.S.

(f) This rule does not apply to containers of milk or milk products which are not to be sold in the State of Florida.

(g) Each processor shall certify to the department the maximum shelf-life of each product in the hands of the consumer under normal storage conditions. Provided, however, the maximum shelf-life of fluid uncultured milk pasteurized at less than 270 F shall not exceed ten days from date of packaging unless technical supporting justification has been supplied to the department, the department has confirmed such shelf-life claims, and specific authority to use a longer shelf-life has been granted by the department.

(2) Shelf – Life Testing and Testing Procedures.

(a) Milk product samples shall be held at 43 F (plus or minus 2 F) for the shelf life period plus four (4) days and analyzed to determine that shelf-life expiration dates stated on the containers assure the consumer of acceptable quality milk and milk products when kept under normal storage conditions. The temperature at the time of collection shall be officially recorded by the collector. Nothing herein contained shall be construed to prohibit the department from taking special samples for analysis and making special tests in order to assure all milk and milk products comply with the minimum standards of freshness, quality and palatability. In the event the department determines a processor’s or a manufacturer’s shelf-life for a given product is improper, the department shall immediately take such samples as are necessary for full and complete recheck of the shelf-life of the product. If the full and complete recheck confirms that the shelf-life of the product is improper, the department shall serve written notice on the processor or manufacturer and the processor or manufacturer immediately upon receipt of such notice shall alter the shelf-life expiration date of the product to comply with the department tests. Compliance shall be with the next processing of the product after receipt of such department notice.

(b) To extend the shelf-life expiration date of a qualifying product, the processor shall submit a written request to the Division of Dairy Industry specifying the product to be tested and supplying test results which indicate that the product is acceptable for at least ten (10) days or for an additional two (2) days over the current code period. This information must be compiled from current records that cover a period of at least thirty (30) days. The department will collect in Florida two series of duplicate samples of the product during a four week period. The first duplicate sample will be used for routine analysis, the second will be stored at 43° F plus or minus 2° F until six (6) days past the expiration date and then evaluated as acceptable or unacceptable. Both series of samples must be acceptable for six (6) days past the expiration date for the extension request to be granted. If acceptable, the processor will be notified in writing and the product must remain at this new code level for at least six (6) months before any additional code is requested. If unacceptable, the processor will be notified in writing and at least six (6) months must pass before another request is initiated for the product.

(3) Chemical, bacteriological and temperature standards for manufacture of grade A products:

Grade A raw milk for pasteurization, ultra pasteurization or aseptic processing.

| Temperature, Bacterial Limits, Drugs, and Somatic | Standards shall be the same as those listed in Section 7 of the PMO. |
| --- | --- |
| Cell Count |  |
| Added Water | Freezing point not to exceed -0.526º H. |

Grade A pasteurized or ultra pasteurized milk and milk products and bulk shipment heat treated milk products.

| Temperature, Bacterial Limits, Coliform, Phosphatase, and Drugs | Standards shall be the same as those listed in Section 7 of the PMO. |
| --- | --- |
| Added Water | Freezing point not to exceed -0.526º H. |

Grade A aseptically processed milk and milk products.

| Temperature, Bacterial Limits and Limits and Drugs | Standards shall be the same as those listed in Section 7 of the PMO. |
| --- | --- |
| Added Water | Freezing point not to exceed -0.526º H. |

(4) Chemical, bacteriological and temperature standards for Frozen Desserts:

Raw Milk and Cream.

| Temperature | Not to exceed 45º F (7º C). |
| --- | --- |
| Bacterial Limits | Milk – not to exceed 500,000 CFU/ml. In no case shall raw milk have a standard plate or direct microscopic clump count in excess of 1,000,000 CFU/ml. |
| Drugs | Milk and cream – No positive result with drug residue methods referenced in Section 6 of the PMO. |
| Somatic Cell Count | Not to exceed 750,000/ml; Goat’s milk – Not to exceed 1,500,000. |

Frozen Desserts and Other Products Defined in this chapter.

| Temperature | Pasteurized Mix (plain) 45º F (7º C). Pasteurized Mix (flavored) 45º F (7º C). Frozen Desserts 0º F (-17.8º C). Other – 0º F (-17.8º C). |
| --- | --- |
| Bacterial Limits* | Pasteurized Mix (plain) 50,000 CFU/gram. Pasteurized Mix (flavored) 50,000 CFU/gram. Frozen Desserts – 50,000 CFU/gram. Other – 50,000 CFU/gram. |
| Drugs | No positive result with drug residue methods referenced in Section 6 of the PMO. |
| Coliform | Pasteurized Mix (plain) 10 CFU/gram. Pasteurized Mix (flavored) 20 CFU/gram. Frozen Desserts (plain) 10 CFU/gram. Frozen Desserts (bulky flavored) 20 CFU/gram. Other (plain) 10 CFU/gram. Other (bulky flavored) 20 CFU/gram. |
| Phosphatase | Less than 1 microgram per ml. (less than 500 milliunits/L by the Fluorometric Procedure) or equivalent. |

*Not applicable to cultured products

Dry Dairy Products

Dry dairy products used as ingredients in frozen desserts shall meet the requirements for “Extra Grade” or better as defined by the U.S. Standards for Grades for the particular product.

(5) Chemical, Bacteriological, and Temperature Standards for Manufactured Milk Products.

Raw milk for manufactured milk products.

| Temperature | Cooled to 50º F (10º C) or less within four (4) hours or less, of the commencement of the first milking, and to 45º F (7º C) or less within two hours after the completion of milking. Provided, the blend temperature after the first and subsequent milkings does not exceed 50º F (10º C). |
| --- | --- |
| Bacterial limits | Individual producer milk not to exceed 500,000 CFU/ml. prior to commingling with other producer milk. Not to exceed 1,000,000 CFU/ml. as commingled milk prior to processing. |
| Drugs | No positive result with drug residue methods referenced in Section 6 of the PMO. |
| Somatic Cell Count | Individual producer milk: Not to exceed 750,000 per ml. Goat milk: Not to exceed 1,000,000 per ml. |

Cheeses made with pasteurized milk or pasteurized reconstituted milk.

| Temperature | Cheeses shall comply with 7 CFR Part 58.154. |
| --- | --- |
| Coliforms | Not to exceed 10/gram. |
| Phosphatase | Negative |

Cheeses made from non-pasteurized (raw) milk shall comply with 7 CFR Part 58.439.

| Temperature | Cheeses shall comply with 7 CFR Part 58.154. |
| --- | --- |
| Coliforms | Not to exceed 10/gram. |
| Phosphatase | Negative |
| E. coli | <1/gram |
| Pathogens | None |

Butter

| Temperature | Not to exceed 40°F. |
| --- | --- |
| Coliforms | Not to exceed 10/gram. |
| Mold | Not to exceed 20/gram. |

Rulemaking Authority 502.014, 503.031 FS. Law Implemented 502.014, 502.042, 502.091, 503.031 FS. History–New 9-21-67, Amended 9-26-69, 12-24-71, 1-26-81, 8-31-82, 8-16-84, Formerly 5D-1.07, Amended 10-9-86, 5-19-87, 12-29-88, 6-27-90, 8-29-93, 12-4-94, 7-2-95, 10-15-03, 4-14-08, Formerly 5D-1.007, Formerly 5K-4.043.

## 5K-10.004 Future Dairy Farms, Milk Plants, Manufacturing Milk Plants and Frozen Dessert Plants.

(1) Milk barn, stable or parlor and milkhouse or room construction.

(a) Walls, ventilation and light. Walls shall be of smooth finish impervious to water. Ten percent of wall area shall be windowed of the ventilating type, unless adequate mechanical ventilation is furnished. Pipes penetrating walls shall be sufficiently tight as to prevent any open space between the pipe and the wall penetration.

(b) Ceiling. Ceilings shall have a height of 9 feet for milkhouse or room and stanchion type barn and 10 feet 6 inches for parlor type barn. A stanchion or parlor type barn used for the milking of goats shall have a minimum ceiling height of 8 feet. If there is a feed storage area above, the ceiling should be tongue and groove double floor with a layer of felt between the floors. There should be no open beams beneath the ceiling.

(c) Floors. Floors shall be constructed of concrete or tile that is slip-proof to animals and sloped for drainage one-quarter inch per foot; provided, that when a floor flush system is installed a minimum slope of one-eighth (1/8'') inch per foot is required.

(d) Door and window frames. Door and window frames shall be constructed of material and finish to resist decay or corrosion.

(e) Placement of equipment. Pumps, motors, sinks and other permanent type equipment should be fastened to the wall with no contact to the floor if possible. Where practical, machinery and equipment shall be located in a room separate from the milk collecting room.

(f) Milkers pit. The milkers pit shall be a minimum of 5 feet wide.

(g) Space between milk storage tanks and walls and ceilings. There shall be a distance of 18 inches between milk storage tank and walls; and 4 feet between the top of the milk storage tank and ceiling; and a distance of 3 feet between milk storage tanks within the same room to secure adequate ventilation and sufficient space for cleaning. Milk storage tanks may be bulkheaded through the wall into the milkroom. If the tanks protrude through the wall to accommodate a top opening manhole and/or agitator the distance between tanks, sidewalls and ceiling still apply.

(h) Milk Storage Tank Design. A sampling cock shall be provided on all milk storage silo and horizontally mounted tanks designed with the manhole lid in the vertical end or wall of the tank. The sampling cock shall be installed on the lid to allow for easy removal for cleaning and sanitizing and shall be considered part of the milk tank. The sampling cock shall be used for the purpose of regulatory and hauler sampling only.

(i) Properly prepared plans for all milk barns, stable or parlor and milkhouse or room regulated under this chapter which are hereafter constructed, reconstructed or extensively altered shall be submitted to the department for approval before work is begun.

(2) Milk plant, frozen dessert plant, receiving station or transfer station construction.

(a) Walls. Walls shall be of smooth finish impervious to water.

(b) Ceiling. Ceilings shall be of a smooth finish impervious to water.

(c) Floors and drains. Floors shall be constructed of concrete or tile; slip proof and sloped to drain.

(d) Door and window frames. Door frames shall be of steel or steel alloy and window frames shall be constructed of a corrosive resistant metal.

(e) Placement of equipment. Equipment should be located at least 18 inches from walls and a minimum distance of 3 feet is suggested between pieces of equipment in order to give the operators of such equipment sufficient room to pass between pieces of equipment comfortably.

(f) Stainless steel pipelines are properly identified. Identification shall be made with colored tape or plastic bands which will remain in place and retain its coloring under normal conditions of use. The following colors shall be used:

Red – Raw Milk Lines

Blue – Pasteurized Products Lines

Green – Cleaning Solution Lines (Supply and Return)

Yellow – Water Lines (Applicable to Stainless Stell Lines Only)

The direction of flow in each line shall also be indicated by an arrow on the pipe, tape, or plastic band. The proper placement of colored bands and directional arrows on pipelines shall be determined by the department to ensure easy identification of the product in the pipe and direction of flow.

(g) Properly prepared plans for all plants regulated under this chapter which are hereafter constructed, reconstructed or extensively altered shall be submitted to the department for approval before work is begun.

(3) Manufacturing milk plants.

(a) Properly prepared plans for all plants regulated under this chapter which are hereafter constructed, reconstructed or extensively altered shall be submitted to the department for approval before work is begun.

(b) Pasteurization equipment shall comply with all applicable requirements set forth in the PMO.

(c) All raw (non-pasteurized) milk cheese shall be aged in accordance with CFR 7 Part 58.439 and shall be aged at the manufacturing plant.

(d) Reconstituted milk used for making cheese shall be pasteurized or the cheese shall be aged in accordance with CFR 7 Part 58.439.

(e) Maunfacturers of aged cheese shall maintain a log sheet showing the date and time each batch or lot of cheese was placed into and removed from the curing or aging room.

(f) Milk tank trucks used for hauling milk or milk products for manufacturing purposes shall comply with the PMO.

(g) Manufacturing milk plants in existence prior to the adoption of this rule shall have one (1) year from the date of adoption to comply with the requirements set forth in this rule.

Rulemaking Authority 502.014, 503.031 FS. Law Implemented 502.014, 502.053, 502.091, 502.121, 503.031 FS. History–New 9-21-67, Amended 10-27-67, 3-19-69, 1-26-81, 8-16-84, Formerly 5D-1.12, Amended 6-27-90, 7-2-95, 10-15-03, 4-14-08, Formerly 5D-1.012, Formerly 5K-4.044.

## 5K-10.006 Hemp Extract

(1) Products. Milk, Milk Products, and Frozen Desserts containing Hemp or Hemp Extract are subject to the requirements of Chapter 502, F.S., and Chapter 5K-10, F.A.C., in addition to the requirements of this rule. Grade “A” milk and milk products to which Hemp Extract has been added shall be considered “Substitute Milk” or “Substitute Milk Products” as defined in Chapter 502, F.S. In addition to the requirements in Section 502.165, F.S., Substitute Milk and Substitute Milk Products containing Hemp Extract are subject to the requirements of Chapter 5K-10, F.A.C.

(2) Definitions. The definitions provided in Sections 502.012 and 581.217, F.S., and the following shall apply to this rule:

(a) “Approved Source” for the purposes of this rule means Hemp Frozen Dessert Manufacturer, Hemp Substitute Milk Manufacturer, or Hemp Substitute Milk Product Manufacturer manufacturing, processing, packing, holding, or preparing or selling Substitute Milk, Substitute Milk Products, or Frozen Desserts at wholesale or retail that meets local, state, or federal food safety standards from the jurisdiction of origin.

(b) “Batch Number” or “Lot Number” means the Substitute Milk, Substitute Milk Products, and Frozen Desserts containing Hemp Extract produced during a period of time under similar conditions and identified by a specific code that allows traceability.

(c) “Expiration Date” means the month and year as determined by the manufacturer, packer, or distributor on the basis of tests or other information showing that the product, until that date, under the conditions of handling, storage, preparation, and use per label directions, will when consumed, contain not less than the quantity of each ingredient as set forth on its label.

(d) “Hemp” is defined in Section 581.217(3)(d), F.S.

(e) “Hemp Extract” is defined in Section 581.217(3)(e), F.S. Hemp Extract does not include any material, compound, mixture or preparation that contains any quantity of Synthetic Cannabinoids as defined in Section 893.03(1)(c)190., F.S.

(f) “Hemp Frozen Dessert Manufacturer” means a person who manufactures, processes, converts, partially freezes, or freezes any mix or frozen dessert containing Hemp Extract for distribution or sale.

(g) “Hemp Substitute Milk Manufacturer” means any place, premises, or establishment where Substitute Milk containing Hemp Extract is collected, handled, processed, stored, pasteurized, ultra-pasteurized, aseptically processed and packaged, retort processed after packaging, condensed, dried, packaged, bottled, or prepared for distribution at wholesale.

(h) “Hemp Substitute Milk Product Manufacturer” means any place, premises, or establishment where Substitute Milk Products containing Hemp Extract is collected, handled, processed, stored, pasteurized, ultra-pasteurized, aseptically processed and packaged, retort processed after packaging, condensed, dried, packaged, bottled, or prepared for distribution at wholesale.

(i) “Ingestion” means the process of taking food into the body through the mouth and into the gastrointestinal tract through eating or drinking.

(j) “Total delta-9 tetrahydrocannabinol concentration” means [delta-9 tetrahydrocannabinol] + (0.877 x [tetrahydrocannabinolic acid]).

(3) Permits and Fees. Hemp Substitute Milk, Hemp Substitute Milk Products, and Hemp Frozen Dessert Manufacturers shall obtain a permit and pay the applicable fee required in Rule 5K-10.002, F.A.C.

(4) Requirements.

(a) Substitute Milk, Substitute Milk Products, and Frozen Desserts containing Hemp Extract must be obtained from an Approved Source. The Hemp Frozen Dessert Manufacturer, Hemp Substitute Milk Manufacturer, or Hemp Substitute Milk Product Manufacturer shall provide to the department, upon request, a valid dairy or food safety license/permit and the most recent dairy or food safety inspection report from the Approved Source.

(b) Substitute Milk, Substitute Milk Products, and Frozen Desserts containing Hemp Extract must be stored and transported in accordance with Chapter 5K-10, F.A.C. Substitute Milk, Substitute Milk Products, and Frozen Desserts containing Hemp Extract must be packaged in containers minimizing the exposure to light to prevent degradation of the Cannabinoids.

(c) Substitute Milk, Substitute Milk Products, and Frozen Desserts containing Hemp Extract shall not contain a Total delta-9 tetrahydrocannabinol concentration of more than 0.3% on a dry weight basis.

(5) Contaminants. In addition to the requirements listed in Chapter 502, F.S., and Rule 5K-10.004, Substitute Milk, Substitute Milk Products, and Frozen Desserts containing Hemp Extract shall be considered adulterated pursuant to Section 502.181(2), F.S., if contaminants are detected at levels greater than those listed in this rule.

(a) Pesticide Limits. The following list of contaminants does not constitute authorization to use or apply any of the following during Hemp cultivation or processing.

1. Abamectin, 300 parts per billion.

2. Acephate, 3,000 parts per billion.

3. Acequinocyl, 2,000 parts per billion.

4. Acetamiprid, 3,000 parts per billion.

5. Aldicarb, 100 parts per billion.

6. Azoxystrobin, 3,000 parts per billion.

7. Bifenazate, 3,000 parts per billion.

8. Bifenthrin, 500 parts per billion.

9. Boscalid, 3,000 parts per billion.

10. Captan, 3,000 parts per billion.

11. Carbaryl, 500 parts per billion.

12. Carbofuran, 100 parts per billion.

13. Chlorantraniliprole, 3,000 parts per billion.

14. Chlordane, 100 parts per billion.

15. Chlorfenapyr, 100 parts per billion.

16. Chlormequat chloride, 3,000 parts per billion

17. Chlorpyrifos, 100 parts per billion.

18. Clofentezine, 500 parts per billion.

19. Coumaphos, 100 parts per billion.

20. Cyfluthrin, 1,000 parts per billion.

21. Cypermethrin, 1,000 parts per billion.

22. Daminozide, 100 parts per billion.

23. DDVP (Dichlorvos), 100 parts per billion.

24. Diazinon, 200 parts per billion.

25. Dimethoate, 100 parts per billion.

26. Dimethomorph, 3,000 parts per billion.

27. Ethoprop(hos), 100 parts per billion.

28. Etofenprox, 100 parts per billion.

29. Etoxazole, 1,500 parts per billion.

30. Fenhexamid, 3,000 parts per billion.

31. Fenoxycarb, 100 parts per billion.

32. Fenpyroximate, 2,000 parts per billion.

33. Fipronil, 100 parts per billion.

34. Flonicamid, 2,000 parts per billion.

35. Fludioxonil, 3,000 parts per billion.

36. Hexythiazox, 2,000 parts per billion.

37. Imazalil, 100 parts per billion.

38. Imidacloprid, 3,000 parts per billion.

39. Kresoxim-methyl, 1,000 parts per billion.

40. Malathion, 2,000 parts per billion.

41. Metalaxyl, 3,000 parts per billion.

42. Methiocarb, 100 parts per billion.

43. Methomyl, 100 parts per billion.

44. Methyl parathion, 100 parts per billion.

45. Mevinphos, 100 parts per billion.

46. Myclobutanil, 3,000 parts per billion.

47. Naled, 500 parts per billion.

48. Oxamyl, 500 parts per billion.

49. Paclobutrazol, 100 parts per billion.

50. Pentachloronitrobenzene, 200 parts per billion.

51. Permethrin, 1,000 parts per billion.

52. Phosmet, 200 parts per billion.

53. Piperonyl butoxide, 3,000 parts per billion.

54. Prallethrin, 400 parts per billion.

55. Propiconazole, 1,000 parts per billion.

56. Propoxur, 100 parts per billion.

57. Pyrethrins, 1,000 parts per billion.

58. Pyridaben, 3,000 parts per billion.

59. Spinetoram, 3,000 parts per billion.

60. Spinosad A & D, 3,000 parts per billion.

61. Spiromesifen, 3,000 parts per billion.

62. Spirotetramat, 3,000 parts per billion.

63. Spiroxamine, 100 parts per billion.

64. Tebuconazole, 1,000 parts per billion.

65. Thiacloprid, 100 parts per billion.

66. Thiamethoxam, 1,000 parts per billion.

67. Trifloxystrobin, 3,000 parts per billion.

(b) Residual Solvent Limits.

1. 1,2-Dichloroethene, 5 parts per million

2. 1,1-Dichloroethene, 8 parts per million

3. Acetone, 5,000 parts per million

4. Acetonitrile, 410 parts per million

5. Benzene, 2 parts per million

6. Butane, 2,000 parts per million

7. Chloroform, 60 parts per million

8. Ethanol, 5,000 parts per million

9. Ethyl Acetate, 5,000 parts per million

10. Ethyl Ether, 5,000 parts per million

11. Ethylene Oxide, 5 parts per million

12. Heptane, 5,000 parts per million

13. Hexane, 290 parts per million

14. Isopropyl Alcohol, 500 parts per million

15. Methanol, 3,000 parts per million

16. Methylene Chloride, 600 parts per million

17. Pentane, 5,000 parts per million

18. Propane, 2,100 parts per million

19. Toluene, 890 parts per million

20. Trichloroethylene (1,1,2-Trichloroethene), 80 parts per million

21. Xylenes, Total (ortho-, meta-, para-), 2170 parts per million

(c) Metals Limits.

1. Cadmium, 0.5 micrograms/gram.

2. Lead, 0.5 micrograms/gram.

3. Arsenic, 1.5 micrograms/gram.

4. Mercury, 3.0 micrograms/gram.

(d) Biological Limits.

1. Shiga toxin-producing Escherichia coli (STEC E. coli) and other pathogenic E. coli, none present.

2. Listeria monocytogenes, none present.

3. Salmonella, none present.

(e) Mycotoxin Limits.

1. Total Aflatoxin (B1, B2, G1, G2), 20 parts per billion.

2. Ochratoxin, 20 parts per billion.

(f) Cannabinoid Limits. Total delta-9 tetrahydrocannabinol concentration shall not exceed 0.3% on a dry weight basis.

(g) If a testing sample is found to contain levels of any pathogen, toxicant, residual solvent, metal, or pesticide not enumerated in this rule or by Florida law the Substitute Milk, Substitute Milk Product, or Frozen Dessert containing Hemp Extract shall be considered adulterated.

(6) Labeling.

(a) Substitute Milk, Substitute Milk Products, and Frozen Desserts containing Hemp Extract must be labeled in accordance with Chapter 502, F.S., Section 581.217(7), F.S., and 21 CFR 101 and must declare the number of milligrams of Hemp Extract. 21 CFR 101 (Revised April 1, 2019) is hereby incorporated by reference and available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-11459.

(b) If specific cannabinoids are marketed, the number of milligrams of each cannabinoid per serving must be declared on the label. The serving size shall be displayed on the nutrition facts label of the product.

(c) The label and advertisement shall not contain claims indicating the product is intended for diagnosis, cure, mitigation, treatment, or prevention of disease, rendering it a drug as defined in 21 U.S.C. 321(g)(1).

(7) Disposal.

(a) Laboratory samples found to contain more than a Total delta-9 tetrahydrocannabinol concentration of 0.3% on a dry weight basis shall be disposed of in accordance with 21 CFR 1317. 21 CFR 1317 (Revised April 1, 2019) is hereby incorporated by reference and available online at http://www.flrules.org/Gateway/reference.asp?No=Ref-11460.

(b) Substitute Milk, Substitute Milk Products, or Frozen Desserts containing a Total delta-9 tetrahydrocannabinol concentration that exceeds 0.3% on a dry weight basis shall be detained pursuant to Section 502.014, F.S. Substitute Milk, Substitute Milk Products, or Frozen Desserts containing a Total delta-9 tetrahydrocannabinol concentration that exceeds 0.3% on a dry weight basis which have been detained pursuant to Section 502.014, F.S., shall not be further subdivided or renumbered such that the integrity of the lot for identification is not maintained. The establishment shall not shall not dispose of the Substitute Milk, Substitute Milk Products, or Frozen Desserts in any manner until written permission is given by the department or a court of competent jurisdiction.

(c) Upon receipt of written permission by the department or a court of competent jurisdiction, the Substitute Milk, Substitute Milk Products, or Frozen Desserts shall be disposed of in accordance with the Hemp Waste Disposal Manual FDACS-08115, 10/19, incorporated in paragraph 5B-57.014(6)(b), F.A.C., or in the manner provided for by a court of competent jurisdiction. Upon destruction of the product, the establishment shall notify the department via Notice of Disposal FDACS-14419, 10/19, incorporated in paragraph 5K-4.034(7)(c), F.A.C.

(8) Penalties. Violations of this rule will be evaluated, and penalties imposed in accordance with Rule 5K-10.005, F.A.C.

Rulemaking Authority 502.014, 502.053, 570.07(23) FS. Law Implemented 502.012, 502.014, 502.032, 502.042, 502.053, 502.091, 502.121, 502.165, 502.231, 581.217(7) FS. History–New 1-1-20.