# CHAPTER 61-37

# FLORIDA ENERGY CONSERVATION STANDARDS

# 61-37.003 	Products, Standards and Test Methods

# 61-37.004 	Certification

# 61-37.005 	Identification

## 61-37.003 Products, Standards and Test Methods.

The standards and test methods as required herein pertain to specific covered products.

(1) Refrigerators, Refrigerator-Freezers, and Freezers: Test Methods. Manufacturers of any refrigerator, refrigerator-freezer or freezer to be sold or installed in Florida that is covered by this rule shall cause the testing of one randomly selected sample of each model of covered product by a test laboratory accredited under the National Voluntary Laboratory Accreditation Program (NVLAP) or, where no laboratory accreditation program category exists under this program for a covered product, testing shall be conducted by an independent test laboratory. Testing shall be conducted according to the following test methods.

(a) Fresh food refrigerated volume, freezer refrigerated volume, and total refrigerated volume shall be determined using the standard ANSI/AHAM HRF-1-1988, which is incorporated by reference herein, and may be obtained from the American National Standards Institute, 1430 Broadway, New York, New York 10018, (212)642-4900.

(b) The energy consumption shall be determined using the test procedure for refrigerators and freezers in 10 Code of Federal Regulations (CFR) Section 430.22(a) and (b) (2000), which is incorporated by reference herein, and may be obtained from the Department of Business and Professional Regulation, Office of Codes & Standards, 2601 Blairstone Road, Tallahassee, Florida 32399-0772.

(2) Fluorescent Lamp Ballasts for Lighting Equipment: Test Methods. Manufacturers of lamp ballasts for fluorescent lighting equipment to be sold or installed in Florida that is covered by this rule shall cause the testing of samples of each model of fluorescent lamp ballast by a test laboratory accredited under the National Voluntary Laboratory Accreditation Program (NVLAP) or, where no laboratory accreditation category exists under this program for a covered product, testing shall be conducted by an independent test laboratory.

(a) Sample ballasts shall be tested to insure that the Ballast Efficacy Factor certified under the provisions of Rule 61-37.004, F.A.C., shall be no greater than the mean of the sample or the lower 97 1/2 percent confidence limit of the true mean divided by 0.95. A minimum of four ballasts of each model shall be randomly selected and tested.

(b) The power input, and relative light output shall be determined in accordance with the standard, ANSI C82.2-1984 which is incorporated by reference herein, and may be obtained from the American National Standards Institute, 1430 Broadway, New York, New York 10018, (212)642-4900.

(3) Showerheads: Test Method. Manufacturers of showerheads to be sold or installed in Florida that are covered by this rule shall cause the testing of samples of each model. Initial certification of showerheads mandated to occur by January 1, 1988, may contain testing reports developed by the manufacturers’ test laboratory and certified by the manufacturer to be true and accurate. Certifications of showerheads made after January 1, 1990, shall contain results of testing reports conducted by a test laboratory accredited under the National Voluntary Laboratory Accreditation Program (NVLAP) or, where no laboratory accreditation category exists under this program for a covered product, testing shall be conducted by an independent test laboratory. The method of testing shall be in accordance with standard ASME A112.18.1-2000, which is incorporated by reference herein, and may be obtained from the American National Standards Institute, 1430 Broadway, New York, New York 10018, (212)642-4900. Showerheads shall be tested in the assembled configuration in which they are packaged and sold. Showerheads in which a flow restricting mechanism is not mechanically retained, as defined below, when packaged and sold shall be tested with the flow restricting mechanism removed. Mechanically retained shall mean that the insert cannot be shaken out of the showerhead, but would require a force of at least eight pounds to remove the insert. All showerheads with the flow restrictors mechanically retained at the point of manufacture shall be tested with the flow restrictor mechanism in place. Showerheads with a radially drilled hole which is sealed when the flow restricting mechanism is in position, but which sprays water out of the side of the showerhead when the flow restricting mechanism is removed shall also be tested with the flow restricting mechanism in place.

Rulemaking Authority 553.954, 553.961 FS. Law Implemented 553.955(8)(c), 553.957, 553.961, 553.963 FS. History–New 12-31-87, Amended 10-12-89, 12-11-00, Formerly 9B-44.003.

## 61-37.004 Certification.

(1) Test reports submitted with certification statements by manufacturers shall be based on testing performed not earlier than two years prior to the certification submittal. The test report shall be a copy of the report produced by the testing laboratory and shall be consistent with the presentation of information required by the test standard applicable to the covered product and for showerheads shall indicate whether they are tested with or without inserts where applicable.

Certification statements for luminaires and showerhead assemblies that contain a ballast or showerhead manufactured and certified by others shall identify both ballast or showerhead and luminaire or assembly model numbers. A list of ballasts or showerheads officially certified in Florida that will be included as part of the product must be contained in the certification package. However, no test report is required where the ballast or showerhead referenced has been certified by its manufacturer. Where a company utilizes one showerhead in a number of assemblies, one showerhead certification submittal may be made that includes a list of that company’s assembly models containing that showerhead. The certification for showerheads shall certify that the showerhead is packaged and shipped with or without removable inserts as applicable. The declaration of compliance shall be provided on Form 971-87, which is incorporated by reference herein, effective 12/31/87, and may be obtained from the Department of Business and Professional Regulation, Office of Codes & Standards, 2601 Blairstone Road, Tallahassee, Florida 32399-0772.

(2) Certification statements not complete and accurate shall be returned to the manufacturer by the Department within 45 days after receipt with a description of incomplete or inaccurate information for correction. The date a corrected certification statement is received shall begin a new 45 day response cycle.

(3) The results of all tests performed for certification shall be retained by the manufacturer for a period of three years from date of certification.

(4) Manufacturers or distributors of covered products that participate in a nationally recognized product certification program may submit Form 971-87 with all applicable information included and a copy of the program’s directory listing ratings of energy efficiency that indicate the covered product meets the minimum energy conservation standards required by Section 553.963, F.S.

Rulemaking Authority 553.954 FS. Law Implemented 553.971 FS. History–New 12-31-87, Amended 10-12-89, 12-11-00, Formerly 9B-44.004.

## 61-37.005 Identification.

(1) Section 553.971(4), F.S., requires identifying information to appear on each product.

(2) The manufacturer shall show on the product and on the outside of the shipping carton for any covered product, and unit carton in the case of plumbing fittings, sufficient information to permit the determination of whether the appliance complies with the requirements of this rule chapter, and shall include items (a), (b) and (c) of Section 553.971(4), F.S. This information shall be readily accessible, and accessibility shall not require removal of any covering while on display or when installed. Sufficient information to determine compliance with this rule shall be determined as follows:

(a) Ballasts may be labeled with either the Ballast Efficacy Factor (BEF), or a symbol of the letter E within a circle, on the product in accordance with the requirements of P.L. 100-357, as amended, in lieu of items (b) and (c).

(b) Showerheads may be labeled with either the flow rate (the actual tested flow rate or 3 gpm) or the marking “ANSI A112.18.1M” on the product in lieu of items (b) and (c). Where the showerhead fitting is packaged with other component parts for sale, the package must also bear the assembly model number in addition to the fitting model number.

Rulemaking Authority 553.954 FS. Law Implemented 553.971 FS. History–New 12-31-87, Amended 10-12-89, Formerly 9B-44.005.