14-51.021 General Service Signs.

General service signing is used when such services are infrequent, and not within sight of the interchange.

(1) General Criteria.

(a) Requests for general service signing (except Logo signing) shall be directed to the District Traffic Operations Engineer.

(b) Signing for general services is considered supplemental to overall signing.

(c) General service signs, including signing for state agency buildings, have a white legend on blue background, except for multi-modal facilities.

(d) The name of the operating agency, community, group, individual, or enterprise shall not appear on the service sign, except for state agency buildings, and other facilities meeting the criteria established in this rule chapter.

(e) Symbol signs for Hospital, Airport, Amtrak, Greyhound, Cruise-based Seaports, and Commuter Rail can be used in urban or rural areas, when they qualify based on criteria established in the Sign Evaluation Process (Rule 14-51.013, F.A.C.).

(f) Tourist Information Centers will use word legend signs. The results of an International Signing Study showed that the international tourist understood the word message more than the “i” or “?” symbol.

(g) In no case shall signing be erected that would function primarily as advertisements for businesses.

(h) Signs for a Hospital shall be erected on the State Highway System in advance of the interchange which provides the most practical route to that facility when the hospital facility has an emergency room open 24 hours each day, 7 days a week. Where more than one hospital meeting the criteria is available from any one interchange, only the hospital located closest to the exit point shall be signed or trailblazed. The purpose of the Hospital sign is to provide direction to motorists in need of immediate medical services.

(i) Tourist Information Center signs will be erected on the State Highway System when:

1. The signing requests are received from local government; and

2. The destination provides continuous service for a minimum of eight hours a day, seven days a week; and

3. The destination is operated exclusively by a non-profit organization, or is approved by local government to operate as a tourist information center; but

4. If the Tourist Information Center is operated on a seasonal basis, the signs shall be removed during the off season.

(j) In no case shall information relating to general services be displayed until trailblazer signing has been installed to direct motorists from the exit to the service.

(2) Standards.

(a) Except as otherwise specified in Rule 14-85.004, F.A.C., Logo Sign Program, where logo signs are utilized, general signs shall not be used. Signing for general services off the Department’s right of way will not be provided when those services are conveniently located off an interchange.

(b) Except as otherwise specified in Rule 14-85.004, F.A.C., Logo Sign Program, only symbol signs will be used to advise of the availability of Gas, Food, Lodging, Camping, Hospital, and Phone on rural limited access facilities. Symbol signs for Hospital can be used in urban areas based on criteria established in the Sign Evaluation Process (Rule 14-51.013, F.A.C.).

(c) When three or fewer of these services are available at a given interchange and it is unlikely that more than three services will be provided in the near future, the symbol signs denoting these services will be appended to the advance guide sign. At locations where the “NEXT EXIT 00 MILES” panel is attached to the advance guide sign, the symbol service signs will be appended to the exit direction sign. If four or more services are available at an interchange or are anticipated in the near future, it will be necessary to install a supplemental roadside sign denoting the available services by symbols, with the bottom line of copy reading “NEXT RIGHT” or the interchange exit number.

(3) Guidelines. Each general service sign has its own set of criteria that must be met in order for signing to be provided on limited access facilities:

(a) Gas.

1. Service station facility is located within 1 mile of the exit ramp terminal;

2. Is open for continuous service a minimum of 16 hours each day, 7 days a week;

3. Provides vehicle services including fuel and oil;

4. Provides public rest rooms; and

5. Has a telephone available for public use.

(b) Food.

1. A restaurant facility is located within 1 mile of the exit ramp terminal;

2. Serves a complete meal and is open for continuous service a minimum of 14 hours each day, 7 days a week;

3. Provides public rest rooms;

4. Has a telephone available for public use; and

5. Is licensed as meeting the requirements of the Florida Department of Business Regulation, Division of Hotels and Restaurants, and the local County Health Department.

(c) Lodging.

1. The lodging facility is located within 1 mile of the exit ramp terminal;

2. Is equipped with 20 or more units for rent;

3. Has a telephone available for public use; and

4. Is licensed as meeting the requirements of Florida Department of Business Regulations, Division of Hotels and Restaurants, and the local County Health Department.

(d) Camping.

1. The camping facility is located within 5 miles of the exit ramp terminal;

2. Is equipped with a minimum of 25 rental camp sites;

3. Is equipped with indoor sanitary toilet and bathing facilities;

4. Has a telephone available for public use; and

5. Is licensed as meeting the requirements of the local County Health Department.

(e) Signs for a Hospital will be erected in rural and urban areas in advance of an interchange when:

1. The hospital facility is located not more than 10 miles from the exit ramp terminal; and

2. In the event a hospital meets the criteria, but another hospital is closer by continuing along the limited access facility to another exit, the first hospital will not be signed for.

(f) Signs for a Tourist Information Center will be erected when the center is located on a direct route from the limited access highway and not more than 1 mile from the exit ramp;

(g) Telephone symbol signs will be erected when:

1. The telephone is a public telephone available for use 24 hours a day, 7 days a week; and

2. Is located within the immediate interchange area, not more than 1/2 mile from the interstate or exit ramp, and the immediate interchange is located in an isolated rural area.

3. Signs denoting Telephone shall not be installed in advance of interchanges where Gas, Food, Lodging, or Camping is identified since a criterion for signing for these services includes the availability of a telephone for public use.

Specific Authority 316.0745 FS. Law Implemented 316.0745 FS. History–New 3-27-05.