## 40B-5.028 Plugging of Storage and Disposal Wells, Cavities, and Reservoirs.

(1) The abandonment of a storage or disposal well, a cavity, or reservoir shall require the filing of a notice of intention to abandon on a prescribed form. The plugging procedure shall be submitted by the applicant and approved by the District before plugging operations are commenced.

(2) The plugging specification shall specify the type and amount of plugging material to be used, depths at which bridges may be set, depths and lengths of cement plugs, and other requirements for adequate plugging.

(3) Fluids and gases shall be confined to the strata in which they occur by the use of mud-laden fluid, cement, other suitable material, or combinations thereof. The amount, type, and kind of material and the method of placement shall be prescribed or approved by the District.

(4) The surface or drive pipe shall be abandoned with the hole except when otherwise approved by the District and a cement plug, welded plate, or other approved seal placed at the top of the pipe.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.106, 373.126, 373.133, 373.171 FS. History–New 4-20-78, Formerly 16H-5.28, 40B-5.28.