## 40D-3.060 General Permit for Monitoring Wells.

(1) A general permit is hereby granted for the construction, repair, modification or abandonment of a piezometer or monitoring well authorized as part of a site assessment, remedial action plan or pilot study at contaminated sites regulated by the Department of Environmental Protection Division of Waste Management pursuant to Chapter 376, F.S., provided all of the following conditions are met:

(a) Work is conducted by a licensed water well contractor or under the supervision of a licensed water well contractor;

(b) The nominal casing size shall be no larger than 4 inches in diameter;

(c) Total well borehole depth does not exceed 150 feet;

(d) Work complies with all applicable construction, location, casing and grouting requirements set forth in Chapter 40D-3, F.A.C.; and,

(e) A State of Florida Well Completion Report, signed by the licensed water well contractor who conducted or supervised the work is submitted to the District in accordance with the requirements of Rule 40D-3.411, F.A.C., for each well authorized by this general permit.

(2) The State of Florida Well Completion Report, Form No. LEG-R.005.02 (6/10) available at https://www.flrules.org/Gateway/reference.asp?No=Ref-05528 is incorporated by reference in Rule 40D-3.411, F.A.C. Copies may be obtained from the District’s website at www.watermatters.org or from District offices.

Rulemaking Authority 373.044, 373.113, 373.171, 373.309, 373.337 FS. Law Implemented 373.118, 373.306, 373.308, 373.309, 373.313, 373.316 FS. History–New 7-12-15.