Notice of Bid/Request for Proposal

DEPARTMENT OF EDUCATION

University of North Florida

ITB# 22-26 Data Closet Emergency Power Upgrade

Notice of Invitation to Bid

UNIVERSITY OF NORTH FLORIDA PROCUREMENT SERVICES ITB# 22-26 DATA CLOSET EMERGENCY POWER UPGRADE

The University of North Florida Board of Trustees, a public body corporate, is requesting the services of a Florida Certified Electrical Contractor to perform multiple data closet emergency power upgrades across UNF campus and residence buildings. Work is located at the University of North Florida, 1 UNF Drive, Jacksonville, FL 32224.

Project information

Contractor to provide labor and material to connect existing IT Rack Receptacles to nearest 120/208-volt emergency panel, provide red in color outlets and plates to existing and new circuits if not red in color, and provide labeling for each circuit. Provide nameplates on all panels, transfer switches, disconnect switches, and branch breakers in the switchboard; nameplates shall indicate panel designation and type of power. Provide labeling at each existing receptacle within the existing Independent Distribution Frame (IDF) and or Main Distribution Frame (MDF) room to denote circuit number and panel served. The label shall also denote location of panel. Existing emergency systems and panels at the buildings shall be metered for one week to confirm the system can support the new circuits. Provide report to UNF and Engineer for review. See plans and specifications.

The proposed schedule for this project is:

Advertisement 					April 21, 2022

Pre-Bid meeting					May 9, 2022, 2:00 p.m.

Site Visit – UNF Main Campus	May 10, 2022, 8:00 a.m.

Site Visit – UNF Residence		May 11, 2022, 8:00 a.m.

Deadline for questions			May 18, 2022, 12:00 p.m.

Response to questions				May 23, 2022

Bid Opening				May 31, 2022, 2:00 p.m.

Responses will only be accepted electronically through the UNF Bid Portal. Responses delivered in-person, by mail, by fax, or by email will be deemed non-responsive.

Bonds& Insurance

The University requires a Builders Risk policy for this project. Additional insurance requirements as provided in the University's Terms and Conditions and resulting contract, if any, will apply.

A Bid Security in the amount of five percent (5%) of the total contract price is required. For details on acceptable bid security formats, see Information for Bidders above. The Contract, if over $100,000, will require a 100% Performance and Payment Bond.

Solicitation documents, forms, drawings and descriptive project information may be obtained online at https://bids.sciquest.com/apps/Router/PublicEvent?CustomerOrg=UNF