Notice of Proposed Rule

DEPARTMENT OF ENVIRONMENTAL PROTECTION

Division of Air Resource Management

RULE NOS.:	RULE TITLES:

62-210.200	Definitions

62-210.300	Permits Required

62-210.310	Air General Permits

PURPOSE AND EFFECT: The purpose of the proposed rule (OGC No. 16-0106) is to amend paragraph 62-210.300(3)(a), F.A.C., to update provisions for fossil fuel steam generators, hot water generators, and other external combustion heating units with heat input capacity less than 100 million Btu per hour. The rule revision will allow units that meet the requirements of 40 CFR Part 63, Subpart JJJJJJ to maintain the existing permit exemption. This proposed rule also revises Rule 62-210.310, F.A.C., to address the circumstances under which temporary and relocatable sources, including emissions units operating under an Air General Permit (AGP), may collocate at an otherwise permitted facility, as well as revisions to the AGP for Chromium Electroplaters to reflect updates to 40 CFR Part 63, Subpart N. Clarifying and corrective revisions to existing rule language in Rules 62-210.200, 62-210.300, and 62-210.310, F.A.C., are also proposed.

SUMMARY:  Revisions include amendments to eliminate obsolete definitions, updates permit exemptions, and minor clarifying or corrective revisions to existing language.

OTHER RULES INCORPORATING RULE 62-210.200, F.A.C:  62-4.050, 62-110.104, 62-210.220, 62-210.300, 62-210.340, 62-210.370, 62-212.500, 62-212.720, 62-213.202, 62-213.300, 62-213.400, 62-213.410, 62-213.412, 62-213.420, 62-213.440, 62-214.100, 62-296.100, 62-296.340, 62-296.401, 62-296.417, 62-296.470, 62-296.480, 62-296.600, 62-255.320, 62-701.200, F.A.C.

EFFECT ON THOSE OTHER RULES: There will be no effect on other rules.

OTHER RULES INCORPORATING RULE 62-210.300, F.A.C:  62-210.200, 62-210.310, 62-210.350, 62-210.360, 62-210.920, 62-212.300, 62-213.300, 62-256.300, 62-256.700, 62-296.320, 62-296.401, 62-296.406, 62-296.414, 62-296.417, 62-296.570, 62-737.800, F.A.C.

EFFECT ON THOSE OTHER RULES: There will be no effect on other rules.

OTHER RULES INCORPORATING RULE 62-210.310, F.A.C:  62-210.300, 62-210.920, 62-213.300, F.A.C.

EFFECT ON THOSE OTHER RULES: The rule changes will have the intended effect for Rule 62-213.300, F.A.C. There will be no effect on other rules.

SUMMARY OF STATEMENT OF ESTIMATED REGULATORY COST: The agency has determined that amendments of these rules will not have an adverse impact on small business or likely increase regulatory costs in excess of $200,000 in the aggregate within one year after the implementation of the rule. A statement of estimated regulatory costs (SERC) has not been prepared by the agency. The Agency has determined that the proposed rule is not expected to require legislative ratification based on the statement of estimated regulatory costs, or, if no SERC is required, the information expressly relied upon and described herein: The Department has determined that the amendments to these rules will not increase regulatory costs for any entity because it updates the rules to ensure that existing permit exemptions are authorized and reduces the restrictions for permitted relocatable sources. Any person who wishes to provide a proposal for a lower cost regulatory alternative, must do so in writing within 21 days of this notice.

RULEMAKING AUTHORITY: 403.061 FS.

LAW IMPLEMENTED: 403.031, 403.061, 403.087, 403.814, FS.

IF REQUESTED WITHIN 21 DAYS OF THE DATE OF THIS NOTICE, A HEARING WILL BE SCHEDULED AND ANNOUNCED IN THE FAR.

THE PERSON TO BE CONTACTED REGARDING THE PROPOSED RULE IS: Terri Long, Florida Department of Environmental Protection, Division of Air Resource Management, 2600 Blair Stone Road, MS 5500, Tallahassee, Florida, 32399-2400. Telephone (850)717-9023.  E-mail: Terri.Long@dep.state.fl.us.

THE FULL TEXT OF THE PROPOSED RULE IS:

## 62-210.200 Definitions.

The following words and phrases when used in this chapter and in Chapters 62-204, 62-212, 62-213, 62-214, 62-296, and 62-297, F.A.C., shall, unless the context clearly indicates otherwise, have the following meanings:

(1) through (134) No change.

(135) “Gas/Gas Method” – Either of two EPA methods for determining capture efficiency which rely only on gas phase measurements. One method, prescribed in paragraph 62-297.450(2)(a), F.A.C., requires construction of a temporary total enclosure to assure all otherwise unconfined air pollutant emissions are measured. The other method, prescribed in paragraph 62-297.450(2)(c), F.A.C., uses the room or building which houses the emissions activity, process, or source as an enclosure.

(136) through (162) renumbered (135) through (161) No change.

(163) “Liquid/Gas Method” – Either of two EPA methods for determining capture efficiency which require both gas phase and liquid phase measurements and analysis. One liquid/gas method, prescribed in paragraph 62-297.450(2)(b), F.A.C., requires construction of a temporary enclosure. The other, prescribed in paragraph 62-297.450(2)(d), F.A.C., uses the room or building which houses the emissions activity, process, or source as an enclosure.

(164) through (306) renumbered (162) through (304) No change.

Rulemaking Authority 403.061, 403.8055 FS. Law Implemented 403.031, 403.061, 403.087, 403.0872, 403.8055 FS. History–Formerly 17-2.100, Amended 2-9-93, 11-28-93, Formerly 17-210.200, Amended 11-23-94, 4-18-95, 1-2-96, 3-13-96, 3-21-96, 8-15-96, 10-7-96, 10-15-96, 5-20-97, 11-13-97, 2-5-98, 2-11-99, 4-16-01, 2-19-03, 4-1-05, 7-6-05, 2-2-06, 4-1-06, 9-4-06, 9-6-06, 1-10-07, 5-9-07, 7-16-07, 3-16-08, 10-12-08, 6-29-09, 3-11-10, 6-29-11, 12-4-11, 3-28-12, 10-23-13, _______.

## 62-210.300 Permits Required.

Unless exempted from permitting pursuant to this rule or Rule 62-4.040, F.A.C., the owner or operator of any facility or emissions unit which emits or can reasonably be expected to emit any air pollutant shall obtain appropriate authorization from the Department prior to undertaking any activity at the facility or emissions unit for which such authorization is required. The Department grants authorization to conduct such activities by individual air permit or by air general permit. Activities requiring authorization by individual air construction permit are addressed at subsection 62-210.300(1), F.A.C., and activities requiring authorization by individual air operation permit are addressed at subsection 62-210.300(2), F.A.C. Authorization by air general permit is addressed at subsection 62-210.300(4), F.A.C. All emission limitations, controls, and other requirements imposed by any individual air permit shall be at least as stringent as any limitations and requirements contained in or enforceable under the State Implementation Plan (SIP) or Designated Facility Plan. Except as provided at Rule 62-213.460, F.A.C., being authorized to construct, operate, or undertake any other activity by individual air permit or air general permit does not relieve the owner or operator of a facility or emissions unit from complying with any emission limiting standards or other requirements of the air pollution rules of the Department or any other such requirements under federal, state, or local law.

(1) through (2) No change.

(3) Exemptions from Permitting. Except as otherwise provided herein, an owner or operator shall not be required to obtain an air construction permit or non-Title V air operation permit, or to use an air general permit pursuant to Rule 62-210.310, F.A.C., for any facility, emissions unit, or pollutant-emitting activity that satisfies the applicable permitting exemption criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., or has been exempted from permitting pursuant to Rule 62-4.040, F.A.C. Failure of a facility, emissions unit, or activity to satisfy the exemption criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., does not preclude such facility, emissions unit, or activity from being considered for exemption pursuant to Rule 62-4.040, F.A.C. Notwithstanding the above, no emissions unit or activity shall be exempt from the requirement to obtain an air construction permit or non-Title V air operation permit, or to use an air general permit pursuant to Rule 62-210.310, F.A.C., if it would be subject to any unit-specific limitation or requirement, unless compliance with such limitation or requirement is specifically listed as a condition of exemption. Furthermore, no new, reconstructed, or modified emissions unit or activity shall be exempt from the requirement to obtain an air construction permit if its emissions would contribute to a major modification or to any modification that would be a major modification but for the use, in whole or in part, of the baseline actual-to-projected actual applicability test in Rule 62-212.400, F.A.C. An emissions unit or pollutant-emitting activity exempt from the requirement to obtain an air construction permit shall not be exempt from the permitting requirements of Chapter 62-213, F.A.C., if it is contained within a Title V source or if its emissions, in combination with the emissions of other emission units and activities at the facility, would cause the facility to be classified as a Title V source. Exemption from the requirement to obtain an air construction permit or non-Title V air operation permit, or to use an air general permit pursuant to Rule 62-210.310, F.A.C., does not relieve the owner or operator of a facility or emissions unit from complying with any limitation or requirement applicable to such facility or emissions unit.

#### (a) Categorical and Conditional Exemptions. Except as otherwise provided at subsection 62-210.300(3), F.A.C., above, the following facilities, emissions units, and pollutant-emitting activities shall be exempt from any requirement to obtain an air construction permit or non-Title V air operation permit, or to use an air general permit pursuant to Rule 62-210.310, F.A.C.

1. through 32. No change.

33. Fossil fuel steam generators, hot water generators, and other external combustion heating units with heat input capacity equal to or less than 10 million Btu per hour, provided all the following conditions are met with respect to each such unit.

a. through b. No change.

c. The unit is a gas-fired boiler, which, for the purposes of this exemption, is defined as any boiler that burns gaseous fuels not combined with any solid fuels and burns liquid fuel only during periods of gas curtailment, gas supply interruption, startups, or periodic testing of liquid fuel. Periodic testing of liquid fuel shall not exceed a combined total of 48 hours during any calendar year The unit shall not burn used oil or any fuels other than natural gas or propane, except that fuel oil with a sulfur content not exceeding 1.0 percent by weight may be burned during periods of natural gas curtailment.

34. Fossil fuel steam generators, hot water generators, and other external combustion heating units with heat input capacity less than 100 million Btu per hour, provided all the following conditions are met with respect to each such unit.

a. The unit is not subject to the Acid Rain Program, or any other unit-specific limitation or requirement other than any such limitation or requirement that may apply pursuant to 40 C.F.R. Part 63, Subpart JJJJJJ, adopted and incorporated by reference at Rule 62-204.800, F.A.C.

b. through h. No change.

i. If the boiler is subject to 40 C.F.R. Part 63, Subpart JJJJJJ, the owner shall comply with all limitations and requirements of Subpart JJJJJJ that apply to the boiler.

35. Stationary Reciprocating Internal Combustion Engines, provided all the following conditions are met with respect to each such engine.

a. through e. No change.

f. If the engine is a stationary compression ignition reciprocating internal combustion engine that is subject to 40 C.F.R. Part 60, Subpart IIII, adopted and incorporated by reference at Rule 62-204.800, F.A.C., or by virtue of modification or reconstruction becomes subject to such subpart, the owner or operator shall comply with all limitations and requirements of Subpart IIII that apply to the engine.

g. If the engine is a stationary spark ignition reciprocating internal combustion engine that is subject to 40 C.F.R. Part 60, Subpart JJJJ, adopted and incorporated by reference at Rule 62-204.800, F.A.C., or by virtue of modification or reconstruction becomes subject to such subpart, the owner or operator shall comply with all limitations and requirements of Subpart JJJJ that apply to the engine.

h. If the engine is a stationary reciprocating internal combustion engine subject to 40 C.F.R. Part 63, Subpart ZZZZ, adopted and incorporated by reference at Rule 62-204.800, F.A.C., the owner or operator shall comply with all limitations and requirements of Subpart ZZZZ that apply to the engine. If emissions testing is required pursuant to Subpart ZZZZ, all reports and notifications, including notifications of upcoming tests, and reports shall be submitted to the Department in accordance with the provisions of Subpart ZZZZ.

36. No change.

(b) Generic and Temporary Exemptions.

1. through 2. No change

3. Temporary Exemption for Emissions Units at Certain Title V Sources. Except for an emissions unit that is subject to any applicable regulation or permitting requirement under Rule 62-212.400 or 62-212.500, F.A.C.; any emissions standard or other requirement adopted by reference prior to July 1, 1995, in Rule 62-204.800, F.A.C.; any requirement established pursuant to Rule 62-296.330, F.A.C.; or any Reasonably Available Control Technology (RACT) provisions under Rules 62-296.500 through 62-296.712, F.A.C.; an emissions unit that is described in a timely and complete permit application under Chapter 62-213, F.A.C., and not subject to an existing valid air permit, shall be exempt from the permitting requirements of this chapter, Chapter 62-4 and Rule 62-212.300, F.A.C., until a final determination on a permit application under Chapter 62-213, F.A.C., is made. In addition, no emissions unit shall be exempt under this paragraph if its emissions cause or contribute to a significant net emissions increase under Rule 62-212.400 or 62-212.500, F.A.C., which would trigger preconstruction review, or if it is constructed or modified, as defined under Rule 62-210.200, F.A.C., subsequent to November 23, 1994. Any applicant exercising this exemption shall provide notification of such exemption to the Department, and further authorizes the Department to inspect these emissions units at the Department’s discretion. Emissions units subject to existing valid permits shall continue to operate consistent with those permits as provided under subparagraph 62-213.420(1)(b)2., F.A.C. This exemption is available only to emissions units contained within either facilities that were Title V sources on or before October 25, 1995, and that commenced operation on or before that date, or facilities that became Title V sources by operation of law after October 25, 1995, and have timely applied for an initial Title V air operation permit.

4. renumbered 3. No change.

(c) Conditional Exemptions from Title V Air Permitting. Except as otherwise provided herein, the following facilities shall be exempt from the requirement to obtain a Title V air operation permit under the provisions of Chapter 62-213, F.A.C., provided the conditions of exemption for each such facility are met. Facilities exempt from Title V air permitting pursuant to subparagraph 62-210.300(3)(c)2., F.A.C., are not exempt from the requirement to obtain an air construction permit or non-Title V air operation permit. A facility shall not be entitled to an exemption from Title V air permitting under this rule if it is a Title V source pursuant to paragraph (f), (g), or (h) of the definition of “major source of air pollution” or the facility would be classified as a Title V source as a result of the combined potential to emit regulated pollutants of all emissions units at the facility.

1. No change

2. Facilities comprising asphalt concrete plants, provided the following conditions are met.

a. through i. No change

j. An asphalt plant claiming this exemption from Title V air permitting shall not collocate with, or relocate to, any Title V source unless the Title V permit specifically allows such facility to be collocated with or relocated to the Title V source and operated under the authority of the Title V permit while onsite at the Title V source. An asphalt plant cannot apply this exemption if it creates a Title V source in combination with any other collocated facilities, emissions units, or pollutant-emitting activities, including any such facility, emissions unit, or activity that is otherwise exempt from permitting.

k. renumbered j. No change.

(4) through (6) No change.

(7) Transfer of Air Permits.

(a) No change.

(b) For an air general permit, the provisions of paragraph 62-210.300(7)(a) and Rule 62-4.120, F.A.C., do not apply. Thirty (30) days before using an air general permit, the new owner must submit a registration to the Department in accordance with subsection 62-210.310(2) 62-210.300(2), F.A.C.

Rulemaking Authority 403.061 FS. Law Implemented 403.031, 403.061, 403.087, 403.814 FS. History–Formerly 17-2.210, Amended 11-28-93, Formerly 17-210.300, Amended 11-23-94, 4-2-95, 4-18-95, 10-16-95, 1-2-96, 3-13-96, 3-21-96, 5-13-96, 8-15-96, 10-7-96, 5-20-97, 11-13-97, 2-5-98, 2-11-99, 4-16-01, 6-21-01, 7-6-05, 2-2-06, 1-10-07, 5-9-07, 3-16-08, 10-12-08, 6-29-11,               .

## 62-210.310 Air General Permits.

## (1) No change.

### (2) General Procedures. This subsection sets forth general procedures for use of any of the air general permits provided at subsections 62-210.310(4) and (5), F.A.C.

### (a) Determination of Eligibility. A facility is eligible to use an air general permit under this rule if it meets all specific eligibility criteria given in the applicable air general permit at subsection 62-210.310(4) or (5), F.A.C., and the following general criteria.

### 1. through 2. No change.

## 3. The facility shall not be collocated with, or relocated to, an existing Title V source unless the Title V permit allows such facility to be collocated with or relocated to the Title V source and operated under the authority of the Title V permit while onsite at the Title V source.

## 4. through 5. renumbered 3. through 4. No change.

## (b) through (f) No change.

## (3) No change.

## (4) Air General Permits for Facilities Claiming Conditional Exemption from Title V Air Permitting.

## (a) No change.

## (b) Air General Permit for Facilities Comprising Stationary Reciprocating Internal Combustion Engines.

## 1. A facility comprising one (1) or more stationary reciprocating internal combustion engines shall be eligible to use this air general permit provided it meets the general eligibility criteria of paragraph 62-210.310(2)(a), F.A.C., and the following specific criteria.

## a. through b. No change.

2. A facility using this air general permit shall comply with the general conditions given at subsection 62-210.310(3), F.A.C., and the following specific conditions.

a. Total fuel consumption by all stationary reciprocating internal combustion engines at the facility shall not exceed 20,000 gallons per year of gasoline, 250,000 gallons per year of diesel fuel, 1.15 million gallons per year of propane, 40 million standard cubic feet per year of natural gas, or an equivalent prorated amount if multiple fuels are used.

b. through c. No change.

## d. If the stationary compression ignition reciprocating internal combustion engine is subject to 40 C.F.R. Part 60, Subpart IIII, adopted and incorporated by reference at Rule 62-204.800, F.A.C., or by modification or reconstruction becomes subject to such subpart, the owner or operator shall comply with all limitations and requirements of Subpart IIII that apply to the engine.

## e. If the stationary spark ignition reciprocating internal combustion engine is subject to 40 C.F.R. Part 60, Subpart JJJJ, adopted and incorporated by reference at Rule 62-204.800, F.A.C., or by modification or reconstruction becomes subject to such subpart, the owner or operator shall comply with all limitations and requirements of Subpart JJJJ that apply to the engine.

## f. No change.

## 3. The registration for this air general permit shall include all the following information.

## a. through b. No change.

## c. For each compression ignition reciprocating internal combustion engine subject to 40 C.F.R. Part 60, Subpart IIII, adopted and incorporated by reference at Rule 62-204.800, F.A.C., the engine manufacturer; model number; whether it is an emergency engine as per the definition at 40 C.F.R. Part 60, Subpart IIII, adopted and incorporated by reference at Rule 62-204.800, F.A.C. (yes or no); whether there is a manufacturer certification for the engine (yes or no); and the displacement (liters per cylinder).

## d. For each spark ignition reciprocating internal combustion engine subject to 40 C.F.R. Part 60, Subpart JJJJ, adopted and incorporated by reference at Rule 62-204.800, F.A.C., the engine manufacturer; model number; whether it is an emergency engine as per the definition at 40 C.F.R. Part 60, Subpart JJJJ, adopted and incorporated by reference at Rule 62-204.800, F.A.C. (yes or no); whether there is a manufacturer certification for the engine (yes or no); and the rated capacity (horsepower).

## e. For each compression ignition reciprocating internal combustion engine subject to 40 C.F.R. Part 63, Subpart ZZZZ, adopted and incorporated by reference at Rule 62-204.800, F.A.C., but not subject to 40 C.F.R. Part 60, Subpart IIII, adopted and incorporated by reference at Rule 62-204.800, F.A.C., the engine manufacturer; model number; whether it is an emergency engine or limited use engine as per the definitions at 40 C.F.R. Part 63, Subpart ZZZZ, adopted and incorporated by reference at Rule 62-204.800, F.A.C. (yes or no); engine displacement (liters per cylinder); and rated capacity (horsepower).

## f. For each spark ignition internal reciprocating combustion engine subject to 40 C.F.R. Part 63, Subpart ZZZZ, adopted and incorporated by reference at Rule 62-204.800, F.A.C., but not subject to 40 C.F.R. Part 60, Subpart JJJJ, adopted and incorporated by reference at Rule 62-204.800, F.A.C., the engine manufacturer; model number; whether it is an emergency engine or limited use engine as per the definitions at 40 C.F.R. Part 63, Subpart ZZZZ, adopted and incorporated by reference at Rule 62-204.800, F.A.C. (yes or no); engine type (two stroke lean burn, four stroke lean burn, or four stroke rich burn); and rated capacity (horsepower).

## (c) through (f) No change.

## (5) Air General Permits for Miscellaneous Facilities.

### (a) No change.

### (b) Air General Permit for Facilities Comprising Concrete Batching Plants.

### 1. through 3. No change.

4. A facility using this air general permit may collocate with other facilities that separately registered for, and are also using, the concrete batching plant air general permit, and with facilities using the nonmetallic mineral processing plant air general permit at paragraph 62-210.310(5)(e), F.A.C., even if under the control of different persons, provided the following conditions are met.

a. No change.

b. The total fuel consumption by all emissions units authorized by the air general permit at the collocation site shall not exceed 275,000 gallons of diesel fuel, 23,000 gallons per year of gasoline, 44 million standard cubic feet per year of natural gas, or 1.3 million gallons per year of propane, or an equivalent prorated amount if multiple fuels are used.

c. through d. No change.

5. Under the authority of this air general permit, a relocatable concrete batching plant may perform a non-routine task, such as making concrete for a construction project, at a facility with authorization by individual air construction or non-Title V air operation permit, without revision to the facility’s individual air permit. Any such concrete batching plant shall remain at the individually permitted facility for no more than six (6) months from the day it relocates to such facility. The owner or operator of such concrete batching plant shall keep records to indicate how long the plant has been at the permitted facility.

6. No change.

### (c) through (d) No change.

### (e) Air General Permit for Facilities Comprising Nonmetallic Mineral Processing Plants (Crushing Operations).

1. through 4. No change.

5. Under the authority of this air general permit, a relocatable nonmetallic mineral processing plant may perform a non-routine task, such as crushing concrete for a demolition project, at a facility with authorization by individual air construction or non-Title V air operation permit, without revision to the facility’s individual air permit. Any such nonmetallic mineral processing plant shall not be deployed at a single site for more than six (6) months in any consecutive twelve (12) months. The owner or operator of such nonmetallic mineral processing plant shall keep records to indicate how long the plant has been at the permitted facility. No nonmetallic mineral processing plant using this air general permit shall perform a task routinely done at the individually permitted facility, such as crushing recycled asphalt pavement (rap) at an asphalt plant, unless operation of the nonmetallic mineral processing plant is authorized by the air construction permit or non-Title V air operation permit, as applicable, for the permitted facility.

6. No change.

(f) No change.

(g) Air General Permit for Facilities Comprising Ethylene Oxide Sterilizers.

1. through 3. No change.

4. The registration for this air general permit shall include all the following information.

a. through d. No change.

(h) Air General Permit for Facilities Comprising Halogenated Solvent Degreasers.

1. through 3. No change.

4. The registration for this air general permit shall include all the following information.

a. through e. No change.

(i) Air General Permit for Facilities Comprising Chromium Electroplaters and Anodizers.

1. through 3. No change.

4. The registration for this air general permit shall include all the following information.

a. For each hard chromium electroplating tank machine, whether the tank machine is existing or new as defined at 40 C.F.R. Part 63, Subpart N; whether the tank is open surface or enclosed as defined at 40 C.F.R. Part 63, Subpart N; date of purchase; date of control device installation; type of control device (packed-bed scrubber, composite mesh pad, packed-bed scrubber and composite mesh pad, fume suppressant, fume suppressant with a wetting agent, fiber-bed mist eliminator, or wetting agent); and applicable 40 C.F.R. Part 63, Subpart N standard (0.03 mg/dscm, 0.015 mg/dscm, or an alternative emission rate as determined in 40 C.F.R. 63.344 standard for multiple tanks under common control).; and

b. wWhether the facility's cumulative potential rectifier capacity is greater than or equal to 60 million ampere-hours per year (yes or no).

b.c. For each decorative chromium electroplating or chromium anodizing tank machine, whether the tank machine is existing or new as defined at 40 C.F.R. Part 63, Subpart N; date of purchase; date of control device installation; type of control device (packed-bed scrubber, composite mesh pad, packed-bed scrubber and composite mesh pad, fume suppressant, fume suppressant with a wetting agent, fiber-bed mist eliminator, or wetting agent); and applicable 40 C.F.R. Part 63, Subpart N standard (0.01 mg/dscm, 45 dynes/cm, or, for trivalent chromium bath decorative electroplating tanks only, records of bath components for trivalent chromium tanks, or alternative standard for multiple tanks under common control).

c.d. The compliance demonstration method (initial performance test, or use of a wetting agent to reduce emissions so as to meet the existing surface tension limit, or, for trivalent chromium bath decorative electroplating tanks only, records of bath components).

(j) Air General Permit for Facilities Comprising Asbestos Manufacturers and Fabricators.

1. through 3. No change.

4. The registration for this air general permit shall indicate whether the facility is classified as asbestos manufacturing, asbestos fabrication, or both.

(k) Air General Permit for Facilities Comprising Secondary Aluminum Sweat Furnaces.

1. through 3. No change.

4. The registration for this air general permit shall include all the following information.

a. through b. No change.

Rulemaking Authority 403.061 FS. Law Implemented 403.031, 403.061, 403.087, 403.814 FS. History–New 1-10-07, Amended 5-9-07, 10-12-08, 6-29-11,              .

NAME OF PERSON ORIGINATING PROPOSED RULE:  Terri Long, Division of Air Resource Management

NAME OF AGENCY HEAD WHO APPROVED THE PROPOSED RULE: Jonathan P. Steverson, Secretary

DATE PROPOSED RULE APPROVED BY AGENCY HEAD: January 31, 2017

DATE OF NOTICE OF PROPOSED RULE DEVELOPMENT PUBLISHED IN FAR: June 8, 2016