# CHAPTER 62-312

DREDGE AND FILL ACTIVITIES

62-312.010 	Scope of Part I

62-312.020 	Definitions

62-312.030 	Jurisdiction

62-312.040 	Jurisdictional Declaratory Statements

62-312.045 	Jurisdictional Intent

62-312.050 	Exemptions

62-312.060 	Procedures to Obtain a Permit

62-312.065 	Additional Requirements and Procedures for Concurrent Review of Related Applications

62-312.070 	Short Form Applications for Certain Dredging or Filling

62-312.080 	Standards for Issuance or Denial of a Permit

62-312.082 	Duration of Permits

62-312.085 	Periodic Review of Permits

62-312.090 	Emergency Classification and Procedures

62-312.100 	Modification of Permits

62-312.200 	Scope of Part II

62-312.210 	Procedures to Obtain a Long-Term Permit

62-312.220 	Standards for Issuance or Denial of a Long-Term Permit

62-312.300 	Intent

62-312.310 	Definitions

62-312.320 	Incorporation of Mitigation into the Permit Application Process

62-312.330 	Mitigation Proposals

62-312.340 	Evaluation of Mitigation Proposals

62-312.350 	Determination of Success for Mitigation Projects

62-312.360 	Pre-Construction Mitigation

62-312.370 	Restrictions on Property Use

62-312.380 	Release from Responsibility

62-312.390 	Financial Responsibility

62-312.400 	Intent

62-312.410 	General Criteria

62-312.420 	Permitting Requirements for Piers

62-312.430 	Permitting Requirements for Marinas

62-312.440 	Permitting Requirements for Shoreline Stabilization

62-312.450 	Mitigation

62-312.460 	Special Consideration

62-312.800 	Scope of Part V

62-312.801 	General Permit to U.S. Forest Service for Minor Works Within National Forests in Florida

62-312.803 	General Permit for Installation or Maintenance of Boat Ramps

62-312.804 	General Permit for Riprap

62-312.805 	General Permit for Headwalls and Culverts Associated with a Stormwater Discharge Facility

62-312.806 	General Permit to the Florida Department of Transportation for Minor Works Within FDOT Rights-of-Way or Easements

62-312.807 	General Permit for the Construction of Artificial Reefs

62-312.808 	General Permit for Certain Piers and Associated Structures

62-312.809 	General Permit to the Florida Department of Transportation for Minor Bridge Construction

62-312.810 	General Permit to Perform Prospecting Activities for Phosphate Minerals

62-312.811 	General Permit for Temporary Dragline Crossings of Waterways

62-312.812 	General Permit for Low Water Crossings

62-312.813 	General Permit for the Installation of Fences

62-312.814 	General Permit to Florida Game and Fresh Water Fish Commission, U.S. Forest Service, and County and Municipal Governments for the Construction of Freshwater Fish Attractors

62-312.815 	General Permit for Ski Jumps and Slalom Courses

62-312.816 	General Permit for the Construction or Maintenance of Culverted Driveway or Roadway Crossings and Bridges of Artificial Waterways

62-312.817 	General Permit for the Construction of Aerial Pipeline Crossings of Certain Waters

62-312.818 	General Permit for Subaqueous Utility Crossings of Artificial Waterways

62-312.819 	General Permit for the Limited Dredging of Sediment for Aquatic Plant Management Purposes

62-312.822 	General Permit for the Construction and Maintenance of Electric Power Lines by Electric Utilities

62-312.823 	General Permit for Floating Vessel Platforms and Floating Boat Lifts

62-312.824 	General Permit to Counties and Municipalities to Pave Existing County or Municipally Owned and Maintained Roads, including the Repair and Replacement of Bridges that are Part of the Roadway

62-312.825 	General Permit to U.S. Army Corps of Engineers for Environmental Restoration or Enhancement Activities

62-312.900 	Wetland Resource Forms

## 62-312.010 Scope of Part I.

This part provides the requirements and procedures for obtaining permits and jurisdictional declaratory statements from the Department pursuant to Sections 403.91 through 403.929, F.S. Dredging or filling which is grandfathered by subsections 403.913(6), (8) and (9), F.S., is governed by Rules 62-312.150 and 62-312.160, F.A.C. The requirements of this part are in addition to and not in lieu of the water quality standards which are required by other portions of these sections. Except for the definitions contained in Rule 62-312.020, F.A.C., which shall also apply to activities regulated under Part IV of Chapter 373, F.S., the provisions of this Part shall only apply to activities in the geographical territory of the Northwest Florida Water Management District and to activities grandfathered under Sections 373.414(9), (11), (12)(a), (13), (14), (15) and (16), F.S.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061, 403.813, 403.814 FS. History–New 12-10-84, Amended 8-7-85, Formerly 17-12.010, 17-312.010, Amended 10-3-95.

## 62-312.020 Definitions.

As used in this chapter:

(1) “Agricultural activities” includes all necessary farming and forestry operations which are normal and customary for the area, such as site preparation, clearing, fencing, contouring to prevent soil erosion, soil preparation, plowing, planting, harvesting, construction of access roads, and placement of bridges and culverts, provided such operations do not impede or divert the flow of surface waters.

(2) “Agricultural water management systems” means farming and forestry water management or irrigation systems and farm ponds which are permitted pursuant to Chapter 373, F.S., or which are exempt from the permitting provisions of that Chapter.

(3) “Canal” is a trench, the bottom of which is normally covered by water with the upper edges of its two sides normally above water.

(4) “Channel” is a trench, the bottom of which is normally covered entirely by water, with the upper edges of its sides normally below water.

(5) “Department” is the Florida Department of Environmental Protection or its delegatee as provided in the Operating Agreements Concerning Management And Storage of Surface Waters Regulation, And Wetland Resource Regulation adopted by reference in Rule 62-113.200, F.A.C.

(6) “Drainage ditch” or “irrigation ditch” is a man-made trench dug for the purpose of draining water from the land or for transporting water for use on the land and is not built for navigational purposes.

(7) “Dredging” is the excavation, by any means, in waters of the state. It is also the excavation (or creation) of a water body which is, or is to be, connected to any of the waters listed in subsection 62-312.030(2), F.A.C., directly or via an excavated water body or series of excavated water bodies.

(8) “Embedment” is the placement of transmission or distribution lines, pipes or cables into the bottoms of waters of the State by minimal displacement of bottom material and without the creation of a trench, or trough, through the use of techniques such as plowing-in, weighing-in, or non-trenching jets.

(9) “Entrenchment” is the placement of transmission or distribution lines, pipes or cables into the bottoms of waters of the State by the creation of a defined trench, or trough, through the use of such devices as clamshells, dredges, trenching jets, or other devices which produce similar results.

(10) “Estuary” means a semi-enclosed, naturally existing coastal body of water which has a free connection with the open sea and within which seawater is measurably diluted with fresh water derived from riverine systems.

(11) “Filling” is the deposition, by any means, of materials in waters of the state.

(12) “Insect control impoundment dikes” means artificial structures, including earthen berms, constructed and used to impound waters for the purposes of insect control.

(13) “Lagoon” means a naturally existing coastal zone depression which is below mean high water and which has permanent or ephemeral communications with the sea, but which is protected from the sea by some type of naturally existing barrier.

(14) “Materials” is matter of any kind, including but not limited to, sand, clay, silt, rock, dredged material, construction debris, solid waste, pilings or other structures, ash, and residue from industrial and domestic processes. The term shall not include the temporary use and placement of lobster pots, crab traps, or similar devices or the placement of oyster cultch pursuant to Section 379.2525, F.S., or Chapter 62B-5, F.A.C.

(15) “Original Design Specifications” shall consist of drawings of record prepared and sealed by a registered professional engineer or a professional land surveyor following completion of a project constructed in compliance with a valid department permit. For projects constructed where prior departmental authorization was not required or where original design specifications were not a requirement of the permit, original design specifications may instead include other competent and substantial evidence of pre-existing conditions, including but not limited to evidence adduced from soil borings, on-site conditions, prior surveys, aerial photographs, or other exhibits acceptable to the department.

(16) “Riprap” is a sustaining wall made to reduce the force of waves and to protect the shore from erosion and consists of unconsolidated boulders, rocks, or clean concrete rubble with no exposed reinforcing rods or similar protrusions.

(17) “Seawall” means a man-made wall or encroachment, except riprap, made to break the force of the waves and to protect the shore from erosion.

(18) “Swale” means a manmade trench which:

(a) Has a top width-to-depth ratio of the cross-section equal to or greater than 6:1, or side slopes equal to or greater than 3 feet horizontal to 1 foot vertical;

(b) Contains contiguous areas of standing or flowing water only following a rainfall event;

(c) Is planted with or has stabilized vegetation suitable for soil stabilization, stormwater treatment, and nutrient uptake; and

(d) Is designed to take into account the soil erodibility, soil percolation, slope, slope length, and drainage area so as to prevent erosion and reduce pollutant concentration of any discharge.

(19) “Vertical seawall” is a seawall the waterward face of which is at a slope greater than 75 degrees to the horizontal. A seawall with sloping riprap on the waterward face shall not be considered a vertical seawall.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.031, 403.061, 403.803, 403.911, 403.912 FS. History–New 12-10-84, Amended 8-30-88, 3-26-89, Formerly 17-12.020, Amended 11-16-92, Formerly 17-312.020.

## 62-312.030 Jurisdiction.

(1) Pursuant to Sections 403.031(12) and 403.913, F.S., dredging and filling conducted in, on, or over those surface waters of the state as provided in this section, require a permit from the Department unless specifically exempted in Sections 403.813, 403.913, 403.927, F.S., or Rule 62-312.050, F.A.C.

(2) For the purposes of this rule surface waters of the state are those waters listed below and excavated water bodies, except for waters exempted by subsection 62-312.050(4), F.A.C., which connect directly or via an excavated water body or series of excavated water bodies to those waters listed below:

(a) Atlantic Ocean out to the seaward limit of the state’s territorial boundaries;

(b) Gulf of Mexico out to the seaward limit of the state’s territorial boundaries;

(c) Bays, bayous, sounds, estuaries, lagoons and natural channels and natural tributaries thereto;

(d) Rivers, streams and natural tributaries thereto, excluding those intermittent streams, tributaries or portions thereof defined in subsection 403.913(5), F.S. Standard hydrological methods shall be used to determine which streams constitute intermittent streams and intermittent tributaries. An intermittent stream or intermittent tributary means a stream that flows only at certain times of the year, flows in direct response to rainfall, and is normally an influent stream except when the ground water table rises above the normal wet season level. Those portions of a stream or tributary which are intermittent and are located upstream of all nonintermittent portions of the stream or tributary are not subject to dredge and fill permitting unless there is a continuation of jurisdiction as determined pursuant to Rule 62-301.400, F.A.C.

(e) Natural lakes, except:

1. Those where one person, other than the state, owns the entire lake to its landward extent as delineated by applicable Department rule; or

2. Those that become dry each year and are without standing water; or

3. Those of no more than 10 acres in landward extent with a maximum average depth of 2 feet or less existing throughout the year;

(f) The waters as defined in Sections 403.031(12)(a), (b), F.S.

(g) Waters within mosquito control impoundments constructed as part of a governmental mosquito control program, excluding those portions which have become jurisdictional based on a change to vegetative dominance as defined in Rule 62-301.400, F.A.C., solely because of construction of the impoundment. Specifically included as jurisdictional are those areas which were naturally occurring waters of the state before construction of the impoundment but which have had their connection to other waters of the state severed as a result of the construction of dikes. Also included as jurisdictional are areas where vegetative dominance of jurisdictional species as defined in Rule 62-301.400, F.A.C., has been lost solely because of construction of the impoundment.

(3) The landward extent of surface waters of the state, for the purpose of this chapter, shall be determined in accordance with Rule 62-301.400, F.A.C. and Sections 403.817, 403.8171, and 403.913, F.S.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.031, 403.061, 403.813, 403.817, 373.414 FS. History–New 12-10-84, Amended 3-26-89, Formerly 17-12.030, Amended 12-7-93, Formerly 17-312.030, Amended 8-7-95.

## 62-312.040 Jurisdictional Declaratory Statements.

(1) Pursuant to Section 403.914(1), F.S., a property owner, a person who has power of eminent domain, or any other person with a legal or equitable interest in a property may petition the department for a formal jurisdictional determination. The petition shall contain:

(a) A vicinity map showing the location, including Section, Township and Range, and areal extent of the property in question;

(b) Written authorization to enter the property signed by the property owner;

(c) Four copies of blue line prints of recent aerial photographs which accurately reflect the current conditions on the site with the property boundaries to be inspected clearly delineated, along with identification of all major roads and the north bearing;

(d) A statement indicating whether the petitioner wants the line between the upland and the area of Department jurisdiction to be staked.

(2) The petition for a jurisdictional declaratory statement shall be processed by the Department in accordance with Sections 403.914(1) and (3), F.S. If additional information is necessary to determine jurisdiction, the Department shall request and the petitioner shall furnish any or all of these items:

(a) An original U.S.G.S. 7.5 minute series or a more detailed topographic map of the site with the contours at intervals specified by the Department which are appropriate to the specific site. Specific areas may have to be surveyed by the petitioner.

(b) Hydrological data needed to determine connections between water bodies or to determine the presence of intermittent streams, including rainfall data, data on duration and volume of water flow, ground water level data, data on the location of natural or man-made watercourses on or abutting the site, including locations of culverts and sizes, and similar information.

(c) Recent aerial photographs of sufficient detail to determine the dominant vegetation on a site by photointerpretation. Black and white or color glossy photographs, blue line prints of aerial photographs, or false color infrared photographs may be required, depending upon the site.

(d) If the line is to be staked, the services of a registered surveyor or representative thereof shall be available to accompany the Department representative to survey the staked line. The Department shall be provided a copy of the survey properly certified in accordance with Chapter 472, F.S.

(3) If the line is not to be staked and surveyed, it shall be drawn by the Department on the blue line prints of aerial photographs. However, the line so drawn may represent only an approximation of the actual jurisdiction because of inherent characteristics in drafting or cartography. The accuracy of the determination will be dependent upon the level of detail and accuracy of the information provided.

(4) Each person who receives a proposed jurisdictional declaratory statement may publish, or may be required to publish, and provide proof of publication to the Department, at his own expense, a notice of the proposed declaratory statement in a newspaper of general circulation in the area affected, using the format prescribed in Rule 62-110.106, F.A.C. Publication of a Notice of Proposed Jurisdictional Declaratory Statement shall be required for areas where the environmental sensitivity of the area is reasonably expected to result in heightened public concern or a request for administrative proceedings. Failure of the petitioner to publish a required notice within 30 days of the Department’s request shall constitute withdrawal of the petition. The Department shall also publish a notice of the proposed jurisdictional declaratory statement in the Florida Administrative Weekly.

(5) Petitions for jurisdictional declaratory statements shall be accompanied by the following fees which shall be based on the entire property for which the petition is filed:

(a) For property 0 – 50 acres in size $250;

(b) For property 50 + – 100 acres in size $500;

(c) For property 100 + – 500 acres in size $1,000;

(d) For property 500 + – 750 acres in size $2,000;

(e) For property 750 + – 1000 acres in size $2,500;

(f) For property greater than 1000 acres in size – $2,500 (plus $500 for each 500 acres over 1000 acres, up to a maximum of $10,000);

(g) If the environmental complexity of the area requires extensive evaluation, the Department may charge additional fees based on the actual salary rate of the staff who provide the services, plus the actual expenses of the Department. However, the total fees may not exceed $10,000;

(h) The fee for a later petition for a jurisdictional declaratory statement on property for which a jurisdictional declaratory statement exists and which requires minimal field investigation by the Department is $250.

(6)(a) Within 30 days of the receipt of a petition for a jurisdictional declaratory statement, the Department shall notify the applicant of any additional information which may be necessary. The Department shall complete the assessment and issue notice of the proposed agency action within 60 days of receipt of a complete petition. The notice shall be published by the petitioner in a newspaper of general circulation in the area affected. The provisions of Sections 120.569 and 120.57, F.S., are applicable to declaratory statements under this section. Any person whose substantial interests will be affected may petition for a hearing within 14 days after the publication of notice. If no petition for a hearing is filed, the Department shall issue the jurisdictional declaratory statement within 10 days after termination of the 14-day waiting period.

(b) A jurisdictional declaratory statement is binding for 5 years, if physical conditions on the site do not change to alter jurisdiction.

(c) A petitioner who disputes the proposed agency action may withdraw the petition without prejudice at any point before final agency action.

(d) The Department may revoke a jurisdictional declaratory statement if it finds that the petitioner has submitted inaccurate information in the petition.

(e) A jurisdictional declaratory statement obtained pursuant to this section is final agency action and is in lieu of a declaratory statement of jurisdiction obtainable pursuant to Section 120.565, F.S.

(7) The Department also may issue informal preapplication jurisdictional determinations or otherwise institute jurisdictional determinations on its own initiative as provided by law.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.817, 403.912, 403.913, 403.914 FS. History –New 10-16-84, Amended 3-26-89, Formerly 17-12.040, Amended 3-12-90, 9-8-92, Formerly 17-312.040.

## 62-312.045 Jurisdictional Intent.

The Department recognizes that the natural border of certain water bodies listed in Rule 62-312.030, F.A.C., may be difficult to establish because of seasonal fluctuations in water levels and other characteristics unique to a given terrain. The intent of the vegetation indices in Rules 62-301.400 and subsection 62-301.200(3), F.A.C., is to guide in the establishment of the border of the water bodies listed in Rule 62-312.030, F.A.C. It is the intent of this section to include, in the boundaries of such water bodies, areas which are customarily submerged and which are contiguous to a recognizable water body (i.e., areas within the landward extent of waters of the state as defined in subsections 62-301.200(3) and (4), F.A.C.). Isolated areas that infrequently flow into or otherwise exchange water with a described water body are not intended to be included within the dredge and fill jurisdiction of the Department. The vegetation indices in subsection 62-301.200(3) and Rule 62-301.400, F.A.C., are presumed to accurately delineate the landward extent of such water bodies.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.031, 403.061, 403.062, 403.087, 403.912 FS., Section 9, Chapter 84-79, Laws of Florida. History–New 12-10-84, Amended 3-26-89, Formerly 17-12.045, 17-312.045.

## 62-312.050 Exemptions.

(1) No permit shall be required under this chapter for dredging or filling specified in Section 403.813(1), F.S., except for those projects which are subject to one or more of the general permits in Part V of Chapter 62-312, F.A.C. No permit under this chapter shall be required for dredging or filling authorized by paragraphs 62-4.040(1)(a) or (b), F.A.C., or for dredging or filling which has been approved pursuant to Chapter 62-17, 62-23, or 62-45, F.A.C., or for the projects listed below.

(a) The installation of overhead transmission lines where the support structures are not constructed in waters of the state and which do not create a navigational hazard.

(b) The installation of aids to navigation, including bridge fender piles, “No Wake” and similar regulatory signs, and buoys associated with such aids, provided that the devices are marked pursuant to Section 327.40, F.S.

(c) The installation and repair of mooring pilings and dolphins associated with private docking facilities.

(d) The installation of private docks of 500 square feet or less of surface area over the landward extent of waters of the State or 1000 square feet or less of surface area over the landward extent of waters of the State for docks which are not located in Outstanding Florida Waters and any of which:

1. Is used for recreational, non-commercial activities, associated with the mooring or storage of boats and boat paraphernalia; and

2. Is constructed or held in place by pilings, including floating docks, so as not to involve filling or dredging other than that necessary to install the pilings; and

3. Does not substantially impede the flow of water or create a navigational hazard; and

4. Is the sole dock constructed pursuant to this exemption as measured along the shoreline for a minimum distance of 65 feet, unless the parcel of land or individual lot as platted is less than 65 feet in length along the shoreline, in which case there may be one exempt dock allowed per parcel or lot. For the purposes of this section, multi-family living complexes and other types of complexes or facilities associated with the proposed private dock shall be treated as one parcel of property regardless of the legal division of ownership or control of the associated property. Construction of a private dock under this exemption does not require the Department to issue a subsequent permit to construct a channel to provide navigational access to the dock. Activities associated with a private dock shall include the construction of structures attached to the pier which are only suitable for the mooring or storage of boats (i.e., boatlifts).

(e) The performance of maintenance dredging of existing manmade canals, channels, and intake and discharge structures, where the spoil material is to be removed and deposited on a self-contained, upland spoil site which will prevent the escape of the spoil material and return water from the spoil site into surface waters of the state, provided no more dredging is performed than is necessary to restore the canal, channels, and intake and discharge structures to original design specifications, and provided that control devices are used at the dredge site to prevent turbidity and toxic or deleterious substances from discharging into adjacent waters during maintenance dredging. This exemption shall apply to all canals constructed before April 3, 1970, and to those canals constructed on or after April 3, 1970, pursuant to all necessary state permits. This exemption shall not apply to the removal of a natural or manmade barrier separating a canal or canal system from adjacent waters of the state. Where no previous permit has been issued by the Board of Trustees of the Internal Improvement Trust Fund or the United States Army Corps of Engineers for construction or maintenance dredging of the existing manmade canal or intake or discharge structure, such maintenance dredging shall be limited to a depth of no more than 5 feet below mean low water.

(f) The installation and maintenance to design specifications of boat ramps on artificial bodies of water where navigational access to the proposed ramp exists, or the installation and maintenance to design specifications of boat ramps open to the public in any waters of the state where navigational access to the proposed ramp exists and where construction of the proposed ramp will be less than 30 feet wide and will involve the removal of less than 25 cubic yards of material from the waters of the state. All material removed shall be placed upon a self-contained upland site so as to prevent the escape of the spoil material and return water from the spoil site into the waters of the state. For the purpose of this exemption, artificial bodies of water shall include, but not be limited to, residential canal systems, canals permitted by a water management district created under Section 373.069, F.S., and artificially created portions of the Florida Intracoastal Waterway.

(g) Construction of seawalls or riprap, including only that backfilling needed to level the land behind the seawalls or riprap, in artificially created waterways where such construction will not violate existing water quality standards, impede navigation or adversely affect flood control. An artificially created waterway shall be defined as a body of water that has been totally dredged or excavated and which does not overlap natural surface waters of the state. For the purpose of this exemption, artificially created waterways shall also include existing residential canal systems. This exemption does not apply to the construction of vertical seawalls in estuaries or lagoons unless the proposed construction is within an existing man-made canal where the shoreline is currently occupied in whole or in part by vertical seawalls.

(h) Construction of private docks in artificially created waterways (as defined in paragraph 62-312.050(1)(g), F.A.C.) where construction will not violate water quality standards, impede navigation, or adversely affect flood control.

(i) The replacement or repair of private or commercial docks provided that no fill material other than the dock pilings is to be used, and provided that the replacement or the repaired dock is in the same location and of the same configuration and dimensions as the dock being replaced or repaired. A dock must be functional and able to provide access to a boat or boats moored at the dock before this exemption may be used.

(j) The restoration of a seawall or riprap at its previous location or upland of or within one foot waterward of its previous location. No filling can be performed except in the actual restoration of the seawall or riprap. No construction shall be undertaken without necessary title or leasehold interest, especially where private and public ownership boundaries have changed as a result of natural occurrences such as accretion, reliction and natural erosion. Restoration and repair shall be performed using the criteria set forth in Section 403.918(5), F.S. (Supp. 1992). This exemption shall be limited to functioning seawalls or riprap where there is no exchange of waters through or around the seawall or riprap of sufficient quantity, duration or frequency so that the restoration of the seawall or riprap could cause or contribute to a violation of state water quality standards or other criteria listed in Section 403.918, F.S. (Supp. 1992). This exemption does not constitute an exception from the permitting requirements of Chapter 161, F.S.

(k) The maintenance of functioning insect control structures, dikes and irrigation and drainage ditches, provided that spoil material is deposited on a self-contained upland spoil site which will prevent the escape of the spoil material and return water into surface waters of the state. In the case of insect control structures, if the cost of using a self-contained upland spoil site is so excessive as determined by the Department of Health and Rehabilitative Services, pursuant to subsection 403.088(1), F.S., that it will inhibit the proposed insect control, existing spoil sites or dikes may be used, upon notification to the Department. In the case of insect control where upland spoil sites are not used pursuant to this exemption, turbidity control devices shall be used to confine the spoil material discharge to that area previously disturbed when the receiving body of water is used as a potable water supply, is designated as approved waters for shellfish harvesting by the Department of Environmental Protection, or functions as a habitat for commercially or recreationally important shellfish or finfish. In all cases, no more dredging is to be performed than is necessary to restore the dike or irrigation or drainage ditch to its original design specifications. This exemption shall apply to man-made trenches dug for the purpose of draining water from the land or for transporting water for use on the land and which are not built for navigational purposes. This exemption does not include navigable residential canal systems.

(l) Repair or replacement of existing functional pipes or culverts which discharge or convey stormwater, run-off, or drainage; including the repair or replacement of existing functional pipes or culverts which directly discharge or convey stormwater from stormwater treatment and management systems. In all cases, the pipes or culverts shall be repaired or replaced to their previous invert elevations, cross sectional area, and length, however, the material used for the pipe or culvert may be different from the original composition. This exemption does not authorize construction activities or procedures that cause violations of water quality standards as listed in Chapter 62-302, F.A.C., and Rule 62-4.242, F.A.C. Examples of some activities where water quality standards can be expected to be violated include: repair or replacement activities that cause impoundment of water flow; increased flow in downstream waters; increased scour of the waterbody; alterations of the waterbody upstream or downstream of the culvert; dredging to re-align the channel or other channel modifications; work performed without properly installed or maintained turbidity screens or erosion and siltation controls; deposition of spoil materials in jurisdictional waters; or the cleaning, filling, or construction of structures in natural, previously undisturbed jurisdictional waters.

(m) Construction and maintenance of swales.

(n) The construction at electrical power plant sites, including power lines on the power plant sites, which have been approved pursuant to the Florida Electrical Power Plant Siting Act, Chapter 403, Part II, F.S., where dredging and filling activities have been reviewed and approved as part of the site certification.

(o) For activities grandfathered pursuant to Rules 62-312.150 and 62-312.160, F.A.C., the deposition of up to and including 25 cubic yards of material in areas of waters of the state where transitional vegetation species, as described in subsection 62-301.200(3), F.A.C., are the dominant species, except in Class II waters. No person shall be entitled to more than one exemption under this provision every six months. If at any time the Department determines that the cumulative effect of successive filling by a person either under this provision or under some other provision of this section may have a significant effect on water quality, it may suspend the application of this exemption provision to that person by notifying him in writing.

(p) The construction of, or dredging or filling in, artificial waterways, except in Class II waters, behind control structures permitted by a water management district created under Section 373.069, F.S., except those:

1. To be used for residential purposes; or

2. Which directly connect to works of said water management district; or

3. To be constructed in waters of the state.

(q) The construction of, or dredging or filling in, highway drainage ditches and artificial waterways, except in Class II waters, which are not used for residential purposes, and which serve as artificial tributaries only following the occurrence of rainfall and which normally do not contain contiguous areas of standing water.

(r) The installation of subaqueous transmission and distribution lines laid on, or embedded in, the bottoms of waters of the State, except in Class I and Class II waters and aquatic preserves provided that no dredging or filling is necessary.

(s) The replacement or repair of subaqueous transmission and distribution lines laid on, or embedded in, the bottoms of waters of the State.

(t) The construction of vertical seawalls in waters of the State, other than in an estuary or lagoon, and the construction of riprap revetments, where such construction is between and adjoins at both ends existing seawalls or riprap, follows a continuous and uniform construction line with the existing seawalls or riprap, is no more than 150 feet in length, and does not violate existing water quality standards, impede navigation, or adversely affect flood control. However, this shall not affect the permitting requirements of Chapter 161, F.S. Construction shall be in accordance with Section 403.918(6), F.S. (Supp. 1992).

(u) The replacement or repair of open-trestle foot bridges and vehicular bridges that are 100 feet or less in length and two lanes or less in width, provided that no more dredging or filling is performed than that necessary to replace or repair pilings, and that the structure to be replaced or repaired is the same length, the same configuration, and in the same location as the original bridge. No debris from the original bridge shall be allowed to remain in waters of the State.

(v) The restoration of less than 100 feet in length of insect control impoundment dikes and the connection of such impoundments to tidally influenced waters. Such impoundments shall be connected to tidally influenced waters for at least 6 months each year, beginning September 1 and ending February 28 if feasible, or operated in accordance with an impoundment management plan approved by the Department. The connection shall be of sufficient cross-sectional area to allow beneficial tidal influence. Restoration shall involve no more dredging than needed to restore the dike to original design specifications, and such that the final elevation of the dredge area shall be within 2 feet of immediately adjacent bottom elevations. For the purposes of this paragraph, restoration shall not include maintenance of impoundment dikes of insect control impoundments.

(2) Where a water management district has been delegated stormwater permitting by the Department, no dredge or fill permit is required for the construction of, and dredging and filling in, irrigation or drainage ditches constructed in the uplands, including those connecting otherwise isolated areas owned entirely by one person and dominated by the plant indicator species in Rule 62-301.400, F.A.C. This exemption only applies to a ditch for which the point of connection to other waters of the state is no more than 35 square feet in total cross-sectional area and which normally has a water depth of no more than 3 feet. The total cross-sectional area at the point of connection to other waters of the state shall be maintained by the landowner so as not to exceed the design limitations of this exemption. This exemption does not authorize dredging in waters of the state other than in ditches as described in this subsection. All applicable permits except dredge and fill permits are required for discharges to these ditches or connected areas. This exemption does not apply to ditches in or connected to the waters described in Sections 403.031(13)(a) and (b), F.S. (1991), Outstanding Florida Waters, Class I waters, or Class II waters.

(3) No permit under this chapter shall be required for agricultural activities or agricultural water management systems regulated by Water Management Districts. The Department may require a stormwater permit or appropriate discharge permit at the ultimate point of discharge from an agricultural water management system or a group of connected agricultural water management systems. If land served by a water management system is converted to a use other than an agricultural use, the water management system, or the portion of the system which serves that land, will be subject to the provisions of this chapter.

(4) No permit under this chapter shall be required for dredging or filling in waters which are contained in those artificially constructed stormwater treatment and conveyance systems designed solely for the purpose of stormwater treatment and that are regulated by the Department or the water management district.

(5) Where stormwater permitting is delegated to a water management district, no permit under this Chapter shall be required for dredging or filling which is required to connect stormwater management facilities to waters and which is incidental to the construction of such stormwater management facilities. Incidental dredging or filling shall include:

(a) Headwalls and discharge structures;

(b) Erosion control devices or structures to dissipate energy which are associated with discharge structures;

(c) Outfall pipes less than 20 feet in length in waters provided the pipe does not interfere with navigation;

(d) The connection of ditches dug through the uplands where the dredging or filling for the connection to waters extends less than 20 feet in length in waters; and

(e) Other dredging or filling which the Department determines will have a similar effect as those activities listed above.

(6) The performance of work pursuant to the provisions of the exemptions described above does not relieve an applicant from meeting the permitting or performance requirements of other Department sections. Nothing in this section shall prohibit the Department from taking appropriate enforcement action to abate or prohibit any activity otherwise exempt from permitting pursuant to this section if the Department can demonstrate that the exempted activity has caused water pollution in violation of Chapter 403, F.S. All works pursuant to the exemptions in this section shall be constructed so as to not violate water quality standards.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.031, 403.061, 403.161, 403.812, 403.813, 403.912, 403.913, 403.918 FS. History–New 12-10-84, Amended 11-11-85, 8-30-88, 3-26-89, Formerly 17-12.050, Amended 3-12-90, 7-11-90, 4-12-92, Formerly 17-312.050.

## 62-312.060 Procedures to Obtain a Permit.

(1) Unless specifically exempt, permits shall be required for dredging or filling, including but not limited to construction of: artificial reefs, groins, jetties, breakwaters, riprap or seawalls, revetments and similar type structures; marinas, docks, wharfs, piers, marine railroads, walkways, mooring pilings, dolphins and similar structures; boat ramps, lifts or similar launching facilities; ski ramps or other similar structures; utility installations, navigational aids, commercial signs or similar obstructions; canals, canal locks, bridges or similar crossing structures; as well as dredging or excavating by any means and filling or placing of material in, on or over waters of the state listed in Rule 62-312.030, F.A.C.

(2) Application for a permit shall be made on forms prescribed by the Department and listed in subsection 62-312.900(1), F.A.C., and shall be accompanied by the appropriate processing fee as listed in Rule 62-4.050, F.A.C. Any application for a permit to dredge or fill shall constitute an application for certification of compliance with state water quality standards where necessary. Similarly, an application for certification shall constitute an application for permit.

(3) Applications for short-term dredge or fill permits pursuant to Rule 62-312.070, F.A.C., shall be filed with the appropriate Department district office, and shall be processed and issued by that office. Applications for other permits to dredge or fill shall be filed with the Bureau of Wetland Resource Management in Tallahassee. See Chapter 62-101, F.A.C., for locations and addresses of Department offices. All applications and supporting documents shall be filed in quadruplicate.

(4) To ensure protection of public health, safety and welfare, all engineering drawings and related materials, as defined by Chapter 471, F.S., provided with the application shall be signed and sealed by a professional engineer in accordance with Chapter 471, F.S. and subsection 62-4.050(3), F.A.C. Any land survey associated with an application shall be certified by a registered land surveyor in accordance with Chapter 472, F.S.

(5) Within thirty days after receipt of an application for permit or receipt of additional information, the Department shall examine the application or information, notify the applicant of any apparent errors or omissions, and request any additional information needed to clarify the information on the application or in a subsequent submittal. The applicant shall have ninety days after the Department mails a timely request for additional information to submit that information to the Department. If an applicant requires more than ninety days in which to respond to a request for additional information, the applicant may notify the Department in writing of the circumstances, at which time the application shall be held in active status for one additional period of up to ninety days. Additional extensions shall be granted for good cause shown by the applicant. A showing that the applicant is making a diligent effort to obtain the requested additional information shall constitute good cause. Failure of an applicant to provide the timely requested information by the applicable deadline shall result in denial of the application. Requests for additional information shall be governed by Section 403.0876, F.S. Additional information which may be required to evaluate an application includes but is not limited to:

(a) A hydrographic study or hydrologic evaluation, prepared under the supervision of the Department, which will demonstrate the flow of water, predict the effect of the proposed dredging or filling on the flow of water, predict areas of erosion or shoaling, predict the effect of the proposed dredging or filling on water quality and water resources; and

(b) Sampling and test analyses of ambient water or sediments, core borings, surveys of existing resources such as grassbeds and other habitats, or any other information necessary to evaluate the proposed dredging or filling in accordance with Sections 403.918, F.S. (Supp. 1992) and 403.919, F.S. (1991).

(6) The Department shall notify the applicant if the dredging or filling for which a permit is sought is exempt from permitting. The notice shall be given within 30 days of receipt of the original application or within 10 days of receipt of additional information which demonstrates to the Department that the proposed dredging or filling is exempt. Upon determination that a dredging or filling activity is exempt from permitting, the Department shall refund the application processing fee.

(7) Upon receipt of an application for a permit, the Department shall forward a copy of the application:

(a) Within 24 hours, to the appropriate office of the U.S. Army Corps of Engineers unless specifically authorized by the Corps to do otherwise; and

(b) Within 10 days by certified mail, to the chief executive officer of each county and municipality which has jurisdiction over the area for which a permit is requested.

(8) If at any time during processing of the application it appears that the dredging or filling may take place on state-owned lands, the District Office shall send a copy of the application to the Division of State Lands, Department of Environmental Protection.

(9) Upon receipt of a complete application, including any timely requested additional information, the Department shall forward a copy of the application to and request comments from:

(a) The Florida Fish and Wildlife Conservation Commission for all standard form applications; and

(b) Any other persons who have asked for a copy of the application.

(10) During the processing of the permit application, the Department shall determine whether or not the application, as submitted, meets the criteria contained in Sections 403.918(1) and (2)(a)1.-7., F.S. (Supp. 1992) and 403.919, F.S. (1991) If the project, as designed, fails to meet the permitting criteria, the Department shall discuss with the applicant any modifications to the project that may bring the project into compliance with the permitting criteria. The applicant shall respond to the Department, in writing, as to whether or not the identified modification to the proposed project is practicable and whether the applicant will make the identified modification. The term “modification” shall not be construed as including the alternative of not implementing the project in some form. When the Department determines that the project, as submitted or modified, fails to meet the criteria contained in Sections 403.918(1) and (2)(a)1.-7., F.S. (Supp. 1992) and 403.919, F.S. (1991), the applicant may propose mitigation measures to the Department as provided in Chapter 62-312, Part III, F.A.C. Nothing herein shall imply that the Department may not deny an application for a permit, as submitted or modified, if it fails to meet the criteria in Section 403.918(2)(a), F.S. (Supp. 1992), or that mitigation must be accepted by the Department.

(11) If a certification or permit application is made for a dredging or filling activity in Class I waters which are the source of water for a potable water system, the person or legal entity using the waters for such system shall be notified by the Department and shall be given an opportunity to comment on the proposed dredging or filling activity.

(12) The Department shall forward a copy of the application to and request comments from the adjacent waterfront property owners unless the number of adjacent waterfront property owners is so extensive that personal notice is impractical. In those cases, the Department shall require the applicant to publish either the Notice of Application or the Notice of Proposed Agency Action on Permit Application pursuant to Rule 62-110.106, F.A.C. The notice of application shall be published within 14 days after a complete application is filed with the Department, unless the names of the adjacent owners are not properly provided by the applicant, in which case the Department may require publication within 14 days after such timely requested information is received.

(13) Applications for permits processed pursuant to Rules 62-312.010 through 62-312.110, F.A.C., shall be approved or denied within 90 days after receipt of the original application, or receipt of the timely requested additional information, or corrections of errors or omissions. The 90-day period shall be tolled by initiation of a proceeding pursuant to Sections 120.569 and 120.57, F.S., or by request for publication of public notice pursuant to Section 403.815, F.S., and Rule 62-110.106, F.A.C., or by request for a soils assessment pursuant to Section 403.913(3), F.S. (1991). Any application for a permit that is not approved or denied within the time prescribed by Sections 120.60 and 403.815, and 403.0876, F.S., shall be deemed approved in accordance with subsection 120.60(2), F.S.

(14) Applicants shall publish a Notice of Application or a Notice of Proposed Agency Action on a Permit Application if required by Rule 62-110.106, F.A.C., and Section 403.815, F.S.

(15) An applicant may request a zone of mixing in accordance with Rule 62-4.244, F.A.C.

(16) Each application for a permit shall be accompanied by a processing fee, except for applications filed by departments of the executive branch established pursuant to Chapter 20, F.S., and water management districts established pursuant to Chapter 373, F.S. The check shall be made payable to the Department of Environmental Protection. The processing fee is non-refundable except as provided for in Section 120.60, F.S., and in this section. Processing fees are as set forth in Rule 62-4.050 F.A.C.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.813, 403.912, 403.913, 403.919, 403.921, 403.922, 403.923, 403.927 FS. History–New 10-16-84, Amended 8-28-85, 1-3-89, 3-26-89, Formerly 17-12.060, 17-312.060, Amended 8-16-98.

## 62-312.065 Additional Requirements and Procedures for Concurrent Review of Related Applications.

(1) A single application shall be submitted and reviewed for activities that require a short form wetland resource (dredge and fill) permit under subsections 373.414(11), (12), (13), (14), (15), or (16), F.S., or Section 373.4145, F.S., and a proprietary authorization under Chapter 253 or 258, F.S., to use sovereign submerged lands. In such cases, the application shall not be deemed complete, and the timeframes for approval or denial shall not commence, until all information required by applicable provisions of subsections 373.414(11), (12), (13), (14), (15), or (16), F.S., or Section 373.4145, F.S., and the proprietary authorization under Chapters 253 or 258, F.S., and rules adopted thereunder for both the short form or standard form wetland resource permit and the proprietary authorization is received.

(2) No application under this section shall be approved until all the requirements of applicable provisions of subsections 373.414(11), (12), (13), (14), (15), or (16), F.S., or Section 373.4145, F.S., and the proprietary authorization under Chapter 253 or 258, F.S., and rules adopted thereunder for both the short form or standard form wetland resource permit and the proprietary authorization are met. The approval shall be subject to all permit conditions imposed by such rules.

(3) For an application reviewed under this section for which a request for proprietary authorization to use sovereign submerged lands has been delegated to the Department or a water management district to take final action without action by the Board of Trustees of the Internal Improvement Trust Fund, the Department or water management district shall issue a consolidated notice of intent to issue or deny the wetland resource permit and the proprietary authorization within 90 days of receiving a complete application under this section. Waiving or tolling the timeframes for final action on the application under this section shall constitute a waiver or tolling of the timeframes for the wetland resource permit application.

(4) For an application reviewed under this section for which the request for proprietary authorization to use sovereign submerged lands has not been delegated to the Department or a water management district to take final action without action by the Board of Trustees of the Internal Improvement Trust Fund, the application shall be reviewed and final agency action taken in accordance with the procedures in paragraphs 373.427(2)(a)-(c), F.S.

(5) The issuance of the consolidated notice of intent to issue or deny, or upon issuance of the recommended consolidated notice of intent to issue or deny pursuant to subsection (4), the Department or water management district shall be deemed to be in compliance with the timeframes for approval or denial in Section 120.60(1), F.S. Failure to satisfy these timeframes shall not result in approval by default of the application to use sovereign submerged lands. Also, if an administrative proceeding under Section 120.57, F.S., is properly requested on both the wetland resource permit and the proprietary authorization under this section, the review shall be conducted as a single consolidated administrative proceeding. If an administrative proceeding under Section 120.57, F.S., is properly requested on either the wetland resource permit or the proprietary authorization under this section, final agency action shall not be taken on either authorization until the administrative proceeding is concluded.

(6) Appellate review of any consolidated order under this section is governed by the provisions of Section 373.4275, F.S.

(7) For an activity requiring an individual permit under Section 161.041, F.S., and a short form or standard form wetland resource (dredge and fill) permit under subsections 373.414(11), (12), (13), (14), (15), or (16), F.S., or Section 373.4145, F.S., a joint coastal permit shall be required, as provided in Chapter 62B-49, F.A.C., in place of the above noted permits.

(8) This section shall be applicable to all applications for wetland resource permits under subsections 373.414(11), (12), (13), (14), (15), or (16), F.S., or Section 373.4145, F.S., and proprietary authorizations under Chapter 253 or 258, F.S., to use sovereign submerged lands, that are received by the Department, Suwannee River Water Management District, St. Johns River Water Management District, Southwest Florida Water Management District or South Florida Water Management District after the effective date of this rule section. If an applicant requests that its applications for wetland resource permits under subsections 373.414(11), (12), (13), (14), (15), or (16), F.S., or Section 373.4145, F.S., and proprietary authorization under Chapter 253 or 258, F.S., to use sovereign submerged lands, received prior to the effective date of this rule section, be processed under this rule section, such request shall be granted if the applications for both are incomplete as of the effective date of this rule section.

(9) Nothing in this section shall be construed to limit an applicant’s ability to make separate applications for stages, phases, or portions of a project separate from an activity requiring both a standard form or short form wetland resource permit under subsections 373.414(11), (12), (13), (14), (15), or (16), F.S., or Section 373.4145, F.S., and a proprietary authorization under Chapter 253 or 258, F.S.

(10) The provision of this Section shall also apply to the Suwannee River Water Management District, St. Johns River Water Management District, Southwest Florida Water Management District and South Florida Water Management District when such Districts are processing a standard form or short form wetland resource permit application under subsections 373.414(11), (12), (13), (14), (15) or (16), F.S., or Section 373.4145, F.S., which, under this section, also requires a proprietary authorization under Chapters 253 or 258, F.S.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 120.60, 161.041, 161.055, 253.03, 253.77, 258.42, 258.43, 373.414(11)-(16), 373.4145, 373.427, 373.4275, 403.061 FS. History–New 10-12-95.

## 62-312.070 Short Form Applications for Certain Dredging or Filling.

(1) Applicants for the types of dredging or filling listed in subsection (2) below shall make application on Form 62-312.900(1), F.A.C., to the district office serving the area in which the dredging or filling is proposed. One or more of the types of dredging or filling listed below may be combined in one application. If any portion of the proposed dredging or filling exceeds any of the following criteria for a short form application, the application shall be processed as a standard form application by the Bureau of Wetland Resource Management and the appropriate standard form (Bureau Review) fee shall be applied. The filing of successive short form (District Review) applications within three years which results in the total scope of the dredging and filling exceeding any of the following short form criteria, shall result in the succeeding applications being processed as a standard form application. Once processing of a standard form application has begun by the Bureau of Wetland Resource Management, the Bureau shall continue to process the application whether or not subsequent changes or modifications to the project would otherwise reduce the project to meet the short form criteria, unless the project is subsequently delegated to the Districts for review by the Secretary or his designee pursuant to agreement by the Department and the applicant. If at any time during the review of a short form application the Department determines that the project exceeds the short form criteria listed in subsection (2), the application shall be transferred to the Bureau and processed as a standard form application unless continued processing of the application is delegated to the Districts by the Secretary or by his Designee, and the appropriate processing fee shall be required.

(2) Dredging or filling in, on or over waters of the state, including construction over waters of the state which is associated with the dredging or filling for which a short form application shall be used:

(a) Except for dredging or filling associated with mosquito control activities, projects which affect a total of less than 10 acres of jurisdictional waters of the state. For the purposes of subsection (2), “affect” shall be defined as directly dredging or filling in jurisdictional areas, severing jurisdictional waters from other waters of the state, or creating new jurisdictional waters of the state, and shall not include mitigation activities determined to be appropriate by the Department.

(b) New docking facilities which:

1. Total less than 10 wet slips, and are not associated with facilities which are commercial or provide supplies or services required for boating activities; or

2. Consist of the addition of not more than 20 docking slips to existing functional docking facilities where the total facility will not exceed 50 slips and the existing and proposed slips are not associated with commercial facilities or facilities which provide supplies or services required for boating activities; or

3. Consist of modifications to a maximum of 10 existing functional slips, regardless of the size of the existing facility, providing that the modifications do not result in the addition of new commercial slips or new slips which provide supplies or services required for boating activities.

For the purposes of paragraph (b), commercial dockage facilities shall not include those associated with non water-related facilities such as restaurants, office parks, or other similar establishments which do not provide supplies or services required for boating activities.

(c) New riprap of any length, and new vertical seawalls, bulkheads, or similar shoreline protection structures which do not exceed 500 linear feet of shoreline.

(d) The installation of buoys, aids to navigation, signs, fences, and ski ramps, and the installation of fish attractors by the Florida Game and Fresh Water Fish Commission.

(e) Dredging or filling associated with salvage operations, including treasure salvage, regardless of the area affected.

(f) Dredging or filling associated with bridge demolition activities not previously authorized by a currently valid Department permit.

(g) The installation of subaqueous transmission and distribution lines laid on or embedded (as defined in subsection 62-312.020(7), F.A.C.) in the bottoms of waters of the state, carrying water, wastewater, electricity, communication cables, oil or gas, except as exempted by paragraph 62-312.050(1)(r) or (s), F.A.C.

(h) The construction of artificial reefs regardless of the amount of filling involved.

(i) Any other project or category of project delegated by the Secretary or his designee for short form review which could be reviewed more appropriately by the District office, due to reasons such as: extensive consultations or preapplication meetings between the district and the applicant prior to submittal of an application; extensive knowledge of a site or history of a project by district staff; or prior involvement with the district on previous, related phases of a multi-phase project; and the project does not consist of unique or unusual circumstances which may affect other properties or types of projects outside of the district. In such cases where the project is delegated by the Secretary for processing by the district, the fee shall remain unchanged from the fee otherwise appropriate for the project.

(3) Notwithstanding the provisions of subsection (2) above, any project which may be more appropriately processed by the Bureau of Wetland Resource Management, for reasons such as: the project has the potential to affect other projects or properties outside of the district; the project has the potential for large scale environmental effects that transcend county, district, or state boundaries; the project involves extensive multi-agency coordination which could best be accomplished by processing at the Bureau level; the project involves unproven technology or experimental procedures that will require statewide oversight or extensive multi-agency coordination; or the project has been the subject of extensive prior consultations or preapplication meetings between Bureau staff and the applicant prior to submittal of the application; then the project shall be assigned by the Secretary or his designee, to be processed by the Bureau provided that the fee shall remain unchanged from the fee otherwise appropriate for the project.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.813, 403.911, 403.912 FS. History–New 10-16-84, Amended 3-26-89, Formerly 17-12.090, Amended 3-12-90, 4-12-92, Formerly 17-312.070.

## 62-312.080 Standards for Issuance or Denial of a Permit.

(1) In accordance with Section 403.918(1), F.S. (Supp. 1992), no permit shall be issued unless the applicant has provided the Department with reasonable assurance based on plans, test results or other information that the proposed dredging or filling will not violate water quality standards.

(2) No permit shall be issued unless the applicant provides the Department with reasonable assurance based on plans, test results or other information that the project is not contrary to the public interest in accordance with Section 403.918(2), F.S. (Supp. 1992).

(3) No permit shall be issued for dredging or filling which significantly degrades or is within an outstanding Florida Water unless the applicant complies with Section 403.918(2), F.S. (Supp. 1992), and Rule 62-4.242, F.A.C.

(4) A permit may contain specific conditions reasonably necessary to assure compliance with Section 403.918, F.S. (Supp. 1992)

(5) The Department may deny a permit in accordance with Section 120.60, F.S., if the applicant fails to correct errors or omissions, or to supply additional information requested by the Department, or to publish a required public notice within the time set forth in a notice of intent to deny the permit.

(6) The Department recognizes the special value and importance of Class II waters to Florida’s economy as existing or potential sites of commercial and recreational shellfish harvesting and as a nursery area for fish and shellfish.

(a) Accordingly, the Department shall deny a permit for dredging or filling in Class II waters which are not approved for shellfish harvesting unless the applicant submits a plan or proposes a procedure to protect those waters and waters in the vicinity. The plan or procedure shall detail the measures to be taken to prevent significant damage to the immediate project area and to adjacent areas and shall provide reasonable assurance that the standards for Class II waters will not be violated.

(b) The Department also shall deny a permit for dredging or filling in any class of waters where the location of the project is adjacent or in close proximity to Class II waters, unless the applicant submits a plan or proposes a procedure which demonstrates that the dredging or filling will not have a negative effect on the Class II waters and will not result in violations of water quality standards in the Class II waters.

(7) Permits for dredging or filling directly in Class II or Class III waters which are approved for shellfish harvesting by the Department of Agricultural and Consumer Services shall not be issued. However, the Department may issue permits or certifications for maintenance dredging of navigational channels, the construction of shoreline protection structures, the installation of transmission and distribution lines for carrying potable water, electricity or communication cables in rights-of-way previously used for such lines, for clam and oyster culture, and for private, single family boatdocks that meet the following Department of Environmental Protection criteria for installation in Class II or Class III waters approved for shellfish harvesting:

(a) There shall be no more than two boats moored at the dock;

(b) No overboard discharges of trash, human or animal waste, or fuel shall occur at the dock;

(c) Any non-water dependent structures, such as gazebos or fish cleaning stations, shall be located on the uplands;

(d) Prior to the mooring of any boat at the dock, there shall be existing structures with toilet facilities located on the uplands;

(e) Any proposed shelter shall have enclosed sides;

(f) The mooring area shall be located in waters sufficiently deep to prevent bottom scour by boat propellers; and

(g) Any structures located over grassbeds shall be designed so as to allow for the maximum light penetration practicable.

(8)(a) For phosphate mining which occurs within the Southwest Florida Water Management District and which is exempt from its permitting requirements pursuant to subsection 40D-4.051(9), F.A.C., no permit shall be issued unless the applicant provides reasonable assurance that the activity will be in compliance with the substantive requirements of Chapter 373, Part IV, F.S., as implemented by paragraphs 40D-4.031(1)(a), (b), (d), (l), (2)(a), (b), (d), (g), (h), (j), (m) and (n), F.A.C., except that paragraphs (1)(d) and (2)(d) apply within the mine only after the completion of mining and reclamation of the permitted dredge and fill project site.

(b) Applicants for a permit covered by Paragraph (a) above, shall submit, in addition to the information required by DEP form 62-312.900(1), information which is applicable to the paragraphs cited in paragraph (a) above. The applicant shall submit seven copies of the application and all supporting information.

(c) This subsection (62-312.080(8), F.A.C.), does not apply to activities for which a complete application was filed with the Department before October 1, 1986.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.042, 373.403, 373.413, 373.414(11)-(16), 373.4145, 373.416, 373.426, 403.031, 403.061, 403.815, 403.912, 403.913, 403.918, 403.919 FS. History–New 12-10-84, Amended 10-15-86, 3-26-89, Formerly 17-12.070, Amended 10-13-92, Formerly 17-312.080.

## 62-312.082 Duration of Permits.

(1) Permits for dredging or filling under Rules 62-312.010 through 62-312.110, F.A.C., shall not be valid for more than 10 years. The Department may issue a permit for less than 10 years if the proposed dredging or filling will require less than 10 years to complete or if the applicant does not provide sufficient information to accurately assess the effects of the dredging or filling for a ten-year period. All Department wetland resource permits issued under Rules 62-312.010 through 62-312.110, F.A.C., shall be effective on the date of execution by the Department.

(2) Permits for maintenance dredging, including snagging operations, of river channels which are not part of a deepwater port as defined in Chapter 62-45, F.A.C., shall not be valid for more than five years.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.816, 403.912, 403.921 FS. History–New 10-16-84, Formerly 17-12.072, Amended 3-26-89, 12-17-90, Formerly 17-312.082.

## 62-312.085 Periodic Review of Permits.

(1) Pursuant to subsection 403.921(1), F.S. (1991), the Department shall review each permit that is issued for more than 5 years at the end of the first 5-year period and each subsequent 5-year period thereafter, if applicable. The Department review shall begin 90 days before the end of the 5-year period and shall include a notice to the permittee. The Department shall review the file and inspect the project site for compliance with the terms of the permit, including the General and Specific Conditions and Monitoring Requirements.

(2) If the Department determines that the permittee is not in compliance with the terms of the permit, revocation or suspension of the permit may be initiated pursuant to Rule 62-4.100, F.A.C.

(3) As an element of the five-year periodic review, the Department shall notify the permittee of any additional permit conditions to be added to the original permit based on sections adopted during the preceding five-year period.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.912, 403.921 FS. History–New 10-16-84, Amended 3-26-89, Formerly 17-12.075, 17-312.085.

## 62-312.090 Emergency Classification and Procedures.

Special consideration shall be given to the following emergency situations:

(1) Class A.

(a) Those emergencies which involve the loss of human life, limb, or property due to calamitous occurrences such as but not limited to hurricanes, tornadoes, fires, floods, high winds, or the breaks of dams or levees.

(b) No permit shall be required for temporary measures taken to correct or give relief from Class A emergencies. Immediately after the occurrence of a Class A emergency, the appropriate district office of the Department shall be notified of the emergency. Within 14 calendar days after the correction of the emergency, a report to the district office of the Department shall be made outlining the details of the emergency and the steps taken for its temporary relief. The report shall be a written description of all of the work performed involving dredge and fill activities and shall set forth any pollution control measures which were used or are being used to prevent pollution of waters of the state. A permit shall be required in connection with dredge and fill activities for permanent measures in relief of Class A emergencies.

(2) Class B.

(a) Other disasters such as but not limited to bridge collapses, sudden and unpredictable structural collapses, and sudden and unpredictable hazards to navigation which do not threaten the immediate loss of life or property but will require immediate action for relief.

(b) No permit shall be required for temporary measures needed to correct or give relief from Class B emergencies. Temporary measures shall be limited to only those minimum works required to protect against the potential loss of life, limb, health or property or which immediately threaten plant and animal life. The appropriate district office of the Department shall be notified within 24 hours after occurrence of a Class B emergency, and a written report shall be given within 14 calendar days after the temporary measures are completed. The report shall be a written description of all works which have been performed as well as the pollution control measures which were used. A permit shall be required in connection with dredge and fill activities for permanent measures taken for the relief of Class B emergencies.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.912 FS. History–New 10-16-84, Amended 3-26-89, Formerly 17-12.080, 17-312.090.

## 62-312.100 Modification of Permits.

In accordance with subsection 62-4.080(2), F.A.C., modifications to an existing, currently valid permit may be requested by the permittee. The Department will determine whether the requested modification is minor or major based on the magnitude and nature of the proposed change and the potential for environmental effects different from those previously determined for the project. Minor modifications shall be requested by letter, with revised drawings attached as appropriate. Minor modifications may include time extensions where the total time of the original permit plus the extension remains within the range of time allowed for the fee established in Rule 62-4.050, F.A.C., for the original permit issued. Requests for time extensions which would cause the total time of the original permit plus the extension to exceed the appropriate range of time shall be considered major modifications. Major modifications shall be requested by submittal of a completed application form and the appropriate fee and shall be processed by the Department according to Rules 62-312.060 and .080, F.A.C.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.912, 403.919, 403.921, 403.922, 403.923, 403.924, 403.925, 403.927, 403.929 FS. History–New 10-16-84, Amended 3-26-89, Formerly 17-12.100, 17-312.100.

## 62-312.200 Scope of Part II.

This part shall apply to applications for permits for periods in excess of 10 years, except for maintenance dredging permits processed in accordance with Chapter 62-45, F.A.C. The provisions of this Part shall only apply to activities in the geographical territory of the Northwest Florida Water Management District and to activities grandfathered under Sections 373.414(9), (11), (12)(a), (13), (14), (15) and (16), F.S. Applications shall be processed in accordance with Part I of this chapter except where Part I is in conflict with this Part.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 12-10-84, Amended 3-26-89, Formerly 17-12.200, 17-312.200, Amended 10-3-95.

## 62-312.210 Procedures to Obtain a Long-Term Permit.

(1) Application for permit.

(a) Application for permit under this part shall use DEP Form 62-312.900(1), F.A.C., supplemented with DEP Form 62-312.900(5), F.A.C.

(b) All technical studies and other data collection required to complete the application shall be undertaken at the applicant’s expense. However, the applicant may use any data compiled by others which is pertinent.

(c) An application fee as set forth in Rule 62-4.050, F.A.C., shall accompany the application.

(2) Department review. The Department shall review the application according to Part I of this chapter except that an application for a long-term permit shall be approved or denied within 135 days after receipt of the original completed application, or receipt of the timely requested additional information, or correction of errors or omissions. The 135-day period shall be tolled in accordance with Section 120.60 or 403.815, F.S.

(3) Notice. The applicant shall publish a public notice in accordance with Rule 62-110.106, F.A.C., except that the notice shall be surrounded by a prominent black border with a three-column heading in bold letters:

“Notice of Proposed Agency Action on an Application for a Long Term Permit for (name of applicant)”

The notice shall be prepared by the department following the format set forth in Rule 62-110.106, F.A.C., and shall be paid for by the applicant.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414, 373.4145, 403.815 FS. History–New 10-16-84, Amended 3-26-89, Formerly 17-12.210, 17-312.210, Amended 8-16-98.

## 62-312.220 Standards for Issuance or Denial of a Long-Term Permit.

The standards set forth in Rule 62-312.080, F.A.C., shall apply to long-term permits.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.031, 403.061, 403.912, 403.913, 403.918, 403.919 FS. History–New 12-10-84, Amended 3-26-89, Formerly 17-12.220, 17-312.220.

## 62-312.300 Intent.

The provisions of this part shall only apply to activities in the geographical territory of the Northwest Florida Water Management District and to activities grandfathered under Sections 373.414(9), (11), (12)(a), (13), (14), (15) and (16), F.S.

(1) It is the intent of this section to implement Section 403.918(2)(b), F.S. (Supp. 1992), by establishing criteria to be followed in evaluating proposals to mitigate the adverse impacts of dredging and filling in waters of the state that caused the project to be not permittable.

(2) Part III shall apply to those permit applications submitted pursuant to Sections 403.91-.929, F.S. (1991), and Chapter 62-312, F.A.C. Part III shall not apply to any person who has a valid Department permit or has submitted a complete dredge and fill permit application as of the effective date of this section, unless the permit or application is substantially modified or the applicant elects to proceed under these sections. Modifications or changes to a project made in response to suggestions by the Department or modifications or changes to a project that result in the incorporation of mitigation or the reduction of wetland impacts shall not be considered substantial modifications for purposes of this subsection.

(3) The Department will, in each case, first explore project modifications that would reduce or eliminate the adverse environmental impacts of the project, and will suggest any such modifications to the applicant either in addition to or in lieu of mitigation, as provided in subsection 62-312.060(10), F.A.C. The applicant shall consider modifications to the project proposed by the Department, whether or not a mitigation proposal has been submitted.

Should such mutual consideration of modification and mitigation not result in a permittable project the Department must deny the permit.

(4) The Department shall consider any mitigation proposed by a permit applicant in accordance with this section. Mitigation may be proposed by a permit applicant, or suggested by the Department only where the proposed dredging and filling would otherwise be unable to meet the criteria of Sections 403.918(1) and (2)(a), F.S. (Supp. 1992), and Rule 62-312.080, F.A.C. However, mitigation may not be required by the Department. Mitigation is neither necessary for nor applicable to projects covered by general permits or projects exempt from the requirements for individual dredge and fill construction permits.

(5) It is understood that in certain circumstances mitigation proposals for dredging and filling projects will not be able to offset the adverse impacts of the project sufficiently to yield a permittable project. Such instances may include projects that are in or that would significantly degrade Outstanding Florida Waters, the presence of endangered species or the likelihood that a particular wetland type may not be successfully created.

(6) The Department recognizes that other agencies are concerned with adverse impacts on waters of the state and may require mitigation for such impacts. Mitigation or reclamation required by other agencies will be acceptable to the Department to the extent that such mitigation or reclamation fulfills and Department’s statutory requirements. If not, additional measures shall be necessary to fulfill the Department’s requirements. It is the intent of the Department to reduce duplication of regulatory requirements. To that end, inspections, reports or other similar reviews of mitigation projects by the Department of Environmental Protection or other agencies will be used to augment the Department’s determination of compliance with permit requirements.

(7) The amount, type and location of mitigation, if any, required of electric utilities conducting dredge and fill activities for the purpose of providing energy service shall be determined in conjunction with the criteria in Section 403.918, F.S. (Supp. 1992), in recognition of the fact that such activities generally promote the public interest.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 1-3-89, Formerly 17-12.300, 17-312.300, Amended 10-3-95.

## 62-312.310 Definitions.

As used in this Part:

(1) “Cash equivalent” means a readily negotiable instrument that can be guaranteed convertible to cash upon presentation for the life of the requirement for financial responsibility without penalty, discount or interruption.

(2) “Enhance” means to improve existing altered or affected waters of the state or other wetlands. Such action would include, but not be limited to, successfully removing exotic or nuisance species, successfully planting indigenous wetland species, or improving the water regime or hydroperiod. In water bodies where existing ambient water quality does not meet standards, enhancement shall also include improvements in the water quality of the receiving body of water for those parameters which do not meet standards. If the permit applicant is responsible for adversely affecting the functions of the waters of the state in violation of regulations applicable at the time of the action, a proposal for the subsequent improvement of those functions shall not be considered enhancement.

(3) “Exotic species” means a plant species which is not indigenous to the geographic area under consideration. Whether or not a plant species is indigenous to the area may be determined from floristic information available about the natural range of the plant species.

(4) “Function” means the major physical, biological and chemical processes occurring in the waters of the state. Functions would include, but are not limited to, the following: fish and wildlife habitat, water quality enhancement, ground water recharge and erosion control.

(5) “Mining areas” means areas of land that have been disturbed by the severance of solid minerals as defined in subsection 211.30(2), F.S.

(6) “Mitigation” means an action or series of actions that will offset the adverse impacts on the waters of the state that cause a proposed dredge and fill project to be not permittable. “Mitigation” does not mean:

(a) Avoidance of environmental impacts by restricting, modifying or eliminating the proposed dredging and filling.

(b) Cash payments, unless payments are specified for use in a previously identified, Department endorsed, environmental or restoration project and the payments initiate a project or supplement an ongoing project. The project shall be sponsored or approved by a governmental agency and the adverse impacts of the dredge and fill project shall be offset by that previously identified project.

(7) “Modifications” means changes in the design of a proposed project, but does not include the alternative of not implementing the project in some form.

(8) “Nuisance species” means species of flora and fauna which meet the definition contained in subsetion 62-302.200(15), F.A.C.

(9) “Project” means that portion of a proposed dredging, filling, development, construction or mining activity which is subject to the Department’s dredge and fill permitting criteria and other applicable requirements.

(10) “Reference waters” means the waters of the state which are to be used as a standard for judging the mitigation proposal and the mitigation success. The reference waters may be the waters which are to be adversely affected by the dredge and fill project; the waters which were present at the site prior to such man-induced changes as drainage canals, dikes and berms; or other waters of the same type as the proposed mitigation site and in the vicinity of the project which are substantially equivalent to or less degraded than the project site. The decision as to which are to be the reference waters shall be approved by the Department.

(11) “Soil” means that earth material which has been so modified and acted upon by physical, chemical and biological agents that it will support rooted plants.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.912, 403.913, 403.918 FS. History–New 1-3-89, Formerly 17-12.310, 17-312.310.

## 62-312.320 Incorporation of Mitigation into the Permit Application Process.

(1) Mitigation proposals may be evaluated after consideration of the project as specified in subsection 62-312.060(10) and Rule 62-312.300, F.A.C. Mitigation proposals for proposed mining areas may be submitted with the permit application, but this shall not imply that reasonable modifications to applications for proposed mining areas may not be required. If the mitigation proposal is submitted after the Department has issued an intent to deny the dredge or fill permit application and the Department thereafter decides to issue the requested dredge or fill permit then the Department shall require the applicant to publish notice of the Department’s proposed action to grant the permit in the same manner as provided by Rule 62-110.106, F.A.C.

(2) The mitigation proposal, unless submitted with a mining application, if offered by the applicant, shall be made as a modification to the application and shall be reviewed during the final processing of the application. If a mitigation proposal is approved, the permit issued by the Department shall contain appropriate conditions specifying the mitigation activities to be undertaken by the permittee, establishing criteria for determining the success of the mitigation, and establishing monitoring requirements.

(3) Any permit issued with approved mitigation shall be issued for a period of time determined by the Department to allow for construction of the project and completion of all required mitigation. The application shall be accompanied by a fee as specified in subsection 62-312.060(15), F.A.C., based on the time needed to complete the dredge and fill project and to complete construction of the mitigation. A single additional fee of $500 will be required for projects in which the monitoring and evaluation to determine success of the mitigation will be required beyond the period of time to which the permit fee would ordinarily apply.

(4) If at least 90 days prior to the expiration date of the permit, the mitigation is not expected to be or is not deemed to be successful pursuant to Rule 62-312.350, F.A.C., the permittee shall submit to the Department a proposed agreement for continued monitoring until the mitigation is successful as defined by Rule 62-312.350, F.A.C. The agreement shall include implementing remedial measures, including but not limited to the following:

(a) A description of the conditions existing at the mitigation site.

(b) A written explanation of why the mitigation has not been determined to be successful.

(c) A written explanation and description, including drawings if necessary, of what efforts will be made to correct of modify the mitigation to achieve success.

(d) A proposed monitoring program to evaluate the success of the mitigation.

(e) A statement of the time anticipated to achieve the success of the mitigation.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.912, 403.913, 403.918, 403.919, 403.921 FS. History–New 1-3-89, Formerly 17-12.320, 17-312.320.

## 62-312.330 Mitigation Proposals.

When those negative aspects of the proposed dredging and filling project have been identified that would otherwise result in action to deny a permit, an appropriate mitigation proposal may be developed and submitted to the Department for review. The goal of the mitigation proposal shall be to offset the expected adverse impacts of the project that have resulted in the project being deemed unpermittable such that the resulting project with mitigation is not contrary to the public interest or, in the case of Outstanding Florida Waters, is clearly in the public interest.

Each mitigation proposal submitted to the Department that involves the creation, enhancement or preservation of a particular type of waters of the state shall be in writing and shall include the following information:

(1) Description of mitigation area. A description of the waters of the state to be created, enhanced or protected as a result of the mitigation activity, which shall include, where applicable, the type and functions of the waters of the state to be enhanced, its area, species present or to be planted, plant density, anticipated source of plants, soils and hydrologic regime. Based on the size or complexity of the mitigation proposal, the Department shall require further information including but not limited to data on the drainage basin, topography, proposed hydrologic regime and methodology to be used, when necessary to properly evaluate the mitigation proposal.

(2) Description of the “reference waters”. Where reference waters will be used for judging the mitigation success, a description of the reference waters including the type and function, area, flora and fauna present and their densities, hydrologic regime and soils. Based on the size and complexity of the reference waters the Department may require further information including but not limited to data on the drainage basin, topography, soil profile, and groundwater and surface water conditions.

(3) Description of proximal habitat. When unpermittable adverse effects are expected to be incurred by fish and wildlife, a description, including location, of any nearby or adjacent areas that may provide habitat for fauna displaced from the project area, or of any areas which may serve as sources of faunal recolonization.

(4) Monitoring plan. A plan for monitoring the success of a creation or enhancement project.

(5) Mitigation cost estimate. A written estimate of the cost of the mitigation shall be submitted. If the cost will exceed $25,000 a detailed estimate shall be submitted and shall include costs associated with earthmoving, planting, consultant fees and monitoring, reflecting the cost of the mitigation. Federal, state, county and municipal governments and state political subdivisions, and investor owned utilities regulated by the Public Service Commission, shall be exempt from this requirement.

(6) Sufficient legal interest. In order to obtain a dredge and fill permit which includes mitigation measures, the applicant must provide the Department with documentation of its sufficient legal interest in the site to be used for mitigation. Sufficient legal interest may include, but is not limited to, fee title, a license or consent of use, a lease or easement, or written authorization from the property owner.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.912, 403.913, 403.918 FS. History–New 1-3-89, Formerly 17-12.330, 17-312.330.

## 62-312.340 Evaluation of Mitigation Proposals.

The Department recognizes that each mitigation proposal must be evaluated on a case by case basis. It is necessary to first determine the probability that the proposed mitigation will offset the actual adverse impacts of the dredging and filling, including cumulative impacts, as identified by those negative aspects of the project that resulted in a negative permitting balance. The Department in making this determination will consider the likelihood that the mitigation will be successful.

The permit applicant shall provide the Department with reasonable assurances that the mitigation shall meet the success criteria in Rule 62-312.350, F.A.C., and shall comply with the following standards, where applicable:

(1) Type of waters of the state.

(a) Reclamation activities pursuant to Section 211.32, F.S., may be considered as mitigation to the extent that the type, nature, and function of the biological systems existing prior to mining are restored or improved. For waters and mining activities that fall under the jurisdiction of the Florida Department of Environmental Protection pursuant to Chapter 378, F.S., approved DEP reclamation plans that have been reviewed and favorably commented upon in writing by the Department prior to final approval by DEP will be presumed to be acceptable as mitigation by the Department with respect to the waters addressed in those plans. This presumption may only be rebutted by evidence that the plans do not fulfill the Department’s statutory and regulatory requirements.

(b) For other activities, the Department will identify the functions that will be impacted by the project and that have resulted in the project being determined to be contrary to the public interest pursuant to Sections 403.918(1) and (2)(a), F.S. (Supp. 1992). Based on that analysis the Department will judge whether the mitigation proposal will offset those identified negative aspects of the dredge and fill project. Offsetting the adverse impacts will usually be best addressed through protection, enhancement or creation of the same type of waters (e.g., Spartina marsh, cypress swamp, etc.), as those being affected by the proposed project. However, where the waters being affected have been significantly altered by human activity or other factors such as, but not limited to, drainage or invasion of exotic or nuisance species, a mitigation proposal utilizing other types of waters may be considered. Where mitigation using other types of waters is considered, preference will usually be given to utilization of the type of waters that were historically present before alteration.

(2) Ratios for created waters of the state. The mitigation proposed shall be sufficient to offset the adverse impacts expected to occur due to the proposed dredging and filling that render the project unpermittable. For mitigation involving the creation of waters of the state, the Department shall use as a guideline two acres created for each acre adversely impacted by the proposed dredging or filling. This guideline is for preliminary planning purposes only and the actual extent of wetland creation may be more or less based on a consideration of the factors listed in paragraphs (a) through (h) below.

(a) The length of time that can be expected to elapse before the functions of the waters of the state identified during the permitting process as being adversely affected have been restored or offset.

(b) Any special designation or classification specified in Chapter 62-4, 62-302 or 62-312, F.A.C., affecting the water body.

(c) The type of waters to be created and the likelihood of successfully creating that type of waters.

(d) Whether or not the waters of the state to be affected by the proposed dredging or filling are functioning as natural, healthy waters of the state of that type, and the current condition and relative value of functions being performed by the areas affected by the proposed activity compared to the proposed character and quality of the wetlands to be created.

(e) Whether the waters of the state are unique for that geographical area.

(f) For mine reclamation activities subject to Chapter 211, F.S., Part II, whether the ratio is consistent with the mine reclamation plan submitted to the Department of Environmental Protection.

(g) The presence or absence of exotic or nuisance plant species within the waters of the state to be disturbed or altered.

(h) Whether the proposed project eliminates waters or changes waters from one type to another.

(3) Ratios for enhanced waters of the state. It is recognized that stressed wetlands provide some degree of wetland function. When enhancement is proposed, the Department must make a judgment regarding the degree of enhancement expected to occur. The degree of expected enhancement must be weighed against the adverse impacts identified in the evaluation of the dredge and fill project. In general, ratios for enhanced waters shall be higher than for created waters. Factors that should be considered in establishing a ratio include:

(a) The degree to which the wetlands to be enhanced have been stressed.

(b) The type of stress the wetlands to be enhanced have experienced.

(c) The cause of the stress.

(d) Whether the proposed method of enhancement is one that will be low maintenance or self-regulating once implemented.

(e) The likelihood that the proposed enhancement will be successful in offsetting the adverse impacts of the dredge and fill project that caused the project to be not permittable.

(4) Protection of the mitigation area. The permit applicant shall propose appropriate methods to assure that the created or enhanced waters will not be adversely affected during the establishment phase by secondary impacts resulting from human activities such as, but not limited to, boat traffic and other recreational uses. Such assurances may include, but shall not be limited to, restricting access to the site.

(5) Exotic or nuisance species. The proposed mitigation plan shall include a requirement that exotic and nuisance species be removed from the mitigation area. The plan shall also include reasonable measures to assure that these species do not invade the mitigation area in such numbers as to affect the likelihood of success of the project. Depending on the topography of the area and the species involved, such measures could include, but not be limited to, continuing maintenance and/or a buffer zone.

(6) Location of mitigation area. Because the adverse impacts of a dredge and fill project rarely occur off-site, mitigation activities off-site are not generally acceptable unless they would better offset the adverse impacts. There are some instances where on-site mitigation may not be possible or may be restricted, such as, but not limited to, road projects and utility corridors. In such instances, the mitigation should be in close proximity to the dredge and fill site, in the same waterbody or within the same drainage basin, if possible. The negative aspects of the dredge and fill project must be offset by the off-site mitigation, as in any other mitigation.

When fish and wildlife habitat functions are a concern, several points shall be considered:

(a) The types of habitat function being performed at the site; such as fishery nursery area, rookery, multi-species habitat, foraging value, shelter value.

(b) The species to be affected by the project.

(c) The relative value of the site; such as whether it is the last remaining area of that habitat in the vicinity or whether the site is pristine.

(d) Whether the proposed off-site mitigation can reasonably be expected to offset the impacts of the project on specific habitat functions that would be affected as a result of the project.

(7) Use of donor sites. The use of waters of the state as plant or soil donor sites, where such use involves any dredging or filling, shall not be allowed except pursuant to an exempted activity, a Department permit or consent order.

(8) Location of donor site. Whenever practical, waters of the state which are to be dredged or filled shall be utilized as plant or soil donor sites for mitigation under this Part.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.912, 403.913, 403.918, 403.919, 403.921 FS. History–New 1-3-89, Formerly 17-12.340, 17-312.340.

## 62-312.350 Determination of Success for Mitigation Projects.

(1) Success criteria. Due to the wide range of types of projects which may be used to create or enhance existing waters, specific success criteria will be determined on a case-by-case basis. A determination that the mitigation area will be compared to a reference water will be specified by conditions in the permit when there is insufficient information available to judge the successful creation or enhancement of the type of wetland involved. In comparing the mitigation area to a reference water, it is not the intent of the Department to require that the mitigation area exactly duplicate or replicate the reference water. The reference water is to be used as a guide to the Department to assure that the mitigation area will be sufficiently similar to the reference water to meet the permitting criteria. Success must be measured in terms of whether the objectives of the mitigation can be realized. The success criteria to be included in the permit conditions must clearly address the minimum requirements necessary to attain a determination of success (e.g., percent cover by wetland vegetation, vegetation is reproducing naturally, target water quality standards are met, etc.). The mitigation will be judged to be successful if:

(a) All applicable water quality standards are met. However, where reference waters are used as a standard for dissolved oxygen, the daily and seasonal fluctuations of dissolved oxygen in the reference waters of the state shall be maintained;

(b) The mitigation project has a hydrologic regime sufficient to sustain it in a viable condition; and

(c) The specific success criteria contained in the permit are met.

(2) Climatic impacts. The Department shall take the occurrence of extreme or unusual climatic conditions into consideration when evaluating the success of the created or enhanced waters.

(3) Subsequent to determination of success by the Department, the waters of the state created or enhanced as mitigation can be used for purposes permittable pursuant to Chapters 62-6 and 62-25, F.A.C.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.912, 403.913, 403.918 FS. History–New 1-3-89, Formerly 17-12.350, 17-312.350.

## 62-312.360 Pre-Construction Mitigation.

(1) Pre-construction mitigation is mitigation that is constructed and determined to be successful after issuance of the dredge and fill permit, but prior to construction of the dredge and fill project. If pre-construction mitigation is proposed, the proposal shall contain the information required for any mitigation proposal.

(2) The Department may accept as mitigation, creation, enhancement or preservation activities that meet all other requirements of this section, and that predate a permit application. However, any such activities are at the risk of the applicant prior to inclusion as a permit condition, and the mitigation must offset the identified adverse impacts of the project for which the permit is requested.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.912, 403.913, 403.918 FS. History–New 1-3-89, Formerly 17-12.360, 17-312.360.

## 62-312.370 Restrictions on Property Use.

(1) Property restrictions as mitigation.

(a) Conservation easements or other such deed restrictions, and land conveyances, will be considered as mitigation only where they offset potential adverse impacts of the proposed dredging and filling, including cumulative impacts pursuant to Section 403.919, F.S. (1991)

(b) Property restrictions and conveyances may be considered as mitigation when they would preclude development in wetlands otherwise unprotected by the regulatory processes in Section 403.918, F.S. (Supp. 1992), or in waters of the state that may be subject to future dredge and fill permit applications. In certain circumstances property restrictions on or conveyance of uplands adjacent to protected wetlands will be acceptable. The evaluation of the lands proposed for restriction or conveyance will be considered with respect to whether they would offset the negative aspects of the dredge and fill project that have rendered it unpermittable.

(2) Conservation easements on mitigation areas.

(a) A conservation easement for any mitigation area created, enhanced or reclaimed as part of a mitigation proposal may be required as a condition of the dredge and fill permit under the following circumstances:

1. If the applicant proposes mitigation which, upon completion, would be outside the Department’s dredge and fill jurisdiction, and the applicant cannot provide reasonable assurance that the mitigation of adverse impacts will not be lost after completion of the mitigation, the Department may require a conservation easement for such mitigation area, equal in duration to the period of time necessary to provide such reasonable assurance.

2. If necessary to provide a reasonable period of time for establishment of a functioning system, the Department may require a temporary conservation easement for the mitigation area, equal in duration to the period necessary for establishment of a functioning system in such area.

(b) The Department may accept a comparable use restriction such as, but not limited to, state or federal ownership.

(3) Requirements for conservation easements. Any conservation easement provided under subsection 62-312.370(1), F.A.C., shall be perpetual, and all conservation easements shall be consistent with the requirements of Section 704.06, F.S.

(a) It shall be the responsibility of the permit applicant to provide for a survey of the boundaries of any property which is being conveyed to the State or for which a conservation easement is being provided.

(b) The recording of the conservation easement is required and shall be the responsibility of the permittee.

(4) Title to mitigation area. The applicant shall demonstrate sufficient title to the created or enhanced waters of the state to meet the requirements of paragraphs 62-312.370(3)(a)-(b), F.A.C., above, or shall provide the appropriate conveyance from the owner or owners holding such title so that the requirements are met.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.912, 403.913, 403.918, 403.919, 403.921 FS. History–New 1-3-89, Formerly 17-12.370, 17-312.370.

## 62-312.380 Release from Responsibility.

After receipt by the Department of the executed conservation easement, when required by subsection 62-312.370(2), F.A.C., and upon determination by the Department that the mitigation is successful, the permittee shall be released from all responsibility for the waters of the state created or enhanced as mitigation.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.912, 403.913, 403.918, 403.921 FS. History–New 1-3-89, Formerly 17-12.380, 17-312.380.

## 62-312.390 Financial Responsibility.

(1) Applicability.

(a) Each dredge and fill permit that involves mitigation shall require the permittee to provide evidence of financial resources necessary to conduct mitigation activities in a manner prescribed by the Department, to conduct mitigation monitoring and to conduct any necessary corrective action indicated by this monitoring. Permittees whose mitigation is deemed successful pursuant to Rule 62-312.350, F.A.C., prior to dredging or filling shall be exempt from this requirement. Federal, state, county and municipal governments and state political subdivisions, and investor owned utilities regulated by the Public Service Commission, shall also be exempt from this requirement.

(b) The permittee shall be required to submit proof of financial responsibility pursuant to Rule 62-4.110, F.A.C. Applicants whose mitigation is estimated to cost less than $25,000 shall be exempted from this requirement.

(2) Amount. The assurance of financial responsibility provided by the permittee shall be in an amount equal to 110% of the cost estimate included as part of the mitigation plan submitted under the requirements of Rule 62-312.330, F.A.C.

(3) Duration of financial responsibility. The financial documents submitted by the permittee under the requirements of this section shall be effective on or prior to the date that the activity authorized by the permit commences and shall continue to be effective through the date of notification of final release by the Department in accordance with subsection 62-312.390(5), F.A.C.

(4) Methods for demonstrating financial responsibility. Assurance of financial responsibility required under this section may be provided by any of the following methods, at the discretion of the applicant:

(a) Cash or cash equivalent.

(b) Letter of credit.

(c) Performance bond.

(d) An audited annual financial statement submitted by a Certified Public Accountant representing that the permittee has a tangible net worth equal to or in excess of 110 percent of the cost of the mitigation plan. For purposes of this paragraph, “tangible net worth” means total assets, not including intangibles such as goodwill and rights to patents or royalties, minus total liabilities, computed in accordance with generally accepted accounting principles.

(e) A demonstration that the applicant meets the financial test and corporate guarantee requirements set forth in 40 C.F.R. Section 264.143(f), F.S., as incorporated by reference at subsection 62-30.180(1), F.A.C. Where the referenced test is used to provide evidence of financial resources necessary to conduct mitigation activities the term “closure and post-closure cost estimates” as set forth therein, shall generally be construed as meaning “mitigation cost estimates.”

(f) A demonstration that the applicant meets the self-bonding provisions set forth at 30 C.F.R. Section 800.23. Where the referenced provisions are used to provide evidence of financial resources necessary to conduct mitigation activities, the term “surface coal mining and reclamation operations”, as set forth therein, shall generally be construed as meaning “mitigation activities.”

(5) Final release of the permittee from financial responsibility requirements. Within thirty days of the Department determining that the mitigation is successful, in accordance with Rule 62-312.350, F.A.C., the Secretary will notify the permittee in writing that the permittee is no longer required by this section to maintain financial assurance for mitigation. On determination by the Department that mitigation has been successful, the Department shall authorize return and release of all funds held or give written authorization to the permittee for cancellation of a bond or termination of a letter of credit or other financial guarantee.

(6) Partial release of the permittee from financial responsibility requirements. As phases of the mitigation plan, such as earth moving or other construction, are completed in accordance with the approved mitigation plan, and funds expended, the Department shall authorize a reduction in the amount of financial responsibility to the amount of mitigation expenditures remaining.

(7) Incapacity of permittees, guarantors, or financial institutions.

(a) A permittee must notify the Secretary by certified mail of the commencement of a voluntary or involuntary proceeding under Title XI (Bankruptcy), U.S. Code naming the permittee as debtor, within 10 business days after the commencement of the proceeding.

(b) A permittee who fulfills the requirements of this section by obtaining a letter of credit or surety bond will be deemed to be without the required financial assurance or liability coverage in the event of bankruptcy, insolvency, or a suspension or revocation of license or charter of the issuing institution. The permittee must reestablish financial assurance within 60 days after such an event.

(8) Use of a financial mechanism for multiple projects. A permittee may use a mechanism specified in subsection 62-312.390(4), F.A.C., to meet the financial responsibility requirements of this section. Evidence of financial responsibility must include a list of projects and the amount of funds assured for each project. The mechanism must be no less than the sum of funds that would be necessary in accordance with subsection 62-312.390(2), F.A.C., if separate mechanisms had been established for each project. As additional permits are issued which require mitigation, the amount of financial assurance provided by the mechanism may be increased in accordance with subsection 62-312.390(2), F.A.C., and the project added to the list.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.912, 403.913, 403.918, 403.921 FS. History–New 1-3-89, Formerly 17-12.390, 17-312.390.

## 62-312.400 Intent.

(1) Part IV pertains to Outstanding Florida Waters, exclusive of all artificial water bodies, within Monroe County, as identified in Rule 62-302.700, F.A.C., and is in addition to all other applicable Departmental rules relating to environmental resource permit or grandfathered dredge and fill permit applications under Part IV of Chapter 373, F.S. Artificial water bodies shall be defined as any water body created by dredging, or excavation, or by the filling in of its boundaries, including canals as defined in subsection 62-312.020(3), F.A.C., and borrow pits or waters resulting from rock mining activities.

(2)(a) The Environmental Regulation Commission finds that the waters of the Florida Keys and other Outstanding Florida Waters in Monroe County are an irreplaceable asset which require special protection.

(b) Further, the Florida Legislature in adopting Section 380.0552, F.S., recognized the value of the Florida Keys to the State as a whole by designating the Keys an Area of Critical State Concern. This rule implements Section 403.061(34), F.S., and is intended to provide the most stringent protection for the applicable waters allowable by law.

(3) Pursuant to Section 380.0552(7), F.S. (1986 Supp.), the specific criteria set forth in this section are intended to be consistent with the Principles for Guiding Development as set forth in Chapter 28-29, F.A.C. (August 23, 1984), and with the principles set forth in that statute. However, the criteria in this rule does not apply to all waters within the Florida Keys. These criteria do not apply to artificial waterbodies within the Florida Keys, as described in subsection 62-312.400(1), F.A.C. In addition, the four foot water depth restriction for piers which do not provide commercial marine supplies or services and which are designed to moor between three and nine boats are not applicable within the Outstanding Florida Waters that are within the boundaries of the City of Key West or within Everglades National Park or areas north of the Park within Monroe County. Docking facilities in those areas shall instead be subject to the three foot depth restrictions specified in paragraph 62-312.420(2)(a), F.A.C. However, all other provisions of this part are applicable in those areas.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 6-8-88, Amended 3-26-89, Formerly 17-12.400, 17-312.400, Amended 10-3-95.

## 62-312.410 General Criteria.

(1) Subject to the provisions of the mitigation section of this part (Rule 62-312.450, F.A.C.), no environmental resource permit or grandfathered dredge and fill permit under Part IV of Chapter 373, F.S., shall be issued for any activity in Outstanding Florida Waters in Monroe County if such activity:

(a) Alone or in combination with other activities damages the viability of a living stony coral community (Scleraoctinia and Milleporina), soft coral community (Alcynoacea, Gorgonacea and Pennatulacea), macro marine algae community (Chlorophyta, Phaeophyta and Rhodophyta), sponge bed community (Porifera), or marine seagrass (Hydrocharitaceae and Cymodoceae) bed community. This prohibition shall not include algae unattached to the bottom, nor shall it include algae growing landward of the mean high water line or growing as an epiphyte or periphyte on woody plants. For the purposes of this Part a marine seagrass bed or marine macroalgae community means an area dominated by the listed biota having an areal extent of at least 100 square feet. This paragraph does not imply that the Department cannot restrict the impact on smaller areas for such species based on other Department rules;

(b) Has been initiated or completed without benefit of an environmental resource permit or dredge and fill permit required by the Department.

(2) Subject to the provisions of the mitigation section of this part (Rule 62-312.450, F.A.C.), no permit shall be issued for the placement of fill in Outstanding Florida Waters in Monroe County unless expressly authorized by this rule or unless the Department determines that under applicable rules a permit may be issued in the following situations:

(a) Filling for projects which have been proposed by a governmental entity, public authority or public or private utility; or

(b) Filling for any other projects located within the landward extent of wetlands identified solely by vegetative dominance as described in paragraph 62-340.300(2)(b), F.A.C. Such areas do not include open waters or wetlands identified by vegetative dominance as described in paragraph 62-340.300(2)(a), F.A.C., or by the provisions of paragraph 62-340.300(2)(c) or (d), F.A.C.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 6-8-88, Amended 2-21-89, 3-26-89, Formerly 17-12.410, 17-312.410, Amended 10-3-95.

## 62-312.420 Permitting Requirements for Piers.

(1) No permit shall be issued for a pier which requires the dredging of an access channel or mooring basin unless such dredging is exempt from Department permitting requirements.

(2) Any pier used for the dockage of water crafts not exempt from permitting requirements pursuant to Section 403.813(1)(b), F.S., shall be evaluated on the following criteria:

(a) For piers designed to moor three or more boats, water depths at the specific mooring site shall not be less than four feet mean low water. However, within those areas specified in subsection 62-312.400(3), F.A.C., where the specified additional conditions of this part are not applicable, water depths at any specific mooring site shall not be less than three feet, except at marinas. Such water depths at marinas shall be at least four feet, as described in this Part.

(b) For piers designed to moor one or two boats, water depths at the specific mooring site shall not be less than 3 feet mean low water.

(c) The applicant shall affirmatively demonstrate to the Department that adequate depths exist for ingress and egress of boats to the mooring site, and in no case shall the depth of the access area be less than the minimum depths necessary to avoid damage to a seagrass bed community or other biological communities listed in paragraph 62-312.410(1)(a), F.A.C.

(d) The applicant shall affirmatively demonstrate that proposed construction techniques shall protect the viability of a seagrass bed community or other biological communities as listed in paragraph 62-312.410(1)(a), F.A.C.

(e) Boat mooring sites shall not be located over a seagrass bed community at depths less than five feet mean low water or a coral reef regardless of water depth.

(f) All portions of the pier facility other than the specific mooring sites shall be designed in a manner which will prevent the mooring of watercraft other than at the specific mooring sites. The “specific mooring site” shall be defined as the dockage and associated loading areas including only those portions of finger piers not used solely to provide access.

(g) Sewage pump out facilities shall be provided at any site which provides dockage for ten or more vessels or at which a liveaboard vessel is proposed to be docked. Rule 64E-6.010, F.A.C. (1991), provide certain requirements for the servicing and maintenance of portable or temporary toilets and holding tank systems and the disposal of domestic septage from such systems.

(3) Any pier or other overwater structure, except vehicular bridges, not used for the dockage of water craft shall be evaluated on the following criteria:

(a) The applicant shall affirmatively demonstrate that proposed construction techniques shall protect the viability of a seagrass bed community or other biological communities listed in paragraph 62-312.410(1)(a), F.A.C.

(b) Piers or other overwater structures shall be constructed at an appropriate elevation to prevent the dockage of water craft.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 6-8-88, Formerly 17-12.420, 17-312.420, Amended 10-3-95.

## 62-312.430 Permitting Requirements for Marinas.

Marinas shall be evaluated on the following criteria. For the purpose of this Part a marina shall be defined as a dockage facility providing ten or more wet storage slips or providing commercial marine products or services.

(1) Fueling facilities shall have automatic shutoff valves.

(2) Fuel storage or pumping facilities shall not be located on over-water structures.

(3) Spill containment equipment shall be located on site sufficient to prevent the discharge of pollutants into state waters beyond the marina boundary. Personnel trained in the use of the containment equipment shall be in attendance during all operating hours. At any time such personnel are not in attendance, fuel facilities shall be adequately secured to prevent use.

(4) Sewage pumpout facilities shall be provided.

(5) Water depths at the specific mooring sites shall not be less than four feet mean low water.

(6) The applicant shall affirmatively demonstrate to the Department that adequate depths exist for ingress and egress of boats to the mooring sites and in no case shall the depths of the access area be less than the minimum depth specified in subsection (5).

(7) Proposed construction techniques shall protect the viability of a seagrass bed community or other biological communities as listed in paragraph 62-312.410(1)(a), F.A.C.

(8) Boat mooring sites shall not be located over a seagrass bed community or coral reef regardless of water depth.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 6-8-88, Formerly 17-12.430, 17-312.430, Amended 10-3-95.

## 62-312.440 Permitting Requirements for Shoreline Stabilization.

(1) Permit applications for shoreline stabilization shall be evaluated on the following criteria:

(a) Except as provided in paragraphs 403.813(1)(e) and 373.414(5)(b), F.S., and Chapter 62-330, F.A.C., vertical seawalls as defined by Chapter 62-330, F.A.C., shall not be permitted within the waters regulated by this Part.

(b) Native aquatic vegetation shall be used for shore line stabilization, except at sites where an applicant can affirmatively demonstrate that the use of vegetation, including the existing undisturbed vegetation on site, will not prevent erosion. The Department may allow the use of rip rap and other sloping revetments provided that:

1. No dredging and/or filling will be authorized other than that necessary for safe and efficient installation of the revetment;

2. Filter cloth underliners shall be used for all revetments;

3. The slope of the revetment shall be no steeper than 2 Horizontal:1 Vertical;

4. No revetment shall be placed over or within a sea grass bed community; and

5. Only rocks two feet in diameter or larger shall be used as the outer layer of a rip rap revetment.

(2) Beach renourishment and restoration projects subject to Chapter 161, F.S., are not subject to the provisions of this section.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 6-8-88, Amended 3-26-89, Formerly 17-12.440, 17-312.440, Amended 10-3-95.

## 62-312.450 Mitigation.

Notwithstanding any of the prohibitions contained in this rule, the Department shall consider mitigation pursuant to Section 373.414(1)(b), F.S., and applicable Department rules to determine whether the project may otherwise be permittable. In any application for mitigation, the applicant shall demonstrate before issuance of any permit for the construction of the intended project that the proposed mitigation will be effective. Mitigation shall not be permitted where it appears after due considerations that construction of the intended project will cause irreplaceable damage to the site.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 6-8-88, Formerly 17-12.450, 17-312.450, Amended 10-3-95.

## 62-312.460 Special Consideration.

Notwithstanding any of the prohibitions contained in this Part, the Department may issue permits for dredging and filling required for the maintenance, construction, or reconstruction of the Overseas Highway (U.S. 1) where the applicant has demonstrated that the proposed project is necessary for the protection of the public health, safety, or welfare and complies with all other Department rules.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061 FS. History–New 6-8-88, Formerly 17-12.460, 17-312.460, Amended 10-3-95.

## 62-312.800 Scope of Part V.

The provisions of this Part shall only apply to activities in the geographical territory of the Northwest Florida Water Management District and to activities grandfathered under Sections 373.414(9), (11), (12)(a), (13), (14), (15) and (16), F.S. The scope and definitions of this part are provided in Rules 62-4.510 and 62-4.520, F.A.C. Persons wishing to use one or more of the general permits shall be subject to the notice provision of Rule 62-4.530, F.A.C., before any work is conducted as authorized herein. The general conditions provided pursuant to Rule 62-4.540, F.A.C., and the fee provisions of Rule 62-4.050, F.A.C., shall be applicable to all of the general permits in this Part.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.061, 403.813, 403.814 FS. History–New 3-26-89, Formerly 17-12.800, 17-312.800, Amended 10-3-95.

## 62-312.801 General Permit to U.S. Forest Service for Minor Works Within National Forests in Florida.

(1) A general permit is hereby granted to the U.S. Forest Service to conduct the works described below:

(a) Culvert placement, replacement, and maintenance in streams of less than fifteen (15) cubic feet per second average discharge at the culvert location or draining less than 5,000 acres in the Apalachicola National Forest, 10,000 acres in the Osceola National Forest, and 7,500 acres in the Ocala National Forest, except for culverts associated with low water crossings.

(b) Bridge construction, replacement and maintenance for structures up to 400 feet in length and two lanes or less in width, pursuant to the restrictions listed in Section 403.813(1)(l), F.S.;

(c) Construction and maintenance of low-water crossings (hard surface crossings over which water flows during storm events or immediately thereafter);

(d) Bathing beach restoration at developed recreation sites where maintenance dredging is less than 100 cubic yards per year and less than 100 cubic yards per single occurrence;

(e) Dock construction, replacement and maintenance for docks of up to 1000 square feet of over water surface area, in Outstanding Florida Waters subject to restrictions listed in Section 403.813(1)(b) and (d), F.S.;

(f) Temporary stream channel diversions necessary to complete projects detailed in paragraphs (a), (b) and (c) of this section;

(g) Channel clearing and shaping to facilitate maximum hydraulic efficiency of designed structures detailed in paragraphs (a), (b), and (c) of this section.

(2) This general permit is subject to the general conditions of Rule 62-4.540, F.A.C., and the following specific conditions:

(a) The U.S. Forest Service shall submit to the appropriate DEP district office once a year a schedule including location, typical drawings and approximate commencement date for the activities planned for that year.

(b) The U.S. Forest Service or its contractors shall follow Best Management Practices pursuant to Section 208 of Public Law 95-217 and detailed in the Silviculture Best Management Practices Manual, published by the Florida Division of Forestry, Department of Agriculture and Consumer Services, and referenced in paragraph 62-25.030(1)(a), F.A.C.

(c) The U.S. Forest Service or its contractors shall utilize appropriate turbidity control measures while actively dredging or filling within stream channels or springs.

(d) The U.S. Forest Service or its contractors shall stabilize fill areas and stream banks disturbed by the activity by revegetation except where the fill area is a bathing beach. If revegetation is inappropriate, riprap may be used.

(e) The U.S. Forest Service or its contractors shall limit stream channel relocation to those streams having an average annual discharge of fifteen (15) cubic feet per second or less. The length of relocated channels or those significantly altered shall be limited to 200 feet per stream. A stream channel shall be altered only when such a measure will reduce the long term adverse water quality impacts and will maintain or restore the stream’s natural hydraulic capability.

(f) The U.S. Forest Service or its contractors shall limit bridge construction to those bridges spanning bank to bank with no causeway approaches in the flood plain. This limitation does not apply to maintenance of existing bridges.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 253.123, 253.124, 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.817 FS. History–New 7-8-82, Formerly 17-4.55, 17-4.550, Amended 3-26-89, Formerly 17-12.801, 17-312.801.

## 62-312.803 General Permit for Installation or Maintenance of Boat Ramps.

(1) A general permit is hereby granted to any person installing or maintaining a boat ramp; provided

(a) This general permit shall apply to only those boat ramps not exempt from permitting pursuant to Section 403.813(1)(c), F.S.; and

(b) No ramp shall be installed under this general permit unless navigational access to the proposed ramp exists; and

(c) There shall be no filling other than the actual boat ramp surface and incidental filling associated with recontouring the land under the ramp to create a level grade; and

(d) There shall be no more than 25 cubic yards of material removed for installation of the boat ramp surface; and

(e) The installation or use of the boat ramp shall not interfere with navigation in the water body; and

(f) The above-water, level portion of the ramp shall be landward of the mean or ordinary high water line; and

(g) All spoil material shall be deposited on self-contained upland spoil site which shall be located so as to prevent the escape of spoil material into waters of the state; and

(h) Maintenance dredging shall be limited to that amount of material necessary to restore the ramp to its original configuration and dimension; and

(i) The boat ramp shall not infringe upon the riparian rights of adjacent property owners; and

(j) The permittee shall remit to the Board of Trustees of the Internal Improvement Trust Fund payment for material removed from sovereignty or state-owned lands in accordance with the schedule established by the Board.

(2) This general permit shall be subject to the general conditions in Rule 62-4.540, F.A.C., and the following specific conditions:

(a) Turbidity curtains or similar devices shall be utilized to prevent violation of state water quality standards.

(b) The installation of a boat ramp does not obligate the Department to approve any subsequent request to dredge for navigational access.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 253.123, 253.124, 373.414(11)-(16), 474.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.817 FS. History–New 7-8-82, Formerly 17-4.57, 17-4.570, Amended 3-26-89, Formerly 17-12.803, 17-312.803.

## 62-312.804 General Permit for Riprap.

(1) A general permit is hereby granted to any person installing riprap at the toe of an existing vertical seawall, provided

(a) The riprap consists only of natural boulders or clean concrete rubble six (6) inches to three (3) feet in diameter or in average dimensions; and

(b) The slope of the riprap is no steeper than 2H:1V and the horizontal distance is no more than eight (8) feet; and

(c) There are no reinforcing rods or other similar protrusions in concrete rubble and all rubble or boulders are free of attached sediments; and

(d) Neither the distance nor the use of the riprap interferes with navigation or infringes upon the riparian rights of the adjacent property owners; and

(e) There is no filling or dredging associated with the placement of riprap other than the riprap material itself.

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and specific conditions as follows:

(a) Turbidity curtains or similar devices where appropriate shall be utilized to prevent violation of state water quality standards; and

(b) Installation of the structure does not obligate the Department to approve any subsequent request to dredge for navigational access; and

(c) There shall be no backfilling to obtain useable upland or to straighten an otherwise sinuous shoreline; and

(d) There shall be no filling or backfilling to reclaim land lost by avulsion or erosion.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 253.123, 253.124, 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.817 FS. History–New 7-8-82, Formerly 17-4.58, 17-4.580, Amended 3-26-89, Formerly 17-12.804, 17-312.804.

## 62-312.805 General Permit for Headwalls and Culverts Associated with a Stormwater Discharge Facility.

(1) A general permit is hereby granted to any person to construct headwalls and culverts associated with a stormwater discharge facility; provided,

(a) A stormwater permit has been granted to the permittee by the Department or an entity on behalf of the Department; and

(b) The discharge from the stormwater system is to an artificial waterway; and

(c) The culvert shall not extend waterward of the headwall; and

(d) The culvert and the headwall shall not extend more than one (1) foot waterward of the existing shoreline.

(2) This general permit shall be subject to the general conditions in Rule 62-4.540, F.A.C., and the specific conditions as follows:

(a) Turbidity curtains or similar devices shall be utilized where appropriate to prevent violation of state water quality standards; and

(b) There shall be no backfilling to obtain useable upland or to straighten an otherwise sinuous shoreline.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 253.123, 253.124, 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.817 FS. History–New 7-8-82, Formerly 17-4.59, 17-4.590, 17-12.805, 17-312.805.

## 62-312.806 General Permit to the Florida Department of Transportation for Minor Works Within FDOT Rights-of-Way or Easements.

(1) A general permit is hereby granted to the Florida Department of Transportation to conduct the work described below:

(a) The extension of existing culverts and crossing approaches to accommodate widening of the roadway where excavation or deposition of material shall not exceed 1000 cubic yards in waters of the state and the area from which material is excavated or to which material is deposited shall not exceed a total of 0.25 acres at any one location (project site). The 1000 cubic yardage limitation shall be separately applied to excavation and deposition of material.

(b) Relocation, recontouring, widening, or reconstruction of existing highway drainage ditches through uplands provided the floor elevation of the ditch is not deepened below the original design elevation and provided that the work does not cause a change in the hydrology of any jurisdictional wetlands which are connected to or which are adjacent to the ditch.

(c) Culvert placement, replacement and maintenance associated with existing roadways, in streams of less than 10 cubic feet per second average discharge at the culvert location or streams draining less than 10 square miles, provided that construction does not cause scour in the downstream waters or increase the velocity of the water downstream, the material excavated or deposited as fill shall not exceed 1000 cubic yards in waters of the State, and the cross sectional area of the culvert shall not be reduced if it had been previously permitted by the Department as a wildlife crossing.

(d) Temporary stream channel diversions necessary to complete projects detailed in paragraph (c) above, provided the area used for the temporary diversion is restored to its previous contours and elevations.

(e) Channel clearing and shaping, not to exceed a combined total of 0.5 acres of dredging and/or filling in waters of the State, to facilitate maximum hydraulic efficiency of structures authorized by paragraph (c) above, where the spoil material is used on an upland portion of the project or is deposited on a self-contained, upland spoil site. Escape of spoil material and/or return water from the spoil deposition area into waters of the State is prohibited.

(f) Repair of existing concrete bridge pilings by the construction of pile jackets, provided that the permanent outer form is composed of inert materials and the quantity of material shall not exceed 300 cubic yards of dredging or 300 cubic yards of filling per project. Although the bottom sediments within the forms may be removed by jetting or pumping, and may not be recoverable, proper turbidity control measures shall be employed as necessary to prevent violations of state water quality standards.

(2) This general permit shall be subject to the general conditions of Rule 62-4.450, F.A.C., and the following specific conditions:

(a) The permittee shall use best management practices, including turbidity curtains or similar devices, in strict adherence to the Florida Department of Transportation “Standard Specifications for Road and Bridge Construction, Edition of 1986” to prevent violation of State water quality standards.

(b) As soon as possible following completion of slope construction, the fill areas and the banks of the water body shall be stabilized with vegetation and/or riprap to prevent erosion. Temporary erosion controls for all exposed soils within jurisdictional areas shall be completed within seven calendar days of the most recent construction activity. Prevention of erosion of exposed earth in jurisdictional areas is a construction priority, and completed slopes shall not remain unstabilized while other construction continues.

(c) Any area outside of the project area which is disturbed by the permitted construction activities shall be restored to its pre-construction state, including but not limited to re-contouring, revegetation, etc.

(d) In addition to complying with the notice provisions of Rule 62-4.530, F.A.C., at least 90 days prior to commencement of construction, the permittee will notify the appropriate Department district office of the date the permitted construction activities are planned to begin and within 90 days following completion of construction, a notice will be sent by letter of the date construction activities are completed.

(e) The permittee shall limit stream channel relocation to streams which have an average annual discharge of 10 cubic feet per second or less. The length of relocated channels or those significantly altered shall be limited to 200 feet per stream. A stream channel shall be altered only when such a measure will reduce the long term adverse water quality impacts and will maintain or restore the stream’s natural hydraulic capability.

(f) This general permit shall not apply to ditch construction in Class I or Class II surface waters or waters designated as Outstanding Florida Waters.

(g) This general permit authorizes certain minor dredge and fill activities only and does not relieve the permittee from compliance with any other applicable Department sections.

(3) This general permit shall apply only where the widening of the existing roadway has received all required permits for stormwater discharge before the start of construction.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.817, 403.912, 403.913, 403.918-.921, 403.931 FS. History–New 4-26-84, Formerly 17-4.66, 17-4.660, Amended 1-1-89, 3-26-89, Formerly 17-12.806, Amended 7-11-90, 1-29-91, Formerly 17-312.806.

## 62-312.807 General Permit for the Construction of Artificial Reefs.

(1) A general permit is hereby granted to any person to construct an artificial reef, provided:

(a) The material to be used shall be clean concrete or rock, or clean steel boat hulls; and

(b) The material shall be free of soils, oil and greases, debris, litter, putrescible substances or other pollutants; and

(c) The material shall be firmly anchored to the bottom and shall not be indiscriminately dumped; and

(d) The material shall be placed so that the top of the reef does not exceed 1/2 the distance from the bottom to the surface of the water unless a greater distance is required for safe navigation. At no time shall the distance between the top of the reef and the surface of the water be less than 6 feet.

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and the following specific conditions:

(a) The permittee shall conduct a survey of the bottomland on which the reef is to be built and shall submit the survey to the Department with notice pursuant to Rule 62-4.530, F.A.C., demonstrating that the bottom does not have grassbeds, or hardbottom or other corals; and

(b) There shall be no reefs constructed in shallow bay or estuarine bottoms; and

(c) There shall be no “white goods”, asphalt material, tires or other pollutant materials used in construction of the reef; and

(d) The site shall be marked with buoys to ensure that no material is deposited outside of the site; and

(e) The permittee shall notify the National Ocean Service, National Oceanographic and Atmospheric Association, U.S. Department of Commerce, Rockville, Maryland, of the precise location of the reef.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 253.123, 253.124, 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.817 FS. History–New 4-26-84, Formerly 17-4.68, 17-4.680, 17-12.807, 17-312.807.

## 62-312.808 General Permit for Certain Piers and Associated Structures.

(1) A general permit is hereby granted to any person to construct minor works as described below:

(a) Construction of private, single-family piers along with associated boat lifts where the pier:

1. Does not accommodate the mooring of more than two water craft; and

2. Does not, together with its walkways and end “T” or “L”, exceed 6 feet in width; and

3. Is constructed in waters or to waters that are sufficiently deep to avoid bottom scour by vessel operation or by prop dredging.

(b) Construction of boat shelters associated with a pier where the shelter has no walls or doors.

(c) Construction of an extension to an existing private, single-family pier where the extension is no more than 6 feet in width and is designed to enhance safety of boat use, to reach navigable water depths, or to accommodate a larger boat.

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and specific conditions as follows:

(a) Construction shall not occur over submerged grassbeds.

(b) There shall be no bait houses, storage shelters, sun decks, gazebos, screen porches, wet bars, living quarters, or other non-water-dependent structures over waters of the state or on the pier.

(c) The pier and its use shall not interfere with navigation in the water body.

(d) There shall be no dredging associated with pier construction other than that required for installation of the pilings for the pier and mooring of the water craft.

(e) There shall be no fish cleaning facilities, boat repair facilities or equipment and fueling facilities on the pier.

(f) The pier and its use shall not infringe on the riparian rights of adjacent property owners and shall be in accordance with the Rules of the Board of Trustees of the Internal Improvement Trust Fund, when construction occurs on state-owned bottomland.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 253.123, 253.124, 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.817 FS. History–New 4-26-84, Formerly 17-4.69, 17-4.690, Amended 3-26-89, Formerly 17-12.808, 17-312.808.

## 62-312.809 General Permit to the Florida Department of Transportation for Minor Bridge Construction.

(1) A general permit is hereby granted to the Florida Department of Transportation to conduct the work described below:

(a) The construction of bridges and approaches parallel and adjacent to existing bridges where the combined total of dredging and filling, both temporary and permanent, in waters of the State does not exceed 0.50 acre.

(b) The replacement or modification of bridges and approaches where the combined total of dredging and filling, both temporary and permanent, in waters of the State does not exceed 0.50 acre.

(c) The construction of bridges over waters of the State where no permanent dredging or filling is required other than placement of bridge support structures, and the combined total of temporary dredging and filling does not exceed 0.25 acre.

(d) Channel clearing and shaping, not to exceed a combined total of 0.5 acres of dredging and/or filling in waters of the State, to facilitate maximum hydraulic efficiency of the structures detailed in paragraphs (a) and (b) above, where the spoil material is used on an upland portion of the project or is deposited on a self-contained, upland spoil site. Escape of spoil material and/or return water from the spoil deposition area into waters of the State is prohibited.

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and the following specific conditions:

(a) In addition to compliance with the notice provisions of Rule 62-4.530, F.A.C., at least 90 days prior to commencement of construction the permittee will notify the appropriate Department district office of the date the permitted construction activities are planned to begin, and within 90 days following completion of construction, the permittee will notify by letter the appropriate Department district office of the date construction activities were completed.

(b) No access or work channels are authorized by this general permit.

(c) Temporary fill roads may not be constructed waterward of mean high water or ordinary high water.

(d) All temporary fill areas shall be regarded to original elevations and revegetated with native wetland species.

(e) This general permit shall not apply to bridge construction in Class I or Class II surface waters, or waters designated as Outstanding Florida Waters.

(f) Hydraulic openings of new bridges constructed under paragraph (1)(c) above shall be sufficient to prevent downstream scour, increased downstream water velocities, and significant backwater conditions upstream of the bridge structure.

(g) Minimum horizontal and vertical navigational clearances on new or replacement bridges over navigable waters of the United States shall be established in accordance with procedures outlined in the U.S. Coast Guard Bridge Administration Manual, COMDTINST M16590.5, May 7, 1982.

(h) Horizontal and vertical clearances for replacement bridge structures shall meet or exceed those of the bridge being replaced.

(i) Horizontal and vertical clearances on parallel bridges adjacent to existing bridges shall meet or exceed those of the existing bridge.

(j) The permittee shall limit crossings of any particular stream to an average of one every 0.5 mile.

(k) Temporary erosion controls for all exposed soils within jurisdictional areas shall be completed within seven calendar days of the most recent construction activity.

(l) The fill areas and the banks of the water body shall be stabilized with vegetation and/or riprap as soon as possible following completion of slope construction. This stabilization is considered a construction priority, and completed fill slopes in jurisdictional areas shall not remain unstabilized while other construction continues.

(m) This general permit does not authorize the use of dredged material for roadway construction.

(n) The permittee shall use best management practices, including turbidity curtains or similar devices, in strict adherence to the Florida Department of Transportation “Standard Specifications for Road and Bridge Construction, Edition of 1986” to prevent violations of State water quality standards.

(o) This general permit authorizes dredging and filling activities associated with minor bridge construction only and does not relieve the permittee from compliance with any other applicable Department sections.

(3) This general permit shall apply only where all required permits for stormwater discharge have been received prior to beginning of construction.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.817, 403.912, 403.913, 403.918, 403.931 FS. History–New 7-11-90, Amended 1-29-91, Formerly 17-312.809.

## 62-312.810 General Permit to Perform Prospecting Activities for Phosphate Minerals.

(1) A general permit is hereby granted to any person engaged in or proposed to engage in the mining of phosphatic ore within the boundaries of the Department of Environmental Protection Northeast and Southwest Districts as described in Rule 62-101.020, F.A.C., to perform prospecting activities for phosphate minerals within certain portions of waters of the state, except in Outstanding Florida Waters, Aquatic Preserves, Class I waters, Class II waters, or waters approved for shellfish harvesting; provided:

(a) Prospecting activities shall be defined as the conducting of activities that are considered normal and reasonably necessary in order to retrieve core samples of subsurface geologic sediments for the specific purpose of locating, mapping and determining the quantities and quality of any phosphorus bearing strata or deposits.

(b) Vehicles utilized in prospecting activities shall be of a type generating minimum ground pressure in order to minimize rutting and other environmental impacts, or the disturbed area along each prospecting line shall be restored to original contours upon completion of the prospecting activities along that specific alignment. In areas within the landward extent of waters of the state identified as wooded wetlands, the permittee shall choose alignments which will minimize the destruction of mature wetland trees.

(c) Disturbance within the landward extent of waters of the state identified as herbaceous wetlands shall be no wider than twenty-five (25) feet along any portion of the prospect line and disturbance within the landward extent of waters of the state identified as wooded wetlands shall be no wider than fifteen (15) feet along any portion of the prospect line, except at the immediate site of the drill hole where disturbance shall not exceed twenty-five (25) feet in width and no activities regulated by the Department associated with prospecting shall occur outside the fifteen (15) foot and twenty-five (25) foot limits, respectively, and

(d) An individual prospecting line shall not extend into waters of the state more than one-third (1/2) of the width of the landward extent of the water body involved, unless prospecting is conducted by hand carried drilling devices in which case full penetration of the water body shall be allowed except as restricted by paragraph (1)(f). When hand carried drilling devices are used all drilling tailings shall be returned to the drill hole and no spoil shall be left on the surface, and

(e) No prospecting activities shall occur in open waters (areas of water bodies not supporting emergent vegetation), such as lakes, ponds, streams, and rivers, and

(f) A minimum interval of six hundred and sixty (660) feet shall exist between individual parallel prospecting lines. A minimal distance of three hundred and thirty (330) feet shall be maintained between the alignment of the prospecting line originating from opposing sides of water bodies. When hand carried drilling devices are to be used for total penetration of the wetland, the minimal interval of three hundred and thirty (330) feet between prospecting lines shall apply.

(g) No debris or spoil shall be mechanically placed outside of the twenty-five (25) foot width allowed above, and

(h) The disturbed area along each prospecting line within herbaceous wetlands shall be replanted with indigenous native species using acceptable reclamation practices unless evidence exists that substantial natural revegetation has commenced within one growing season. The disturbed area along each prospecting line with wooded wetlands shall be replanted with indigenous native tree species using acceptable reclamation practices and the permittee shall institute necessary maintenance activities to insure the survival of the planted indigenous native trees. The restored sites shall be maintained free of any new growth of Schinus terebinthifolius (Brazilian pepper), Melaleuca quinquenervia (Punk tree), and Casuarina spp. (Australian pine). The restored site shall also be managed in a manner where Typha spp. (cattails) shall not be permitted to manifest a vegetative dominance to a degree which would result in water quality violations.

(2) This general permit is subject to the general conditions of Rule 62-4.540, F.A.C., and the following specific conditions:

(a) A person wishing to utilize this general permit shall submit to the appropriate DEP district office, an annual schedule of proposed prospecting activities within the prospect areas including location maps, aerial photographs showing the proposed prospecting lines, and approximate commencement and completion dates for the activities planned for each prospect area. The annual schedule, or modifications to the annual schedule, must be submitted at least thirty (30) days prior to the commencement of the proposed activity. Where practicable, the annual schedule should be filed with the Department no later than June 1 for the fiscal year July 1 through June 30.

(b) Appropriate turbidity and erosion control measures shall be utilized, as necessary, to prevent violation of state water quality standards.

(c) The prospecting activities shall be in accordance with the sections promulgated under the authority of the Board of Trustees of the Internal Improvement Trust Fund when they occur on state-owned bottomland.

(d) When requested, the Department and its employees shall keep confidential all information submitted by the permittee as provided in Section 403.111, F.S.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History–New 9-3-86, Formerly 17-4.750, 17-12.810, 17-312.810.

## 62-312.811 General Permit for Temporary Dragline Crossings of Waterways.

(1) A general permit is hereby granted to any person engaged in or proposing to engage in the mining of a phosphatic ore within the boundaries of the Department of Environmental Protection Northeast and Southwest Districts as described in Rule 62-101.200, F.A.C., for the construction of temporary dragline crossings within certain waters of the state, except in Outstanding Florida Waters, Aquatic Preserves, Class I waters, Class II waters, or waters approved for shellfish harvesting; provided:

(a) The crossing is of a ditch or artificially channelized portion of a water body or at a documented location of a previously existing dragline crossing within the preceding five (5) years, of a natural water body, and is not a navigable water body. The term navigable, for the purpose of this permit, means the water body is capable of use by small craft, and

(b) Only clean sand fill shall be utilized in the construction of the crossing, and

(c) When demucking or removal of topsoil is necessary for the construction of the crossing, the muck and/or topsoil shall be retained at a nearby upland location and returned to the crossing site for the restoration activities, and

(d) Adequate culverts are installed to maintain the natural and seasonal volume and flow of water, and

(e) The top width of the fill shall not exceed one hundred and fifty (150) feet and the toe to toe width of the fill shall not exceed two hundred (200) feet and the side slopes shall be no steeper than 3H:1V, and the lateral limits of disturbance of the wetlands shall be no more than twenty (20) feet on each side of the fill, and

(f) The crossing shall not infringe on the riparian rights of adjacent property owner(s) without written consent of the adjacent property owner(s), and

(g) The crossing shall not remain in place for more than one (1) year, unless the crossing is for a one-way access in which case it shall not remain in place for more than six (6) months, and

(h) The area must be restored to original topographic contours within sixty (60) days of the abandonment of the dragline crossing, which shall be after the dragline has crossed the water body.

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and specific conditions as follows:

(a) Appropriate turbidity and erosion control measures shall be utilized to prevent violation of state water quality standards.

(b) The holder of the general permit shall act in accordance with the sections promulgated under the authority of the Board of Trustees of the Internal Improvement Trust Fund when the crossing occurs on state-owned bottomland.

(c) Upon restoration of original topographic contours at a temporary dragline crossing site, the permittee shall at the end of the first growing season provide the opportunity for inspection of the site by the appropriate DEP district office staff. If in the opinion of the Department, satisfactory revegetation of the site has not occurred, the permittee shall initiate, conduct and maintain a revegetation program for the site. For the purpose of this general permit, revegetation of a waterway shall be with native species in similar composition to those species which were present at the site or in the contiguous wetland prior to the temporary dragline crossing. The restored site shall be maintained free of any new growth of Schinus terebinthifolius (Brazilian pepper), Melaleuca quinquenervia (Punk tree), and Casuarina spp. (Australian pine). The restored site shall also be managed in a manner where Typha spp. (cattails) shall not be permitted to manifest vegetative dominance to a degree which would result in water quality violations.

(d) A person wishing to utilize this general permit shall submit to the appropriate DEP district office, an annual schedule of proposed temporary dragline crossing areas including location maps, aerial photographs with proposed temporary dragline crossings, typical drawings, and approximate commencement and completion dates for the activities planned. Additionally, the plans shall include proposed restoration procedures for each temporary dragline crossing. The annual schedule, or modifications to the annual schedule, must be submitted, together with the required documentation, at least thirty (30) days prior to the commencement of the proposed activity. Where practicable, the annual schedule and documentation should be filed with the Department no later than June 1 for the fiscal year July 1 through June 30.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History–New 9-3-86, Formerly 17-4.760, 17-12.811, 17-312.811.

## 62-312.812 General Permit for Low Water Crossings.

(1) A general permit is hereby granted to any person engaged in or proposing to engage in the mining of a mineralized non-metallic ore to move equipment and vehicles, excluding dredges, through and across waters of the state during periods of low water, except in Outstanding Florida Waters, Aquatic Preserves, Class I waters, Class II waters, or waters approved for shellfish harvesting; provided:

(a) The only dredging or filling which is performed will be that caused by the movement of the vehicle or equipment through the water, and

(b) The maximum water depth along the crossing shall not exceed two (2) feet during the time the crossing is utilized, and

(c) Vegetative debris shall not be deposited within waters of the state, and

(d) That the lateral width of disturbance shall in no case exceed that necessary to move the vehicles and equipment through and across the water body and shall in no case be greater than fifty (50) feet, and

(e) That the distance between crossings on an individual water body shall be at least five thousand (5000) feet, except that at sites where a documented four (4) wheel vehicular access exists, crossings may be at a spacing of twenty-five hundred (2500) feet.

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and specific conditions as follows:

(a) The person wishing to utilize this general permit shall to the maximum degree practicable initiate planning activities to locate crossings at sites which will cause least environmental impact. To the maximum degree practicable the permittee shall coordinate with the appropriate DEP district office.

(b) Appropriate turbidity and erosion control measures shall be utilized, as necessary, to prevent violation of state water quality standards, and

(c) Upon restoration of an individual low water crossing site, the permittee shall at the end of the first growing season provide the opportunity for inspection of the site by the appropriate DEP district office staff. If in the opinion of the Department, satisfactory revegetation program for the site has not occurred, the permittee shall initiate, conduct and maintain a revegetation of the waterway. For the purpose of this general permit, revegetation of the site shall be with native species in similar composition to those species which were present at the site or in the contiguous wetland prior to the low water crossing. The restored site shall be maintained free of any new growth of Schinus terebinthifolius (Brazilian pepper), Melaleuca quinquenervia (Punk tree), and Casuarina spp. (Australian pine). The restored site shall also be managed in a manner where Typha spp. (cattails) shall not be permitted to manifest vegetative dominance to a degree which would result in water quality violations.

(d) A person wishing to utilize this general permit shall submit to the appropriate DEP district office, an annual schedule of proposed low water crossing sites including location maps, aerial photographs with proposed low water crossing sites, typical drawings, and approximate commencement and completion dates for the activities planned. Additionally, the plans shall include proposed restoration procedures for each low water crossing. The annual schedule, or modifications to the annual schedule, must be submitted, together with the required documentation, at least thirty (30) days prior to the commencement of the proposed activity. Where practicable, the annual schedule and documentation should be filed with the Department no later than June 1 for the fiscal year July 1 through June 30.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History–New 9-3-86, Formerly 17-4.770, 17-12.812, 17-312.812.

## 62-312.813 General Permit for the Installation of Fences.

(1) A general permit is hereby granted to any person installing a fence in waters of the state, except in Outstanding Florida Waters, Aquatic Preserves, Class II waters, or waters approved for shellfish harvesting; provided:

(a) The structure shall not block navigation, create a navigational hazard, impede the natural flow of water by itself or through the accumulation of debris, and

(b) No fence shall be installed into open waters (areas of water bodies not supporting emergent vegetation) of any navigable river, stream, canal, or tributary thereto, a distance of more than twenty-five (25) feet, or more than twenty percent (20%) of the width of the open water, whichever is less, and in any lake shall not extend more than fifteen (15) feet waterward of the landward extent of waters of the state, and

(c) The fence will be constructed of wire attached to wood or mental posts which project at least two (2) feet above the minimum flood or ordinary high water elevation of the waterway, and

(d) In navigable waters and all lakes, the structure shall be adequately marked with reflectors visible from both directions paralleling the shoreline, and

(e) Dredging or filling performed shall be limited to that necessary to install individual fence posts, and

(f) The installation shall not infringe on the riparian rights of adjacent property owners and shall be in accordance with the sections promulgated under the authority of the Board of Trustees of the Internal Improvement Trust Fund when installation occurs on state-owned bottomland.

(2)(a) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and the following specific condition:

(b) Turbidity curtains or similar devices shall be utilized, as necessary, to prevent violation of state water quality standards.

(3) This general permit shall not be used to regulate agricultural installation of fences pursuant to Section 403.913, F.S.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History– New 9-3-86, Formerly 17-4.780, 17-12.813, 17-312.813.

## 62-312.814 General Permit to Florida Game and Fresh Water Fish Commission, U.S. Forest Service, and County and Municipal Governments for the Construction of Freshwater Fish Attractors.

(1) A general permit is hereby granted to the Florida Game and Fresh Water Fish Commission, the U.S. Forest Service, and County and Municipal Governments to construct a fish attractor in fresh water lakes; provided:

(a) That any fish attractor to be constructed by County or Municipal Government must have the written approval of the Florida Game and Fresh Water Fish Commission, and

(b) The material to be used shall be clean concrete or rock, or brush, or logs, or trees, and

(c) The material shall be free of soils, preservatives, oil and greases, debris, litter, putrescible substances, “white goods”, asphalt material, tires, or other pollutants, and

(d) The material shall be firmly anchored to the bottom and shall not be indiscriminately dumped, and

(e) The size of an individual fish attractor shall not exceed one quarter of an acre in area, and

(f) The material shall be placed so that the top of the fish attractor is at least three (3) feet below the surface of the water at ordinary low water and shall be outside any posted navigational channels.

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and the following specific conditions:

(a) No fish attractor material shall be placed on or in areas vegetated by aquatic herbs or algae (except nuisance exotics), and

(b) The site shall be marked with a buoy or buoys to ensure that no material is deposited outside of the site.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History–New 9-3-86, Formerly 17-4.790, 17-12.814, 17-312.814.

## 62-312.815 General Permit for Ski Jumps and Slalom Courses.

(1) A general permit is hereby granted to any person to install ski jumps and slalom courses, except in Aquatic Preserves, Outstanding Florida Waters, and posted manatee areas; provided:

(a) The structures and their uses will not impede the natural flow of water, create a navigational hazard or otherwise interfere with the public use of waters of the state, and

(b) No ski jump or slalom course shall be installed under this general permit unless navigational access to the proposed structure(s) exists, and

(c) The structure(s) shall be placed at locations with a minimum water depth of six (6) feet, and shall be placed at least three hundred (300) feet from any shoreline that is not under the ownership or control of the permittee, and

(d) The ski jump and/or slalom course shall be flagged to mark the location of the race course, and

(e) There shall be no dredging, filling, or construction activities associated with the ski structure(s) other than the installation and removal of the ski jump and/or slalom course, and

(f) The ski jump and/or slalom course and its (their) use shall not infringe on the riparian rights of adjacent property owners and shall be in accordance with the sections promulgated under the authority of the Board of Trustees of the Internal Improvement Trust Fund when installation occurs on state-owned bottomland, and

(g) Installation shall not occur over submerged marine grassbeds, or other areas of aquatic herbs or algae, except nuisance exotics.

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and the following specific conditions:

(a) The installation of a ski jump or slalom course does not obligate the Department to approve any subsequent request for a dredge or fill permit at the site.

(b) The permittee shall submit to the appropriate DEP district office a set of plans indicating the location of the ski course and ski jump on the lake, the depth of water, and how the course will be marked.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History–New 9-3-86, Amended 10-28-87, Formerly 17-4.800, 17-12.815, 17-312.815.

## 62-312.816 General Permit for the Construction or Maintenance of Culverted Driveway or Roadway Crossings and Bridges of Artificial Waterways.

(1) A general permit is hereby granted to any person for the purpose of constructing or maintaining a driveway or roadway which crosses an artificial waterway; provided

(a) This general permit shall apply only to wholly artificial, non-navigable drainage conveyances within the Department’s jurisdiction, and

(b) A culvert or culverts are placed under the roadway or driveway, and

(c) The size and number of the culvert(s) shall be adequate to pass normal high water stages of the artificial water body being crossed. In no instance shall the culvert(s) provide a smaller cross-sectional area or discharge capacity than any upstream culvert, and

(d) The elevation of the culvert invert shall be at the existing bottom grade of the artificial waterway, and

(e) The length of the driveway, roadway or bridge crossing the waterway shall not exceed fifty (50) feet top of bank to top of bank, and

(f) The top width of the driveway, roadway, or bridge shall not exceed 75 feet and the toe to toe width shall not exceed 100 feet and the side slopes shall be not steeper than 2H:1V, and

(g) Clean fill used for the crossing must be obtained from uplands or from a dredge site approved through a dredge and fill permit, exemption, or general permit, and

(h) There shall be no additional dredging, filing, or construction activities, except as exempted by statute or section, and those directly involved in the construction or maintenance of the proposed crossing or bridge, and

(i) The maintenance of the roadway, driveway or bridge shall continue to provide at least the same volume of discharge through the culvert(s).

(2) This general permit shall be subject to the general conditions of Rule 62-4.540, F.A.C., and the following specific conditions:

(a) Turbidity curtains or similar devices shall be utilized, as required, to prevent violation of state water quality standards.

(b) This general permit does not relieve the permittee of the responsibility for obtaining stormwater management system approval where it is required.

(c) The permittee shall stabilize fill areas and waterway banks disturbed by the activity by revegetation or riprap as necessary to prevent erosion, siltation or turbid runoff into state waters.

(d) If dewatering is performed, all temporary fill dikes and dewatering discharges shall be installed and constructed so that no upstream flooding or impoundment occurs and no siltation, erosion or turbid discharges into waters of the state occur in violation of Rules 62-4.242 and 62-302, F.A.C. Any temporary works shall be completely removed, and all areas upstream and downstream from the crossing shall be restored to grades, elevations and conditions which existed before construction.

(3) This general permit shall not be used to regulate agricultural crossings of drainage conveyances pursuant to Section 403.913, F.S.

(4) This general permit shall apply only to a maximum of two (2) crossings on a given parcel of property with a minimum distance of five hundred (500) feet between crossings. Maintenance shall be allowed at any and all existing structures meeting the specifications of this general permit.

(5) This general permit shall not apply to the following activities and/or conditions where:

(a) Relocation of all or part of the artificial waterway is required, or

(b) Dredging or filling activities are required, other than for the proposed culvert crossing, except as exempted by statute or section.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History–New 9-3-86, Formerly 17-4.810, Amended 3-26-89, Formerly 17-12.816, 17-312.816.

## 62-312.817 General Permit for the Construction of Aerial Pipeline Crossings of Certain Waters.

(1) A general permit is hereby granted to any person constructing an aerial pipeline crossing of artificial waterways, including man-made canals, and drainage ditches, as defined in Section 403.803, F.S., and natural water bodies, where the width of the waters of the state is no greater than twenty-five (25) feet; provided:

(a) They are not located in Outstanding Florida Waters, Aquatic Preserves, Class I waters, Class II waters, or waters approved for shellfish harvesting, and are used for the transport of the following materials: potable water, raw non-wastewater (well water, reservoir water, etc.), treated domestic waste, phosphate matrix slurry, phosphatic clay or sand tailings, recirculated water from beneficiation processes, electrical power cables and conduits that are not subject to the provisions of Sections 403.52-.539, F.S., and telephone and other electronic communication cables and conduits, and

(b) There shall be a minimum clearance of five (5) feet above the elevation of the mean or ordinary high water line, or no lower than existing pipeline structures in the area, and

(c) The structure does not create a navigational hazard or impede the natural flow of water, and

(d) The dredging performed shall be restricted to that quantity necessary for actual installation of the support piles, and no fill other than the support piles shall be placed within waters of the state, and any disturbance of the side slopes of the waterway shall be stabilized with native vegetation, and

(e) Work activities for the installation of the aerial pipeline crossing shall be restricted to a width of no more than thirty (30) feet on each side of the pipeline alignment. In cases where multiple pipes are to be installed along the same alignment the thirty (30) foot width shall commence from the outermost pipes. For the purposes of this general permit, no more than three (3) pipes shall be placed along a given alignment, and in no case shall the total disturbance area exceed seventy-five (75) feet in width, and

(f) Construction techniques necessary for the installation of the aerial pipeline, including the transport and placement of materials, shall not disturb the adjacent bottoms or adversely affect water quality.

(2) This general permit shall be subject to the general conditions in Rule 62-4.540, F.A.C., and the following specific conditions:

(a) Turbidity curtains or similar devices shall be utilized, as necessary, to prevent violation of state water quality standards.

(b) Any pipeline transporting authorized materials, other than potable water or raw non-wastewater, shall be subject to the following spill prevention design criteria:

1. Double piping (pipe within a pipe) constructed in such a manner that any leakage from the inside pipe into the outside pipe shall be conveyed to spill detention areas constructed in areas outside the landward extent of waters of the state, and

2. Pressure sensitive devices designed to detect any leak shall be installed proximal to the aerial crossing, and shall be designed in a manner to both visually and audibly alert the appropriate authorities that a leak is in progress.

(c) The Department shall be notified of any leak or failure of any of the pipes associated with the aerial crossing.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History–New 9-3-86, Formerly 17-4.820, 17-12.817, Amended 11-27-91, Formerly 17-312.817.

## 62-312.818 General Permit for Subaqueous Utility Crossings of Artificial Waterways.

(1) A general permit is hereby granted to any person constructing, repairing or replacing a subaqueous utility crossing of artificial waterways, which are defined for purposes of this section as residential canal systems and all other bodies of water that have been totally dredged or excavated and which do not overlap natural surface waters of the State, and which were not created as a part of a mitigation plan; provided:

(a) The work is not located in Outstanding Florida Waters, Aquatic Preserves, Class I waters, Class II waters or waters approved for shellfish harvesting by the Department of Environmental Protection; and

(b) Such construction shall be limited only to non-navigable watercourses or to those waterways in which navigation can be maintained at all times without the necessity of removing or relocating turbidity control devices to allow boat passage; and

(c) No dredging or filling shall be conducted in jurisdictional wetlands, as defined in Rule 62-301.400, F.A.C., which are located landward of the top of the banks of an artificial waterway. Dredging and back filling of littoral zones and wetland vegetation growing on the side slopes of the artificial waterway may be performed only as is reasonably necessary to install the subaqueous utility line crossing and restore the banks to their original design specifications; and

(d) There shall be no dewatering or construction of temporary berms or dikes; and

(e) The maximum length of the utility crossing shall not exceed 150 ft. from top of bank to top of bank. Excavated trench dimensions shall be limited to a depth of not more than 10 ft. below existing bottom contours and a trench top width of not more than 10 ft.; and

(f) The maximum width of the area disturbed by equipment during construction shall be no more than 30 ft. wide; and

(g) All previously excavated contours are restored with on site native backfill, coarse sand, or clean, non-toxic rock bedding or cap material, as appropriate, within 72 hours following installation of the utility line; and

(h) This general permit shall only authorize utility installations extending from bank to opposite bank on a particular waterway. The placement of utility lines paralleling the watercourse alignment is not authorized; and

(i) Placement of the utility line shall not result in a navigational hazard. Customary navigation through the waterway shall be maintained at all times during installation.

(2) This general permit shall be subject to the general conditions in Rule 62-4.540, F.A.C., and the following specific conditions:

(a) Measures shall be taken as necessary to prevent violations of state water quality standards during and after construction arising from the work, including but not limited to the use of turbidity screens, staked filter cloth, and staked hay bales. Where turbidity screens, filter cloth, hay bales, and similar structural measures are not expected to be sufficient to contain turbid runoff, additional measures, such as restricting work to periods of low flow and dry season months, shall be taken to ensure that construction can be performed in a manner which will not violate water quality standards; and

(b) All erodable ground areas and slopes disturbed during construction shall be revegetated with sod, mulch, seed, wetland species, or otherwise appropriately stabilized (such as with seawalls or riprap in accordance with paragraph 62-312.050(1)(g), F.A.C.) within 72 hours after installation of the utility line and at any other time as necessary to prevent erosion, siltation, or turbid discharges exceeding 29 NTU’s above background into waters of the State; and

(c) Temporary or permanent spoil disposal sites shall be located exclusively on uplands, and shall be sited or designed to prevent erosion, siltation, turbidity in excess of 29 NTU’s above background, or other discharges into waters of the state; and

(d) The utility crossing shall be designed in accordance with generally recognized practices of sound engineering; and

(e) Signs of a legible size and nature shall be installed and maintained at conspicuous locations to identify the alignment and type of the utility line within waters of the State.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.814, 403.912, 403.913, 403.918, 403.919 FS. History–New 11-16-89, Formerly 17-312.818.

## 62-312.819 General Permit for the Limited Dredging of Sediment for Aquatic Plant Management Purposes.

(1) A general permit is hereby granted to any person engaged in limited dredging of sediment for aquatic plant management purposes; provided:

(a) This general permit shall apply to only those activities that have a valid Chapter 62C-20, F.A.C., permit for aquatic plant control already issued by the Florida Department of Environmental Protection in which the conditions for limited dredging have been set forth in the supplemental conditions of the Chapter 62C-20, F.A.C., permit. For the purposes of this general permit, a valid Chapter 62C-20, F.A.C., permit shall hereinafter be referred to as a valid Department of Environmental Protection Aquatic Plant Control Permit;

(b) Sediment removal for aquatic plant management purposes shall be limited to only those lakes with naturally occurring sand bottoms, and only those vegetated areas within lakes, to their landward extent, that have a minimum of eighty percent areal coverage of Typha spp. (cattail) within the project area;

(c) Only unconsolidated, flocculent detrital material from decaying vegetation shall be removed under this general permit. The depth to which the detrital material may be removed shall be as determined by the Department of Environmental Protection through a site inspection during the review of a Department of Environmental Protection Aquatic Plant Control Permit, but in any event shall not exceed three feet of sediment, and in no case shall the removal include the natural mineral soil material which underlays the detrital material;

(d) Sediment removal shall not occur where the water depth above the unexcavated sediments exceeds three feet, or from areas which are located more than two hundred feet waterward of the existing water line, at the time of the Department of Environmental Protection Aquatic Plant Control Permit application site inspection;

(e) The distance along the shoreline from which sediment may be removed shall not exceed five hundred linear feet;

(f) All spoil material shall be deposited in an upland spoil site which is located and designed so as to prevent the escape of spoil material into waters of the State. The deposition of material into the upland spoil site shall either be through direct deposit, or following initial deposition into self-contained trucks for transfer to the upland spoil site, or as the final step following the use of a temporary stockpile site. Temporarily stockpiled material may be located within the landward extent of waters of the State for a period not to exceed twenty four hours, and must be located within unvegetated areas or within areas from which sediments are identified to be removed in the Department of Environmental Protection Aquatic Plant Control Permit. Temporary spoil stockpile sites shall not be located in areas of standing water, and must be placed and contained to prevent runoff into any areas of standing water;

(g) Dredged sites required by the Department of Environmental Protection to be revegetated shall be planted according to specifications as defined in the Department of Environmental Protection Aquatic Plant Control Permit. Only indigenous plant species obtained from a nursery source approved by the Department of Environmental Protection shall be planted. Dredged sites required by the Department of Environmental Protection Aquatic Plant Control Permit to be revegetated shall be planted at a minimum of fifty percent areal coverage within each revegetation area. The installation of vegetation required by the Department of Environmental Protection Aquatic Plant Control Permit shall be completed within one year following notice to use this general permit. Within the project area, at least sixty percent areal coverage of the planted species or of other plant species which are listed in Rule 62-301.400, F.A.C., and which are found to be acceptable by the Department of Environmental Protection under the requirements of the Department of Environmental Protection Aquatic Plant Control Permit, shall be achieved within two years following installation of the required vegetation. The restored site shall also be managed in a manner where cattail and other undesirable plants, as determined by the Department of Environmental Protection and specified in the Department of Environmental Protection Aquatic Plant Control Permit, shall not be allowed to constitute more than ten percent areal coverage during the term of the valid Department of Environmental Protection Aquatic Plant Control Permit;

(2) This general permit is subject to the general conditions of Rules 62-4.530 and 62-4.540, F.A.C., and the following specific conditions:

(a) All sediment and cattail removal operations must conform to conditions imposed by the Department of Environmental Protection Aquatic Plant Control Permit, and must be performed in a manner which does not cause violations of State water quality standards;

(b) The permittee shall use best management practices, such as properly installed and maintained turbidity curtains or similar devices, at all times during the execution of permitted activity to prevent violations of State water quality standards;

(c) Additional dredging activities are not authorized by this general permit and shall not occur except as authorized by statute or Department section.

(d) There shall be no filling or backfilling of any kind associated with the work other than incidental sediments which may be attached to vegetation which is planted pursuant to the valid Department of Environmental Protection Aquatic Plant Control Permit;

(e) Dredging activities, when they occur on state-owned bottom land, shall be in accordance with the sections promulgated under the authority of the Board of Trustees of the Internal Improvement Trust Fund.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.062, 403.087, 403.813, 403.814, 403.817, 403.912, 403.913 FS. History–New 12-17-90, Formerly 17-312.819.

## 62-312.822 General Permit for the Construction and Maintenance of Electric Power Lines by Electric Utilities.

(1) Definitions. Terms used in this section shall have the meaning specified below:

(a) “Access areas” shall mean areas which are cleared to allow equipment to reach existing electrical structures or the proposed location of electrical structures;

(b) “Existing facilities” shall mean existing power lines, substations or power plants;

(c) “Impact site” shall mean that portion of a wetland area within the right-of-way either surrounded by uplands within the right-of-way or lying between upland segments of the right-of-way within which clearing of vegetation to the ground is proposed to occur;

(d) “Maintenance” shall mean, for purposes of this section only, any activity conducted to preserve, restore, repair, remove, or replace an existing power line, so long as the activity does not involve dredge and fill activities beyond the removal of the existing structure and the installation of the new structure and the activity does not increase the voltage of existing power lines. An activity does not qualify as maintenance if it results in relocation of an existing structure or facility more than 10 feet in any direction from its original location. Maintenance shall not mean the construction of new power lines or the repair and replacement of existing structures that require dredge and fill activities to provide access to the site;

(e) “Power line” shall mean the conductors, supporting structures, and related hardware installed or maintained by electric utilities as defined in Section 366.02(2), F.S.;

(f) “Project” shall mean the proposed or existing power line for which use of the general permit is proposed;

(g) “Selective clearing” shall mean the cutting or control of vegetation by hand, herbicide, or mechanized equipment that minimizes soil compaction, to a height no lower than the water level at the time of cutting or ground level in areas without standing water. This would include removal of the cut trees from the wetland in cases where leaving the trees would preclude revegetation or impound waterflow. This shall not mean the non-selective aerial or broadcast application of herbicides;

(h) “Siting board” means the Governor and Cabinet as defined in Section 403.503(6), F.S.;

(i) “Wetlands” shall mean those areas within the landward extent of waters of the state as defined in Rule 62-301.400, F.A.C., and regulated under Sections 373.4145, F.S., and isolated and non-isolated wetlands regulated under Part IV of Chapter 373, F.S.; and

(j) “Work areas” shall mean areas surrounding the electrical support structures, towers, poles, and guy wires which must be cleared to enable equipment to install and maintain the power line.

(2) A general permit is granted to electric utilities for the construction of power lines, provided the following provisions are met;

(a) The project is not covered by a certification issued under Part II of Chapter 403, F.S.;

(b) All permanent fill shall be at grade. Fill shall be limited to that necessary for electrical support structures, including towers, poles, and guy wires, stabilizing backfill necessary for the aforementioned structures, and at-grade access roads limited to a width of 20 ft.;

(c) Access and work areas may be cleared to the ground, including removal of stumps as necessary; however, such clearance shall be limited to the following:

1. A linear access area of up to 25 ft. wide between electrical support structures;

2. An access area of up to 25 ft. wide from the edge of the power line right of way to electric support structures; and

3. Work areas around the electrical support structures, towers, poles, and guy wires;

(d) Vegetation in wetlands under the conductor and up to 20 feet on either side of the outermost conductor may be cut or removed by hand or by mechanized equipment to a height no lower than the soil surface. Any mechanized equipment that is used shall minimize soil compaction. Except for Brazilian pepper, Australian pine and Melaleuca, clearing in the remainder of the project right-of-way within wetlands shall be limited to selective clearing of vegetation which has an expected mature height of 14 ft. or more. During construction and while conducting normal maintenance activities, the permittee shall eradicate all Brazilian pepper, Australian pine, and Melaleuca from the wetland portion of the right-of-way. During the initial clearing event, and during subsequent maintenance cycles, EPA approved herbicides may be used on the following:

1. Vegetation growing within the area that was formerly cleared to the ground;

2. Vegetation with an expected mature height of over 14 ft. growing within the remainder of the right of way; and

3. Any specimen of exotic vegetation within the right of way;

(e) Not more than 15 acres of forested wetlands may be cleared to the ground within each 10 mile section of the project, whether or not filling activities occur within the wetlands. In sections where filling activities, as defined in Rule 62-312.020, F.A.C., occur, not more than 4 acres of forested wetland may be cleared to the ground within each 10 mile section of the project, with no more than one impact site exceeding 0.5 acres per 10 mile section. The one impact site which may exceed 0.5 acres shall not exceed 2.0 acres. Areas that are dominated by (90% or greater aerial coverage) exotic species shall not be included in the acreage calculation of clearing to ground of forested wetlands. The 10-mile sections shall be measured from the beginning of the project to the terminus of the project, or vice versa, and the sections shall not end in a wetland. In cases where the section does end in a wetland, the Department shall designate the closest landward edge of the wetland as the section terminus;

(f) Erosion and turbidity control methods shall be implemented as necessary to insure that state water quality standards for turbidity are met. The applicant shall submit to the Department, along with the notice of intent to use this general permit, a narrative that documents the applicant will use erosion and turbidity control methods that are consistent with generally accepted industry practice;

(g) Diversion and impoundment of surface waters shall be limited to incidental diversion during construction, and diversion which occurs around support structures, towers, guy wires, and poles;

(h) The proposed construction and clearing shall be conducted in a manner that does not adversely affect threatened or endangered species. The applicant shall submit to the Department, along with the notice of intent to use this general permit, a narrative summary of surveys that have been performed on the existence and potential existence of threatened and endangered species within and adjacent to the project, and the expected effects on these species; and

(i) The proposed construction and clearing shall not result in a permanent change to existing ground surface elevation.

(3) The maintenance of existing power lines as defined in paragraph (1)(d), and the clearing of vegetation in wetlands to construct new power lines that do not require the placement of structures in wetlands or other dredge and fill activities, does not require an individual or general permit.

(4) This general permit shall not apply to any portion of a project located in forested wetlands located within 550 feet from the mean or ordinary high water line of a named waterbody designated as an Outstanding Florida Water.

(5) The provisions of this general permit apply to the permitting requirements of the Department, any water management district, and any local government implementing Part IV of Chapter 373, F.S.

(6) This general permit shall be subject to the procedures and general conditions in Rules 62-4.530 and 62-4.540, F.A.C.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.814 FS. History–New 1-19-94, Formerly 17-312.822.

## 62-312.823 General Permit for Floating Vessel Platforms and Floating Boat Lifts.

(1) A general permit for all activities that are not otherwise exempt under Section 403.813(1)(s), F.S., is hereby granted to the owner of an individual, detached, private single-family residence to construct and remove floating vessel platforms or floating boat lifts at their residence, subject to the limitations and conditions described herein. All the criteria, conditions, and limitations contained herein are applicable solely for the purposes of this general permit.

(2) In artificially created waterways, floating vessel platforms or floating boat lifts are authorized at a dock or seawall associated with an individual, detached, private single-family residence on the contiguous uplands, provided that all of the following conditions are met.

(a) The cumulative over-water (including wetlands) surface area of the floating vessel platforms or floating boat lifts must not exceed 1,000 square feet, either alone or in combination with any other floating vessel platforms or floating boat lifts along the applicant’s shoreline.

(b) The floating vessel platforms or floating boat lifts, along with the vessel or vessels stored on the platforms or lifts:

1. Are located at least 10 feet inside of the applicant’s riparian rights lines, at least 10 feet inside of the applicant’s property lines, or if owned by someone other than the applicant or the state, at least 10 feet inside the applicant’s projected property lines, using the same methodology used to locate and project riparian rights lines; and

2. Do not extend more than 25 percent into the width of the artificially created waterway, as measured from approximate mean high water to approximate mean high water in tidal waters, or from approximate ordinary high water to approximate ordinary high water in non-tidal waters.

(c) For purposes of this general permit, an artificially created waterway shall be defined as a body of water that has been totally created by dredging, filling, or excavation, with the upper edges of its two sides above wetlands and other surface waters, including canal systems where the adjoining land use consists primarily of private, single-family residences.

(d) Floating vessel platforms and floating boat lifts shall be directly attached to docks or seawalls, as applicable, with lines, cables, chains, or collars around pilings in a manner that will not adversely affect submerged resources and without the use of bottom anchors.

(3) In waters that are not artificially created waterways, floating vessel platforms or floating boat lifts are authorized provided that all of the following conditions are met.

(a) The cumulative over-water (including wetlands) surface area of the floating vessel platforms or floating boat lifts must not exceed 675 square feet in waters that are not Outstanding Florida Waters, or 300 square feet within Outstanding Florida Waters, either alone or in combination with any other floating vessel platforms or floating boat lifts along the applicant’s shoreline.

(b) The floating vessel platforms or floating boat lifts, along with the vessel or vessels stored on the platforms or lifts:

1. Are located at least 10 feet inside of the applicant’s riparian rights lines, at least 10 feet inside of the applicant’s property lines, or if owned by someone other than the applicant or the state, at least 10 feet inside the applicant’s projected property lines, using the same methodology used to locate and project riparian rights lines; and

2. Do not extend into the waterbody by more than 25 percent of its width, as measured from approximate mean high water to approximate mean high water in tidal waters, or from approximate ordinary high water to approximate ordinary high water in non-tidal waters.

(c) The floating vessel platforms or floating boat lifts are authorized only at a dock or along a seawall associated with an individual, detached, private single-family residence on the contiguous uplands, where:

1. The dock or seawall was built in conformance with a permit issued under Sections 403.91 through 403.929, 1984 Supplement to the Florida Statutes 1983, as amended, or Part IV of Chapter 373, F.S., provided the permit, any associated sovereignty submerged lands authorization required under Chapter 253 or 258, F.S., and any required local governmental authorization did not reflect or require a defined mooring area. For purposes of this general permit, a defined mooring area shall be defined as one that is clearly delineated by mooring pilings or finger piers or which is otherwise clearly labeled as such on the drawings associated with the above permit or submerged lands authorization;

2. The dock or seawall was exempt under Section 403.813(1), F.S.; or

3. The dock or seawall was legally constructed prior to July 1, 1975, and is still functional.

(d) The location where the floating vessel platforms or floating boat lifts are to be placed must have less than a one percent coverage of light-dependent benthic resources, as determined according to subsection 62-312.823(6), F.A.C.

(e) Floating vessel platforms and floating boat lifts shall be directly attached to docks or seawalls, as applicable, with lines, cables, chains, or collars around pilings in a manner that will not adversely affect submerged resources and without the use of bottom anchors.

(4) Floating vessel platforms and floating boat lifts authorized under this general permit must be constructed, operated, and used so as to:

(a) Be for the exclusive use of residents (or their guests) of the individual, detached, single-family upland residence on the contiguous uplands, and must not be used for or in association with any multi-family, revenue-generating, or commercial purpose. For purposes of this general permit, an individual, detached, single-family residence does not include duplexes, triplexes or quadruplexes;

(b) Be used solely for the purpose of storing a vessel or vessels, such that the vessel or vessels are stored out of the water at all times when not in use;

(c) Be located in an area having, at all times, including when a vessel is being loaded or driven onto the floating vessel platform or floating boat lift, a minimum distance of at least two feet between the bottom of a fully loaded floating vessel platform or floating boat lift and either the bottom of the waterbody or the top of any submerged resources (at mature height for the area), whichever is less, as measured at mean low water in tidal areas or mean annual low water in non-tidal areas;

(d) Not cause significant adverse impacts to submerged lands, wetlands, shellfish areas, or other biological resources;

(e) Not cause or result in violations of water quality standards during construction or use, including when vessels are driven onto or off of the floating vessel platform or floating boat lift;

(f) Not be located within an aquatic preserve, as designated and described in Chapter 258, F.S.;

(g) Not be added to structures or located in areas where boat mooring is specifically prohibited under conditions of a permit issued in accordance with Sections 403.91 through 403.929, 1984 Supplement to the Florida Statutes 1983, as amended, or Part IV of Chapter 373, F.S., an authorization under Chapter 253 or 258, F.S., or other form of authorization issued by a local government;

(h) Not substantially impede the flow of water, adversely affect flood control, create a navigational hazard, or otherwise adversely impede navigation; and

(i) Comply with the general conditions in Rule 62-4.540, F.A.C., and, if on submerged lands owned by the Board of Trustees of the Internal Improvement Trust Fund, the conditions in subsection (5) of this general permit.

(5) Compliance with all the terms and conditions of this general permit, including the general conditions in paragraphs (5)(a) and (b) below, shall constitute authorization to use and occupy submerged lands owned by the Board of Trustees of the Internal Improvement Trust Fund. The following general conditions shall be binding upon the grantee, and shall be enforceable under Chapters 253 and 403, F.S.

(a) All floating vessel platforms or floating boat lifts under this general permit must be installed, operated and maintained in conformance with all the applicable terms and conditions of Rules 18-21.004 and 18-21.0041, F.A.C.

(b) All floating vessel platforms or floating boat lifts under this general permit that are located on any lands under the jurisdiction or management of the Department’s Division of Recreation and Parks must have prior written approval by the Division of Recreation and Parks, and such approval must be submitted with the notice to use this general permit.

(6)(a) Where required in accordance with paragraph 62-312.823(3)(d), F.A.C., notice to use this general permit shall include a report of a resource reconnaissance performed by a person with expertise in the field of marine science, aquatic ecology, or biology. The reconnaissance must be conducted during April, May, June, July, August, September, or October within one year prior to submittal of the notice to use this general permit, and shall encompass the submerged bottom where the floating vessel platform or floating boat lift is to be placed. The reconnaissance must document the absence or presence (including amount and height) of light-dependent resources, which, for purposes of this general permit, shall consist of: submerged or emergent rooted aquatic macrophytes, and attached marine macro-algae. The report also must document the water depths at mean low water (in tidal waters) or mean annual low water (in non-tidal waters) at the nearshore edge, center, and farshore edge of the proposed location of the floating vessel platform or floating boat lift. The report shall include: a statement signed by the person performing the reconnaissance to the effect that the findings in the report accurately describe the conditions as they existed during the reconnaissance; a description of the date, time, and climatic conditions when the reconnaissance was done; the name of the person or persons performing the reconnaissance and their qualifications; a scaled or fully dimensioned sketch that clearly delineates the area inspected, including both a depiction of the configuration of the proposed floating vessel platform or floating boat lift in relation to the area inspected, any identifying features (including existing and proposed structures along the shoreline); and any notes or other specific findings that the person performing the reconnaissance desires to include. Resource presence or absence shall be documented and mapped using standard field methods. When present, the percent cover and height of the light-dependent resources shall be determined and reported using the resource survey procedures described in paragraph (6)(b). All methods used shall be clearly described in the report of the resource survey.

(b) Resource surveys shall be performed using the following procedures:

1. Resource percent cover – A visual estimate of the percent cover of the light-dependent resources on the bottom directly beneath the footprint of the area to be occupied by the floating vessel platform or floating boat lift shall be reported and depicted on the sketch required in paragraph (6)(a). When resources are present, their location shall be shown on the sketch and dominant community types labeled (such as by dominant macrophyte species or as “attached macro marine algae community”). Percent cover estimates shall be based on either stem-count or canopy-cover standard methodologies published in vegetation monitoring literature, such as J. Braun-Blanquet, Plant Sociology: The Study of Plant Communities (Hafner Publishing, New York 1972).

2. Height of resources – The average mature height, for the general waterbody, of each of the resources identified in subparagraph (6)(b)1., above, shall be provided. Alternatively, where the average mature height of the resources for the waterbody is not known, the height of the tallest resource specimen shall be reported (to the nearest centimeter) for each different community type within the footprint where the floating vessel platform or floating boat lift is to be located. For macrophyte resources, the height shall be determined by combing with fingers the blades of each macrophyte species vertically up along a meter stick, and measuring the composite or average height of the blades.

(7) Permittees are advised that all in-water activities associated with construction or replacement of a floating vessel platform or floating boat lift, and all vessel operation within a manatee “No Entry Zone” or a “Motorboat Prohibited Zone” must be in compliance with Chapter 68C-22, F.A.C.

(8) The notice to use this general permit (Form 62-312.900(1)) must contain an attached statement from the applicant certifying that the applicant contacted the county and applicable municipal local government with jurisdiction over the dock or seawall to which a floating vessel platform or floating boat lift is to be attached, and the county and municipal local government verified that the applicant’s floating vessel platform or floating boat lift will not be located in an area where the local government has issued an authorization prohibiting boat mooring or defining a boat mooring area.

(9) This general permit does not place additional limits or restrictions on the construction, operation, and maintenance of floating vessel platforms and floating boat lifts that otherwise are exempt under Section 403.813(1), F.S.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1), 403.813(1), 403.814(1) FS. Law Implemented 253.04, 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.813(1), 403.814(1) FS. History–New 8-4-05.

## 62-312.824 General Permit to Municipalities to Pave Existing Municipally Owned and Maintained Roads, including the Repair and Replacement of Bridges that are Part of the Roadway.

A general permit is hereby granted to municipalities to pave existing municipally owned and maintained roads that lack a permanent pavement surface, such as concrete or asphalt. This includes: the repair and stabilization of such roads in preparation of paving; the repair or replacement of bridges and culverts that are part of the roadway; construction or alteration of associated stormwater management systems; other work reasonably necessary to pave the road; and the construction, alteration, operation, and maintenance of systems and works authorized under this general permit, provided all of the terms and conditions below are met.

(1) The existing road and any associated bridges:

(a) Must have been constructed prior to January 1, 2002, and in continuous use as a municipally owned and maintained road (including any associated bridge or bridges) thereafter. For the purposes of this general permit, municipal ownership shall include roads that have been presumed to be dedicated in accordance with Section 95.361, F.S.; and

(b) Must not: be located in, on, over; directly discharge to; or significantly degrade Outstanding Florida Waters.

(2) The proposed road and any bridge work, together:

(a) Must not exceed two traffic lanes;

(b) Must not expand the number of existing traffic lanes, except that any single-lane bridges may be widened to two travel lanes, provided the bridge widening does not exceed that reasonably necessary to connect the bridge with the road being paved;

(c) Must not result in a total paved roadway surface (including travel lanes, safety shoulders, and bike paths) that is more than 32 feet wide, or 36 feet wide for bridges;

(d) Must be constructed, operated, and maintained within roadway and bridge right-of-way owned by the municipality, including where ownership is through presumed dedication in accordance with Section 95.361, F.S.;

(e) Must not realign the roadway;

(f) Must not involve any more dredging or filling of surface waters of the state than is reasonably necessary to prepare the roadway for paving, including all work to repair, extend, or replace any culverts, other drainage structures, and bridges associated with the roadway, and to construct or reconfigure surface water management systems associated with the paving. However, the amount of such dredging and filling, both temporary and permanent, must not impact more than 0.5 acre of surface waters of the state for a total and complete project, with the allowance of an additional 0.5 acre of work in roadside ditches constructed through uplands. A “total and complete project” shall consist of the total amount of work needed to pave, and prepare for paving, all unpaved segments of a single named or number (state road number) roadway. The sum of all wetland and other surface water impacts associated with phases of paving the named or numbered roadway must not exceed the above acreage limits. However, the total acreage limits for this general permit shall not include the work conducted to prepare the roadway for paving when the preparation is done in accordance with:

1. All the terms and conditions of routine custodial maintenance;

2. An exemption adopted under Part IV of Chapter 373, F.S.;

3. An exemption contained in Section 403.813(1), F.S.; or

4. Any other general permit adopted under Part IV of Chapter 373, F.S.;

(g) Must not adversely affect wetlands or other surface waters outside of the footprint of any dredging and filling;

(h) Must not reduce existing water conveyance or treatment capacity or adversely affect existing offsite drainage patterns;

(i) Must not cause adverse upstream or downstream flooding or drainage; and

(j) Must not adversely affect receiving waters.

(3) Activities conducted under this general permit must comply with the general conditions for general permits contained in Rule 62-4.540, F.A.C., and all the specific conditions in paragraphs (a) through (j), below.

(a) Roadside swales, establishment of permanent vegetative cover, or other effective means of stormwater management within the right-of-way must be incorporated into the project, and must be designed, constructed, operated and maintained to prevent increases in pollution loading or changes in the point of discharge that can cause adverse impacts to receiving waters or offsite property.

(b) No debris from the removal of existing roadway, bridge, culvert, and other surface water management features shall be placed within surface waters of the state.

(c) Creosote must not be a component of any pilings, pile jackets, headwalls, bulkheads, or other structural components used in roadway, bridge, culvert, or other surface water management structures.

(d) Any bridge or culvert must not cross a stream or other watercourse having a drainage area upstream of the work of more than ten (10) square miles.

(e) Bridges and other water conveyance features must be designed, constructed, operated, and maintained to convey normal flows and overtopping during a 25-year, 24-hour storm event.

(f) Best management practices for erosion and sediment control must be used to prevent water quality violations during and after construction. These shall include a construction-phase water management and erosion control plan that is designed and implemented to include site-specific measures adapted from practices and procedures described in the following publications that are adopted herein and incorporated by reference:

1. The guidelines set forth in Chapter 6 of The Florida Development Manual: A Guide to Sound Land and Water Management, Vol. II, Florida Department of Environmental Regulation, June 1988; and

2. The provisions set forth in The Florida Stormwater, Erosion, and Sediment Control Inspector’s Manual, Florida Department of Environmental Protection and Florida Department of Transportation, Fifth Impression, June 2005.

(g) Temporary or permanent vegetative cover must be established on both sides of the pavement within the road right-of-way and along water conveyances as soon as practicable, but in no case more than seven (7) days after construction activities have ceased in portions of the site where construction activities have temporarily or permanently ceased.

(h) Activities conducted and authorized by this permit must be operated and maintained by the municipality for the life of the system.

(i) Applicants are advised that the drawings, materials, and statements above, including any submitted construction plans and supporting calculations, must be signed, sealed, and dated by an appropriate registered professional in accordance with Sections 373.117 and 403.0877, F.S., and Chapter 471, 472, 481, or 492, F.S., when the design of the system requires the services of such registered professional. For purposes of this rule, an “appropriate registered professional” means a professional registered in Florida with the necessary expertise in the fields of hydrology, drainage, flood control, erosion and sediment control, and stormwater pollution control to design and certify stormwater management systems. Examples of appropriate registered professionals are professional engineers licensed under Chapter 471, F.S., professional landscape architects licensed under Chapter 481, F.S., professional surveyors and mappers licensed under Chapter 472, F.S., and professional geologists licensed under  Chapter 492, F.S.

(j) The performance of routine custodial maintenance of structures and activities within the roadway alignment, such as replacement of culverts in kind to their former size, grade, and elevation, and the performance of activities qualifying for an exemption under Part IV of Chapter 373 or Section 403.813(1), F.S., such as maintenance of ditches and swales to prior design specifications in accordance with Section 403.813(1)(g) or (j), F.S., or under other general permits adopted under Chapter 62-312, F.A.C., may be conducted to prepare the roadway for paving in advance of using this general permit, and any dredge and fill volumes associated with such work shall not be included within the limits established in paragraph (2)(f) of this general permit.

(4)(a) In accordance with Section 403.813(1)(t), F.S., this general permit shall not require submittal of a fee.

(b) A separate stormwater permit under Chapter 62-25, F.A.C., is not required for activities that qualify under the terms and conditions of this general permit.

(5) Notices to use this general permit must be submitted to the Department on form 62-312.900(6), F.A.C. In addition to the information required on that form, this notice must also include the materials required in paragraphs (5)(a) or (b), below.

(a) For roads that are not subject to overtopping by a one percent-chance storm event and do not require: any fill to elevate the roadway (other than the base and pavement up to a maximum height of eight (8) inches, and sub-base work provided there is no net addition of fill); any grading of side slopes; any alteration, expansion, or modification of drainage structures and bridges; any work in surface waters of the state; or more than minor shoulder work to level the shoulders to meet the new pavement:

1. A project description that describes the work to be done, including a statement signed by the responsible official in the municipality that the proposed activity will comply with the limitations in paragraph (5)(a) herein, and all the other terms and conditions of this general permit;

2. A location map in sufficient detail to enable persons who are unfamiliar with the site to find the road to be paved, including the beginning and ending limits of the proposed activity;

3. A fully dimensioned or scaled plan view, and fully dimensioned or scaled cross sectional views that clearly depict and distinguish the road right-of-way and the footprint of existing and proposed work at typical sections, including the width, height, and slopes of existing and proposed grades; thickness of sub-base, base, and pavement layers; and shoulder work; and

4. A copy of a Federal Emergency Management Agency flood insurance rate map or a map signed and sealed by an appropriate registered professional that demonstrates that the road segments to be paved are not subject to overtopping by a one percent-chance storm event.

(b) For all other roads to be paved under this general permit:

1. All the information requested in paragraph (5)(a) above, plus a summary of the total amount of proposed dredging and filling in surface waters of the state (in square feet or acreage);

2. A fully dimensioned or scaled plan view that clearly depicts and distinguishes all areas of proposed dredging and filling, the limits of proposed surface water management systems, and the location of all culverts, other drainage structures, and bridges that are proposed to be altered;

3. Fully dimensioned or scaled cross sections that clearly depict and distinguish dredging and filling at typical sections, including at culvert, other drainage system, and bridge modifications;

4. Fully dimensioned or scaled typical cross sections of surface water management system alterations;

5. An erosion and sedimentation control plan demonstrating compliance with the provisions of paragraphs (3)(f) and (g) of this general permit; and

6. If design of the project requires the services of an appropriate registered professional in accordance with Sections 373.117 and 403.0877, F.S., and Chapter 471, 472, 481, or 492, F.S., all supporting drawings, materials, statements, construction plans, and calculations that are required to be signed, sealed, and dated by the registered professional.

(c) Notice to use this general permit is not required for subsequent routine custodial maintenance activities that may be required to the systems authorized under this general permit.

(6) Projects that have previously qualified under the exemption in Section 403.813(1)(t), F.S., following notice to the Department, but have not been fully implemented as of the effective date of this general permit, are authorized under this general permit to be completed under the terms of that exemption until March 15, 2008.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1), 403.813(1)(t) FS. Law Implemented 373.414(11)-(16), 373.4145, 403.061, 403.087, 403.088, 403.813(1)(t), 403.814, 403.817, 403.912, 403.913, 403.918 - .921, 403.931 FS. History–New 3-15-07.

# 62-312.825 General Permit to U.S. Army Corps of Engineers for Environmental Restoration or Enhancement Activities.

(1) A general permit is hereby granted to the U.S. Army Corps of Engineers for the construction, alteration, operation, and maintenance of systems to implement environmental restoration or enhancement activities. In order to qualify for this general permit, the decision documents for the environmental restoration or enhancement activity must have been coordinated through the process described in Section III of the Interagency Coordination Agreement for Civil Works, Florida Department of Environmental Protection, United States Army Corps of Engineers Jacksonville District, United States Army Corps of Engineers Mobile District (February 28, 2006), which is hereby adopted and incorporated by reference. In addition, the environmental restoration or enhancement activity must be funded or conducted by the U.S. Army Corps of Engineers, and be authorized under:

(a) Section 204 of the Water Resources Development Act of 1992, as amended through January 24, 2002 (Beneficial Uses of Dredged Material), which is hereby adopted and incorporated by reference;

(b) Section 206 of the Water Resources Development Act of 1996, as amended through January 24, 2002 (Aquatic Ecosystem Restoration), which is hereby adopted and incorporated by reference; or

(c) Section 1135 of the Water Resources Development Act of 1986, as amended through January 24, 2002 (Project Modifications for Improvement of Environment), which is hereby adopted and incorporated by reference.

(2) The following shall not be eligible for this general permit:

(a) Activities on the sandy beaches of Florida fronting the Atlantic Ocean, the Gulf of Mexico or the Straits of Florida that extend seaward of the mean high water line, including beach restoration, nourishment, disposal of dredged material, beach or inlet structures, or excavation;

(b) Activities proposed to implement mitigation for another activity that requires a permit under Part IV of Chapter 373, F.S., a water quality certification, or coastal zone consistency concurrence;

(c) Activities that involve replacing a natural biological community type with a different type of biological community, such as filling bay bottom to create a marsh, except:

1. To restore or enhance a community that was previously damaged or destroyed by human activities, such as filling a dredged channel to the elevations and community types that existed before dredging; or

2. To restore or enhance a community type that was previously existing, but has been lost through avulsion when it is determined to be in the public interest; or

3. To reduce or eliminate populations of exotic and nuisance species with the goal of enabling replacement by natural, endemic communities;

(d) Activities that adversely affect animal species that are listed as endangered, threatened or of special concern in Rule 68A-27.003, 68A-27.004, or 68A-27.005, F.A.C., and plant species listed in 50 Code of Federal Regulation 17.12, when such plants are located in a wetland or other surface water;

(e) Activities that involve the use of flocculating agents such as polymers and alum;

(f) Activities that would adversely affect historic properties listed in or eligible for listing in the National Register of Historic Places under the provisions of Section 267.061, F.S.

(3) Prior to submittal of the notice to the agency to use this general permit as required and described in paragraph (5)(a), the environmental restoration or enhancement activity must be included in a Feasibility Report, Reevaluation Report, Letter Report or other equivalent Federal environmental decision document that has been reviewed by the state of Florida. Documentation that the state has found the environmental restoration or enhancement activity to be consistent with the Florida Coastal Management Program must be submitted with the notice to use this general permit.

(4) This general permit shall be subject to the following additional provisions and limitations:

(a) Activities authorized under this general permit shall not be available for use as future mitigation credit for a separate activity that requires a permit under Part IV of Chapter 373, F.S., a water quality certification, or a coastal zone consistency concurrence;

(b) The activity must be conducted in a manner that will not adversely affect the value of functions provided to fish and wildlife by wetlands or other surface waters;

(c) The activity must not cause adverse secondary impacts to the water resources, must not adversely impact the maintenance of surface or ground water levels or surface water flows established pursuant to Section 373.042, F.S., must not cause adverse impacts to a work of the District established pursuant to Section 373.086, F.S., and must not adversely affect properties outside the area to be enhanced or restored;

(d) The activity must be capable, based on generally accepted engineering and scientific principles, of being performed and of functioning as proposed;

(e) The activities must not be for the primary purpose of providing or enhancing recreation or other public uses of the lands that are enhanced or restored under this general permit. However, nothing in this general permit shall prohibit areas that are enhanced or restored from being made available for compatible public recreation activities. However, the construction, alteration, operation, removal, maintenance, or abandonment of public recreational facilities, such as parking lots, roads, trails, boardwalks, docks, piers, observation decks, kiosks, and visitor’s centers, or any surface water management system servicing those facilities, are not authorized under this general permit and must be authorized in accordance with Part IV of Chapter 373, and Chapters 253 and 258, F.S., prior to their construction and use.

(f) The activity must not violate the water quality standards set forth in Chapters 62-4, 62-302, 62-520, 62-522, and 62-550, F.A.C., including the anti-degradation provisions of paragraphs 62-4.242(1)(a) and (b), subsections 62-4.242(2) and (3), and Rule 62-302.300, F.A.C., and any special standards for Outstanding Florida Waters and Outstanding National Resource Waters set forth in subsections 62-4.242(2) and (3), F.A.C. Appropriate measures shall be used to control runoff and discharges from the site, such as stabilization of disturbed sediments and soils, and effective deployment and maintenance of turbidity and silt control devices during all phases of construction, and as necessary during operation and maintenance of the system.

(5)(a) The U.S. Army Corps of Engineers must file a notice, using Form 62-312.900(6), describing the proposed activities and providing plans and other information necessary to evaluate whether the activities qualify under the terms and conditions of this general permit, which shall specifically also include:

1. A copy of the Coastal Zone Consistency Concurrence documentation referenced in subsection (3) of this general permit;

2. Documentation of the appropriate federal authorization under which funding is expected; and

3. Copies of the environmental documents that have been developed as part of the early coordination process described in Section III of the Interagency Coordination Agreement for Civil Works, Florida Department of Environmental Protection, United States Army Corps of Engineers Jacksonville District, United States Army Corps of Engineers Mobile District, dated February 28, 2006.

(b) The Department will provide written notification to the U.S. Army Corps of Engineers whether the proposed activity qualifies for this general permit within 30 days of submittal of the written notice, or 30 days after submittal of any errors or omissions needed to correct the notice, as provided in subsection 62-343.090(1), F.A.C. The proposed activity shall not commence until the Department has provided the applicant with an affirmative, written confirmation that the proposed activity qualifies for this general permit.

(6) The Corps is advised that authorization in accordance with Chapters 253 and 258, F.S., and Chapters 18-20 and 18-21, F.A.C., and the Interagency Coordination Agreement for Civil Works, Florida Department of Environmental Protection, United States Army Corps of Engineers Jacksonville District, United States Army Corps of Engineers Mobile District (February 28, 2006), to use sovereignty submerged lands must be obtained from the Board of Trustees of the Internal Improvement Trust Fund prior to any construction authorized under this general permit.

Specific Authority 373.026, 373.043, 373.044, 373.118, 373.406, 373.4145 FS. Law Implemented 373.026, 373.043, 373.046, 373.118, 373.403, 373.413, 373.4145, 373.416, 373.418, 373.419, 373.422, 373.423, 373.426 FS. History–New 12-5-06.

## 62-312.900 Wetland Resource Forms.

The provisions of this part shall only apply to activities in the geographical territory of the Northwest Florida Water Management District and to activities grandfathered under Sections 373.414(9), (11), (12)(a), (13), (14), (15) and (16), F.S. The forms and instructions used by the Department in the Wetland Resource Management Program are adopted and incorporated by reference in this section. The forms are listed by rule number, which is also the form number, and with the subject title and effective date. Copies of forms may be obtained by writing to the Bureau of Submerged Lands and Environmental Resources, MS 2500, Department of Environmental Protection, 2600 Blair Stone Road, Tallahassee, Florida 32399-2400, any local district or branch office of the Department.

(1) Joint Application for Works in the Waters of Florida, October 30, 1991.

(2) Joint U.S. Army Corps of Engineers/Florida Department of Environmental Protection Emergency Permit, November 30, 1982.

(3) Recognition of Jurisdiction Under Chapters 253 and 403, Florida Statutes, November 30, 1982.

(4) Application Guide for Deepwater Port Maintenance Dredging and Disposal 25-Year Permit, March 31, 1984.

(5) Application for Long-Term Permits, October 16, 1984.

(6) Notice of Intent to Construct Works Pursuant to a Wetland Resource General Permit, October 30, 1991.

Specific Authority 373.414(11)-(16), 373.4145, 403.805(1) FS. Law Implemented 120.53(1), 373.409, 373.413, 373.414(9), (11), (12)(a), (13), (14), (15), (16), 373.4145, 373.416, 373.418, 403.0875, 403.814 FS. History–New 11-30-82, Amended 3-31-84, 10-16-84, 5-15-88, Formerly 17-1.203, 17-12.900, Amended 10-9-90, 6-5-91, 10-30-91, 5-25-92, Formerly 17-312.900, Amended 10-3-95.